## Slide 1: Reliable high-speed Grid data delivery using IP Multicast
Karl Jeacle & Jon Crowcroft
firstname.lastname@cl.cam.ac.uk

## Slide 2: Future Grid Context

## Slide 3: Rationale
Would like to achieve high-speed bulk data delivery to multiple sites
Multicasting would make sense
Existing multicast research has focused on sending to a large number of receivers
But Grid is an applied example where sending to a moderate number of receivers would be extremely beneficial

## Slide 4: Multicast availability
Deployment is a problem!
    Protocols have been defined and implemented
    Valid concerns about scalability; much FUD
    “chicken & egg” means limited coverage
Clouds of native multicast
    But can’t reach all destinations via multicast
    So applications abandon in favour of unicast
    What if we could multicast when possible…
    …but fall back to unicast when necessary?

## Slide 5: Planetlab test
Planetlab >100 “random” sites
Key value – if have account on 1 site, have on all
Tested multicast deployment from all to all
Results mixed
Note chance of tx being about to use mcast is to k out of r non zero but chance of all paths to all receivers working is close to zero
(e.g. p of AS doing mcast, average path len a Ass, 1- (1-p)^a per receiver -> [1-(1-p)^a]^r
For r receivers al working, but a lot better for k<r

## Slide 6: Multicast TCP?
TCP
  “single reliable stream between two hosts”
Multicast TCP
  “multiple reliable streams from one to n hosts”
  May seem a little odd, but there is precedent…
    SCE – Talpade & Ammar
    TCP-XMO – Liang & Cheriton
    M/TCP – Visoottiviseth et al

## Slide 7: ACK implosion

## Slide 8: Building Multicast TCP
Want to test multicast/unicast TCP approach
  But new protocol == kernel change
  Widespread test deployment difficult
Build new TCP-like engine
  Encapsulate packets in UDP
  Run in userspace
  Performance is sacrificed…
  …but widespread testing now possible

## Slide 9: TCP/IP/UDP/IP
Sending
Application
TCP
IP
UDP
IP
Receiving
Application
TCP
IP
UDP
IP
If natively implemented
test deployment

## Slide 10: TCP engine
Where does initial TCP come from?
Could use BSD or Linux
  Extracting from kernel could be problematic
More compact alternative
  lwIP = Lightweight IP
  Small but fully RFC-compliant TCP/IP stack
lwIP + multicast extensions = “TCP-XM”

## Slide 11: TCP
SYN
SYNACK
ACK
FIN
FIN
ACK
ACK
ACK
DATA
Sender
Receiver

## Slide 12: TCP-XM
Sender
Receiver 1
Receiver 2
Receiver 3

## Slide 13: TCP-XM connection
Connection
  User connects to multiple unicast destinations
  Multiple TCP PCBs created
  Independent 3-way handshakes take place
  SSM or random ASM group address allocated
    (if not specified in advance by user/application)
  Group address sent as TCP option
  Ability to multicast depends on TCP option

## Slide 14: TCP-XM transmission
Data transfer
  Data replicated/enqueued on all send queues
  PCB variables dictate transmission mode
  Data packets are multicast
  Retransmissions are unicast
  Auto switch to unicast after failed multicast
Close
  Connections closed as per unicast TCP

## Slide 15: TCP-XM reception
Receiver
  No API-level changes
  Normal TCP listen
  Auto-IGMP join on TCP-XM connect
  Accepts data on both unicast/multicast ports
  tcp_input() accepts:
    packets addressed to existing unicast destination…
    …but now also those addressed to multicast group

## Slide 16: What happens to the cwin?
Multiple receivers
  Multiple PCBs
  Multiple congestion windows
Default to min(cwin)
  i.e. send at rate of slowest receiver
Avoid by splitting receivers into groups
  Group according to cwin / data rate

## Slide 17: API changes
Only relevant if natively implemented!
Sender API changes
    New connection type
    Connect to port on array of destinations
    Single write sends data to all hosts
TCP-XM in use:
conn = netconn_new(NETCONN_TCPXM);
netconn_connectxm(conn, remotedest, numdests, group, port);
netconn_write(conn, data, len, …);

## Slide 18: PCB changes
Every TCP connection has an associated Protocol Control Block (PCB)
TCP-XM adds:
struct tcp_pcb {
…
struct ip_addr group_ip; // group addr
enum tx_mode txmode; // uni/multicast
u8t nrtxm; // # retrans
struct tcp_pcb *nextm; // next “m” pcb
}

## Slide 19: Linking PCBs
*next points to the next TCP session
*nextm points to the next TCP session that’s part of a particular TCP-XM connection
Minimal timer and state machine changes
next
nextm
M1
next
nextm
U1
next
nextm
M2
next
nextm
M3
next
nextm
U2

## Slide 20: TCP Group Option
New group option sent in all TCP-XM SYN packets
Presence implies multicast capability
Non TCP-XM hosts will ignore (no option in SYNACK)
Sender will automatically revert to unicast
1 byte
1 byte
4 bytes
kind=50
len=6
Multicast Group Address

## Slide 21: Initial tests: speed

## Slide 22: Initial tests: efficiency

## Slide 23: Future
To do:
  Protocol work
    Parallel unicast / multicast transmission
    Fallback / fall forward
    Multicast look ahead
    Multiple groups
    Globus integration
  Experiments
    Local network
    UK eScience centres
    Intel PlanetLab

## Slide 24: eScience volunteers…
In place
  Cambridge
  Imperial
  Manchester?
  UCL
Nearly
  Oxford
  Southampton
Not quite
  Belfast
  Cardiff
  Daresbury
  Newcastle
Not at all
  Rutherford
  Edinburgh
  Glasgow

## Slide 25: Planetlab europe
Talking to intel about more EU sites doing planetlab
Possibly specialise (or enhance) To add e.g. 3G wireless and WiFi at site)
Could allow more local experimentation without the usual “Big Science” hassle of engaging with NRN and Geant
Also have a lot of EU Datagrid sites already
Some with good (netherlight/starlight/uklight) connectivirt to each other and US
Can do some Big Science networking
One goal is to see if TCP-XP can go faster than FAST TCP 

## Slide 26: Hybrid, Purist, Overlay
Pure argument is to leave incentive for subscriber to demand and provider to deploy ip native mc
Hasn’t worked (15 years after first had idea)
Hybrid schemes not much examined (SCE prob. One of few)
Hybrid retains understanding gained in unicast and mcast incentives
Overlay requires lots of new mechanisms to be debugged
P2P promising, but side by side problems alluded to in Diot’s anti-deployment paper still apply
Probably good for “grid”like users (shared incentive to forward for others)

## Slide 27: All done!
Thanks for listening!
Questions?