## Slide 1: Proactive Multi-path Routing
Jing Shen, Jon Crowcroft
State Key Lab of CAD&CG
ZheJiang University
P.R.China
& University of Cambridge, Computer Laboratory, UK

## Slide 2: Outline
Challenge in Network Provisioning
Why do we always fail with TE&QoS?
Theoretical Analysis of Traffic Transmission
Proactive Multi-path Routing
Performance Evaluation
Discussion

## Slide 3: Challenge in Network Provisioning
End-to-End QoS
Load Balancing
There are times that a part of network is congested while adjacent part(s) is/are idle!
Notes: End-to-end QoS asks a well facilitated network infrastructure, and a well designed routing system
Load balancing asks the auto-adjustment of load distribution over network
We only have SPF based routing protocols which rely on static link state information
Internet traffic grows exponentially and distribute un-uniformly ISPs rely on predication of network usage to upgrade their network

## Slide 4: Solutions we are using
Congestion Control - RED - ECN
Route Optimization - Link Weight Optimization - Profile Based Routing
They are not effective in high speed networks!
Notes: For e2e congestion control mechanism in high speed network:
1) network must be able to buffer huge amount of traffic; 2) Before end system react burst introducing congestion
may have finished; 3) for multimedia applications on UDP, more burden will be introduced to high level protocols
For Route Optimization:
1)Both solutions rely on long-run observation, and could not deal with congestion introduced by burst
2)The frequency of optimization is also a problem

## Slide 5: Why do we often fail in network provisioning?
Traffic properties iare overlooked in routing mechanism design
Routing mechanism must be designed with traffic
characteristics, network connectivity, administration in mind.
Notes: Traffic Characteristics:
self-similar in flow/packet arrivals
Heavy-tailed flow size distribution
Un-uniformed distribution in networks

## Slide 6: Theoretical Analysis

## Slide 7: Bursty Traffic Transmission in High Speed Network (Xun Su)
or, k indicates a set of links whose load are below the threshold y*
Notes: 1) There is n disjoint links between source s and destination t, each link with same capacity c ;
2) Flow arrives to s for destination t with Lamda(sd), and average duration time is miu(-1)
3) Traffic is dispersed equally onto k links
Indication: network node should route its connection requests actively over a large set of paths if these requests are mostly short and arrive frequently, or direct its connection requests to the least loaded path if these requests are mostly long and arriving infrequently.

## Slide 8: Indications of Theoretical Analysis
Notes: Internet Traffic could be taken as a mixture of long-lived but less frequent flows and a large amount of bursty flows
Long lived flows should be transferred along the least burdened path
Bursy flows should be dispersed onto multiple paths
Because, most of current algorithm measure link “length” by considering its available capacity, least burdened
Path usually means “the shortest path”.

## Slide 9: Some Key Problems in Traffic Dispersion
Do the k paths need to be disjoint?
How could the path set to keep up with time varying network status?
  No
Path computation could be scheduled periodically or triggered by some threshold conditions
Notes: The k path need not to be totally disjoint
a) the target of traffic dispersion is to make use of more resource, when a new path is calculated, it’s
ensured new resource is introduced
b) overlapping between logical paths between different source-destination pair is unavoidable
c) if we constraint path computing to disjoint paths, node with one outgoing link will always fail although
there is idled resource
2. The frequency of path computation should be carefully optimized to avoid route flapping

## Slide 10: Some Key Problems in Traffic Dispersion (cont.)
How could traffic be dispersed onto multiple paths with different quality?
How many paths should be used in dispersity routing?
  Evaluate path quality carefully
  Dispersion policy should be designed with full consideration on path quality, service equality and load balancing requirements
  Two or three recommended values
Notes: Xun suggested a dynamic path set relating to flow arrival rate, duration time, link update period;
It’s difficult to implement such a result in networks.
Most of current networks have a diameter less than 10 and node degree is usually below 4, so 2 or
3 recommended values may be reasonable.

## Slide 11: Proactive Multi-path Routing

## Slide 12: Basic ideas
Key decisions
  Spreading traffic flows according to path quality
  Migrating long-lived flows only if QoS could be guaranteed
Advantages
  More resource for burst absorbing
  Flow distribution is optimized
  Fewer link state update messages
Notes: Traffic is dispersed at flow level
Flows are assigned to logical path according to their quality in traffic transmission
3) Two possible ways to improve network performance
a) resource reservation for long-lived flows b) optimizing routes for long-lived flows on basis of traffic dispersion
trunk reservation for long-lived flows are not adopted for 3 reasons:
1) if a part of resource is reserved for long-lived or burst, it’s difficult to estimate how much resource should be
reserved and overhead of link state maintenance is high;
2) it’s difficult to predict whether a link carries a shortest path in dynamic routing system, if resource is to be
reserved along the shortest path
3) long-lived flows could be assigned to shortest path if path quality metric and dispersion policy is chosen
carefully

## Slide 13: Key Components of P.M.R.
Compute and establish K paths
Path evaluation and traffic dispersion
Detecting long-lived flows and rerouting

## Slide 14: Compute and Establish K paths
Link Metrics
  Bandwidth related metric
Algorithm
  Extended Dijkstra or labling algorithm
Path Establishment
  CR-LDP/RSVP-TE in MPLS networks
  Signaling as that of MPOA in ATM networks
Periodical Re-computation

## Slide 15: Path evaluation and traffic dispersion
Evaluation Policy | Quality Evaluation | Flow Assignment Policy
“random” | Each path is considered the same | Random
“wrr-bw” | Bottleneck_bandwidth | W.R.R.
“wrr-bp” | Bottleneck_bandwidth/path_cost | W.R.R.
“wrr-bh” | Bottleneck_bandwidth/hop_count | W.R.R.
Notes: “random” emphasizes the equal treating between paths; W.R.R. stands for weighted round robin
“wrr-bw” emphasizes throughput of a e2e logical path;
“wrr-bp” emphasizes e2e transmission delay;
“wrr-bh” emphasizes resource consumed;
Path quality is evaluated periodically or triggered by some threshold conditions, with our approach triggered policy
Is preferred, that is when number of links announcing new state reach a threshold percentage of total number of links.

## Slide 16: Detecting long-lived flows and rerouting
Flow is identified by information in packet header
Edge router monitor flow transmission
Two or more feature flow identification is preferred

## Slide 17: State Machine of MPR

## Slide 18: Performance Evaluation

## Slide 19: Simulation Setup
Ingress | Egress | Hop Distance | Arrival rate
1 | 12 | 4 | 10.6
0 | 14 | 4 | 10.6
2 | 17 | 4 | 10.6
9 | 11 | 4 | 10.6
6 | 17 | 3 | 10.6
4 | 13 | 3 | 10.6
10 | 8 | 2 | 10.6
Notes: Bilateral link capacity: 155 bandwidth request: [1.14,2.46]
Link state update period: 10s
Hold time: Pareto distributed, Poisson arrival process

## Slide 20: Network Throughput ( non-uniformed traffic pattern)
Notes: performance improvement of our scheme under non-uniformed traffic pattern is evident

## Slide 21: Network Throughput (uniformed traffic pattern)

## Slide 22: Stale Link State information (non-uniformed traffic pattern)
Notes: 1) although both methods succeed in path finding performance of single path routing is much more
sensitive to inaccuracies in link-state information
2) when link state update period increases performance of our approach is more stable than that of
single path routing either in absolute measurement or in relative measurement.

## Slide 23: Traffic Aggregation
Notes: Observation:
as aggregation increases advantage of proactive multipath routing over single path routing dismisses
somewhat but still significant

## Slide 24: Effect of Hot Spot
Notes: Method:
keeping total ejection rate the same, node 1 sends a part of its traffic to node 17 at a rate of 3.6 flows
per second, and so does node 0 to node 13.
Observation:
the improvement of network performance achieved by our approach over dynamic single path routing
is still significant (20% to 90% of congestion removed)

## Slide 25: Doing with long-lived Flows (choice of flow trigger)
Flow trigger of 20s
if ( LSA period
20s -> 50s )
then
( flows migrated
3.4% -> 0.03% ) &&
( flows detected
3.95% -> 3.58% )
Notes: we focus on single feature classification in simulation experiments.
The policy is relating flow-trigger with time scale of link state advertisement
Observation:
a) Link state update period has little effect on flow detection, while the number of migrated flow
decreases if link state update period is lengthened
b) congestion curve shows a cup-like shape
We argue that it reflects some of the essentials in two or more feature classification
1) active time could be the basic metric for flow classification.

## Slide 26: Tuning for Performance

## Slide 27: Choice of Path Quality Evaluation Trigger
Notes: network congestion decreases with increase of evaluation frequency
computation overhead increases very quickly when evaluation trigger decreases
0.3 for evaluation trigger

## Slide 28: Number of Path (non-uniformed traffic -pattern)
Notes: network performance does not always improve with the increase of path number
congestion status varies with both path number and path quality metric

## Slide 29: Number of Path (non-uniformed traffic pattern)
Notes: In network with uniformed traffic pattern, all policies have cup-like congestion curves
The reason is two folds:
a) when traffic is uniformly distributed, little resource may be idled;
b) path overlapping happens anywhere and load accumulation may be magnified by dispersity routing
discrete value 1, 4 and 7 can be the candidates for path number.

## Slide 30: Discussion

## Slide 31: Maintenance Overhead Control
Establish multipath only between those src-dest pair with heavy load eg. router A -> Router B
Path Computing happens with long period
More intelligent link state advertisement policy
For Interdomain routing, traffic is dispersed according to both link state and commercial policy
Notes: MPR is a type of source routing, which requires the edge router establishes the edge-to-edge routing path;
2. Theoretically, multiple paths need to be set up between each possible source-destination pair
But, it’s not forceful requirement.
3. We propose some way to control the overhead of path maintenance and traffic dispersion:
a) as we know traffic is not uniformly distributed in network, so ISP can determine traffic by long-time observation
starting from the traffic pattern, multiple paths could be only established between communication pairs
with heavy load;
b) the multiple path could be recomputed with a long period or when some links broken
in fact, router can compute multiple paths on basis of static link metric, eg. Bandwidth
c) Link bandwidth can be divided into several class, e.g. 10%, 20% , 30% etc; LSA is triggered only when link
state move to a new class and keep in that state for some time, eg. Bandwidth consumed move from 10-20% of
link bandwidth to 30%-40% for more than half of LSA period, new state is announced
d) In interdomain routing, each AS is considered as a node, link between edge routers is considered link,
edge-to-edge path is considered to be sequence of AS, traffic is dispersed according to link state and commercial policies.

## Slide 32: Thank You!