## Slide 1
Computer Networking
Lent Term M/W/F 11-midday
LT1 in Gates Building
Slide Set 3
Andrew W. Moore
andrew.moore@cl.cam.ac.uk
January 2014

## Slide 2: Topic 4: Network Layer
Our goals:
understand principles behind network layer services:
  network layer service models
  forwarding versus routing (versus switching)
  how a router works
  routing (path selection)
  IPv6
For the most part, the Internet is our example – again.

## Slide 3
Name: a something
Address: Where a something is
Routing: How do I get to the something

## Slide 4: Addressing (at a conceptual level)
Assume all hosts have unique IDs
No particular structure to those IDs
Later in topic I will talk about real IP addressing
Do I route on location or identifier?
If a host moves, should its address change?
  If not, how can you build scalable Internet?
  If so, then what good is an address for identification?

## Slide 5: Packets (at a conceptual level)
Assume packet headers contain:
  Source ID, Destination ID, and perhaps other information
Destination
Identifier
Source
Identifier
Payload
Why include
this?

## Slide 6: Switches/Routers
Multiple ports (attached to other switches or hosts)
Ports are typically duplex (incoming and outgoing)
incoming links
outgoing links
Switch

## Slide 7: A Variety of Networks
ISPs: carriers
  Backbone
  Edge
  Border (to other ISPs)
Enterprises: companies, universities
  Core
  Edge
  Border (to outside)
Datacenters: massive collections of machines
  Top-of-Rack
  Aggregation and Core
  Border (to outside)

## Slide 8: Switches forward packets
EDINBURGH
OXFORD
GLASGOW
UCL
Destination | Next Hop
GLASGOW | 4
OXFORD | 5
EDIN | 2
UCL | 3
Forwarding Table
111010010
EDIN
switch#2
switch#5
switch#3
switch#4

## Slide 9: Forwarding Decisions
When packet arrives..
  Must decide which outgoing port to use
  In single transmission time
  Forwarding decisions must be simple
Routing state dictates where to forward packets
  Assume decisions are deterministic
Global routing state means collection of routing state in each of the routers
  Will focus on where this routing state comes from
  But first, a few preliminaries….

## Slide 10: Forwarding vs Routing
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
Routing: “control plane”
  Computing paths the packets will follow
  Routers talking amongst themselves
  Jointly creating the routing state
Two very different timescales….
Notes: 8/Feb/2012

## Slide 11: Context and Terminology
“End hosts”
“Clients”, “Users”
“End points”
“Interior Routers”
“Border Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Route” or “Path”

## Slide 12: Context and Terminology
111010010
MIT
Destination
Destination
Destination
Destination
Destination
Destination
Destination
Destination
MIT
Internet routing protocols are responsible for constructing and updating the forwarding tables at routers

## Slide 13: Routing Protocols
Routing protocols implement the core function of a network
  Establish paths between nodes
  Part of the network’s “control plane”
Network modeled as a graph
  Routers are graph vertices
  Links are edges
  Edges have an associated “cost”
    e.g., distance, loss
Goal: compute a “good” path from source to destination
  “good” usually means the shortest (least cost) path
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 14: Internet Routing
Internet Routing works at two levels
Each AS runs an intra-domain routing protocol that establishes routes within its domain
  (AS -- region of network under a single administrative entity)
  Link State, e.g., Open Shortest Path First (OSPF)
  Distance Vector, e.g., Routing Information Protocol (RIP)
ASes participate in an inter-domain routing protocol that establishes routes between domains
  Path Vector, e.g., Border Gateway Protocol (BGP)

## Slide 15: Addressing (for now)
Assume each host has a unique ID (address)
No particular structure to those IDs
Later in course will talk about real IP addressing

## Slide 16: Outline
Link State
Distance Vector
Routing: goals and metrics (if time)

## Slide 17: Link-State

## Slide 18: Link State Routing
Each node maintains its local “link state” (LS)
  i.e., a list of its directly attached links and their costs
(N1,N2)
(N1,N4)
(N1,N5)
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6

## Slide 19: Link State Routing
Each node maintains its local “link state” (LS)
Each node floods its local link state
  on receiving a new LS message, a router forwards the message to all its neighbors other than the one it received the message from
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)

## Slide 20: Link State Routing
Each node maintains its local “link state” (LS)
Each node floods its local link state
Hence, each node learns the entire network topology
  Can use Dijkstra’s to compute the shortest paths between nodes
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C

## Slide 21: Dijkstra’s Shortest Path Algorithm
INPUT:
  Network topology (graph), with link costs
OUTPUT:
  Least cost paths from one node to all other nodes
Iterative: after k iterations, a node knows the least cost path to its k closest neighbors
Notes: How many people know this algorithm?
Well, last year….

## Slide 22: Example
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 23: Notation
c(i,j): link cost from node i to j; cost is infinite if not direct neighbors; ≥ 0
D(v): total cost of the current least cost path from source to destination v
p(v): v’s predecessor along path from source to v
S: set of nodes whose least cost path definitively known
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Source

## Slide 24: Dijkstra’s Algorithm
1 Initialization:
2 S = {A};
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v);
6 else D(v) = ;
7
8 Loop
9 find w not in S such that D(w) is a minimum;
10 add w to S;
11 update D(v) for all v adjacent to w and not in S:
12 if D(w) + c(w,v) < D(v) then
// w gives us a shorter path to v than we’ve found so far
13 D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;
c(i,j): link cost from node i to j
D(v): current cost source  v
p(v): v’s predecessor along path from source to v
S: set of nodes whose least cost path definitively known

## Slide 25: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
D(B),p(B)
2,A
D(C),p(C)
5,A
D(D),p(D)
1,A
D(E),p(E)
D(F),p(F)
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
1 Initialization:
2 S = {A};
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v);
6 else D(v) = ;
…

## Slide 26: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
D(B),p(B)
2,A
D(C),p(C)
5,A
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
D(D),p(D)
1,A
D(E),p(E)
D(F),p(F)

## Slide 27: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
D(B),p(B)
2,A
D(C),p(C)
5,A
D(D),p(D)
1,A
D(E),p(E)
D(F),p(F)
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 28: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 29: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 30: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
ADEB
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 31: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
ADEB
ADEBC
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 32: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 33: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
To determine path A  C (say), work backward from C via p(v)

## Slide 34: The Forwarding Table
Running Dijkstra at node A gives the shortest path from A to all destinations
We then construct the forwarding table
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Destination | Link
B | (A,B)
C | (A,D)
D | (A,D)
E | (A,D)
F | (A,D)
Notes: Separate routing and forwarding tables - not always the case. For efficiency, hardware implementation

## Slide 35: Issue #1: Scalability
How many messages needed to flood link state messages?
  O(N x E), where N is #nodes; E is #edges in graph
Processing complexity for Dijkstra’s algorithm?
  O(N2), because we check all nodes w not in S at each iteration and we have O(N) iterations
  more efficient implementations: O(N log(N))
How many entries in the LS topology database? O(E)
How many entries in the forwarding table? O(N)

## Slide 36: Issue#2: Transient Disruptions
Inconsistent link-state database
  Some routers know about failure before others
  The shortest paths are no longer consistent
  Can cause transient forwarding loops
A
E
D
C
B
F
A and D think that this is the path to C
E thinks that this is the path to C
A
E
D
C
B
F
Loop!

## Slide 37: Distance Vector

## Slide 38: Learn-By-Doing
Let’s try to collectively develop distance-vector routing from first principles

## Slide 39: Experiment
Your job: find the (route to) the youngest person in the room
Ground Rules
  You may not leave your seat, nor shout loudly across the class
  You may talk with your immediate neighbors
  (N-S-E-W only) (hint: “exchange updates” with them)
At the end of 5 minutes, I will pick a victim and ask:
  who is the youngest person in the room? (date&name)
  which one of your neighbors first told you this info.?

## Slide 40: Go!

## Slide 41: Distance-Vector

## Slide 42: Example of Distributed Computation
I am one hop away
I am one hop away
I am one hop away
I am two hops away
I am two hops away
I am two hops away
I am two hops away
I am three hops away
I am three hops away
Destination
I am three hops away

## Slide 43: Distance Vector Routing
Each router knows the links to its neighbors
  Does not flood this information to the whole network
Each router has provisional “shortest path” to every other router
  E.g.: Router A: “I can get to router B with cost 11”
Routers exchange this distance vector information with their neighboring routers
  Vector because one entry per destination
Routers look over the set of options offered by their neighbors and select the best one
Iterative process converges to set of shortest paths

## Slide 44: A few other inconvenient aspects
What if we use a non-additive metric?
  E.g., maximal capacity
What if routers don’t use the same metric?
  I want low delay, you want low loss rate?
What happens if nodes lie?

## Slide 45: Can You Use Any Metric?
I said that we can pick any metric. Really?
What about maximizing capacity?

## Slide 46: What Happens Here?
All nodes want to maximize capacity
A high capacity link gets reduced to low capacity
Problem:“cost” does not change around loop
Additive measures avoid this problem!

## Slide 47: No agreement on metrics?
If the nodes choose their paths according to different criteria, then bad things might happen
Example
  Node A is minimizing latency
  Node B is minimizing loss rate
  Node C is minimizing price
Any of those goals are fine, if globally adopted
  Only a problem when nodes use different criteria
Consider a routing algorithm where paths are described by delay, cost, loss

## Slide 48: What Happens Here?
Low price link
Low loss link
Low delay link
Low loss link
Low delay link
Low price link
Cares about price,
then loss
Cares about delay,
then price
Cares about loss,
then delay
Notes: Figure this out. Break into groups….

## Slide 49: Must agree on loop-avoiding metric
When all nodes minimize same metric
And that metric increases around loops
Then process is guaranteed to converge

## Slide 50: What happens when routers lie?
What if a router claims a 1-hop path to everywhere?
All traffic from nearby routers gets sent there
How can you tell if they are lying?
Can this happen in real life?
  It has, several times….

## Slide 51: Link State vs. Distance Vector
Core idea
  LS: tell all nodes about your immediate neighbors
  DV: tell your immediate neighbors about (your least cost distance to) all nodes

## Slide 52: Link State vs. Distance Vector
LS: each node learns the complete network map; each node computes shortest paths independently and in parallel
DV: no node has the complete picture; nodes cooperate to compute shortest paths in a distributed manner
  LS has higher messaging overhead
  LS has higher processing complexity
  LS is less vulnerable to looping

## Slide 53: Link State vs. Distance Vector
Message complexity
LS: O(NxE) messages;
  N is #nodes; E is #edges
DV: O(#Iterations x E)
  where #Iterations is ideally O(network diameter) but varies due to routing loops or the count-to-infinity problem
Processing complexity
LS: O(N2)
DV: O(#Iterations x N)
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  node can advertise incorrect path cost
  each node’s table used by others; error propagates through network

## Slide 54: Routing: Just the Beginning
Link state and distance-vector are the deployed routing paradigms for intra-domain routing
Inter-domain routing (BGP)
  more Part II (Principles of Communications)
  A version of DV

## Slide 55: What are desirable goals for a routing solution?
“Good” paths (least cost)
Fast convergence after change/failures
  no/rare loops
Scalable
  #messages
  table size
  processing complexity
Secure
Policy
Rich metrics (more later)

## Slide 56: Delivery models
What if a node wants to send to more than one destination?
  broadcast: send to all
  multicast: send to all members of a group
  anycast: send to any member of a group
What if a node wants to send along more than one path?

## Slide 57: Metrics
Propagation delay
Congestion
Load balance
Bandwidth (available, capacity, maximal, bbw)
Price
Reliability
Loss rate
Combinations of the above
In practice, operators set abstract “weights” (much like our costs); how exactly is a bit of a black art

## Slide 58: From Routing back to Forwarding
Routing: “control plane”
  Computing paths the packets will follow
  Routers talking amongst themselves
  Jointly creating the routing state
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
Two very different timescales….
Notes: 8/Feb/2012

## Slide 59: Basic Architectural Components of an IP Router
Control Plane
Datapath
per-packet
processing
Switching
Forwarding
Table
Routing
Table
Routing
Protocols
Management
& CLI
Software
Hardware

## Slide 60: Per-packet processing in an IP Router
1. Accept packet arriving on an incoming link.
2. Lookup packet destination address in the forwarding table, to identify outgoing port(s).
3. Manipulate packet header: e.g., decrement TTL, update header checksum.
4. Send packet to the outgoing port(s).
5. Buffer packet in the queue.
6. Transmit packet onto outgoing link.

## Slide 61: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Data
Hdr
Data
Hdr
~1M prefixes
Off-chip DRAM
Address
Table
IP Address
Next Hop
Queue
Packet
Buffer
Memory
~1M packets
Off-chip DRAM

## Slide 62: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Data
Hdr
Data
Hdr
Data
Hdr
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr

## Slide 63: Forwarding tables
Entry | Destination | Port
1 2 ⋮ 232 | 0.0.0.0 0.0.0.1 ⋮ 255.255.255.255 | 1 2 ⋮ 12
~ 4 billion entries
Naïve approach:
One entry per address
Improved approach:
Group entries to reduce table size
Entry | Destination | Port
1 2 ⋮ 50 | 0.0.0.0 – 127.255.255.255 128.0.0.1 – 128.255.255.255 ⋮ 248.0.0.0 – 255.255.255.255 | 1 2 ⋮ 12
IP address
32 bits wide → ~ 4 billion unique address

## Slide 64: IP addresses as a line
0
232-1
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
All IP addresses
Europe
USA
Oxford
Cambridge
Your computer
My computer

## Slide 65: Longest Prefix Match (LPM)
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
Universities
Continents
Planet
Data
To: Cambridge
Matching entries:
Cambridge
Europe
Everywhere
Most specific

## Slide 66: Longest Prefix Match (LPM)
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
Universities
Continents
Planet
Data
To: France
Matching entries:
Europe
Everywhere
Most specific

## Slide 67: Implementing Longest Prefix Match
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
Most specific
Least specific
Searching
FOUND

## Slide 68: Router Architecture Overview
Two key router functions:
run routing algorithms/protocol (RIP, OSPF, BGP)
forwarding datagrams from incoming to outgoing link

## Slide 69: Input Port Functions
Decentralized switching:
given datagram dest., lookup output port using forwarding table in input port memory
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
Physical layer:
bit-level reception
Data link layer:
e.g., Ethernet
see chapter 5

## Slide 70: Three types of switching fabrics (comparison criteria: speed, contention, complexity)

## Slide 71: Switching Via Memory
First generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
Input
Port
Output
Port
Memory
System Bus

## Slide 72: Switching Via a Bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
Lots of ports?? speed up the bus
no contention bus speed =
2 x port speed x port count
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
72

## Slide 73: Switching Via An Interconnection Network
overcome bus bandwidth limitations
Banyan networks, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network

## Slide 74: Output Ports
Buffering required when datagrams arrive from fabric faster than the transmission rate
Scheduling discipline chooses among queued datagrams for transmission
 Who goes next?

## Slide 75: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!

## Slide 76: Input Port Queuing
Fabric slower than input ports combined -> queueing may occur at input queues
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
queueing delay and loss due to input buffer overflow!

## Slide 77: Buffers in Routers
So how large should the buffers be?
Buffer size matters
  End-to-end delay
    Transmission, propagation, and queueing delay
    The only variable part is queueing delay
  Router architecture
    Board space, power consumption, and cost
    On chip buffers: higher density, higher capacity
    Optical buffers: all-optical routers
You are now touching the edge of the research zone……
1.4m long spiral waveguide with input from HeNe laser
Notes: got to hear 11/Feb/2013

## Slide 78: Buffer Sizing Story

## Slide 80: Rule-of-thumb – Intuition
Rule for adjusting W
If an ACK is received: W ← W+1/W
If a packet is lost: W ← W/2
Only W packets may be outstanding
Source
Dest
t
Window size

## Slide 81: Small Buffers – Intuition
Synchronized Flows
Many TCP Flows
Aggregate window has same dynamics
Therefore buffer occupancy has same dynamics
Rule-of-thumb still holds.
Independent, desynchronized
Central limit theorem says the aggregate becomes Gaussian
Variance (buffer size) decreases as N increases
Probability
Distribution
t
Buffer Size
t

## Slide 82: The Internet version of a Network layer
forwarding
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 83: IPv4 Packet Structure 20 Bytes of Standard Header, then Options
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Notes: 15/Feb/2013

## Slide 84: (Packet) Network Tasks One-by-One
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 85: Reading Packet Correctly
Version number (4 bits)
  Indicates the version of the IP protocol
  Necessary to know what other fields to expect
  Typically “4” (for IPv4), and sometimes “6” (for IPv6)
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when IP options are used
Total length (16 bits)
  Number of bytes in the packet
  Maximum size is 65,535 bytes (216 -1)
  … though underlying links may impose smaller limits
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 86: Getting Packet to Destination and Back
Two IP addresses
  Source IP address (32 bits)
  Destination IP address (32 bits)
Destination address
  Unique identifier/locator for the receiving host
  Allows each node to make forwarding decisions
Source address
  Unique identifier/locator for the sending host
  Recipient can decide whether to accept packet
  Enables recipient to send a reply back to source
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 87: Telling Host How to Handle Packet
Protocol (8 bits)
  Identifies the higher-level protocol
  Important for demultiplexing at receiving host
Most common examples
  E.g., “6” for the Transmission Control Protocol (TCP)
  E.g., “17” for the User Datagram Protocol (UDP)
IP header
IP header
TCP header
UDP header
protocol=6
protocol=17
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 88: Special Handling
Type-of-Service (8 bits)
  Allow packets to be treated differently based on needs
  E.g., low delay for audio, high bandwidth for bulk transfer
  Has been redefined several times
Options
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 89: Potential Problems
Header Corrupted: Checksum
Loop: TTL
Packet too large: Fragmentation

## Slide 90: Header Corruption
Checksum (16 bits)
  Particular form of checksum over packet header
If not correct, router discards packets
  So it doesn’t act on bogus information
Checksum recalculated at every router
  Why?
  Why include TTL?
  Why only header?
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 91: Preventing Loops (aka Internet Zombie plan)
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Forwarding loops cause packets to cycle forever
  As these accumulate, eventually consume all capacity
Time-to-Live (TTL) Field (8 bits)
  Decremented at each hop, packet discarded if reaches 0
  …and “time exceeded” message is sent to the source
    Using “ICMP” control message; basis for traceroute

## Slide 92: Fragmentation (some assembly required)
Fragmentation: when forwarding a packet, an Internet router can split it into multiple pieces (“fragments”) if too big for next hop link
Must reassemble to recover original packet
  Need fragmentation information (32 bits)
  Packet identifier, flags, and fragment offset
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 93: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
IPv6 does things differently…
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 94: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
Pop quiz question: What happens when a fragment is lost?

## Slide 95: Fragmentation Details
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Identifier (16 bits): used to tell which fragments belong together
Flags (3 bits):
  Reserved (RF): unused bit
  Don’t Fragment (DF): instruct routers to not fragment the packet even if it won’t fit
    Instead, they drop the packet and send back a “Too Large” ICMP control message
    Forms the basis for “Path MTU Discovery”
  More (MF): this fragment is not the last one
Offset (13 bits): what part of datagram this fragment covers in 8-byte units
Pop quiz question: Why do frags use offset and not a frag number?
Notes: map into memory
further downstream locations doing fragmentation would be v. hard with frag number (you would need reissue or reassemble or some craziness

## Slide 96: Options
End of Options List
No Operation (padding between options)
Record Route
Strict Source Route
Loose Source Route
Timestamp
Traceroute
Router Alert
…..
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 97: IP Addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one interface
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 98: Subnets
IP address:
  subnet part (high order bits)
  host part (low order bits)
What’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of 3 subnets
subnet
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Subnet mask: /24
11011111 00000001 00000011 00000000
subnet
part
host
part
223.1.3.0/24
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address

## Slide 99: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 100: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
DHCP
server
DHCP server: 223.1.2.5
arriving
client
time
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
Lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
arriving DHCP
client needs
address in this
network
Goal: allow host to dynamically obtain its IP address from network server when it joins network
  Can renew its lease on address in use
  Allows reuse of addresses (only hold address while connected an “on”)
  Support for mobile users who want to join network (more shortly)

## Slide 101: IP addresses: how to get one?
Q: How does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 102: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing
information:

## Slide 103: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Notes: 18 feb 2013

## Slide 104: IP addressing: the last word...
Q: How does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 105: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
Datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
All datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,
different source port numbers
Cant get more IP addresses? well there is always…..

## Slide 106: NAT: Network Address Translation
Motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus).

## Slide 107: NAT: Network Address Translation
Implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr.
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 108: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 109: NAT: Network Address Translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument (?)
    NAT possibility must be taken into account by app designers, eg, P2P applications
  address shortage should instead be solved by IPv6

## Slide 110: NAT traversal problem
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible NATted address: 138.76.29.7
solution 1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (138.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
Client
?

## Slide 111: NAT traversal problem
solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATted host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
IGD

## Slide 112: NAT traversal problem
solution 3: relaying (used in Skype)
  NATed client establishes connection to relay
  External client connects to relay
  relay bridges packets between to connections
138.76.29.7
Client
10.0.0.1
NAT
router
1. connection to
relay initiated
by NATted host
2. connection to
relay initiated
by client
3. relaying
established

## Slide 113: Remember this? Traceroute at work…
traceroute munnari.oz.au
traceroute to munnari.oz.au (202.29.151.3), 30 hops max, 60 byte packets
1 gatwick.net.cl.cam.ac.uk (128.232.32.2) 0.416 ms 0.384 ms 0.427 ms
2 cl-sby.route-nwest.net.cam.ac.uk (193.60.89.9) 0.393 ms 0.440 ms 0.494 ms
3 route-nwest.route-mill.net.cam.ac.uk (192.84.5.137) 0.407 ms 0.448 ms 0.501 ms
4 route-mill.route-enet.net.cam.ac.uk (192.84.5.94) 1.006 ms 1.091 ms 1.163 ms
5 xe-11-3-0.camb-rbr1.eastern.ja.net (146.97.130.1) 0.300 ms 0.313 ms 0.350 ms
6 ae24.lowdss-sbr1.ja.net (146.97.37.185) 2.679 ms 2.664 ms 2.712 ms
7 ae28.londhx-sbr1.ja.net (146.97.33.17) 5.955 ms 5.953 ms 5.901 ms
8 janet.mx1.lon.uk.geant.net (62.40.124.197) 6.059 ms 6.066 ms 6.052 ms
9 ae0.mx1.par.fr.geant.net (62.40.98.77) 11.742 ms 11.779 ms 11.724 ms
10 ae1.mx1.mad.es.geant.net (62.40.98.64) 27.751 ms 27.734 ms 27.704 ms
11 mb-so-02-v4.bb.tein3.net (202.179.249.117) 138.296 ms 138.314 ms 138.282 ms
12 sg-so-04-v4.bb.tein3.net (202.179.249.53) 196.303 ms 196.293 ms 196.264 ms
13 th-pr-v4.bb.tein3.net (202.179.249.66) 225.153 ms 225.178 ms 225.196 ms
14 pyt-thairen-to-02-bdr-pyt.uni.net.th (202.29.12.10) 225.163 ms 223.343 ms 223.363 ms
15 202.28.227.126 (202.28.227.126) 241.038 ms 240.941 ms 240.834 ms
16 202.28.221.46 (202.28.221.46) 287.252 ms 287.306 ms 287.282 ms
17 * * *
18 * * *
19 * * *
20 coe-gw.psu.ac.th (202.29.149.70) 241.681 ms 241.715 ms 241.680 ms
21 munnari.OZ.AU (202.29.151.3) 241.610 ms 241.636 ms 241.537 ms
traceroute: rio.cl.cam.ac.uk to munnari.oz.au
(tracepath on pwf is similar)
Three delay measurements from
rio.cl.cam.ac.uk to gatwick.net.cl.cam.ac.uk
* means no response (probe lost, router not replying)
trans-continent
link
Notes: Where did the delay come from??

## Slide 114: Traceroute and ICMP
Source sends series of UDP segments to dest
  First has TTL =1
  Second has TTL=2, etc.
  Unlikely port number
When nth datagram arrives to nth router:
  Router discards datagram
  And sends to source an ICMP message (type 11, code 0)
  Message includes name of router& IP address
When ICMP message arrives, source calculates RTT
Traceroute does this 3 times
Stopping criterion
UDP segment eventually arrives at destination host
Destination returns ICMP “host unreachable” packet (type 3, code 3)
When source gets this ICMP, stops.

## Slide 115: ICMP: Internet Control Message Protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 116: IPv6
Motivated (prematurely) by address exhaustion
  Address field four times as long
Steve Deering focused on simplifying IP
  Got rid of all fields that were not absolutely necessary
  “Spring Cleaning” for IP
Result is an elegant, if unambitious, protocol

## Slide 117: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 

## Slide 118: Summary of Changes
Eliminated fragmentation (why?)
Eliminated header length (why?)
Eliminated checksum (why?)
New options mechanism (next header) (why?)
Expanded addresses (why?)
Added Flow Label (why?)
Notes: got here 20 Feb 2013

## Slide 119: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 120: Philosophy of Changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation
  Eliminated checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header approach)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 121: Comparison of Design Philosophy
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
To Destination and Back (expanded)
Deal with Problems (greatly reduced)
Read Correctly (reduced)
Special Handling (similar)

## Slide 122: Transition From IPv4 To IPv6
Not all routers can be upgraded simultaneous
  no “flag days”
  How will the network operate with mixed IPv4 and IPv6 routers?
Tunneling: IPv6 carried as payload in IPv4 datagram among IPv4 routers

## Slide 123: Tunneling
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
IPv4
IPv4

## Slide 124: Tunneling
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
C
D
IPv4
IPv4
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
A-to-B:
IPv6
E-to-F:
IPv6
B-to-C:
IPv6 inside
IPv4
B-to-C:
IPv6 inside
IPv4

## Slide 125: Improving on IPv4 and IPv6?
Why include unverifiable source address?
  Would like accountability and anonymity (now neither)
  Return address can be communicated at higher layer
Why packet header used at edge same as core?
  Edge: host tells network what service it wants
  Core: packet tells switch how to handle it
    One is local to host, one is global to network
Some kind of payment/responsibility field?
  Who is responsible for paying for packet delivery?
  Source, destination, other?
Other ideas?

## Slide 126
Gluing it together:
How does my Network (address) interact
with my Data-Link (address) ?

## Slide 127: Switches vs. Routers Summary
both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  switches are link layer devices
routers maintain routing tables, implement routing algorithms
switches maintain switch tables, implement filtering, learning algorithms
Notes: FINAL SLIDE IN PART 5

## Slide 128: MAC Addresses (and ARP) or How do I glue my network to my data-link?
32-bit IP address:
  network-layer address
  used to get datagram to destination IP subnet
MAC (or LAN or physical or Ethernet) address:
  function: get frame from one interface to another physically-connected interface (same network)
  48 bit MAC address (for most LANs)
    burned in NIC ROM, also (commonly) software settable

## Slide 129: LAN Addresses and ARP
Each adapter on LAN has unique LAN address
Ethernet
Broadcast address =
FF-FF-FF-FF-FF-FF
= adapter
1A-2F-BB-709-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-6F7-2B-08-53
LAN
(wired or
wireless)

## Slide 130: Address Resolution Protocol
Every node maintains an ARP table
  <IP address, MAC address> pair
Consult the table when sending a packet
  Map destination IP address to destination MAC address
  Encapsulate and transmit the data packet
But: what if IP address not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches result in its ARP table
Notes: Wed 7th start here.

## Slide 131: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B

## Slide 132: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B
1. A sends packet to R. 2. R sends packet to B.

## Slide 133: Host A Decides to Send Through R
A
R
B
Host A constructs an IP packet to send to B
  Source 111.111.111.111, destination 222.222.222.222
Host A has a gateway router R
  Used to reach destinations outside of 111.111.111.0/24
  Address 111.111.111.110 for R learned via DHCP/config

## Slide 134: Host A Sends Packet Through R
Host A learns the MAC address of R’s interface
  ARP request: broadcast request for 111.111.111.110
  ARP response: R responds with E6-E9-00-17-BB-4B
Host A encapsulates the packet and sends to R
A
R
B

## Slide 135: R Decides how to Forward Packet
Router R’s adaptor receives the packet
  R extracts the IP packet from the Ethernet frame
  R sees the IP packet is destined to 222.222.222.222
Router R consults its forwarding table
  Packet matches 222.222.222.0/24 via other adaptor
A
R
B

## Slide 136: R Sends Packet to B
Router R’s learns the MAC address of host B
  ARP request: broadcast request for 222.222.222.222
  ARP response: B responds with 49-BD-D2-C7-52A
Router R encapsulates the packet and sends to B
A
R
B

## Slide 137: Security Analysis of ARP
Impersonation
  Any node that hears request can answer …
  … and can say whatever they want
Actual legit receiver never sees a problem
  Because even though later packets carry its IP address, its NIC doesn’t capture them since not its MAC address
Notes: 1/Fab/2013

## Slide 138: Key Ideas in Both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
  Remember your own address & other host’s addresses
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 139: Why Not Use DNS-Like Tables?
When host arrives:
  Assign it an IP address that will last as long it is present
  Add an entry into a table in DNS-server that maps MAC to IP addresses
Answer:
  Names: explicit creation, and are plentiful
  Hosts: come and go without informing network
    Must do mapping on demand
  Addresses: not plentiful, need to reuse and remap
    Soft-state enables dynamic reuse
Notes: Two key points

## Slide 140: Summary Network Layer
understand principles behind network layer services:
  network layer service models
  forwarding versus routing (versus switching)
  how a router works
  routing (path selection)
  IPv6
Algorthims
  Two routing approaches (LS vs DV)
  One of these in detail (LS)
  ARP