## Slide 1
Computer Networking
Michaelmas/Lent Term
M/W/F 11:00-12:00
LT1 in Gates Building
Slide Set 4
Andrew W. Moore
andrew.moore@cl.cam.ac.uk
2016-2017

## Slide 2: Topic 4: Network Layer
Our goals:
understand principles behind network layer services:
  network layer service models
  forwarding versus routing (versus switching)
  how a router works
  routing (path selection)
  IPv6
For the most part, the Internet is our example – again.

## Slide 3
Name: a something
Address: Where a something is
Routing: How do I get to the something

## Slide 4: Addressing (at a conceptual level)
Assume all hosts have unique IDs
No particular structure to those IDs
Later in topic I will talk about real IP addressing
Do I route on location or identifier?
If a host moves, should its address change?
  If not, how can you build scalable Internet?
  If so, then what good is an address for identification?
Notes: 20-jan-17

## Slide 5: Packets (at a conceptual level)
Assume packet headers contain:
  Source ID, Destination ID, and perhaps other information
Destination
Identifier
Source
Identifier
Payload
Why include
this?

## Slide 6: Switches/Routers
Multiple ports (attached to other switches or hosts)
Ports are typically duplex (incoming and outgoing)
incoming links
outgoing links
Switch

## Slide 7: A Variety of Networks
ISPs: carriers
  Backbone
  Edge
  Border (to other ISPs)
Enterprises: companies, universities
  Core
  Edge
  Border (to outside)
Datacenters: massive collections of machines
  Top-of-Rack
  Aggregation and Core
  Border (to outside)
Notes: 19-jan-2015

## Slide 8: Switches forward packets
EDINBURGH
OXFORD
GLASGOW
UCL
Destination | Next Hop
GLASGOW | 4
OXFORD | 5
EDIN | 2
UCL | 3
Forwarding Table
111010010
EDIN
switch#2
switch#5
switch#3
switch#4

## Slide 9: Forwarding Decisions
When packet arrives..
  Must decide which outgoing port to use
  In single transmission time
  Forwarding decisions must be simple
Routing state dictates where to forward packets
  Assume decisions are deterministic
Global routing state means collection of routing state in each of the routers
  Will focus on where this routing state comes from
  But first, a few preliminaries….

## Slide 10: Forwarding vs Routing
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
Routing: “control plane”
  Computing paths the packets will follow
  Routers talking amongst themselves
  Jointly creating the routing state
Two very different timescales….
Notes: 8/Feb/2012

## Slide 11: Router definitions
1
2
3
4
5
…
N-1
N
N = number of external router “ports”
R = speed (“line rate”) of a port
Router capacity = N x R
R bits/sec

## Slide 12: Networks and routers
AT&T
INTEL
MIT
JANET
core
core
edge (ISP)
edge (enterprise)
home, small business
Notes: Bunch of different kinds of routers: small for homes, routers that connect different ISPs or ISPs to enterprises (edge)

## Slide 13: Examples of routers (core)
72 racks, >1MW
Cisco CRS-1
  R=10/40/100 Gbps
  NR = 922 Tbps
  Netflix: 0.7GB per hour (1.5Mb/s)
  ~600 million concurrent Netflix users

## Slide 14: Examples of routers (edge)
Cisco ASR
  R=1/10/40 Gbps
  NR = 120 Gbps

## Slide 15: Examples of routers (small business)
Cisco 3945E
  R = 10/100/1000 Mbps
  NR < 10 Gbps

## Slide 16: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Processes packets on their way in
Processes packets before they leave
Transfers packets from input to output ports
Input and Output for the same port are on one physical linecard

## Slide 17: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
(1) Implement IGP and BGP protocols; compute routing tables
(2) Push forwarding tables to the line cards

## Slide 18: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect Fabric
Route/Control Processor
Linecards (output)
Constitutes the data plane
Constitutes the control plane
A decision for each packet.
Makes decisions over long time horizons : network change
Notes: Control plane: software. Makes decisions over long time horizons.
Data plane: mostly hardware. A decision for each packet.

## Slide 19: Context and Terminology
“End hosts”
“Clients”, “Users”
“End points”
“Interior Routers”
“Border Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Route” or “Path”
Notes: 2015-12-2

## Slide 20: Context and Terminology
111010010
MIT
Destination
Destination
Destination
Destination
Destination
Destination
Destination
Destination
MIT
Internet routing protocols are responsible for constructing and updating the forwarding tables at routers

## Slide 21: Routing Protocols
Routing protocols implement the core function of a network
  Establish paths between nodes
  Part of the network’s “control plane”
Network modeled as a graph
  Routers are graph vertices
  Links are edges
  Edges have an associated “cost”
    e.g., distance, loss
Goal: compute a “good” path from source to destination
  “good” usually means the shortest (least cost) path
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 22: Internet Routing
Internet Routing works at two levels
Each AS runs an intra-domain routing protocol that establishes routes within its domain
  (AS -- region of network under a single administrative entity)
  Link State, e.g., Open Shortest Path First (OSPF)
  Distance Vector, e.g., Routing Information Protocol (RIP)
ASes participate in an inter-domain routing protocol that establishes routes between domains
  Path Vector, e.g., Border Gateway Protocol (BGP)

## Slide 23: Addressing (for now)
Assume each host has a unique ID (address)
No particular structure to those IDs
Later in course will talk about real IP addressing

## Slide 24: Outline
Link State
Distance Vector
Routing: goals and metrics

## Slide 25: Link-State

## Slide 26: Link State Routing
Each node maintains its local “link state” (LS)
  i.e., a list of its directly attached links and their costs
(N1,N2)
(N1,N4)
(N1,N5)
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6

## Slide 27: Link State Routing
Each node maintains its local “link state” (LS)
Each node floods its local link state
  on receiving a new LS message, a router forwards the message to all its neighbors other than the one it received the message from
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)

## Slide 28: Link State Routing
Each node maintains its local “link state” (LS)
Each node floods its local link state
Hence, each node learns the entire network topology
  Can use Dijkstra’s to compute the shortest paths between nodes
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C

## Slide 29: Dijkstra’s Shortest Path Algorithm
INPUT:
  Network topology (graph), with link costs
OUTPUT:
  Least cost paths from one node to all other nodes
Iterative: after k iterations, a node knows the least cost path to its k closest neighbors
Notes: How many people know this algorithm?
Well, last year….

## Slide 30: Example
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 31: Notation
c(i,j): link cost from node i to j; cost is infinite if not direct neighbors; ≥ 0
D(v): total cost of the current least cost path from source to destination v
p(v): v’s predecessor along path from source to v
S: set of nodes whose least cost path definitively known
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Source

## Slide 32: Dijkstra’s Algorithm
1 Initialization:
2 S = {A};
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v);
6 else D(v) = ;
7
8 Loop
9 find w not in S such that D(w) is a minimum;
10 add w to S;
11 update D(v) for all v adjacent to w and not in S:
12 if D(w) + c(w,v) < D(v) then
// w gives us a shorter path to v than we’ve found so far
13 D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;
c(i,j): link cost from node i to j
D(v): current cost source  v
p(v): v’s predecessor along path from source to v
S: set of nodes whose least cost path definitively known

## Slide 33: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
D(B),p(B)
2,A
D(C),p(C)
5,A
D(D),p(D)
1,A
D(E),p(E)
D(F),p(F)
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
1 Initialization:
2 S = {A};
3 for all nodes v
4 if v adjacent to A
5 then D(v) = c(A,v);
6 else D(v) = ;
…

## Slide 34: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
D(B),p(B)
2,A
D(C),p(C)
5,A
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
D(D),p(D)
1,A
D(E),p(E)
D(F),p(F)

## Slide 35: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
D(B),p(B)
2,A
D(C),p(C)
5,A
D(D),p(D)
1,A
D(E),p(E)
D(F),p(F)
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 36: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 37: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 38: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
ADEB
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 39: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
ADEB
ADEBC
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 40: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
…
8 Loop
9 find w not in S s.t. D(w) is a minimum;
10 add w to S;
update D(v) for all v adjacent
to w and not in S:
If D(w) + c(w,v) < D(v) then
D(v) = D(w) + c(w,v); p(v) = w;
14 until all nodes in S;

## Slide 41: Example: Dijkstra’s Algorithm
Step
0
1
2
3
4
5
set S
A
AD
ADE
ADEB
ADEBC
ADEBCF
D(B),p(B)
2,A
D(C),p(C)
5,A
4,D
3,E
D(D),p(D)
1,A
D(E),p(E)
2,D
D(F),p(F)
4,E
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
To determine path A  C (say), work backward from C via p(v)

## Slide 42: The Forwarding Table
Running Dijkstra at node A gives the shortest path from A to all destinations
We then construct the forwarding table
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Destination | Link
B | (A,B)
C | (A,D)
D | (A,D)
E | (A,D)
F | (A,D)
Notes: Separate routing and forwarding tables - not always the case. For efficiency, hardware implementation

## Slide 43: Issue #1: Scalability
How many messages needed to flood link state messages?
  O(N x E), where N is #nodes; E is #edges in graph
Processing complexity for Dijkstra’s algorithm?
  O(N2), because we check all nodes w not in S at each iteration and we have O(N) iterations
  more efficient implementations: O(N log(N))
How many entries in the LS topology database? O(E)
How many entries in the forwarding table? O(N)

## Slide 44: Issue#2: Transient Disruptions
Inconsistent link-state database
  Some routers know about failure before others
  The shortest paths are no longer consistent
  Can cause transient forwarding loops
A
E
D
C
B
F
A and D think that this is the path to C
E thinks that this is the path to C
A
E
D
C
B
F
Loop!
Notes: here. 12/jan/2014

## Slide 45: Distance Vector

## Slide 46: Learn-By-Doing
Let’s try to collectively develop distance-vector routing from first principles

## Slide 47: Experiment
Your job: find the (route to) the youngest person in the room
Ground Rules
  You may not leave your seat, nor shout loudly across the class
  You may talk with your immediate neighbors
  (N-S-E-W only) (hint: “exchange updates” with them)
At the end of 5 minutes, I will pick a victim and ask:
  who is the youngest person in the room? (date&name)
  which one of your neighbors first told you this info.?

## Slide 48: Go!

## Slide 49: Distance-Vector

## Slide 50: Example of Distributed Computation
I am one hop away
I am one hop away
I am one hop away
I am two hops away
I am two hops away
I am two hops away
I am two hops away
I am three hops away
I am three hops away
Destination
I am three hops away

## Slide 51: Distance Vector Routing
Each router knows the links to its neighbors
  Does not flood this information to the whole network
Each router has provisional “shortest path” to every other router
  E.g.: Router A: “I can get to router B with cost 11”
Routers exchange this distance vector information with their neighboring routers
  Vector because one entry per destination
Routers look over the set of options offered by their neighbors and select the best one
Iterative process converges to set of shortest paths

## Slide 52: A few other inconvenient truths
What if we use a non-additive metric?
  E.g., maximal capacity
What if routers don’t use the same metric?
  I want low delay, you want low loss rate?
What happens if nodes lie?
Notes: 23-Jan-17

## Slide 53: Can You Use Any Metric?
I said that we can pick any metric. Really?
What about maximizing capacity?

## Slide 54: What Happens Here?
All nodes want to maximize capacity
A high capacity link gets reduced to low capacity
Problem:“cost” does not change around loop
Additive measures avoid this problem!

## Slide 55: No agreement on metrics?
If the nodes choose their paths according to different criteria, then bad things might happen
Example
  Node A is minimizing latency
  Node B is minimizing loss rate
  Node C is minimizing price
Any of those goals are fine, if globally adopted
  Only a problem when nodes use different criteria
Consider a routing algorithm where paths are described by delay, cost, loss

## Slide 56: What Happens Here?
Low price link
Low loss link
Low delay link
Low loss link
Low delay link
Low price link
Cares about price,
then loss
Cares about delay,
then price
Cares about loss,
then delay
Notes: Figure this out. Break into groups….

## Slide 57: Must agree on loop-avoiding metric
When all nodes minimize same metric
And that metric increases around loops
Then process is guaranteed to converge

## Slide 58: What happens when routers lie?
What if a router claims a 1-hop path to everywhere?
All traffic from nearby routers gets sent there
How can you tell if they are lying?
Can this happen in real life?
  It has, several times….

## Slide 59: Link State vs. Distance Vector
Core idea
  LS: tell all nodes about your immediate neighbors
  DV: tell your immediate neighbors about (your least cost distance to) all nodes

## Slide 60: Link State vs. Distance Vector
LS: each node learns the complete network map; each node computes shortest paths independently and in parallel
DV: no node has the complete picture; nodes cooperate to compute shortest paths in a distributed manner
  LS has higher messaging overhead
  LS has higher processing complexity
  LS is less vulnerable to looping

## Slide 61: Link State vs. Distance Vector
Message complexity
LS: O(NxE) messages;
  N is #nodes; E is #edges
DV: O(#Iterations x E)
  where #Iterations is ideally O(network diameter) but varies due to routing loops or the count-to-infinity problem
Processing complexity
LS: O(N2)
DV: O(#Iterations x N)
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  node can advertise incorrect path cost
  each node’s table used by others; error propagates through network

## Slide 62: Routing: Just the Beginning
Link state and distance-vector are the deployed routing paradigms for intra-domain routing
Inter-domain routing (BGP)
  more Part II (Principles of Communications)
  A version of DV

## Slide 63: What are desirable goals for a routing solution?
“Good” paths (least cost)
Fast convergence after change/failures
  no/rare loops
Scalable
  #messages
  table size
  processing complexity
Secure
Policy
Rich metrics (more later)

## Slide 64: Delivery models
What if a node wants to send to more than one destination?
  broadcast: send to all
  multicast: send to all members of a group
  anycast: send to any member of a group
What if a node wants to send along more than one path?

## Slide 65: Metrics
Propagation delay
Congestion
Load balance
Bandwidth (available, capacity, maximal, bbw)
Price
Reliability
Loss rate
Combinations of the above
In practice, operators set abstract “weights” (much like our costs); how exactly is a bit of a black art

## Slide 66: From Routing back to Forwarding
Routing: “control plane”
  Computing paths the packets will follow
  Routers talking amongst themselves
  Jointly creating the routing state
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
Two very different timescales….

## Slide 67: Basic Architectural Components of an IP Router
Control Plane
network-change
processing
Datapath
per-packet
processing
Switching
Forwarding
Table
Routing
Table
Routing
Protocols
Management
& CLI
Software
Hardware

## Slide 68: Independent operation!
Control Plane
network-change
processing
Datapath
per-packet
processing
Switching
Forwarding
Table
Routing
Table
Routing
Protocols
Management
& CLI
Software
Hardware
If the control-plane fails…..
The data-path is not affected…
like a loyal pet it will keep going using the current (last) table update
This is a feature not a bug

## Slide 69: Per-packet processing in an IP Router
1. Accept packet arriving on an incoming link.
2. Lookup packet destination address in the forwarding table, to identify outgoing port(s).
3. Manipulate packet header: e.g., decrement TTL, update header checksum.
4. Send packet to the outgoing port(s).
5. Buffer packet in the queue.
6. Transmit packet onto outgoing link.

## Slide 70: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Data
Hdr
Data
Hdr
~1M prefixes
Off-chip DRAM
Address
Table
IP Address
Next Hop
Queue
Packet
Buffer
Memory
~1M packets
Off-chip DRAM

## Slide 71: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Data
Hdr
Data
Hdr
Data
Hdr
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr

## Slide 72: Forwarding tables
Entry | Destination | Port
1 2 ⋮ 232 | 0.0.0.0 0.0.0.1 ⋮ 255.255.255.255 | 1 2 ⋮ 12
~ 4 billion entries
Naïve approach:
One entry per address
Improved approach:
Group entries to reduce table size
Entry | Destination | Port
1 2 ⋮ 50 | 0.0.0.0 – 127.255.255.255 128.0.0.1 – 128.255.255.255 ⋮ 248.0.0.0 – 255.255.255.255 | 1 2 ⋮ 12
IP address
32 bits wide → ~ 4 billion unique address

## Slide 73: IP addresses as a line
0
232-1
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
All IP addresses
Europe
USA
Oxford
Cambridge
Your computer
My computer

## Slide 74: Longest Prefix Match (LPM)
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
Universities
Continents
Planet
Data
To: Cambridge
Matching entries:
Cambridge
Europe
Everywhere
Most specific

## Slide 75: Longest Prefix Match (LPM)
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
Universities
Continents
Planet
Data
To: France
Matching entries:
Europe
Everywhere
Most specific

## Slide 76: Implementing Longest Prefix Match
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
Most specific
Least specific
Searching
FOUND
Notes: 2014-1-23

## Slide 77: Switching Via Memory
First generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
Input
Port
Output
Port
Memory
System Bus
Notes: 2017-1-25

## Slide 78: Switching Via a Bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
Lots of ports?? speed up the bus
no contention bus speed =
2 x port speed x port count
32 Gbps bus, Cisco 5600: sufficient speed for access routers
78

## Slide 79: Switching Via An Interconnection Network
overcome bus bandwidth limitations
Banyan networks, other interconnection nets initially developed to connect processors in multiprocessor stages
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco CRS-1: switches 1.2 Tbps through the interconnection network

## Slide 80: Output Ports
Buffering required when datagrams arrive from fabric faster than the transmission rate
Scheduling discipline chooses among queued datagrams for transmission
 Who goes next?

## Slide 81: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!

## Slide 82
Queueing to Queue….  Who goes next?

## Slide 83: Input Port Queuing
Fabric slower than input ports combined -> queueing may occur at input queues
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
queueing delay and loss due to input buffer overflow!

## Slide 85: Buffers in Routers
So how large should the buffers be?
Buffer size matters
  End-to-end delay
    Transmission, propagation, and queueing delay
    The only variable part is queueing delay
  Router architecture
    Board space, power consumption, and cost
    On chip buffers: higher density, higher capacity
    Optical buffers: all-optical routers
You are now touching the edge of the research zone……
1.4m long spiral waveguide with input from HeNe laser

## Slide 86: Buffer Sizing Story

## Slide 87
Notes: 18 jan 2016

## Slide 88: Rule-of-thumb – Intuition
Rule for adjusting W
If an ACK is received: W ← W+1/W
If a packet is lost: W ← W/2
Only W packets may be outstanding
Source
Dest
t
Window size

## Slide 89: Small Buffers – Intuition
Synchronized Flows
Many TCP Flows
Aggregate window has same dynamics
Therefore buffer occupancy has same dynamics
Rule-of-thumb still holds.
Independent, desynchronized
Central limit theorem says the aggregate becomes Gaussian
Variance (buffer size) decreases as N increases
Probability
Distribution
t
Buffer Size
t
Notes: 2017-1-27

## Slide 90: The Internet version of a Network layer
forwarding
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 91: IPv4 Packet Structure 20 Bytes of Standard Header, then Options
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Notes: 15/Feb/2013

## Slide 92: (Packet) Network Tasks One-by-One
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 93: Reading Packet Correctly
Version number (4 bits)
  Indicates the version of the IP protocol
  Necessary to know what other fields to expect
  Typically “4” (for IPv4), and sometimes “6” (for IPv6)
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when IP options are used
Total length (16 bits)
  Number of bytes in the packet
  Maximum size is 65,535 bytes (216 -1)
  … though underlying links may impose smaller limits
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 94: Getting Packet to Destination and Back
Two IP addresses
  Source IP address (32 bits)
  Destination IP address (32 bits)
Destination address
  Unique identifier/locator for the receiving host
  Allows each node to make forwarding decisions
Source address
  Unique identifier/locator for the sending host
  Recipient can decide whether to accept packet
  Enables recipient to send a reply back to source
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 95: Telling Host How to Handle Packet
Protocol (8 bits)
  Identifies the higher-level protocol
  Important for demultiplexing at receiving host
Most common examples
  E.g., “6” for the Transmission Control Protocol (TCP)
  E.g., “17” for the User Datagram Protocol (UDP)
IP header
IP header
TCP header
UDP header
protocol=6
protocol=17
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 96: Special Handling
Type-of-Service (8 bits)
  Allow packets to be treated differently based on needs
  E.g., low delay for audio, high bandwidth for bulk transfer
  Has been redefined several times
Options
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Notes: 26-jan-2015

## Slide 97: Potential Problems
Header Corrupted: Checksum
Loop: TTL
Packet too large: Fragmentation

## Slide 98: Header Corruption
Checksum (16 bits)
  Particular form of checksum over packet header
If not correct, router discards packets
  So it doesn’t act on bogus information
Checksum recalculated at every router
  Why?
  Why include TTL?
  Why only header?
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 99: Preventing Loops (aka Internet Zombie plan)
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Forwarding loops cause packets to cycle forever
  As these accumulate, eventually consume all capacity
Time-to-Live (TTL) Field (8 bits)
  Decremented at each hop, packet discarded if reaches 0
  …and “time exceeded” message is sent to the source
    Using “ICMP” control message; basis for traceroute

## Slide 100: Fragmentation (some assembly required)
Fragmentation: when forwarding a packet, an Internet router can split it into multiple pieces (“fragments”) if too big for next hop link
Must reassemble to recover original packet
  Need fragmentation information (32 bits)
  Packet identifier, flags, and fragment offset
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 101: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
IPv6 does things differently…
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 102: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
Pop quiz question: What happens when a fragment is lost?

## Slide 103: Fragmentation Details
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Identifier (16 bits): used to tell which fragments belong together
Flags (3 bits):
  Reserved (RF): unused bit
  Don’t Fragment (DF): instruct routers to not fragment the packet even if it won’t fit
    Instead, they drop the packet and send back a “Too Large” ICMP control message
    Forms the basis for “Path MTU Discovery”
  More (MF): this fragment is not the last one
Offset (13 bits): what part of datagram this fragment covers in 8-byte units
Pop quiz question: Why do frags use offset and not a frag number?
Notes: map into memory
further downstream locations doing fragmentation would be v. hard with frag number (you would need reissue or reassemble or some craziness

## Slide 104: Options
End of Options List
No Operation (padding between options)
Record Route
Strict Source Route
Loose Source Route
Timestamp
Traceroute
Router Alert
…..
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Notes: 2017-1-30

## Slide 105: IP Addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one interface
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 106: Subnets
IP address:
  subnet part (high order bits)
  host part (low order bits)
What’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of 3 subnets
subnet
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Subnet mask: /24
11011111 00000001 00000011 00000000
subnet
part
host
part
223.1.3.0/24
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address

## Slide 107: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config (circa 1980’s your mileage will vary)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 108: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
DHCP
server
DHCP server: 223.1.2.5
arriving
client
time
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
Lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
arriving DHCP
client needs
address in this
network
Goal: allow host to dynamically obtain its IP address from network server when it joins network
  Can renew its lease on address in use
  Allows reuse of addresses (only hold address while connected an “on”)
  Support for mobile users who want to join network (more shortly)

## Slide 109: IP addresses: how to get one?
Q: How does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 110: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing
information:

## Slide 111: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Notes: 18 feb 2013

## Slide 112: IP addressing: the last word...
Q: How does an ISP get a block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 113: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
Datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
All datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,
different source port numbers
Cant get more IP addresses? well there is always…..
Notes: 28 Jan 2015

## Slide 114: NAT: Network Address Translation
Motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus).

## Slide 115: NAT: Network Address Translation
Implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr.
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 116: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
Notes: 2016-1-20

## Slide 117: NAT: Network Address Translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument (?)
    NAT possibility must be taken into account by app designers, eg, P2P applications
  address shortage should instead be solved by IPv6

## Slide 118: NAT traversal problem
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible NATted address: 138.76.29.7
solution 1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (138.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
Client
?

## Slide 119: NAT traversal problem
solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATted host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
IGD

## Slide 120: NAT traversal problem
solution 3: relaying (used in Skype)
  NATed client establishes connection to relay
  External client connects to relay
  relay bridges packets between to connections
138.76.29.7
Client
10.0.0.1
NAT
router
1. connection to
relay initiated
by NATted host
2. connection to
relay initiated
by client
3. relaying
established

## Slide 121: Remember this? Traceroute at work…
traceroute munnari.oz.au
traceroute to munnari.oz.au (202.29.151.3), 30 hops max, 60 byte packets
1 gatwick.net.cl.cam.ac.uk (128.232.32.2) 0.416 ms 0.384 ms 0.427 ms
2 cl-sby.route-nwest.net.cam.ac.uk (193.60.89.9) 0.393 ms 0.440 ms 0.494 ms
3 route-nwest.route-mill.net.cam.ac.uk (192.84.5.137) 0.407 ms 0.448 ms 0.501 ms
4 route-mill.route-enet.net.cam.ac.uk (192.84.5.94) 1.006 ms 1.091 ms 1.163 ms
5 xe-11-3-0.camb-rbr1.eastern.ja.net (146.97.130.1) 0.300 ms 0.313 ms 0.350 ms
6 ae24.lowdss-sbr1.ja.net (146.97.37.185) 2.679 ms 2.664 ms 2.712 ms
7 ae28.londhx-sbr1.ja.net (146.97.33.17) 5.955 ms 5.953 ms 5.901 ms
8 janet.mx1.lon.uk.geant.net (62.40.124.197) 6.059 ms 6.066 ms 6.052 ms
9 ae0.mx1.par.fr.geant.net (62.40.98.77) 11.742 ms 11.779 ms 11.724 ms
10 ae1.mx1.mad.es.geant.net (62.40.98.64) 27.751 ms 27.734 ms 27.704 ms
11 mb-so-02-v4.bb.tein3.net (202.179.249.117) 138.296 ms 138.314 ms 138.282 ms
12 sg-so-04-v4.bb.tein3.net (202.179.249.53) 196.303 ms 196.293 ms 196.264 ms
13 th-pr-v4.bb.tein3.net (202.179.249.66) 225.153 ms 225.178 ms 225.196 ms
14 pyt-thairen-to-02-bdr-pyt.uni.net.th (202.29.12.10) 225.163 ms 223.343 ms 223.363 ms
15 202.28.227.126 (202.28.227.126) 241.038 ms 240.941 ms 240.834 ms
16 202.28.221.46 (202.28.221.46) 287.252 ms 287.306 ms 287.282 ms
17 * * *
18 * * *
19 * * *
20 coe-gw.psu.ac.th (202.29.149.70) 241.681 ms 241.715 ms 241.680 ms
21 munnari.OZ.AU (202.29.151.3) 241.610 ms 241.636 ms 241.537 ms
traceroute: rio.cl.cam.ac.uk to munnari.oz.au
(tracepath on pwf is similar)
Three delay measurements from
rio.cl.cam.ac.uk to gatwick.net.cl.cam.ac.uk
* means no response (probe lost, router not replying)
trans-continent
link
Notes: Where did the delay come from??

## Slide 122: Traceroute and ICMP
Source sends series of UDP segments to dest
  First has TTL =1
  Second has TTL=2, etc.
  Unlikely port number
When nth datagram arrives to nth router:
  Router discards datagram
  And sends to source an ICMP message (type 11, code 0)
  Message includes name of router& IP address
When ICMP message arrives, source calculates RTT
Traceroute does this 3 times
Stopping criterion
UDP segment eventually arrives at destination host
Destination returns ICMP “host unreachable” packet (type 3, code 3)
When source gets this ICMP, stops.

## Slide 123: ICMP: Internet Control Message Protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 124
Gluing it together:
How does my Network (address) interact
with my Data-Link (address) ?

## Slide 125: Switches vs. Routers Summary
both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  switches are link layer devices
routers maintain routing tables, implement routing algorithms
switches maintain switch tables, implement filtering, learning algorithms
Notes: FINAL SLIDE IN PART 5

## Slide 126: MAC Addresses (and IPv4 ARP) or How do I glue my network to my data-link?
32-bit IP address:
  network-layer address
  used to get datagram to destination IP subnet
MAC (or LAN or physical or Ethernet) address:
  function: get frame from one interface to another physically-connected interface (same network)
  48 bit MAC address (for most LANs)
    burned in NIC ROM, also (commonly) software settable

## Slide 127: LAN Addresses and ARP
Each adapter on LAN has unique LAN address
Ethernet
Broadcast address =
FF-FF-FF-FF-FF-FF
= adapter
1A-2F-BB-709-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-6F7-2B-08-53
LAN
(wired or
wireless)

## Slide 128: Address Resolution Protocol
Every node maintains an ARP table
  <IP address, MAC address> pair
Consult the table when sending a packet
  Map destination IP address to destination MAC address
  Encapsulate and transmit the data packet
But: what if IP address not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches result in its ARP table
Notes: Wed 7th start here.

## Slide 129: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B

## Slide 130: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B
1. A sends packet to R. 2. R sends packet to B.

## Slide 131: Host A Decides to Send Through R
A
R
B
Host A constructs an IP packet to send to B
  Source 111.111.111.111, destination 222.222.222.222
Host A has a gateway router R
  Used to reach destinations outside of 111.111.111.0/24
  Address 111.111.111.110 for R learned via DHCP/config

## Slide 132: Host A Sends Packet Through R
Host A learns the MAC address of R’s interface
  ARP request: broadcast request for 111.111.111.110
  ARP response: R responds with E6-E9-00-17-BB-4B
Host A encapsulates the packet and sends to R
A
R
B

## Slide 133: R Decides how to Forward Packet
Router R’s adaptor receives the packet
  R extracts the IP packet from the Ethernet frame
  R sees the IP packet is destined to 222.222.222.222
Router R consults its forwarding table
  Packet matches 222.222.222.0/24 via other adaptor
A
R
B

## Slide 134: R Sends Packet to B
Router R’s learns the MAC address of host B
  ARP request: broadcast request for 222.222.222.222
  ARP response: B responds with 49-BD-D2-C7-52A
Router R encapsulates the packet and sends to B
A
R
B

## Slide 135: Security Analysis of ARP
Impersonation
  Any node that hears request can answer …
  … and can say whatever they want
Actual legit receiver never sees a problem
  Because even though later packets carry its IP address, its NIC doesn’t capture them since not its MAC address
Notes: 1/Fab/2013

## Slide 136: Key Ideas in Both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
  Remember your own address & other host’s addresses
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 137: Why Not Use DNS-Like Tables?
When host arrives:
  Assign it an IP address that will last as long it is present
  Add an entry into a table in DNS-server that maps MAC to IP addresses
Answer:
  Names: explicit creation, and are plentiful
  Hosts: come and go without informing network
    Must do mapping on demand
  Addresses: not plentiful, need to reuse and remap
    Soft-state enables dynamic reuse
Notes: Two key points

## Slide 138: No More IPv4 Addresses
IPv4 address space in terms of /8’s
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47
48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79
80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95
96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111
112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127
128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143
144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159
160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175
176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191
192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207
208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223
224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239
240 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255
Class A
Class B
Class C
Class D & E

## Slide 139: No More IPv4 Addresses
24 /8’s on January 12, 2010
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47
48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79
80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95
96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111
112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127
128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143
144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159
160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175
176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191
192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207
208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223
224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239
240 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255

## Slide 140: No More IPv4 Addresses
20 /8’s on April 10, 2010
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47
48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79
80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95
96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111
112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127
128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143
144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159
160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175
176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191
192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207
208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223
224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239
240 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255

## Slide 141: No More IPv4 Addresses
13 /8’s on May 8, 2010
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47
48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79
80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95
96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111
112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127
128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143
144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159
160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175
176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191
192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207
208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223
224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239
240 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255

## Slide 142: No More IPv4 Addresses
7 /8’s on November 30th, 2010
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47
48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79
80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95
96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111
112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127
128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143
144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159
160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175
176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191
192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207
208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223
224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239
240 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255

## Slide 143: No More IPv4 Addresses
0 /8’s on January 31st, 2011!
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47
48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63
64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79
80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95
96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111
112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127
128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143
144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159
160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175
176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191
192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207
208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223
224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239
240 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255

## Slide 144: IPv6
Motivated (prematurely) by address exhaustion
  Address field four times as long
Steve Deering focused on simplifying IP
  Got rid of all fields that were not absolutely necessary
  “Spring Cleaning” for IP
Result is an elegant, if unambitious, protocol

## Slide 145: Larger Address Space
IPv4 = 4,294,967,295 addresses
IPv6 = 340,282,366,920,938,463,374,607,432,768,211,456 addresses
4x in number of bits translates to huge increase in address space!

## Slide 146: Other Significant Protocol Changes
Increased minimum MTU from 576 to 1280
No enroute fragmentation… fragmentation only at source
Header changes
Replace broadcast with multicast
Fragment Offset
Flags
Total Length
Type of Service
IHL
Padding
Options
Destination Address
Source Address
Header Checksum
Protocol
Time to Live
Identification
Version
Next Header
Hop Limit
Flow Label
Traffic Class
Destination Address
Source Address
Payload Length
Version
Field’s Name Kept from IPv4 to IPv6
Fields Not Kept in IPv6
Name and Position Changed in IPv6
New Field in IPv6
Legend
IPv4
IPv6

## Slide 147
IPv4 | IPv6
Addresses are 32 bits (4 bytes) in length. | Addresses are 128 bits (16 bytes) in length
Address (A) resource records in DNS to map host names to IPv4 addresses. | Address (AAAA) resource records in DNS to map host names to IPv6 addresses.
Pointer (PTR) resource records in the IN-ADDR.ARPA DNS domain to map IPv4 addresses to host names. | Pointer (PTR) resource records in the IP6.ARPA DNS domain to map IPv6 addresses to host names.
IPSec is optional and should be supported externally | IPSec support is not optional
Header does not identify packet flow for QoS handling by routers | Header contains Flow Label field, which Identifies packet flow for QoS handling by router.
Both routers and the sending host fragment packets. | Routers do not support packet fragmentation. Sending host fragments packets
Header includes a checksum. | Header does not include a checksum.
Header includes options. | Optional data is supported as extension headers.
ARP uses broadcast ARP request to resolve IP to MAC/Hardware address. | Multicast Neighbor Solicitation messages resolve IP addresses to MAC addresses.
Internet Group Management Protocol (IGMP) manages membership in local subnet groups. | Multicast Listener Discovery (MLD) messages manage membership in local subnet groups.
Broadcast addresses are used to send traffic to all nodes on a subnet. | IPv6 uses a link-local scope all-nodes multicast address.
Configured either manually or through DHCP. | Does not require manual configuration or DHCP.
Must support a 576-byte packet size (possibly fragmented). | Must support a 1280-byte packet size (without fragmentation).

## Slide 148: Roundup: Why IPv6?
Larger address space
Auto-configuration
Cleanup
  Eliminate fragmentation
  Eliminate checksum
    Pseudo-header (w/o Hop Limit) covered by transport layer
  Flow label
  Increase minimum MTU from 576 to 1280
  Replace broadcasts with multicast

## Slide 149: No Checksum!
Provided by transport layer, if needed
Ala TCP, includes pseudo-header
Pseudo-header doesn’t include Hop Limit
  No per-hop re-computation!
  Allows end-to-end implementation (transport layer)
UDP checksum required (wasn’t in IPv4) rfc6936: No more zero
Pseudo-header added to ICMPv6 checksum

## Slide 150: IPv6 Address Notation
RFC 5952
128-bit IPv6 addresses are represented in:
  Eight 16-bit segments
  Hexadecimal (non-case sensitive) between 0000 and FFFF
  Separated by colons
Example:
  3ffe:1944:0100:000a:0000:00bc:2500:0d0b
Two rules for dealing with 0’s
One Hex digit = 4 bits

## Slide 151: 0’s Rule 1 – Leading 0’s
The leading zeroes in any 16-bit segment do not have to be written.
Example
  3ffe : 1944 : 0100 : 000a : 0000 : 00bc : 2500 : 0d0b
  3ffe : 1944 : 100 : a : 0 : bc : 2500 : d0b
  3ffe:1944:100:a:0:bc:2500:d0b

## Slide 152: 0’s Rule 1 – Leading 0’s
Can only apply to leading zeros… otherwise ambiguous results
Example
  3ffe : 1944 : 100 : a : 0 : bc : 2500 : d0b
Could be either
  3ffe : 1944 : 0100 : 000a : 0000 : 00bc : 2500 : 0d0b
  3ffe : 1944 : 1000 : a000 : 0000 : bc00 : 2500 : d0b0
  Which is correct?

## Slide 153: 0’s Rule 1 – Leading 0’s
Can only apply to leading zeros… otherwise ambiguous results
Example
  3ffe : 1944 : 100 : a : 0 : bc : 2500 : d0b
Could be either
  3ffe : 1944 : 0100 : 000a : 0000 : 00bc : 2500 : 0d0b
  3ffe : 1944 : 1000 : a000 : 0000 : bc00 : 2500 : d0b0
  Which is correct?

## Slide 154: 0’s Rule 2 – Double Colon
Any single, contiguous string of 16-bit segments consisting of all zeroes can be represented with a double colon.
ff02 : 0000 : 0000 : 0000 : 0000 : 0000 : 0000 : 0005
ff02 : 0 : 0 : 0 : 0 : 0 : 0 : 5
ff02 : : 5
ff02::5

## Slide 155: 0’s Rule 2 – Double Colon
Only a single contiguous string of all-zero segments can be represented with a double colon.
Example:
2001 : 0d02 : 0000 : 0000 : 0014 : 0000 : 0000 : 0095
Both of these are correct
2001 : d02 :: 14 : 0 : 0 : 95
OR
2001 : d02 : 0 : 0 : 14 :: 95

## Slide 156: 0’s Rule 2 – Double Colon
However, using double colon more than once creates ambiguity
Example
2001:d02::14::95
2001:0d02:0000:0000:0000:0014:0000:0095
2001:0d02:0000:0000:0014:0000:0000:0095
2001:0d02:0000:0014:0000:0000:0000:0095

## Slide 157: Network Prefixes
In IPv4, network portion of address can by identified by either
  Netmask: 255.255.255.0
  Bitcount: /24
Only use bitcount with IPv6
3ffe:1944:100:a::/64
Notes: 2016-1-22

## Slide 158: Special IPv6 Addresses
Default route: ::/0
Unspecified Address: ::/128
  Used in SLAAC (coming later)
Loopback/Local Host: ::1/128
  No longer a /8 of addresses but a single address

## Slide 159: Types of IPv6 Addresses
RFC 4291– “IPv6 Addressing Architecture”
Global Unicast
  Globally routable IPv6 addresses
Link Local Unicast
  Addresses for use on a given subnet
Unique Local Unicast
  Globally unique address for local communication
Multicast
Anycast
  A unicast address assigned to interfaces belonging to different nodes

## Slide 160: Types of IPv6 Addresses
RFC 4291– “IPv6 Addressing Architecture”
Global Unicast
  Globally routable IPv6 addresses
Link Local Unicast
  Addresses for use on a given subnet
Unique Local Unicast
  Globally unique address for local communication
Multicast
Anycast
  A unicast address assigned to interfaces belonging to different nodes

## Slide 161: Global Unicast Addresses
Globally routable addresses
  RFC 3587
3 parts
  48 bit global routing prefix
    Hierarchically-structured value assigned to a site
    Further broken down into Registry, ISP Prefix, and Site Prefix fields
  16 bit Subnet ID
    Identifier of a subnet within a site
  64(!) bit Interface ID
    Identify an interface on a subnet
    Motivated by expected use of MAC addresses (IEEE EUI-64 identifiers) in SLAAC…
  Except GUAs that start with ‘000…’ binary
    Used for, e.g., “IPv4-Mapped IPv6 Addresses” (RFC 4308)

## Slide 162: Global Unicast Addresses
Current ARIN policy is to assign no longer than /32 to an ISP
  American Registry for Internet Numbers
  https://www.arin.net/policy/nrpm.html
  UCSC allocation is 2607:F5F0::/32
IANA currently assigning addresses that start with ‘001…’ binary
  2000::/3
    (2000:: - 3FFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF)
  Supports
    Maximum 229 (536,870,912… 1/8 of an Internet address space of) ISPs
    245 sites (equivalent to 8,192 IASs of sites!)
ISP can delegate a minimum of 216, or 65,535 site prefixes
  Difference between Global Prefix (48 bits) and ISP Prefix (32 bits)

## Slide 163: Subnetting Global Unicast Addresses
Each site can identify 216 (65,535) subnets
  2340:1111:AAAA:1::/64
  2340:1111:AAAA:2::/64
  2340:1111:AAAA:3::/64
  2340:1111:AAAA:4::/64
  ...
Subnet has address space of 264… an IAS of IASs!
Can extend the subnet ID into the interface ID portion of the address…
  Sacrifice ability to use EUI-64 style of SLAAC…
  Maybe not a bad thing… more later

## Slide 164: These are huge numbers!!
Assume average /16’s allocated to ISPs and /22’s allocated to sites in IPv4
And this keeps assumption of /64 subnets!
IPv6 2000::/3 block |  |  | 
Description | Range | Count | Scale vs IPv4
Total # ISPs | /3 – /32 | 229 = 512M | 9,362
Total # Sites | /3 – /48 | 242 = 4T | 1.2M
Sites/ISP | /48 – /64 | 216 = 64K | 1,024
IPv4 class A, B, and C blocks |  |  | 
Total # ISPs | /16 * 7/8 | 57K | 
Total # Sites | /22 * 7/8 | 3.6M | 
Sites/ISP | /16 - /22 | 26 = 64 | 
Notes: Why “7/8” for class A, B, C restriction?
Class A starts with ‘0XX…’ for a total of 4 /3’s
Class B starts with 10X…’ for a total of 2 /3’s
Class C starts with ‘110…’ for 1 /3
Classes D and E start with ‘111…’ for 1/3
Total of 8 /3’s, 7 of which are used in classes A, B, and C… thus 7/8.

## Slide 165: IPv6 Address Space
Allocated
  2000::/3 Global Unicast
  FC00::/7 Unique Local Unicast
  FE80::/10 Link Local Unicast
  FF00::/8 Multicast
Accounts for a bit more than 2125 of the address space.
Unallocated (“Reserved by IETF”)
  /3’s – 4000::, 6000::, 8000::, A000::, C000::
  /4’s – 1000::, E000::
  /5’s – 0800::, F000::
  /6’s – 0400::, F800::
  /7’s – 0200::
  /8’s – 0000::, 0100::
  /9’s – FE00::
  /10’s – FEC0::
Accounts for a little more than 2127, or more than half, of the address space!!
http://www.iana.org/assignments/ipv6-address-space/ipv6-address-space.xml
Notes: Allocated:
2^125 + 2^121 + 2^118 + 2^120
2^118 * (2^7 + 2^3 + 1 + 2^2)
2^118 * (128 + 8 + 1 + 4)
2^118 * 141 > 2^125
Unallocated:
5*2^125 + 2*2^124 + 2*2^123 + 2*2^122 + 2^121 + 2*2^120 + 2^119 + 2^118
5*2^125 + 2^125 + 2^124 + 2^123 + 2^121 + 2^121 + 2^119 + 2^118
6*2^125 + 2^124 + 2^123 + 2*2^121 + 2^119 + 2^118
3*2^126 + 2^124 + 2^123 + 2^122 + 2^119 + 2^118
2^118 * (3*2^8 + 2^6 + 2^5 + 2^4 + 2^1 + 1)
2^118 * (3*256 + 64 + 32 + 16 + 2 + 1)
2^118 * 883 > 2^118 * 512 = 2^118 * 2^9 = 2^127

## Slide 166: Problem with /64 Subnets
Scanning a subnet becomes a DoS attack!
  Creates IPv6 version of 264 ARP entries in routers
  Exhaust address-translation table space
So now we have:
ping6 ff02::1 All nodes in broadcast domain
ping6 ff02::2 All routers in broadcast domain
Solutions
  RFC 6164 recommends use of /127 to protect router-router links
  RFC 3756 suggest “clever cache management” to address more generally

## Slide 167: Types of IPv6 Addresses
RFC 4291– “IPv6 Addressing Architecture”
Global Unicast
  Globally routable IPv6 addresses
Link Local Unicast
  Addresses for use on a given subnet
Unique Local Unicast
  Globally unique address for local communication
Multicast
Anycast
  A unicast address assigned to interfaces belonging to different nodes

## Slide 168: Link-Local Addresses
‘11111110 10…’ binary (FE80::/10)
  According to RFC 4291 bits 11-64 should be 0’s… so really FE80::/64?
For use on a single link.
  Automatic address configuration
  Neighbor discovery (IPv6 ARP)
  When no routers are present
  Routers must not forward
Addresses “chicken-or-egg” problem… need an address to get an address.
Address assignment done unilaterally by node (later)
IPv4 has link-local address (169.254/16, RFC 3927)
  Only used if no globally routable addresses available
Remaining 54 bits

## Slide 170: Types of IPv6 Addresses
RFC 4291– “IPv6 Addressing Architecture”
Global Unicast
  Globally routable IPv6 addresses
Link Local Unicast
  Addresses for use on a given subnet
Unique Local Unicast
  Globally unique address for local communication
Multicast
Anycast
  A unicast address assigned to interfaces belonging to different nodes

## Slide 171: Unique Local Addresses
‘1111110…’ binary (FC00::/7)
Globally unique addresses intended for local communication
  IPv6 equivalent of IPv4 RFC 1918 addresses
Defined in RFC 4193
  Replace “site local” addresses defined in RFC 1884, deprecated in RFC 3879
Should not be installed in global DNS
  Can be installed in “local DNS”

## Slide 172: Unique Local Addresses
4 parts
  “L” bit always 1
  Global ID (40 bits) randomly generated to enforce the idea that these addresses are not to be globally routed or aggregated
  Subnet ID (16 bits)… same as Globally Unique Subnet ID
  Interface ID (64 bits)… same as Globally Unique Interface ID

## Slide 173: Types of IPv6 Addresses
RFC 4291– “IPv6 Addressing Architecture”
Global Unicast
  Globally routable IPv6 addresses
Link Local Unicast
  Addresses for use on a given subnet
Unique Local Unicast
  Globally unique address for local communication
Multicast
Anycast
  A unicast address assigned to interfaces belonging to different nodes

## Slide 174: Multicast Addresses
‘11111111…’ binary (FF00::/8)
Equivalent to IPv4 multicast (224.0.0.0/8)
3 parts
  Flag (4 bits)
  Scope (4 bits)

## Slide 175: Reserved Multicast Addresses
All nodes
  FF01::1 – interface-local; used for loopback multicast transmissions
  FF02::1 – link-local; replaces IPv4 broadcast address (all 1’s host)
All routers
  FF01::2 (interface-local), FF02::2 (link-local)
Solicited-Node multicast
  Used in Neighbor Discovery Protocol (later)
  FF02::FF00:0/104 (FF02::FFXX:XXXX)
  Construct by replacing ‘XX:XXXX’ above with low-order 24 bits of a nodes unicast or anycast address
  Example
    For unicast address 4037::01:800:200E:8C6C
    Solicited-Node multicast is FF02::1:FF0E:8C6C

## Slide 176: Types of IPv6 Addresses
RFC 4291– “IPv6 Addressing Architecture”
Global Unicast
  Globally routable IPv6 addresses
Link Local Unicast
  Addresses for use on a given subnet
Unique Local Unicast
  Globally unique address for local communication
Multicast
Anycast
  A unicast address assigned to interfaces belonging to different nodes

## Slide 177: Anycast Addresses
Allocated from unicast address space
  Syntactically indistinguishable from unicast addresses
An address assigned to more than one node
Anycast traffic routed to the “nearest” host with the anycast address
Typically used for a service (e.g. local DNS servers)
Nodes must be configured to know an address is anycast
  Don’t do Duplicate Address Detection
  Advertise a route?

## Slide 178: A Node’s Required Addresses
Link-local address for each interface
Configured unicast or anycast addresses
Loopback address
All-Nodes multicast interface and link addresses
Solicited-Node multicast for each configured unicast and anycast address
Multicast addresses for all groups the node is a member of
Routers must add
  Subnet-Router anycast address for each interface
    Subnet prefix with all 0’s host part
  All-Routers multicast address
Red = new for IPv6

## Slide 179: Roundup: IPv6 Addresses
“Interface ID” (host part) is 64 bits
New addresses required by all nodes (host or router)
  Link-local address
  All-nodes interface-local and link-local multicast
  Solicited-node multicast for each unicast/anycast address
New addresses required by routers
  All-routers interface-local, link-local and site-local multicast
  Subnet-Router anycast for each interface?

## Slide 180: Host Configuration

## Slide 181: Assigning Address to Interfaces
Static (manual) assignment
  Needed for network equipment
DHCPv6
  Needed to track who uses an IP address
StateLess Address AutoConfiguration (SLAAC)
  New to IPv6
Describe SLAAC in the following…

## Slide 182: SLAAC
RFC 4862 – IPv6 Stateful Address Autoconfiguration
Used to assign unicast addresses to interfaces
  Link-Local Unicast
  Global Unicast
  Unique-Local Unicast?
Goal is to minimize manual configuration
  No manual configuration of hosts
  Limited router configuration
  No additional servers
Use when “not particularly concerned with the exact addresses hosts use”
  Otherwise use DHCPv6 (RFC 3315)

## Slide 183: SLAAC Building Blocks
Interface IDs
Neighbor Discovery Protocol
SLAAC Process

## Slide 184: SLAAC Building Blocks
Interface IDs
Neighbor Discovery Protocol
SLAAC Process

## Slide 185: Interface IDs
Used to identify a unique interface on a link
Thought of as the “host portion” of an IPv6 address.
64 bits: To support both 48 bit and 64 bit IEEE MAC addresses
Required to be unique on a link
Subnets using auto addressing must be /64s.
EUI-64 vs Privacy interface IDs

## Slide 186: IEEE EUI-64 Option for Interface ID
Use interface MAC address
Insert FFFE to convert EUI-48 to EUI-64
FlipUniversal/Local bit to “1”
  Section 2.5.1 RFC 4291

## Slide 187: Privacy Option for Interface ID
Using MAC uniquely identifies a host… security/privacy concerns!
Microsoft(!) defined an alternative solution for Interface IDs (RFC 4941)
Hosts generates a random 64 bit Interface ID
Randomly generated

## Slide 188: SLAAC Building Blocks
Interface IDs
Neighbor Discovery Protocol
SLAAC Process

## Slide 189: NDP
RFC 4861 – Neighbor Discovery for IPv6
Used to
  Determine MAC address for nodes on same subnet (ARP)
  Find routers on same subnet
  Determine subnet prefix and MTU
  Determine address of local DNS server (RFC 6106)
Uses 5 ICMPv6 messages
  Router Solicitation (RS) – request routers to send RA
  Router Advertisement (RA) – router’s address and subnet parameters
  Neighbor Solicitation (NS) – request neighbor’s MAC address (ARP Request)
  Neighbor Advertisement (NA) – MAC address for an IPv6 address (ARP Reply)
  Redirect – inform host of a better next hop for a destination

## Slide 190: NDP RS & RA
Router Solicitation (RS)
  Originated by hosts to request that a router send an RA
  Source = unspecified (::) or link-local address,
  Destination = All-routers multicast (FF02::2)
Router Advertisement (RA)
  Originated by routers to advertise their address and link-specific parameters
  Sent periodically and in response to Router Solicitation messages
  Source = link-local address,
  Destination = All-nodes multicast (FF02::1)
RA (Address, prefix, link MTU)
RS (Need RA from Router)
ipv6 unicast-routing

## Slide 191: NDP NS & NA
Neighbor Solicitation (NS)
  Request target MAC address while providing target of source (IPv4 ARP Request)
  Used to resolve address or verify reachability of neighbor
  Source = unicast or “::” (Duplicate Address Detection… next slide)
  Destination = solicited-node multicast
Neighbor Advertisement (NA)
  Advertise MAC address for given IPv6 address (IPv4 ARP Reply)
  Respond to NS or communicate MAC address change
  Source = unicast, destination = NS’s source or all-nodes multicast (if source “::”)
ipv6 unicast-routing
NS (Request for another node’s Link Layer Address)
NA (Sent in response to NS)

## Slide 192: Duplicate Address Detection
Duplicate Address Detection (DAD) used to verify address is unique in subnet prior to assigning it to an interface
MUST take place on all unicast addresses, regardless of whether they are obtained through stateful, stateless or manual configuration
MUST NOT be performed on anycast addresses
Uses Neighbor Solicitation and Neighbor Advertisement messages
NS sent to solicited-node multicast; if no NA received address is unique
Solicited-node multicast: FF02::1:FF:0/104 w/ last 24 bits of target

## Slide 193: Duplicate Address Detection
My Global Address is
2340:1111:AAAA:1:213:19FF:FE7B:5004
“Tentative”: Need to do Duplicate Address Detection
NS (Neighbor Solicitation)
- Target Address = 2340:1111:AAAA:1:213:19FF:FE7B:5004
Destination: Solicited-Node Multicast Address = FF02::1::FF7B:5004
I need to make sure nobody else has this Global Unicast Address…

## Slide 194: SLAAC Building Blocks
Interface IDs
Neighbor Discovery Protocol
SLAAC Process

## Slide 195: SLAAC Steps
Select link-local address
Verify “tentative” address not in use by another host with DAD
Send RS to solicit RAs from routers
Receive RA with
  router address,
  subnet MTU,
  subnet prefix,
  local DNS server (RFC 6106)
Generate global unicast address
Verify address is not in use by another host with DAD

## Slide 196
NS (Neighbor Solicitation)
Make sure Link-local address is unique
DAD: Okay if no NA returned
Destination: Solicited-Node Multicast Address
Target address = Link-local address
A
Link-local Address =
Link-local Prefix + Interface Identifier (EUI-64 format)
FE80 [64 bits] + [48 bit MAC u/l flipped + 16 bit FFFE]
RS (Router Solicitation)
Get Prefix and other information
RA (Router Advertisement)
Source = Link-local address
Destin = FF02::1 All nodes multicast address
Query = Prefix, Default Router, MTU, options
IPv6 Address =
Prefix + Interface ID (EUI-64 format)
[64 bits] + [48 bit MAC u/l flipped + 16 bit FFFE]
NS (Neighbor Solicitation)
Make sure IPv6 Address is unique
Target Address = IPv6 Address
DAD: Okay if no NA returned
Make sure Link-local address is unique
Create Link-local address
Get Network Prefix to create Global unicast address
DAD

## Slide 197: Prefix Leases
Prefix information contained in RA includes lifetime information
  Preferred lifetime: when an address’s preferred lifetime expires SHOULD only be used for existing communications
  Valid lifetime: when an address’s valid lifetime expires it MUST NOT be used as a source address or accepted as a destination address.
Unsolicited RAs can reduce prefix lifetime values
  Can be used to force re-addressing

## Slide 198: Roundup: ICMPv6
Implements router discovery and ARP functions
ICMPv6 messages
  Router Solicitation/Router Advertisement
  Neighbor Solicitation/Neighbor Advertisement
  (Next hop) Redirect
Duplicate Address Detection (DAD)
  verify unique link-local and global-unicast addresses
  Uses:
    NS/NA (i.e. gratuitous ARP)
    Solicited node multicast address

## Slide 199: Review - SLAAC
Assigns link-local and global-unicast addresses
Goals
  Eliminate manual configuration
  Require minimal router configuration
  Require no additional servers
Host part options
  EUI-64
  Random (“privacy” addresses)
Steps
  Generate link-local address and verify with DAD
  Find router - RS/RA
  Generate global unicast address and verify with DAD

## Slide 200: Improving on IPv4 and IPv6?
Why include unverifiable source address?
  Would like accountability and anonymity (now neither)
  Return address can be communicated at higher layer
Why packet header used at edge same as core?
  Edge: host tells network what service it wants
  Core: packet tells switch how to handle it
    One is local to host, one is global to network
Some kind of payment/responsibility field?
  Who is responsible for paying for packet delivery?
  Source, destination, other?
Other ideas?

## Slide 201: Summary Network Layer
understand principles behind network layer services:
  network layer service models
  forwarding versus routing (versus switching)
  how a router works
  routing (path selection)
  IPv6
Algorthims
  Two routing approaches (LS vs DV)
  One of these in detail (LS)
  ARP
Notes: 30-jan-2015 / 25-jan-2016