## Slide 1: OpenFlow on top of NetFPGA
Part I: Introduction to OpenFlow
NetFPGA Spring School 2010
Some slides with permission from Prof. Nick McKeown.
OpenFlow was originally developed by Stanford University.
Nadi Sarrar
TU-Berlin / T-Labs
Research group Prof. Anja Feldmann, Ph.D.
Notes: <number>

## Slide 2: What is OpenFlow?
OpenFlow on top of NetFPGA - Introduction
<number>
Support experimental protocols in production networks
→ Foundation for innovation
Specify an API to control Ethernet switch forwarding decisions
→ Towards software-defined, open-source networks
Notes: <number>
* Some high-level statements on what OpenFlow is.
* Innovation is hard, because in current network, we lack the possiblity to deploy experimental protocols
* How are we supposed to evaluate new ideas, without testing on real user data traffic?
* By allowing a remote control entity to modify the forwarding table of switches, we gain a very deep control of how a network behaves.
* We can decide, how flows are processed, what fields are modified, to which output port they are forwarded.
* With that approach, we achieve a software-defined network, that can handle production traffic.

## Slide 3: Why OpenFlow?
OpenFlow on top of NetFPGA - Introduction
<number>
Cost
500,000 servers
Fanout of 50  10,000 switches
$10k commercial switch  $100M
$1k custom-built switch  $10M
Savings in 10 data centers = $900M
Control
Optimize for features needed
Customize for services & apps
Quickly improve and innovate
Example:
New data center
Notes: <number>

## Slide 4: Why OpenFlow?
OpenFlow on top of NetFPGA - Introduction
<number>
Network innovation today is difficult:
Switches and routers are “closed”
Software-only approach lacks performance and scalability
→ Need high-performance, programmable networking equipment (substrate)
Notes: <number>

## Slide 5: Networking hardware substrate
OpenFlow on top of NetFPGA - Introduction
<number>
What do we mean by programmable equipment?
Need to define a substrate to build upon.
Let's learn from evolution of the PC!
Notes: <number>

## Slide 6: PC hardware abstraction
OpenFlow on top of NetFPGA - Introduction
<number>
OS abstracts hardware substrate
→ Innovation in applications
Application
Computer
Application
Computer
Operating System
Application
Application
. . .
Notes: <number>

## Slide 7: PC hardware abstraction
OpenFlow on top of NetFPGA - Introduction
<number>
Simple, common, stable, hardware substrate below.
Programmability and competition:
→ Innovation in OS and applications
Windows
(OS)
Computer
Windows
(OS)
App
. . .
Application
Application
. . .
Linux
(OS)
or
Mac OS
(OS)
or
Computer
App
Notes: <number>

## Slide 8: PC hardware virtualization
OpenFlow on top of NetFPGA - Introduction
<number>
Strong isolation model:
→ Innovation in infrastructure
Windows
(OS)
Linux
(OS)
or
Mac OS
(OS)
or
Computer
App
. . .
App
Windows
(OS)
Linux
(OS)
or
Mac OS
(OS)
or
Computer
App
. . .
App
Virtualization
Notes: <number>

## Slide 9: Networking substrate
OpenFlow on top of NetFPGA - Introduction
<number>
Let's apply a similar abstraction model to networking.
Notes: <number>

## Slide 10: Network hardware abstraction
OpenFlow on top of NetFPGA - Introduction
<number>
Simple, common, stable, hardware substrate below.
Programmability and competition:
→ Innovation in network controllers
Computer
Windows
(OS)
App
. . .
Application
Application
. . .
Controller
OpenFlow Network
App
Notes: <number>

## Slide 11: Step 1: Separate intelligence from datapath
OpenFlow on top of NetFPGA - Introduction
<number>
New function!
Operators, users,
3rd party developers, researchers, …
OpenFlow protocol (OFP)
Notes: <number>

## Slide 12: Step 2: Cache decisions in minimal flow-based datapath
OpenFlow on top of NetFPGA - Introduction
<number>
“If header = x, send to port 4”
“If header = ?, send to me”
“If header = y, overwrite header with z, send to ports 5,6”
Flow
Table
OFP
Notes: <number>

## Slide 13: Example
OpenFlow on top of NetFPGA - Introduction
<number>
Host A
Host B
“Default: send to controller”
OFP
Flow Table
Controller
OF Switch
If dest = B: send to port 2”
1
2
Notes: <number>

## Slide 14: Flow
OpenFlow on top of NetFPGA - Introduction
<number>
Flow's can be defined via 10-tuples:
Allows for flexible, multidimensional flow definitions.
Notes: <number>

## Slide 15: Topology slicing
OpenFlow on top of NetFPGA - Introduction
<number>
How to slice the network to allow production and experimental use at the same time?
How to do virtualization?
Again, let's learn from PC's :)
Notes: <number>

## Slide 16: Virtualization
OpenFlow on top of NetFPGA - Introduction
<number>
Strong isolation model:
→ Innovation in infrastructure
Controller 1
App
. . .
App
Virtualization (FlowVisor)
OpenFlow Network
Controller N
. . .
Windows
(OS)
Linux
(OS)
or
Mac OS
(OS)
or
Computer
App
. . .
App
Virtualization
Notes: <number>

## Slide 17: FlowVisor Rob Sherwood (rob.sherwood@stanford.edu)
OpenFlow on top of NetFPGA - Introduction
<number>
OpenFlow
Switch
FlowVisor
Bob’s
Controller
Alice’s
Controller
OpenFlow
Switch
OpenFlow
Switch
OFP
OFP
Notes: <number>

## Slide 18: FlowVisor Rob Sherwood (rob.sherwood@stanford.edu)
OpenFlow on top of NetFPGA - Introduction
<number>
A proxy between switch and guest controller
  Parses and rewrites OpenFlow messages as they pass
Ensures that one experiment doesn’t affect another
Allows rich virtual network boundaries
  By port, by IP, by flow, by time, etc.
Define virtualization rules in software
Notes: <number>

## Slide 19: Available controllers and switches
OpenFlow on top of NetFPGA - Introduction
<number>
NOX (http://noxrepo.org/, GNU GPLv3)
  Provides network-wide view of the topology
  C++ and Python modules make decisions
OpenVSwitch (http://openvswitch.org/, Apache 2)
  Soft-switch, replaces Linux bridge
  Designed to be used with VM's
Simple controller (reference implementation)
Hardware switches:
  Quanta LB4G (Broadcom), HP ProCurve 5400 series, NEC IP8800/S3640, Juniper MX, Cisco Catalyst, NetFPGA
Notes: <number>

## Slide 20: NetFPGA as an OpenFlow switch
OpenFlow on top of NetFPGA - Introduction
<number>
J. Naous et. al., “ Implementing an OpenFlow Switch on the NetFPGA platform”, ANCS 2008
Notes: <number>

## Slide 21: OpenFlow activity in Europe
OpenFlow on top of NetFPGA - Introduction
<number>
Successful EU proposals:
OFELIA (5 OpenFlow islands across Europe, partners from academia and industry)
CHANGE (Flow-processing research, uses OFELIA testbed)
SPARC (Split architecture, MPLS)
Notes: <number>

## Slide 22: Thank you!
OpenFlow on top of NetFPGA - Introduction
<number>
http://www.openflowswitch.org
Notes: <number>

## Slide 23: OpenFlow on top of NetFPGA
Part II: Hands-on workshop
NetFPGA Spring School 2010
Nadi Sarrar
TU-Berlin / T-Labs
Research group Prof. Anja Feldmann, Ph.D.
Notes: <number>

## Slide 24: Exercise overview
OpenFlow on top of NetFPGA - Hands-on workshop
<number>
192.168.1.1
192.168.2.1
PC
PING
OpenFlow
protocol
NetFPGA
Controller
Notes: <number>

## Slide 25: 1. Bitfile
OpenFlow on top of NetFPGA - Hands-on workshop
<number>
PC
OpenFlow
protocol
NetFPGA
Controller
openflow_switch.bit
Bitfile to program the NetFPGA:
/root/openflow/openflow_switch.bit
Download bitfile to NetFPGA:
nf2_download $bitfile
192.168.1.1
192.168.2.1
Notes: <number>

## Slide 26: 2. Kernel modules
OpenFlow on top of NetFPGA - Hands-on workshop
<number>
PC
OpenFlow
protocol
NetFPGA
Controller
openflow_switch.bit
ofdatapath.ko
ofdatapath_netfpga.ko
Load general OpenFlow datapath module:
insmod /root/openflow/ofdatapath.ko
Load NetFPGA datapath module:
insmod /root/openflow/ofdatapath_netfpga.ko
192.168.1.1
192.168.2.1
Notes: <number>

## Slide 27: 3a. Datapath
OpenFlow on top of NetFPGA - Hands-on workshop
<number>
PC
OpenFlow
protocol
NetFPGA
Controller
openflow_switch.bit
ofdatapath.ko
ofdatapath_netfpga.ko
Create a datapath:
dpctl adddp nl:0
Display datapath info:
dpctl show nl:0
192.168.1.1
192.168.2.1
Notes: <number>

## Slide 28: 3b. Datapath
OpenFlow on top of NetFPGA - Hands-on workshop
<number>
PC
OpenFlow
protocol
NetFPGA
Controller
openflow_switch.bit
ofdatapath.ko
ofdatapath_netfpga.ko
Add interfaces to datapath:
dpctl addif nl:0 nf2c0 nf2c1 nf2c2 nf2c3
Display datapath info:
dpctl show nl:0
192.168.1.1
192.168.2.1
Notes: <number>

## Slide 29: 4. Statistics
OpenFlow on top of NetFPGA - Hands-on workshop
<number>
PC
OpenFlow
protocol
NetFPGA
Controller
openflow_switch.bit
ofdatapath.ko
ofdatapath_netfpga.ko
Display flow table entries:
dpctl dump-flows nl:0
Display hardware information:
cat /proc/net/openflow/netfpga
192.168.1.1
192.168.2.1
Notes: <number>

## Slide 30: 5. Controller
OpenFlow on top of NetFPGA - Hands-on workshop
<number>
PC
OpenFlow
protocol
NetFPGA
Controller
controller
ofprotocol
openflow_switch.bit
ofdatapath.ko
ofdatapath_netfpga.ko
Run controller (passive mode):
controller ptcp:localhost:6633
Run OpenFlow protocol daemon (active mode):
ofprotocol nl:0 tcp:localhost:6633
192.168.1.1
192.168.2.1
Notes: <number>

## Slide 31: 5. Controller
OpenFlow on top of NetFPGA - Hands-on workshop
<number>
Userspace
Kernel / Hardware
PC
OpenFlow
protocol
NetFPGA
Controller
controller
ofprotocol
openflow_switch.bit
ofdatapath.ko
ofdatapath_netfpga.ko
Run controller (passive mode):
controller ptcp:localhost:6633
Run OpenFlow protocol daemon (active mode):
ofprotocol nl:0 tcp:localhost:6633
192.168.1.1
192.168.2.1
Notes: <number>

## Slide 32: 6. Testing
OpenFlow on top of NetFPGA - Hands-on workshop
<number>
PC
PING
OpenFlow
protocol
NetFPGA
Controller
controller
ofprotocol
openflow_switch.bit
ofdatapath.ko
ofdatapath_netfpga.ko
Userspace
Kernel / Hardware
Attach two nodes to any two ports.
Assign IP addresses.
IP should work (try to ping).
Monitor flow table: dpctl dump-flows nl:0
192.168.1.1
192.168.2.1
Notes: <number>