## Slide 1: Day 2: NetFPGA Cambridge Spring School Module Development and Testing
Presented by:
Andrew W. Moore and David Miller
(University of Cambridge)
Martin Žádník
(Brno University of Technology)
Cambridge UK
March 15-19, 2010
http://NetFPGA.org

## Slide 2: Outline
Tree Structure
Develop a cryptography module
  Quick overview of XOR “cryptography”
  Implement crypto module
  Write software simulations
  Synthesize
  Write hardware tests

## Slide 3: Tree Structure
NF2
bin
lib
projects
bitfiles
(scripts for running simulations and setting up the environment)
(contains the bitfiles for all projects that have been synthesized)
(stable common modules and common parts needed for simulation/synthesis/design)
(user projects, including reference designs)

## Slide 4: Tree Structure (2)
lib
C
java
Makefiles
Perl5
python
scripts
verilog
(common software and code for reference designs)
(contains software for the graphical user interface)
(makefiles for simulation and synthesis)
(common libraries to interact with reference designs and aid in simulation)
(common libraries to aid in regression tests)
(scripts for common functions)
(modules and files that can be reused for design)

## Slide 5: Tree Structure (3)
projects
doc
include
regress
src
sw
synth
verif
(project specific documentation)
(contains file to include verilog modules from lib, and creates project specific register defines files)
(regression tests used to test generated bitfiles)
(contains non-library verilog code used for synthesis and simulation)
(all software parts of the project)
(contains user .xco files to generate cores and Makefile to implement the design)
(simulation tests)

## Slide 6: Cryptography
Simple cryptography – XOR
A | B | A ^ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 7: Cryptography (cont.)
Example:
Explanation:
  A ^ A = 0
  So, M ^ K ^ K = M ^ 0 = M
Message: | 00111011
Key: | 10110001
Message ^ Key: | 10001010
Message ^ Key ^ Key: | 00111011

## Slide 8: Implementing a Crypto Module (1)
What do we want to encrypt?
  IP payload only
    Plaintext IP header allows routing
    Content is hidden
  Encrypt bytes 35 onward
    Bytes 1-14 – Ethernet header
    Bytes 15-34 – IPv4 header (assume no options)
  Assume all packets are IPv4 for simplicity

## Slide 9: Implementing a Crypto Module (2)
State machine (draw on next page):
  Module headers on each packet
  Datapath 64-bits wide
    34 / 8 is not an integer! 
Inside the crypto module

## Slide 10: Crypto Module State Diagram
Hint: We suggest 4 operational states(3 if you’re feeling adventurous) and one initialization/startup state
Skip
Module
Headers

## Slide 11: State Diagram to Verilog (1)
Module location
  Crypto module to encrypt and decrypt packets
MAC
RxQ
CPU
RxQ
MAC
RxQ
CPU
RxQ
MAC
RxQ
CPU
RxQ
MAC
RxQ
CPU
RxQ
Input Arbiter
Output Port Lookup
MAC
TxQ
CPU
TxQ
MAC
TxQ
CPU
TxQ
MAC
TxQ
CPU
TxQ
MAC
TxQ
CPU
TxQ
Output Queues
Crypto
Notes: <number>

## Slide 12: Inter-module Communication
data
ctrl
wr
rdy

## Slide 13: State Diagram to Verilog (2)
Projects:
  Each design represented by a project
  Format: NF2/projects/<proj_name>
  NF2/projects/crypto_nic
  Consists of:
  Missing:
    Verilog source
    Simulation tests
    Hardware tests
Libraries
Optional software
    State diagram implementation
    Simulation tests
    Regression tests

## Slide 14: State Diagram to Verilog (3)
Projects (cont):
  Pull in modules from NF2/lib/verilog
    Generic modules that are re-used in multiple projects
    Specify shared modules in project’s include/lib_modules.txt
  Local src modules override shared modules
  crypto_nic:
    Local user_data_path.v, crypto.v
    Everything else: shared modules

## Slide 15: State Diagram to Verilog (4)
Your task:
  Copy NF2/lib/verilog/module_template/src/module_template.v to NF2/projects/crypto_nic/src/crypto.v
  Implement your state diagram in src/crypto.v
    Small fallthrough FIFO
    Generic register interface

## Slide 16: Register definitions
Register symbols defined using XML (new in NF2.0)
  All register symbols (both Verilog and PERL) controlled by XML definitions See outputs include/registers.v and lib/Perl5/reg_defines_crypto_nic.pm
  Module specific registers defined in include/crypto.xml
  Module XML must be explicitly included in project XML definition include/project.xml
  More at: http://netfpga.org/foswiki/bin/view/NetFPGA/OneGig/DevelopersGuide#Register_System

## Slide 17: Generic Registers Module
generic_regs # (
.UDP_REG_SRC_WIDTH (UDP_REG_SRC_WIDTH),
.TAG (`CRYPTO_BLOCK_ADDR),
.REG_ADDR_WIDTH (`CRYPTO_REG_ADDR_WIDTH),
.NUM_COUNTERS (0),
.NUM_SOFTWARE_REGS (1),
.NUM_HARDWARE_REGS (0))
crypto_regs (
.reg_req_in (reg_req_in),
…
.reg_src_out (reg_src_out),
…
.software_regs (key),
.hardware_regs (),
…

## Slide 18: Testing: Simulation (1)
Simulation allows testing without requiring lengthy synthesis process
NetFPGA provides Perl simulation infrastructure to:
  Send/receive packets
    Physical ports and CPU
  Read/write registers
  Verify results
Simulations run in ModelSim/VCS

## Slide 19: Testing: Simulation (2)
Simulations located in project/verif
Multiple simulations per project
  Test different features
Example:
  crypto_nic/verif/test_nic_short
    Send one packet from CPU, expect packet out physical port
    Send one packet in physical port, expect packet to CPU

## Slide 20: Testing: Simulation (3)
Useful functions:
  nf_PCI_read32(delay, batch, addr, expect)
  nf_PCI_write32(delay, batch, addr, value)
  nf_packet_in(port, length, delay, batch, pkt)
  nf_expected_packet(port, length, pkt)
  nf_dma_data_in(length, delay, port, pkt)
  nf_expected_dma_data(port, length, pkt)
  make_IP_pkt(length, da, sa, ttl, dst_ip, src_ip)
  encrypt_pkt(key, pkt)
  decrypt_pkt(key, pkt)

## Slide 21: Testing: Simulation (4)
Your task:
  Template files NF2/projects/crypto_nic/verif/test_crypto_encrypt/make_pkts.pl NF2/projects/crypto_nic/verif/test_crypto_decrypt/make_pkts.pl
  Implement your Perl verif tests
    Use the example verif test (test_nic_short)

## Slide 22: Running Simulations
Set env. variables to reference your project
    NF2_DESIGN_DIR=/root/NF2/projects/<project>
    PERL5LIB=/root/NF2/projects/<project>/lib/Perl5:
    /root/NF2/lib/Perl5:
Use command nf2_run_test.pl
  Optional parameters
    --major <major_name>
    --minor <minor_name>
    --gui (starts the default viewing environment)
    test_crypto_encrypt
major
minor

## Slide 23: Running Simulations
When running modelsim interactively:
  Click "no" when simulator prompts to finish
  Changes to Verilog can be recompiled without quitting ModelSim (unless make_pkts.pl has changed):
    bash# cd /tmp/$(whoami)/verif/<projname>;
    make model_sim
    VSIM 5> restart -f; run -a
  Do ensure $NF2_DESIGN_DIR is correct
    bash# echo $NF2_DESIGN_DIR

## Slide 24: Running Simulations (optional)
When running modelsim interactively:
  Create new waveform windows:
    VSIM 4> view -new wave -title <my_title>
  Save waveform windows by clicking ‘disc’ icon
  Restore waveform window:
    VSIM 5> view -new wave -title <my_title>
    VSIM 6> do <my_wave>.do

## Slide 25: Synthesis
To synthesize your project
  Run make in the synth directory (NF2/projects/crypto_nic/synth)

## Slide 26: Regression Tests
Test hardware module
Perl Infrastructure provided to
  Read/Write registers
  Read/Write tables
  Send Packets
  Check Counters

## Slide 27: Example Regression Tests
Reference Router
  Send Packets from CPU
  Longest Prefix Matching
  Longest Prefix Matching Misses
  Packets dropped when queues overflow
  Receiving Packets with IP TTL <= 1
  Receiving Packets with IP options or non IPv4
  Packet Forwarding
  Dropping packets with bad IP Checksum

## Slide 28: Perl Libraries
Specify the Interfaces
  eth1, eth2, nf2c0 … nf2c3
Start packet capture on Interfaces
Create Packets
  MAC header
  IP header
  PDU
Read/Write Registers
Read/Write Reference Router tables
  Longest Prefix Match
  ARP
  Destination IP Filter

## Slide 29: Regression Test Examples
Reference Router
  Packet Forwarding
    regress/test_packet_forwarding
  Longest Prefix Match
    regress/test_lpm
  Send and Receive
    regress/test_send_rec

## Slide 30: Creating a Regression Test
Useful functions:
  nftest_regwrite(interface, addr, value)
  nftest_regread(interface, addr)
  nftest_send(interface, frame)
  nftest_expect(interface, frame)
  encrypt_pkt(key, pkt)
  decrypt_pkt(key, pkt)
  $pkt = NF2::IP_pkt->new(len => $length, DA => $DA, SA => $SA, ttl => $TTL, dst_ip => $dst_ip, src_ip => $src_ip);
  $pkt->packed (with nftest_{send,expect})

## Slide 31: Creating a Regression Test (2)
Your task:
  Template files NF2/projects/crypto_nic/regress/test_crypto_encrypt/run
  Implement your Perl verif tests

## Slide 32: Running Regression Test
Run the command
  nf2_regress_test.pl --project crypto_nic