## Slide 1
Computer Networking
Lent Term
M/W/F 11:00-12:00
LT1 in Gates Building
Slide Set 3 (Topic 5)
Andrew W. Moore
Andrew.Moore@cl.cam.ac.uk
2018-2019

## Slide 2: Topic 5 – Transport
Our goals:
understand principles behind transport layer services:
  multiplexing/demultiplexing
  reliable data transfer
  flow control
  congestion control
  beyond TCP
learn about transport layer protocols in the Internet:
  UDP: connectionless transport
  TCP: connection-oriented transport
  TCP congestion control
  TCP flow control

## Slide 3: Transport Layer
Commonly a layer at end-hosts, between the application and network layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 4: Why a transport layer?
IP packets are addressed to a host but end-to-end communication is between application processes at hosts
  Need a way to decide which packets go to which applications (more multiplexing)

## Slide 5: Why a transport layer?
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Application
Application
Host A
Host B

## Slide 6: Why a transport layer?
Transport
Network
Datalink
Physical
Application
Host A
Host B
Datalink
Physical
browser
telnet
mmedia
ftp
browser
IP
many application processes
Drivers +NIC
Operating System

## Slide 7: Why a transport layer?
Host A
Host B
Datalink
Physical
browser
telnet
mmedia
ftp
browser
IP
many application processes
Datalink
Physical
telnet
ftp
IP
HTTP server
Transport
Transport
Communication between hosts
(128.4.5.6 162.99.7.56)
Communication between processes
at hosts

## Slide 8: Why a transport layer?
IP packets are addressed to a host but end-to-end communication is between application processes at hosts
  Need a way to decide which packets go to which applications (mux/demux)
IP provides a weak service model (best-effort)
  Packets can be corrupted, delayed, dropped, reordered, duplicated
  No guidance on how much traffic to send and when
  Dealing with this is tedious for application developers

## Slide 9: Role of the Transport Layer
Communication between application processes
  Multiplexing between application processes
  Implemented using ports

## Slide 10: Role of the Transport Layer
Communication between application processes
Provide common end-to-end services for app layer [optional]
  Reliable, in-order data delivery
  Paced data delivery: flow and congestion-control
    too fast may overwhelm the network
    too slow is not efficient

## Slide 11: Role of the Transport Layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
  also SCTP, MTCP, SST, RDP, DCCP, …

## Slide 12: Role of the Transport Layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
UDP is a minimalist, no-frills transport protocol
  only provides mux/demux capabilities

## Slide 13: Role of the Transport Layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
UDP is a minimalist, no-frills transport protocol
TCP is the totus porcus protocol
  offers apps a reliable, in-order, byte-stream abstraction
  with congestion control
  but no performance (delay, bandwidth, ...) guarantees

## Slide 14: Role of the Transport Layer
Communication between processes
  mux/demux from and to application processes
  implemented using ports

## Slide 15: Context: Applications and Sockets
Socket: software abstraction by which an application process exchanges network messages with the (transport layer in the) operating system
  socketID = socket(…, socket.TYPE)
  socketID.sendto(message, …)
  socketID.recvfrom(…)
Two important types of sockets
  UDP socket: TYPE is SOCK_DGRAM
  TCP socket: TYPE is SOCK_STREAM

## Slide 16: Ports
Problem: deciding which app (socket) gets which packets
  Solution: port as a transport layer identifier
    16 bit identifier
  OS stores mapping between sockets and ports
  a packet carries a source and destination port number in its transport layer header
For UDP ports (SOCK_DGRAM)
  OS stores (local port, local IP address)  socket
For TCP ports (SOCK_STREAM)
  OS stores (local port, local IP, remote port, remote IP)  socket

## Slide 17
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
IP Payload
Notes: Go through very fast

## Slide 18
4
5
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
IP Payload
Notes: Go through very fast

## Slide 19
4
5
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
6 = TCP 17 = UDP
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
header and Payload
TCP or
UDP
Notes: Go through very fast

## Slide 20
4
5
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
6 = TCP 17 = UDP
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
16-bit Source Port
16-bit Destination Port
More transport header fields ….
header and Payload
TCP or
UDP
Notes: Go through very fast

## Slide 21: Recap: Multiplexing and Demultiplexing
Host receives IP packets
  Each IP header has source and destination IP address
  Each Transport Layer header has source and destination port number
Host uses IP addresses and port numbers to direct the message to appropriate socket

## Slide 22: More on Ports
Separate 16-bit port address space for UDP and TCP
“Well known” ports (0-1023): everyone agrees which services run on these ports
  e.g., ssh:22, http:80
  helps client know server’s port
Ephemeral ports (most 1024-65535): dynamically selected: as the source port for a client process

## Slide 23: UDP: User Datagram Protocol
Lightweight communication between processes
  Avoid overhead and delays of ordered, reliable delivery
UDP described in RFC 768 – (1980!)
  Destination IP address and port to support demultiplexing
  Optional error checking on the packet contents
    (checksum field of 0 means “don’t verify checksum”)
    ((this idea of optional checksum is removed in IPv6))
SRC port
DST port
checksum
length
DATA

## Slide 24: Why a transport layer?
IP packets are addressed to a host but end-to-end communication is between application processes at hosts
  Need a way to decide which packets go to which applications (mux/demux)
IP provides a weak service model (best-effort)
  Packets can be corrupted, delayed, dropped, reordered, duplicated

## Slide 25: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
In a perfect world, reliable transport is easy
But the Internet default is best-effort
All the bad things best-effort can do
  a packet is corrupted (bit errors)
  a packet is lost
  a packet is delayed (why?)
  packets are reordered (why?)
  a packet is duplicated (why?)
Notes: MAKE CLEAR THE OBJECTIVE (function)
- RELIABLE data transfer

## Slide 26: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 27: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
rdt_rcv()
udt_rcv()

## Slide 28: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called by rdt to deliver data to upper
rdt_rcv()
udt_rcv()
udt_rcv(): called when packet arrives on rcv-side of channel

## Slide 29: Reliable data transfer: getting started
We’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 30: KR state machines – a note.
Beware
Kurose and Ross has a confusing/confused attitude to state-machines.
I’ve attempted to normalise the representation.
UPSHOT: these slides have differing information to the KR book (from which the RDT example is taken.)
in KR “actions taken” appear wide-ranging, my interpretation is more specific/relevant.
State
name
State
name
Relevant event causing state transition
Relevant action taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 31: Rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver read data from underlying channel
IDLE
udt_send(packet)
rdt_send(data)
rdt_rcv(data)
IDLE
udt_rcv(packet)
sender
receiver
Event
Action

## Slide 32: Rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that packet received is OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that packet had errors
  sender retransmits packet on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) receiver->sender

## Slide 33: Dealing with Packet Corruption
Time
Sender
Receiver
1
2
.
.
.
2


ack
nack

## Slide 34: rdt2.0: FSM specification
IDLE
udt_send(packet)
rdt_rcv(data)
udt_send(ACK)
udt_rcv(packet) && notcorrupt(packet)
udt_rcv(reply) && isACK(reply)
udt_send(packet)
udt_rcv(reply) &&
isNAK(reply)
udt_send(NAK)
udt_rcv(packet) && corrupt(packet)
Waiting
for reply
IDLE
sender
receiver
rdt_send(data)
L
Note: the sender holds a copy of the packet being sent until the delivery is acknowledged.

## Slide 35: rdt2.0: operation with no errors
L
IDLE
Waiting
for reply
IDLE
udt_send(packet)
rdt_rcv(data)
udt_send(ACK)
udt_rcv(packet) && notcorrupt(packet)
udt_rcv(reply) && isACK(reply)
udt_send(packet)
udt_rcv(reply) &&
isNAK(reply)
udt_send(NAK)
udt_rcv(packet) && corrupt(packet)
rdt_send(data)

## Slide 36: rdt2.0: error scenario
L
IDLE
Waiting
for reply
IDLE
udt_send(packet)
rdt_rcv(data)
udt_send(ACK)
udt_rcv(packet) && notcorrupt(packet)
udt_rcv(reply) && isACK(reply)
udt_send(packet)
udt_rcv(reply) &&
isNAK(reply)
udt_send(NAK)
udt_rcv(packet) && corrupt(packet)
rdt_send(data)

## Slide 37: rdt2.0 has a fatal flaw!
What happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
Handling duplicates:
sender retransmits current packet if ACK/NAK garbled
sender adds sequence number to each packet
receiver discards (doesn’t deliver) duplicate packet
Sender sends one packet,
then waits for receiver
response
stop and wait

## Slide 38: Dealing with Packet Corruption
Time
Sender
Receiver
1
1


ack(1)
ack(1)
What if the ACK/NACK is corrupted?
Packet #1 or #2?
2
P(2)
P(1)
P(1)
Data and ACK packets carry sequence numbers

## Slide 39: rdt2.1: sender, handles garbled ACK/NAKs
IDLE
sequence=0
udt_send(packet)
rdt_send(data)
Waiting
For reply
udt_send(packet)
udt_rcv(reply) &&
( corrupt(reply) ||
isNAK(reply) )
sequence=1
udt_send(packet)
rdt_send(data)
udt_rcv(reply)
&& notcorrupt(reply)
&& isACK(reply)
udt_send(packet)
udt_rcv(reply) &&
( corrupt(reply) ||
isNAK(reply) )
udt_rcv(reply)
&& notcorrupt(reply)
&& isACK(reply)
IDLE
Waiting
for reply
L
L

## Slide 40: rdt2.1: receiver, handles garbled ACK/NAKs
udt_rcv(packet) && corrupt(packet)
Wait for
0 from below
udt_send(NAK)
receive(packet) &&
not corrupt(packet) &&
has_seq0(packet)
udt_rcv(packet) && not corrupt(packet)
&& has_seq1(packet)
udt_send(ACK)
rdt_rcv(data)
Wait for
1 from below
udt_rcv(packet) && not corrupt(packet)
&& has_seq0(packet)
udt_send(ACK)
rdt_rcv(data)
udt_send(ACK)
receive(packet) &&
not corrupt(packet) &&
has_seq1(packet)
receive(packet) && corrupt(packet)
udt_send(ACK)
udt_send(NAK)

## Slide 41: rdt2.1: discussion
Sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “current” pkt has a
  0 or 1 sequence number
Receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 42: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 43: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sequence=0
udt_send(packet)
rdt_send(data)
udt_send(packet)
rdt_rcv(reply) &&
( corrupt(reply) ||
isACK1(reply) )
udt_rcv(reply)
&& not corrupt(reply)
&& isACK0(reply)
Wait for ACK
0
sender FSM
fragment
Wait for
0 from below
receive(packet) && not corrupt(packet)
&& has_seq1(packet)
send(ACK1)
rdt_rcv(data)
udt_rcv(packet) &&
(corrupt(packet) ||
has_seq1(packet))
udt_send(ACK1)
receiver FSM
fragment
L

## Slide 44: rdt3.0: channels with errors and loss
New assumption: underlying channel can also lose packets (data or ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but use of seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 45: rdt3.0 sender
udt_rcv(reply) &&
( corrupt(reply) ||
isACK(reply,1) )
sequence=0
udt_send(packet)
rdt_send(data)
Wait for ACK0
IDLE
state 1
sequence=1
udt_send(packet)
rdt_send(data)
udt_rcv(reply)
&& notcorrupt(reply)
&& isACK(reply,0)
udt_rcv(packet) &&
( corrupt(packet) ||
isACK(reply,0) )
udt_rcv(reply)
&& notcorrupt(reply)
&& isACK(reply,1)
L
L
udt_send(packet)
timeout
udt_send(packet)
timeout
udt_rcv(reply)
IDLE
state 0
Wait for ACK1
L
udt_rcv(reply)
L
L
L

## Slide 46: Dealing with Packet Loss
Time
Sender
Receiver
1
1

ack(1)
P(1)
P(1)
Timer-driven loss detection Set timer when packet is sent; retransmit on timeout
Timeout
P(2)

## Slide 47: Dealing with Packet Loss
Time
Sender
Receiver
1
1

ack(1)
P(1)
P(1)
Timeout
P(2)
duplicate!

## Slide 48: Dealing with Packet Loss
Time
Sender
Receiver
1
.
.
.
1
ack(1)
P(1)
P(1)
Timer-driven retx. can lead to duplicates
Timeout
P(2)
duplicate!
ack(1)

## Slide 49: Performance of rdt3.0
rdt3.0 works, but performance stinks
ex: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  U sender: utilization – fraction of time sender busy sending
  1KB pkt every 30 msec -> 33kB/sec throughput over 1 Gbps link
  network protocol limits use of physical resources!

## Slide 50: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Inefficient if
t << RTT
Notes: 29th end

## Slide 51: Pipelined (Packet-Window) protocols
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver

## Slide 52: A Sliding Packet Window
window = set of adjacent sequence numbers
  The size of the set is the window size; assume window size is n
General idea: send up to n packets at a time
  Sender can send packets in its window
  Receiver can accept packets in its window
  Window of acceptable packets “slides” on successful reception/acknowledgement

## Slide 53: A Sliding Packet Window
Let A be the last ack’d packet of sender without gap;
then window of sender = {A+1, A+2, …, A+n}
Let B be the last received packet without gap by receiver,
then window of receiver = {B+1,…, B+n}
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
n
A
Already ACK’d
Sent but not ACK’d
Cannot be sent
sequence number 

## Slide 54: Acknowledgements w/ Sliding Window
Two common options
  cumulative ACKs: ACK carries next in-order sequence number that the receiver expects
Notes: 27-1-2016

## Slide 55: Cumulative Acknowledgements (1)
At receiver
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
After receiving B+1, B+2
n
Bnew= B+2
Receiver sends ACK(Bnew+1)

## Slide 56: Cumulative Acknowledgements (2)
At receiver
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
After receiving B+4, B+5
n
B
Receiver sends ACK(B+1)
How do we recover?

## Slide 57: Go-Back-N (GBN)
Sender transmits up to n unacknowledged packets
Receiver only accepts packets in order
  discards out-of-order packets (i.e., packets other than B+1)
Receiver uses cumulative acknowledgements
  i.e., sequence# in ACK = next expected in-order sequence#
Sender sets timer for 1st outstanding ack (A+1)
If timeout, retransmit A+1, … , A+n

## Slide 58: Sliding Window with GBN
Let A be the last ack’d packet of sender without gap;
then window of sender = {A+1, A+2, …, A+n}
Let B be the last received packet without gap by receiver,
then window of receiver = {B+1,…, B+n}
n
A
Already ACK’d
Sent but not ACK’d
Cannot be sent
n
B
Received and ACK’d
Acceptable but not yet received
Cannot be received
sequence number 

## Slide 59: GBN Example w/o Errors
Time
Window size = 3 packets
Sender
Receiver
1
{1}
2
{1, 2}
3
{1, 2, 3}
4
{2, 3, 4}
5
{3, 4, 5}
Sender Window
Receiver Window
6
{4, 5, 6}
.
.
.
.
.
.

## Slide 60: GBN Example with Errors
Window size = 3 packets
Sender
Receiver
1
2
3
4
5
6
Timeout
Packet 4
4
5
6

## Slide 61: GBN: sender extended FSM
Wait
udt_send(packet[base])
udt_send(packet[base+1])
…
udt_send(packet[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
udt_send(packet[nextseqnum])
nextseqnum++
}
else
refuse_data(data) Block?
base = getacknum(reply)+1
udt_rcv(reply) &&
notcorrupt(reply)
base=1
nextseqnum=1
udt_rcv(reply)
&& corrupt(reply)
L
L

## Slide 62: GBN: receiver extended FSM
ACK-only: always send an ACK for correctly-received packet with the highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order packet:
  discard (don’t buffer) -> no receiver buffering!
  Re-ACK packet with highest in-order seq #
Wait
udt_send(reply)
L
udt_rcv(packet)
&& notcurrupt(packet)
&& hasseqnum(rcvpkt,expectedseqnum)
rdt_rcv(data)
udt_send(ACK)
expectedseqnum++
expectedseqnum=1
L

## Slide 63: Acknowledgements w/ Sliding Window
Two common options
  cumulative ACKs: ACK carries next in-order sequence number the receiver expects
  selective ACKs: ACK individually acknowledges correctly received packets
Selective ACKs offer more precise information but require more complicated book-keeping
Many variants that differ in implementation details
Notes: 2-Feb-2015 13-Feb-2017

## Slide 64: Selective Repeat (SR)
Sender: transmit up to n unacknowledged packets
Assume packet k is lost, k+1 is not
Receiver: indicates packet k+1 correctly received
Sender: retransmit only packet k on timeout
Efficient in retransmissions but complex book-keeping
  need a timer per packet

## Slide 65: SR Example with Errors
Time
Sender
Receiver
1
2
3
4
5
6
4
7
ACK=5
Window size = 3 packets
{1}
{1, 2}
{1, 2, 3}
{2, 3, 4}
{3, 4, 5}
{4, 5, 6}
{4,5,6}
{7, 8, 9}
ACK=6
{4,5,6}
Timeout
Packet 4
ACK=4

## Slide 66: Observations
With sliding windows, it is possible to fully utilize a link, provided the window size (n) is large enough. Throughput is ~ (n/RTT)
  Stop & Wait is like n = 1.
Sender has to buffer all unacknowledged packets, because they may require retransmission
Receiver may be able to accept out-of-order packets, but only up to its buffer limits
Implementation complexity depends on protocol details (GBN vs. SR)

## Slide 67: Recap: components of a solution
Checksums (for error detection)
Timers (for loss detection)
Acknowledgments
  cumulative
  selective
Sequence numbers (duplicates, windows)
Sliding Windows (for efficiency)
Reliability protocols use the above to decide when and what to retransmit or acknowledge

## Slide 68: What does TCP do?
Most of our previous tricks + a few differences
Sequence numbers are byte offsets
Sender and receiver maintain a sliding window
Receiver sends cumulative acknowledgements (like GBN)
Sender maintains a single retx. timer
Receivers do not drop out-of-sequence packets (like SR)
Introduces fast retransmit : optimization that uses duplicate ACKs to trigger early retx
Introduces timeout estimation algorithms

## Slide 69: Automatic Repeat Request (ARQ)
+ Self-clocking (Automatic)
+ Adaptive
+ Flexible
- Slow to start / adapt
consider high Bandwidth/Delay product
Next lets move from
the generic to the
specific….
TCP arguably the most successful protocol in the Internet…..
its an ARQ protocol

## Slide 70: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Used to mux
and demux

## Slide 71: Last time: Components of a solution for reliable transport
Checksums (for error detection)
Timers (for loss detection)
Acknowledgments
  cumulative
  selective
Sequence numbers (duplicates, windows)
Sliding Windows (for efficiency)
  Go-Back-N (GBN)
  Selective Replay (SR)

## Slide 72: What does TCP do?
Many of our previous ideas, but some key differences
Checksum

## Slide 73: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Computed over header
and data

## Slide 74: What does TCP do?
Many of our previous ideas, but some key differences
Checksum
Sequence numbers are byte offsets

## Slide 75: TCP: Segments and Sequence Numbers

## Slide 76: TCP “Stream of Bytes” Service…
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Application @ Host A
Application @ Host B
Byte 80
Byte 80

## Slide 77: … Provided Using TCP “Segments”
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out

## Slide 78: TCP Segment
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1500 bytes with Ethernet
TCP packet
  IP packet with a TCP header and data inside
  TCP header  20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
  MSS = MTU – (IP header) – (TCP header)
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)

## Slide 79: Sequence Numbers
Host A
ISN (initial sequence number)
Sequence number = 1st byte in segment = ISN + k
k bytes

## Slide 80: Sequence Numbers
Host B
TCP Data
TCP Data
TCP
HDR
TCP
HDR
ACK sequence number
= next expected byte
= seqno + length(data)
Host A
ISN (initial sequence number)
Sequence number = 1st byte in segment = ISN + k
k

## Slide 81: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Starting byte offset of data
carried in this segment
Notes: Number of first byte

## Slide 82
What does TCP do?

## Slide 83: What does TCP do?
Most of our previous tricks, but a few differences
Checksum
Sequence numbers are byte offsets
Receiver sends cumulative acknowledgements (like GBN)

## Slide 84: ACKing and Sequence Numbers
Sender sends packet
  Data starts with sequence number X
  Packet contains B bytes [X, X+1, X+2, ….X+B-1]
Upon receipt of packet, receiver sends an ACK
  If all data prior to X already received:
    ACK acknowledges X+B (because that is next expected byte)
  If highest in-order byte received is Y s.t. (Y+1) < X
    ACK acknowledges Y+1
    Even if this has been ACKed before

## Slide 85: Normal Pattern
Sender: seqno=X, length=B
Receiver: ACK=X+B
Sender: seqno=X+B, length=B
Receiver: ACK=X+2B
Sender: seqno=X+2B, length=B
Seqno of next packet is same as last ACK field

## Slide 86: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Acknowledgment gives seqno just beyond highest seqno received in order
(“What Byte is Next”)

## Slide 87: What does TCP do?
Most of our previous tricks, but a few differences
Checksum
Sequence numbers are byte offsets
Receiver sends cumulative acknowledgements (like GBN)
Receivers can buffer out-of-sequence packets (like SR)

## Slide 88: Loss with cumulative ACKs
Sender sends packets with 100B and seqnos.:
  100, 200, 300, 400, 500, 600, 700, 800, 900, …
Assume the fifth packet (seqno 500) is lost, but no others
Stream of ACKs will be:
  200, 300, 400, 500, 500, 500, 500,…

## Slide 89: What does TCP do?
Most of our previous tricks, but a few differences
Checksum
Sequence numbers are byte offsets
Receiver sends cumulative acknowledgements (like GBN)
Receivers may not drop out-of-sequence packets (like SR)
Introduces fast retransmit: optimization that uses duplicate ACKs to trigger early retransmission

## Slide 90: Loss with cumulative ACKs
“Duplicate ACKs” are a sign of an isolated loss
  The lack of ACK progress means 500 hasn’t been delivered
  Stream of ACKs means some packets are being delivered
Therefore, could trigger resend upon receiving k duplicate ACKs
    TCP uses k=3
But response to loss is trickier….

## Slide 91: Loss with cumulative ACKs
Two choices:
  Send missing packet and increase W by the number of dup ACKs
  Send missing packet, and wait for ACK to increase W
Which should TCP do?

## Slide 92: What does TCP do?
Most of our previous tricks, but a few differences
Checksum
Sequence numbers are byte offsets
Receiver sends cumulative acknowledgements (like GBN)
Receivers do not drop out-of-sequence packets (like SR)
Introduces fast retransmit: optimization that uses duplicate ACKs to trigger early retransmission
Sender maintains a single retransmission timer (like GBN) and retransmits on timeout

## Slide 93: Retransmission Timeout
If the sender hasn’t received an ACK by timeout, retransmit the first packet in the window
How do we pick a timeout value?

## Slide 94: Timing Illustration
1
1
Timeout too long  inefficient
1
1
Timeout too short 
duplicate packets
RTT
Timeout
Timeout
RTT

## Slide 95: Retransmission Timeout
If haven’t received ack by timeout, retransmit the first packet in the window
How to set timeout?
  Too long: connection has low throughput
  Too short: retransmit packet that was just delayed
Solution: make timeout proportional to RTT
But how do we measure RTT?

## Slide 96: RTT Estimation
Use exponential averaging of RTT samples
EstimatedRTT
Time
SampleRTT

## Slide 97: Exponential Averaging Example
RTT
time
EstimatedRTT = α*EstimatedRTT + (1 – α)*SampleRTT
Assume RTT is constant  SampleRTT = RTT
0
1
2
3
4
5
6
7
8
9
EstimatedRTT (α = 0.8)
EstimatedRTT (α = 0.5)

## Slide 98: Problem: Ambiguous Measurements
How do we differentiate between the real ACK, and ACK of the retransmitted packet?
ACK
Retransmission
Original Transmission
SampleRTT
Sender
Receiver
ACK
Retransmission
Original Transmission
SampleRTT
Sender
Receiver

## Slide 99: Karn/Partridge Algorithm
Measure SampleRTT only for original transmissions
  Once a segment has been retransmitted, do not use it for any further measurements
Computes EstimatedRTT using α = 0.875
Timeout value (RTO) = 2 × EstimatedRTT
Employs exponential backoff
  Every time RTO timer expires, set RTO  2·RTO
  (Up to maximum  60 sec)
  Every time new measurement comes in (= successful original transmission), collapse RTO back to 2 × EstimatedRTT

## Slide 100: Karn/Partridge in action
from Jacobson and Karels, SIGCOMM 1988

## Slide 101: Jacobson/Karels Algorithm
Problem: need to better capture variability in RTT
  Directly measure deviation
Deviation = | SampleRTT – EstimatedRTT |
EstimatedDeviation: exponential average of Deviation
RTO = EstimatedRTT + 4 x EstimatedDeviation

## Slide 102: With Jacobson/Karels
Notes: LOWER ESTIMATE! less “old mass” more reaction but wihout jaggers

## Slide 103: What does TCP do?
Most of our previous ideas, but some key differences
Checksum
Sequence numbers are byte offsets
Receiver sends cumulative acknowledgements (like GBN)
Receivers do not drop out-of-sequence packets (like SR)
Introduces fast retransmit: optimization that uses duplicate ACKs to trigger early retransmission
Sender maintains a single retransmission timer (like GBN) and retransmits on timeout

## Slide 104: TCP Header: What’s left?
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
“Must Be Zero” 6 bits reserved
Number of 4-byte words in TCP header; 5 = no options
Notes: 2017-2-15bb§bb

## Slide 105: TCP Header: What’s left?
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Used with URG flag to indicate urgent data (not discussed further)

## Slide 106: TCP Header: What’s left?
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 107: TCP Connection Establishment and Initial Sequence Numbers
Notes: 2016-1-29

## Slide 108: Initial Sequence Number (ISN)
Sequence number for the very first byte
Why not just use ISN = 0?
Practical issue
  IP addresses and port #s uniquely identify a connection
  Eventually, though, these port #s do get used again
  … small chance an old packet is still in flight
TCP therefore requires changing ISN
Hosts exchange ISNs when they establish a connection

## Slide 109: Establishing a TCP Connection
Three-way handshake to establish connection
  Host A sends a SYN (open; “synchronize sequence numbers”) to host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
SYN
SYN ACK
ACK
A
B
Data
Data
Each host tells its ISN to the other host.

## Slide 110: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Flags:
SYN
ACK
FIN
RST
PSH
URG

## Slide 111: Step 1: A’s Initial SYN Packet
A’s port
B’s port
A’s Initial Sequence Number
(Irrelevant since ACK not set)
Advertised window
5
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
ACK
FIN
RST
PSH
URG
A tells B it wants to open a connection…

## Slide 112: Step 2: B’s SYN-ACK Packet
B’s port
A’s port
B’s Initial Sequence Number
ACK = A’s ISN plus 1
Advertised window
5
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
ACK
FIN
RST
PSH
URG
B tells A it accepts, and is ready to hear the next byte…
… upon receiving this packet, A can start sending data
Flags

## Slide 113: Step 3: A’s ACK of the SYN-ACK
A’s port
B’s port
B’s ISN plus 1
Advertised window
20B
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
ACK
FIN
RST
PSH
URG
A tells B it’s likewise okay to start sending
A’s Initial Sequence Number
… upon receiving this packet, B can start sending data

## Slide 114: Timing Diagram: 3-Way Handshaking
Client (initiator)
Server
SYN, SeqNum = x
SYN + ACK, SeqNum = y, Ack = x + 1
ACK, Ack = y + 1
Active Open
Passive Open
connect()
listen()

## Slide 115: What if the SYN Packet Gets Lost?
Suppose the SYN packet gets lost
  Packet is lost inside the network, or:
  Server discards the packet (e.g., it’s too busy)
Eventually, no SYN-ACK arrives
  Sender sets a timer and waits for the SYN-ACK
  … and retransmits the SYN if needed
How should the TCP sender set the timer?
  Sender has no idea how far away the receiver is
  Hard to guess a reasonable length of time to wait
  SHOULD (RFCs 1122 & 2988) use default of 3 seconds
    Some implementations instead use 6 seconds

## Slide 116: Tearing Down the Connection

## Slide 117: Normal Termination, One Side At A Time
Finish (FIN) to close and receive remaining bytes
  FIN occupies one byte in the sequence space
Other host acks the byte to confirm
Closes A’s side of the connection, but not B’s
  Until B likewise sends a FIN
  Which A then acks
SYN
SYN ACK
ACK
Data
FIN
ACK
ACK
time
A
B
FIN
ACK
TIME_WAIT:
Avoid reincarnation
B will retransmit FIN if ACK is lost
Connection now half-closed
Connection now closed
Notes: Why timer? Will get packet with no state!!

## Slide 118: Normal Termination, Both Together
Same as before, but B sets FIN with their ack of A’s FIN
SYN
SYN ACK
ACK
Data
FIN
FIN + ACK
ACK
time
A
B
ACK
Connection now closed
TIME_WAIT:
Avoid reincarnation
Can retransmit FIN ACK if ACK lost

## Slide 119: Abrupt Termination
A sends a RESET (RST) to B
  E.g., because application process on A crashed
That’s it
  B does not ack the RST
  Thus, RST is not delivered reliably
  And: any data in flight is lost
  But: if B sends anything more, will elicit another RST
SYN
SYN ACK
ACK
Data
RST
ACK
time
A
B
Data
RST

## Slide 120: TCP State Transitions
Data, ACK exchanges are in here

## Slide 121: An Simpler View of the Client Side
CLOSED
TIME_WAIT
FIN_WAIT2
FIN_WAIT1
ESTABLISHED
SYN_SENT
SYN (Send)
Rcv. SYN+ACK, Send ACK
Send FIN
Rcv. ACK, Send Nothing
Rcv. FIN, Send ACK
Notes: 4-feb-2015

## Slide 122: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data

## Slide 123
What does TCP do?
  ARQ windowing, set-up, tear-down
Flow Control in TCP

## Slide 124: Recap: Sliding Window (so far)
Both sender & receiver maintain a window
Left edge of window:
  Sender: beginning of unacknowledged data
  Receiver: beginning of undelivered data
Right edge: Left edge + constant
  constant only limited by buffer size in the transport layer
Notes: Picture on board

## Slide 125: Sliding Window at Sender (so far)
Sending process
First unACKed byte
Last byte can send
TCP
Last byte written
Previously
ACKed bytes
Buffer size (B)

## Slide 126: Sliding Window at Receiver (so far)
Receiving process
Next byte needed (1st byte not received)
Last byte read
Last byte received
Received and ACKed
Buffer size (B)
Sender might overrun the receiver’s buffer

## Slide 127: Solution: Advertised Window (Flow Control)
Receiver uses an “Advertised Window” (W) to prevent sender from overflowing its window
  Receiver indicates value of W in ACKs
  Sender limits number of bytes it can have in flight <= W

## Slide 128: Sliding Window at Receiver
Receiving process
Next byte needed (1st byte not received)
Last byte read
Last byte received
Buffer size (B)
W= B - (LastByteReceived - LastByteRead)

## Slide 129: Sliding Window at Sender (so far)
Sending process
First unACKed byte
Last byte can send
TCP
Last byte written
W

## Slide 130: Sliding Window w/ Flow Control
Sender: window advances when new data ack’d
Receiver: window advances as receiving process consumes data
Receiver advertises to the sender where the receiver window currently ends (“righthand edge”)
  Sender agrees not to exceed this amount

## Slide 131: Advertised Window Limits Rate
Sender can send no faster than W/RTT bytes/sec
Receiver only advertises more space when it has consumed old arriving data
In original TCP design, that was the sole protocol mechanism controlling sender’s rate
What’s missing?

## Slide 132: TCP
The concepts underlying TCP are simple
  acknowledgments (feedback)
  timers
  sliding windows
  buffer management
  sequence numbers

## Slide 133: Sizing Windows for Congestion Control
What are the problems?
How might we address them?

## Slide 134
What does TCP do?
  ARQ windowing, set-up, tear-down
Flow Control in TCP
Congestion Control in TCP

## Slide 135
We have seen:
  Flow control: adjusting the sending rate to keep from overwhelming a slow receiver
Now lets attend…
  Congestion control: adjusting the sending rate to keep from overloading the network

## Slide 136: Statistical Multiplexing  Congestion
If two packets arrive at the same time
  A router can only transmit one
  … and either buffers or drops the other
If many packets arrive in a short period of time
  The router cannot keep up with the arriving traffic
  … delays traffic, and the buffer may eventually overflow
Internet traffic is bursty

## Slide 137: Congestion is undesirable
Average
Packet delay
Load
Typical queuing system with bursty arrivals
Must balance utilization versus delay and loss
Average
Packet loss
Load

## Slide 138: Who Takes Care of Congestion?
Network? End hosts? Both?
TCP’s approach:
  End hosts adjust sending rate
  Based on implicit feedback from network
Not the only approach
  A consequence of history rather than planning
Notes: 2016-2-1

## Slide 139: Some History: TCP in the 1980s
Sending rate only limited by flow control
  Packet drops  senders (repeatedly!) retransmit a full window’s worth of packets
Led to “congestion collapse” starting Oct. 1986
  Throughput on the NSF network dropped from 32Kbits/s to 40bits/sec
“Fixed” by Van Jacobson’s development of TCP’s congestion control (CC) algorithms

## Slide 140: Jacobson’s Approach
Extend TCP’s existing window-based protocol but adapt the window size in response to congestion
  required no upgrades to routers or applications!
  patch of a few lines of code to TCP implementations
A pragmatic and effective solution
  but many other approaches exist
Extensively improved on since
  topic now sees less activity in ISP contexts
  but is making a comeback in datacenter environments

## Slide 141: Three Issues to Consider
Discovering the available (bottleneck) bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows

## Slide 142: Abstract View
Ignore internal structure of router and model it as having a single queue for a particular input-output pair
Sending Host
Buffer in Router
Receiving Host
A
B

## Slide 143: Discovering available bandwidth
Pick sending rate to match bottleneck bandwidth
  Without any a priori knowledge
  Could be gigabit link, could be a modem
A
B
100 Mbps

## Slide 144: Adjusting to variations in bandwidth
Adjust rate to match instantaneous bandwidth
  Assuming you have rough idea of bandwidth
A
B
BW(t)

## Slide 145: Multiple flows and sharing bandwidth
Two Issues:
Adjust total sending rate to match bandwidth
Allocation of bandwidth between flows
A2
B2
BW(t)
A1
A3
B3
B1

## Slide 146: Reality
Congestion control is a resource allocation problem involving many flows, many links, and complicated global dynamics

## Slide 147: View from a single flow
Knee – point after which
  Throughput increases slowly
  Delay increases fast
Cliff – point after which
  Throughput starts to drop to zero (congestion collapse)
  Delay approaches infinity
Load
Load
Throughput
Delay
knee
cliff
congestion
collapse
packet
loss

## Slide 148: General Approaches
(0) Send without care
  Many packet drops

## Slide 149: General Approaches
(0) Send without care
(1) Reservations
  Pre-arrange bandwidth allocations
  Requires negotiation before sending packets
  Low utilization

## Slide 150: General Approaches
(0) Send without care
(1) Reservations
(2) Pricing
  Don’t drop packets for the high-bidders
  Requires payment model

## Slide 151: General Approaches
(0) Send without care
(1) Reservations
(2) Pricing
(3) Dynamic Adjustment
  Hosts probe network; infer level of congestion; adjust
  Network reports congestion level to hosts; hosts adjust
  Combinations of the above
  Simple to implement but suboptimal, messy dynamics

## Slide 152: General Approaches
(0) Send without care
(1) Reservations
(2) Pricing
(3) Dynamic Adjustment
All three techniques have their place
Generality of dynamic adjustment has proven powerful
Doesn’t presume business model, traffic characteristics, application requirements; does assume good citizenship

## Slide 153: TCP’s Approach in a Nutshell
TCP connection has window
  Controls number of packets in flight
Sending rate: ~Window/RTT
Vary window size to control sending rate

## Slide 154: All These Windows…
Congestion Window: CWND
  How many bytes can be sent without overflowing routers
  Computed by the sender using congestion control algorithm
Flow control window: AdvertisedWindow (RWND)
  How many bytes can be sent without overflowing receiver’s buffers
  Determined by the receiver and reported to the sender
Sender-side window = minimum{CWND,RWND}
    Assume for this material that RWND >> CWND

## Slide 155: Note
This lecture will talk about CWND in units of MSS
  (Recall MSS: Maximum Segment Size, the amount of payload data in a TCP packet)
  This is only for pedagogical purposes
In reality this is a LIE: Real implementations maintain CWND in bytes

## Slide 156: Two Basic Questions
How does the sender detect congestion?
How does the sender adjust its sending rate?
  To address three issues
    Finding available bottleneck bandwidth
    Adjusting to bandwidth variations
    Sharing bandwidth

## Slide 157: Detecting Congestion
Packet delays
  Tricky: noisy signal (delay often varies considerably)
Router tell endhosts they’re congested
Packet loss
  Fail-safe signal that TCP already has to detect
  Complication: non-congestive loss (checksum errors)
Two indicators of packet loss
  No ACK after certain time interval: timeout
  Multiple duplicate ACKs

## Slide 158: Not All Losses the Same
Duplicate ACKs: isolated loss
  Still getting ACKs
Timeout: much more serious
  Not enough dupacks
  Must have suffered several losses
We will adjust rate differently for each case
Notes: 2017-2-17

## Slide 159: Rate Adjustment
Basic structure:
  Upon receipt of ACK (of new data): increase rate
  Upon detection of loss: decrease rate
How we increase/decrease the rate depends on the phase of congestion control we’re in:
  Discovering available bottleneck bandwidth vs.
  Adjusting to bandwidth variations

## Slide 160: Bandwidth Discovery with Slow Start
Goal: estimate available bandwidth
  start slow (for safety)
  but ramp up quickly (for efficiency)
Consider
  RTT = 100ms, MSS=1000bytes
  Window size to fill 1Mbps of BW = 12.5 packets
  Window size to fill 1Gbps = 12,500 packets
  Either is possible!

## Slide 161: “Slow Start” Phase
Sender starts at a slow rate but increases exponentially until first loss
Start with a small congestion window
  Initially, CWND = 1
  So, initial sending rate is MSS/RTT
Double the CWND for each RTT with no loss
Notes: MSS vs MTU??

## Slide 162: Slow Start in Action
For each RTT: double CWND
Simpler implementation: for each ACK, CWND += 1
D
A
D
D
A
A
D
D
Src
Dest
D
D
1
2
4
3
A
A
A
A
8

## Slide 163: Adjusting to Varying Bandwidth
Slow start gave an estimate of available bandwidth
Now, want to track variations in this available bandwidth, oscillating around its current value
  Repeated probing (rate increase) and backoff (rate decrease)
TCP uses: “Additive Increase Multiplicative Decrease” (AIMD)
  We’ll see why shortly…

## Slide 164: AIMD
Additive increase
  Window grows by one MSS for every RTT with no loss
  For each successful RTT, CWND = CWND + 1
  Simple implementation:
    for each ACK, CWND = CWND+ 1/CWND
Multiplicative decrease
  On loss of packet, divide congestion window in half
  On loss, CWND = CWND/2

## Slide 165: Leads to the TCP “Sawtooth”
Loss
Exponential “slow start”
t
Window

## Slide 166: Slow-Start vs. AIMD
When does a sender stop Slow-Start and start Additive Increase?
Introduce a “slow start threshold” (ssthresh)
  Initialized to a large value
  On timeout, ssthresh = CWND/2
When CWND = ssthresh, sender switches from slow-start to AIMD-style increase
166

## Slide 167
What does TCP do?
  ARQ windowing, set-up, tear-down
Flow Control in TCP
Congestion Control in TCP
  AIMD

## Slide 168
What does TCP do?
  ARQ windowing, set-up, tear-down
Flow Control in TCP
Congestion Control in TCP
  AIMD, Fast-Recovery

## Slide 169: One Final Phase: Fast Recovery
The problem: congestion avoidance too slow in recovering from an isolated loss

## Slide 170: Example (in units of MSS, not bytes)
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped
  What ACKs do they generate?
  And how does the sender respond?

## Slide 171: The problem – A timeline
ACK 101 (due to 102) cwnd=10 dupACK#1 (no xmit)
ACK 101 (due to 103) cwnd=10 dupACK#2 (no xmit)
ACK 101 (due to 104) cwnd=10 dupACK#3 (no xmit)
RETRANSMIT 101 ssthresh=5 cwnd= 5
ACK 101 (due to 105) cwnd=5 + 1/5 (no xmit)
ACK 101 (due to 106) cwnd=5 + 2/5 (no xmit)
ACK 101 (due to 107) cwnd=5 + 3/5 (no xmit)
ACK 101 (due to 108) cwnd=5 + 4/5 (no xmit)
ACK 101 (due to 109) cwnd=5 + 5/5 (no xmit)
ACK 101 (due to 110) cwnd=6 + 1/5 (no xmit)
ACK 111 (due to 101)  only now can we transmit new packets
Plus no packets in flight so ACK “clocking” (to increase CWND) stalls for another RTT

## Slide 172: Solution: Fast Recovery
Idea: Grant the sender temporary “credit” for each dupACK so as to keep packets in flight
If dupACKcount = 3
  ssthresh = cwnd/2
  cwnd = ssthresh + 3
While in fast recovery
  cwnd = cwnd + 1 for each additional duplicate ACK
Exit fast recovery after receiving new ACK
  set cwnd = ssthresh

## Slide 173: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped

## Slide 174: Timeline
ACK 101 (due to 102) cwnd=10 dup#1
ACK 101 (due to 103) cwnd=10 dup#2
ACK 101 (due to 104) cwnd=10 dup#3
REXMIT 101 ssthresh=5 cwnd= 8 (5+3)
ACK 101 (due to 105) cwnd= 9 (no xmit)
ACK 101 (due to 106) cwnd=10 (no xmit)
ACK 101 (due to 107) cwnd=11 (xmit 111)
ACK 101 (due to 108) cwnd=12 (xmit 112)
ACK 101 (due to 109) cwnd=13 (xmit 113)
ACK 101 (due to 110) cwnd=14 (xmit 114)
ACK 111 (due to 101) cwnd = 5 (xmit 115)  exiting fast recovery
Packets 111-114 already in flight
ACK 112 (due to 111) cwnd = 5 + 1/5  back in congestion avoidance

## Slide 175: Putting it all together: The TCP State Machine (partial)
How are ssthresh, CWND and dupACKcount updated for each event that causes a state transition?
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK

## Slide 176: TCP Flavors
TCP-Tahoe
  cwnd =1 on triple dupACK
TCP-Reno
  cwnd =1 on timeout
  cwnd = cwnd/2 on triple dupack
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  incorporates selective acknowledgements

## Slide 177
What does TCP do?
  ARQ windowing, set-up, tear-down
Flow Control in TCP
Congestion Control in TCP
  AIMD, Fast-Recovery, Throughput

## Slide 178: TCP Flavors
TCP-Tahoe
  CWND =1 on triple dupACK
TCP-Reno
  CWND =1 on timeout
  CWND = CWND/2 on triple dupack
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  incorporates selective acknowledgements
Our default assumption

## Slide 179: Interoperability
How can all these algorithms coexist? Don’t we need a single, uniform standard?
What happens if I’m using Reno and you are using Tahoe, and we try to communicate?

## Slide 180: TCP Throughput Equation
Notes: Sort out the replication. XXXX

## Slide 181: A Simple Model for TCP Throughput
A
Loss
t
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 182: A Simple Model for TCP Throughput
A
Loss
t
cwnd

## Slide 183: Implications (1): Different RTTs
Flows get throughput inversely proportional to RTT
TCP unfair in the face of heterogeneous RTTs!
A1
A2
B2
B1
bottleneck
link
100ms
200ms

## Slide 184: Implications (2): High Speed TCP
Assume RTT = 100ms, MSS=1500bytes
What value of p is required to reach 100Gbps throughput
  ~ 2 x 10-12
How long between drops?
  ~ 16.6 hours
How much data has been sent in this time?
  ~ 6 petabits
These are not practical numbers!

## Slide 185: Adapting TCP to High Speed
  Once past a threshold speed, increase CWND faster
  A proposed standard [Floyd’03]: once speed is past some threshold, change equation to p-.8 rather than p-.5
  Let the additive constant in AIMD depend on CWND
Other approaches?
  Multiple simultaneous connections (hack but works today)
  Router-assisted approaches (will see shortly)

## Slide 186: Implications (3): Rate-based CC
TCP throughput is “choppy”
  repeated swings between W/2 to W
Some apps would prefer sending at a steady rate
  e.g., streaming apps
A solution: “Equation-Based Congestion Control”
  ditch TCP’s increase/decrease rules and just follow the equation
  measure drop percentage p, and set rate accordingly
Following the TCP equation ensures we’re “TCP friendly”
  i.e., use no more than TCP does in similar setting

## Slide 187: Recap: TCP problems
Misled by non-congestion losses
Fills up queues leading to high delays
Short flows complete before discovering available capacity
AIMD impractical for high speed links
Sawtooth discovery too choppy for some apps
Unfair under heterogeneous RTTs
Tight coupling with reliability mechanisms
Endhosts can cheat
Could fix many of these with some help from routers!
Routers tell endpoints if they’re congested
Routers tell endpoints what rate to send at
Routers enforce fair sharing

## Slide 188: Router-Assisted Congestion Control
Three tasks for CC:
  Isolation/fairness
  Adjustment*
  Detecting congestion
* This may be automatic eg loss-response of TCP

## Slide 189: How can routers ensure each flow gets its “fair share”?

## Slide 190: Fairness: General Approach
Routers classify packets into “flows”
  (For now) flows are packets between same source/destination
Each flow has its own FIFO queue in router
Router services flows in a fair fashion
  When line becomes free, take packet from next flow in a fair order
What does “fair” mean exactly?

## Slide 191: Max-Min Fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
ai = min(f, ri)
where f is the unique value such that Sum(ai) = C
r1
r2
r3
?
?
?
C bits/s
191

## Slide 192: Example
C = 10; r1 = 8, r2 = 6, r3 = 2; N = 3
C/3 = 3.33 
  Can service all of r3
  Remove r3 from the accounting: C = C – r3 = 8; N = 2
C/2 = 4 
  Can’t service all of r1 or r2
  So hold them to the remaining fair share: f = 4
8
6
2
4
4
2
f = 4:
min(8, 4) = 4
min(6, 4) = 4
min(2, 4) = 2
10

## Slide 193: Max-Min Fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
ai = min(f, ri)
where f is the unique value such that Sum(ai) = C
Property:
  If you don’t get full demand, no one gets more than you
This is what round-robin service gives if all packets are the same size

## Slide 194: How do we deal with packets of different sizes?
Mental model: Bit-by-bit round robin (“fluid flow”)
Can you do this in practice?
No, packets cannot be preempted
But we can approximate it
  This is what “fair queuing” routers do

## Slide 195: Fair Queuing (FQ)
For each packet, compute the time at which the last bit of a packet would have left the router if flows are served bit-by-bit
Then serve packets in the increasing order of their deadlines

## Slide 196: Example
1
2
3
4
5
1
2
3
4
1
2
3
1
2
4
3
4
5
5
6
1
2
1
3
2
3
4
4
5
6
5
5
6
Flow 1
(arrival traffic)
Flow 2
(arrival traffic)
Service
in fluid flow
system
FQ Packet
system
time
time
time
time

## Slide 197: Fair Queuing (FQ)
Think of it as an implementation of round-robin generalized to the case where not all packets are equal sized
Weighted fair queuing (WFQ): assign different flows different shares
Today, some form of WFQ implemented in almost all routers
  Not the case in the 1980-90s, when CC was being developed
  Mostly used to isolate traffic at larger granularities (e.g., per-prefix)

## Slide 198: FQ vs. FIFO
FQ advantages:
  Isolation: cheating flows don’t benefit
  Bandwidth share does not depend on RTT
  Flows can pick any rate adjustment scheme they want
Disadvantages:
  More complex than FIFO: per flow queue/state, additional per-packet book-keeping

## Slide 199: FQ in the big picture
FQ does not eliminate congestion  it just manages the congestion
1Gbps
100Mbps
1Gbps
5Gbps
1Gbps
Blue and Green get 0.5Gbps; any excess will be dropped
Will drop an additional 400Mbps from the green flow
If the green flow doesn’t drop its sending rate to 100Mbps, we’re wasting 400Mbps that could be usefully given to the blue flow

## Slide 200: FQ in the big picture
FQ does not eliminate congestion  it just manages the congestion
  robust to cheating, variations in RTT, details of delay, reordering, retransmission, etc.
But congestion (and packet drops) still occurs
And we still want end-hosts to discover/adapt to their fair share!
What would the end-to-end argument say w.r.t. congestion control?

## Slide 201: Fairness is a controversial goal
What if you have 8 flows, and I have 4?
  Why should you get twice the bandwidth
What if your flow goes over 4 congested hops, and mine only goes over 1?
  Why shouldn’t you be penalized for using more scarce bandwidth?
And what is a flow anyway?
  TCP connection
  Source-Destination pair?
  Source?

## Slide 202: Explicit Congestion Notification (ECN)
Single bit in packet header; set by congested routers
  If data packet has bit set, then ACK has ECN bit set
Many options for when routers set the bit
  tradeoff between (link) utilization and (packet) delay
Congestion semantics can be exactly like that of drop
  I.e., endhost reacts as though it saw a drop
Advantages:
  Don’t confuse corruption with congestion; recovery w/ rate adjustment
  Can serve as an early indicator of congestion to avoid delays
  Easy (easier) to incrementally deploy
    defined as extension to TCP/IP in RFC 3168 (uses diffserv bits in the IP header)

## Slide 203
What does TCP do?
  ARQ windowing, set-up, tear-down
Flow Control in TCP
Congestion Control in TCP
  AIMD, Fast-Recovery, Throughput
Limitations of TCP Congestion Control
Router-assisted Congestion Control (eg ECN)
TCP in detail

## Slide 204: Recap
TCP:
  somewhat hacky
  but practical/deployable
  good enough to have raised the bar for the deployment of new, more optimal, approaches
  though the needs of datacenters might change the status quos
Beyond TCP (discussed in Topic 6):
  QUIC / application-aware transport layers