## Slide 1
Computer Networking
Slide Set 1
Andrew W. Moore
Andrew.Moore@cl.cam.ac.uk

## Slide 2: Topic 1 Foundation
Administrivia
Networks
Channels
Multiplexing
Performance: loss, delay, throughput

## Slide 3
Course Administration
Commonly Available Texts
Computer Networks: A Systems Approach
  Peterson and Davie
  https://book.systemsapproach.org
  https://github.com/SystemsApproach/book
Computer Networking : Principles, Protocols and Practice
Olivier Bonaventure (and friends)
Less GitHub but more practical exercises
https://www.computer-networking.info/
Version 3 draft (UCAM access only)
Other textbooks are available.

## Slide 4: Thanks
Slides are a fusion of material from
  to Stephen Strowes, Tilman Wolf & Mike Zink, Ashish Padalkar , Evangelia Kalyvianaki, Brad Smith, Ian Leslie, Richard Black, Jim Kurose, Keith Ross, Larry Peterson, Bruce Davie, Jen Rexford, Ion Stoica, Vern Paxson, Scott Shenker, Frank Kelly, Stefan Savage, Jon Crowcroft , Mark Handley, Sylvia Ratnasamy, Adam Greenhalgh, and Anastasia Courtney.
Supervision material is drawn from
  Stephen Kell, Andy Rice, and the TA teams of 144 and 168
Finally thanks to the fantastic past Part 1b students and Andrew Rice for all the tremendous feedback.

## Slide 5: What is a network?
A system of “links” that interconnect “nodes” in order to move “information” between nodes
Yes, this is all rather abstract

## Slide 6: What is a network?
We also talk about
or
or even
Yes, abstract, vague, and under-defined….

## Slide 7: There are many different types of networks
Internet
Telephone network
Transportation networks
Cellular networks
Supervisory control and data acquisition networks
Optical networks
Sensor networks
We will focus almost exclusively on the Internet

## Slide 8: The Internet has transformed everything
The way we do business
  E-commerce, advertising, cloud-computing
The way we have relationships
  Facebook friends, E-mail, IM, virtual worlds
The way we learn
  Wikipedia, search engines
The way we govern and view law
  E-voting, censorship, copyright, cyber-attacks

## Slide 9: The Internet transforms everything
The way we do business
  E-commerce, advertising, cloud-computing
The way we have relationships
  Facebook friends, E-mail, IM, virtual worlds
The way we learn
  Wikipedia, search engines
The way we govern and view law
  E-voting, censorship, copyright, cyber-attacks
Taking the dissemination of information to the next level

## Slide 10: Internet research has impact
The Internet started as a research experiment!
Many successful companies have emerged from networking research(ers)

## Slide 11: The Internet is big business
Many large and influential networking companies
  Huawei, Broadcom, AT&T, Verizon, Akamai, Cisco, …
  $132B+ industry (carrier and enterprise alone)
Networking central to most technology companies
  Apple, Google, Facebook, Intel, Amazon, VMware, …

## Slide 12: But why is the Internet interesting?
“What’s your formal model for the Internet?” -- theorists
“Aren’t you just writing software for networks” – hackers
“You don’t have performance benchmarks???” – hardware folks
“Isn’t it just another network?” – old timers at BT
“What’s with all these TLA protocols?” – all
“But the Internet seems to be working…” – my mother

## Slide 13: A few defining characteristics of the Internet

## Slide 14: A federated system
ISP A
user
ISP B
ISP C
user
Tied together by IP -- the “Internet Protocol” : a single common interface between users and the network and between networks
The Internet ties together different networks
  >20,000 ISP networks (the definition is fuzzy)
Internet
Notes: one big cloud is actually…
snip here or there..

## Slide 15: A federated system
A single, common interface is great for interoperability…
…but tricky for business
Why does this matter?
  ease of interoperability is the Internet’s most important goal
  practical realities of incentives, economics and real-world trust, drive topology, route selection and service evolution
The Internet ties together different networks
  >20,000 ISP networks

## Slide 16: Tremendous scale (2020 numbers – so some ‘weird’)
4.57 Billion users (58% of world population)
1.8 Billion web sites
  34.5% of which are powered by the WordPress!
4.88 Billion smartphones (45.4% of population)
500 Million Tweets a day
100 Billion WhatsApp messages per day
1 Billion hours of YouTube video watched per day
500 hours of Youtube video added per minute
2+ billion TikTok installs
60% video streaming
  12.5% of the Internet traffic is native Netflix

## Slide 17: Tremendous scale (2020 numbers – so some ‘weird’)
4.57 Billion users (58% of world population)
1.8 Billion web sites
  34.5% of which are powered by the WordPress!
4.88 Billion smartphones (45.4% of population)
500 Million Tweets a day
100 Billion WhatsApp messages per day
1 Billion hours of YouTube video watched per day
500 hours of Youtube video added per minute
2+ billion TikTok installs
60% video streaming
  12.5% of the Internet traffic is native Netflix
“Internet Scale” refers to such systems

## Slide 18: Enormous diversity and dynamic range
Communication latency: nanoseconds to seconds (109)
Bandwidth: 100bits/second to 400 Gigabits/second (109)
Packet loss: 0 – 90%
Technology: optical, wireless, satellite, copper
Endpoint devices: from sensors and cell phones to datacenters and supercomputers
Applications: social networking, file transfer, skype, live TV, gaming, remote medicine, backup, IM
Users: the governing, governed, operators, malicious, naïve, savvy, embarrassed, paranoid, addicted, cheap …

## Slide 19: Constant Evolution
1970s:
56kilobits/second “backbone” links
<100 computers, a handful of sites in the US (and one UK)
Telnet and file transfer are the “killer” applications
Today
400+Gigabits/second backbone links
40B+ devices, all over the globe
  27B+ IoT devices alone

## Slide 20: Asynchronous Operation
Fundamental constraint: speed of light
Consider:
  How many cycles does your 3GHz CPU in Cambridge execute before it can possibly get a response from a message it sends to a server in Palo Alto?
    Cambridge to Palo Alto: 8,609 km
    Traveling at 300,000 km/s: 28.70 milliseconds
    Then back to Cambridge: 2 x 28.70 = 57.39 milliseconds
    3,000,000,000 cycles/sec * 0.05739 = 172,179,999 cycles!
Thus, communication feedback is always dated
    How much can change with 172 Million instructions

## Slide 21: Prone to Failure
To send a message, all components along a path must function correctly
  software, wireless access point, firewall, links, network interface cards, switches,…
  Including human operators
Consider: 50 components, that work correctly 99% of time  39.5% chance communication will fail
Plus, recall
  scale  lots of components
  asynchrony  takes a long time to hear (bad) news
  federation (internet)  hard to identify fault or assign blame

## Slide 22: A detour

## Slide 23: 8 fallacies of Distributed Systems

## Slide 34: Recap: The Internet is…
A complex federation
Of enormous scale
Dynamic range
Diversity
Constantly evolving
Asynchronous in operation
Failure prone
Constrained by what’s practical to engineer
Too complex for (simple) theoretical models
“Working code” doesn’t mean much
Performance benchmarks are too narrow
Notes: vvvv

## Slide 35: An Engineered System
Constrained by what technology is practical
  Link bandwidths
  Switch port counts
  Bit error rates
  Cost
  …

## Slide 36: Nodes and Links
A
B
Channels = Links
Peer entities = Nodes

## Slide 37: Properties of Links (Channels)
Bandwidth (capacity): “width” of the links
  number of bits sent (or received) per unit time (bits/sec or bps)
Latency (delay): “length” of the link
  propagation time for data to travel along the link (seconds)
Bandwidth-Delay Product (BDP): “volume” of the link
  amount of data that can be “in flight” at any time
  propagation delay × bits/time = total bits in link
bandwidth
Latency
delay x bandwidth
Notes: • Amount of data that can be transmitted per time unit ⇒ transmitted = put into the pipe (wire)
BDP: how many bits the sender must tx. before the 1st bit arrives at the receiver ⇒ the amount of data that could be in transit

## Slide 38: Examples of Bandwidth-Delay
Same city over a slow link:
  BW~100Mbps
  Latency~10msec
  BDP ~ 106bits ~ 125KBytes
To California over a fast link:
  BW~10Gbps
  Latency~140msec
  BDP ~ 1.4x109bits ~ 175MBytes
Intra Datacenter:
  BW~100Gbps
  Latency~30usec
  BDP ~ 106bits ~ 375KBytes
Intra Host:
  BW~100Gbps
  Latency~16nsec
  BDP ~ 1600bits ~ 200Bytes
17km * c = 56μs << 10ms
750m * c = 56μs ≅ 30μs
9708km * c = 32ms << 140ms
25cm * c = 83ps << 16ns
Notes: 17km
750 m
5584km
0.025m

## Slide 39: Packet Delay Sending a 100B packet from A to B?
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
Packet Delay = Transmission Delay + Propagation Delay
Packet Delay =
(Packet Size ÷ Link Bandwidth) + Link Latency
Notes: 2020-1-17

## Slide 40: Packet Delay Sending a 100B packet from A to B?
A
B
100Byte packet
Time
1Mbps, 1ms
1Gbps, 1ms?
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
1GB file in 100B packets
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms
The last bit in the file reaches B at
(107x800x1/109)+1/103s
= 8001ms
107 x 100B packets
Notes: small message (e.g., 1 byte): [1ms vs 100ms] (latency) dominates [1Mbps vs 100Mbps]
large message (e.g., 25 MB): [1Mbps vs 100Mbps] (BW) dominates [1ms vs 100ms]

## Slide 41: Packet Delay: The “pipe” view Sending 100B packets from A to B?
A
B
100Byte packet
Time
1Mbps, 10ms
100Byte packet
100Byte packet
time 
BW 
Packet Transmission Time

## Slide 42: Packet Delay: The “pipe” view Sending 100B packets from A to B?
1Mbps, 10ms (BDP=10,000)
time 
BW 
10Mbps, 1ms (BDP=10,000)
time 
BW 
1Mbps, 5ms (BDP=5,000)
time 
BW 

## Slide 43: Packet Delay: The “pipe” view Sending 100B packets from A to B?
1Mbps, 10ms (BDP=10,000)
time 
BW 
What if we used 200Byte packets??
1Mbps, 10ms (BDP=10,000)
time 
BW 

## Slide 44: Recall Nodes and Links
A
B
Notes: Start from here 24th of Jan

## Slide 45: What if we have more nodes?
One link for every node?
Need a scalable way to interconnect nodes

## Slide 46: Solution: A switched network
Nodes share network link resources
How is this sharing implemented?
Notes: multiple conversations in parallel
resources are shared

## Slide 47: Two examples of switched networks
Circuit switching (used in the POTS: Plain Old Telephone system)
Packet switching (used in the Internet)
Notes: borrow mckeown’s slides (of network with image); add Berkeley and MIT.
box -- links (incoming and outgoing)
packet -- data + header.
header has an address.

## Slide 48: Circuit switching
Telephone
Telephone
Exchange
Exchange

## Slide 49: Circuit switching
(1) Node A sends a reservation request
(2) Interior switches establish a connection -- i.e., “circuit”
(3) A starts sending data
(4) A sends a “teardown circuit” message
Idea: source reserves network capacity along a path
A
B
10Mb/s?
10Mb/s?
10Mb/s?
Notes: multiple conversations in parallel
resources are shared

## Slide 50: Multiplexing
Sharing makes things efficient (cost less)
One airplane/train for 100’s of people
One telephone for many calls
One lecture theatre for many classes
One computer for many tasks
One network for many computers
One datacenter many applications

## Slide 51: Multiplexing
Sharing makes things efficient (cost less)
One airplane/train for 100’s of people
One telephone for many calls
One lecture theatre for many classes
One computer for many tasks
One network for many computers
One datacenter many applications
Lecturer?

## Slide 52: Old Time Multiplexing

## Slide 53: Circuit Switching: FDM and TDM
Frequency Division Multiplexing
frequency
time
Time Division Multiplexing
frequency
time
4 users
Example:
Radio2 88.9 MHz
Radio3 91.1 MHz
Radio4 93.3 MHz
RadioX 95.5 MHz
Radio Schedule
…,News, Sports, Weather, Local, News, Sports,…
Notes: start here 23-jan-2023

## Slide 54: Time-Division Multiplexing/Demultiplexing
Time divided into frames; frames into slots
Relative slot position inside a frame determines to which conversation data belongs
  e.g., slot 0 belongs to orange conversation
Slots are reserved (released) during circuit setup (teardown)
If a conversation does not use its circuit capacity is lost!
Frames
0
1
2
3
4
5
0
1
2
3
4
5
Slots =

## Slide 55: Timing in Circuit Switching
Information
time
Circuit Establishment
Transfer
Circuit
Tear-down
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 56: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfer (once circuit is established)
Cons

## Slide 57: Timing in Circuit Switching
Information
time
Circuit Establishment
Transfer
Circuit
Tear-down
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 58: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfer (once circuit is established)
Cons
  wastes bandwidth if traffic is “bursty”

## Slide 59: Timing in Circuit Switching
Information
time
Circuit Establishment
Transfer
Circuit
Tear-down
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 60: Timing in Circuit Switching
Information
time
Circuit Establishment
Transfer
Circuit
Tear-down
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 61: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes bandwidth if traffic is “bursty”
  connection setup time is overhead

## Slide 62: Circuit switching
Circuit switching doesn’t “route around failure”
A
B

## Slide 63: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes bandwidth if traffic is “bursty”
  connection setup time is overhead
  recovery from failure is slow

## Slide 64: Numerical example
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!
1 / 24 * 1.536Mb/s = 64kb/s
640,000 / 64kb/s = 10s
10s + 500ms = 10.5s
Notes: 640,000b * (1/24) * 1/536Mbps + 500ms
640,000b @ 64kbps = 10s
PLUS 500ms setup

## Slide 65: Two examples of switched networks
Circuit switching (used in the POTS: Plain Old Telephone system)
Packet switching (used in the Internet)
Notes: borrow mckeown’s slides (of network with image); add Berkeley and MIT.
box -- links (incoming and outgoing)
packet -- data + header.
header has an address.

## Slide 66: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”*
01000111100010101001110100011001
Internet Address
Age (TTL)
Checksum to protect header
Header
Data
header
payload

## Slide 67: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”*
01000111100010101001110100011001
Destination Address
Header
Data
header
payload

## Slide 68: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”*
  payload is the data being carried
  header holds instructions to the network for how to handle packet (think of the header as an API)
  In this example, the header has a destination address
  More complex headers may include
    How this traffic should be handled? (first class, second class, etc)
    Who signed for it?
    Were the contents ok?

## Slide 69: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers

## Slide 70: Switches forward packets
EDINBURGH
OXFORD
GLASGOW
UCL
Destination | Next Hop
GLASGOW | 4
OXFORD | 5
EDIN | 2
UCL | 3
Forwarding Table
111010010
EDIN
switch#2
switch#5
switch#3
switch#4

## Slide 71: Timing in Packet Switching
time
payload
hdr
What about the time to process the packet at the switch?
We’ll assume it’s relatively negligible (mostly true)

## Slide 72: Timing in Packet Switching
time
payload
hdr
Could the switch start transmitting as soon as it has processed the header?
Yes! This would be called a “cut through” switch

## Slide 73: Timing in Packet Switching
time
payload
hdr
We will always assume a switch processes/forwards a packet after it has received it entirely. This is called “store and forward” switching

## Slide 74: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers

## Slide 75: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
  no notion of packets belonging to a “circuit”

## Slide 76: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
No link resources are reserved in advance. Instead packet switching leverages statistical multiplexing (stat muxing)

## Slide 77: Multiplexing
Sharing makes things efficient (cost less)
One airplane/train for 100’s of people
One telephone for many calls
One lecture theatre for many classes
One computer for many tasks
One network for many computers
One datacenter many applications

## Slide 78: Three Flows with Bursty Traffic
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 79: When Each Flow Gets 1/3rd of Capacity
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Frequent Overloading

## Slide 80: When Flows Share Total Capacity
Time
Time
Time
No Overloading
Statistical multiplexing relies on the assumption
that not all flows burst at the same time.
Very similar to insurance, and has same failure case

## Slide 81: Three Flows with Bursty Traffic
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 82: Three Flows with Bursty Traffic
Data Rate 1
Data Rate 2
Data Rate 3
Time
Time
Time
Capacity

## Slide 83: Three Flows with Bursty Traffic
Data Rate 1+2+3 >> Capacity
Time
Time
Capacity
What do we do under overload?

## Slide 84: Statistical multiplexing: pipe view
time 
BW 
pkt tx time

## Slide 85: Statistical multiplexing: pipe view

## Slide 86: Statistical multiplexing: pipe view
No Overload

## Slide 87: Statistical multiplexing: pipe view
Transient Overload
Not such a rare event
Queue overload
into Buffer

## Slide 88: Statistical multiplexing: pipe view
Transient Overload
Not such a rare event
Queue overload
into Buffer

## Slide 89: Statistical multiplexing: pipe view
Transient Overload
Not such a rare event
Queue overload
into Buffer

## Slide 90: Statistical multiplexing: pipe view
Transient Overload
Not such a rare event
Queue overload
into Buffer

## Slide 91: Statistical multiplexing: pipe view
Transient Overload
Not such a rare event
Queue overload
into Buffer

## Slide 92: Statistical multiplexing: pipe view
Transient Overload
Not a rare event!
Buffer absorbs transient bursts
But NOT additional capacity
Queue overload
into Buffer

## Slide 93: Statistical multiplexing: pipe view
What about persistent overload?
Will eventually drop packets
Queue overload
into Buffer

## Slide 94: Queues introduce queuing delays
Recall,
packet delay = transmission delay + propagation delay (*)
With queues (statistical multiplexing)
  packet delay = transmission delay + propagation delay + queuing delay (*)
Queuing delay caused by “packet interference”
Made worse at high load
  less “idle time” to absorb bursts
  think about traffic jams at rush hour
  or rail network failure
  (* plus per-hop processing delay that we define as negligible)

## Slide 95: Queuing delay extremes
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queuing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite – or data is lost (dropped).
Notes: 2016-11-16

## Slide 96: Recall the Internet federation
ISP A
user
ISP B
ISP C
user
The Internet ties together different networks
  >20,000 ISP networks
We can see (hints) of the nodes and links using traceroute…
Notes: one big cloud is actually…
snip here or there..

## Slide 97: “Real” Internet delays and routes
awm22@rio:~$ traceroute people.eng.unimelb.edu.au
traceroute to people.eng.unimelb.edu.au (128.250.59.37), 30 hops max, 60 byte packets
1 vlan101.gatwick.net.cl.cam.ac.uk (128.232.32.2) 1.520 ms 1.822 ms 0.709 ms
2 cl-wgb.d-mw.net.cam.ac.uk (193.60.89.5) 0.259 ms 0.256 ms 0.227 ms
3 d-mw.c-ce.net.cam.ac.uk (131.111.6.53) 0.231 ms 0.381 ms 0.357 ms
4 c-ce.b-ec.net.cam.ac.uk (131.111.6.82) 0.317 ms 0.481 ms 0.476 ms
5 ae0.lowdss-ban1.ja.net (146.97.41.37) 2.842 ms 2.846 ms 2.821 ms
6 ae26.lowdss-sbr1.ja.net (146.97.35.245) 2.877 ms 2.805 ms 2.795 ms
7 ae28.londhx-sbr1.ja.net (146.97.33.17) 6.191 ms 6.109 ms 6.325 ms
8 janet.mx1.lon.uk.geant.net (62.40.124.197) 6.319 ms 6.245 ms 6.258 ms
9 138.44.226.6 (138.44.226.6) 169.704 ms 169.722 ms 169.682 ms
10 et-7-3-0.pe1.wmlb.vic.aarnet.net.au (113.197.15.28) 250.954 ms 251.163 ms 251.116 ms
11 * * *
12 4000v-eng-web-people-l.eng.unimelb.edu.au (128.250.59.37) 251.943 ms 251.952 ms 251.962 ms
13 4000v-eng-web-people-l.eng.unimelb.edu.au (128.250.59.37) 252.053 ms 252.018 ms 251.966 ms
14 * * *
15 4000v-eng-web-people-l.eng.unimelb.edu.au (128.250.59.37) 252.215 ms 252.088 ms 252.118 ms
16 4000v-eng-web-people-l.eng.unimelb.edu.au (128.250.59.37) 253.361 ms 253.109 ms 253.461 ms
17 4000v-eng-web-people-l.eng.unimelb.edu.au (128.250.59.37) 253.077 ms 253.832 ms 253.298 ms
18 * * *
….
29 * * *
30 * * *
traceroute: rio.cl.cam.ac.uk to people.eng.unimelb.edu.au
(tracepath on winows is similar)
Three delay measurements from
rio.cl.cam.ac.uk to gatwick.net.cl.cam.ac.uk
* means no response (probe or reply lost, router not replying)
Australian
link
Direct London-Perth
Notes: Where did the delay come from??
2015-11-18

## Slide 98: traceroute: rio.cl.cam.ac.uk to www.caida.org
rio:~$ traceroute --resolve-hostnames www.caida.org
traceroute to www.caida.org (192.172.226.122), 64 hops max
1 128.232.64.2 (vlan398.gatwick.net.cl.cam.ac.uk) 3.760ms 2.060ms 1.226ms
2 193.60.89.5 (cl-wgb.d-mw.net.cam.ac.uk) 53.777ms 67.458ms 0.556ms
3 131.111.7.53 (d-mw.c-hi.net.cam.ac.uk) 0.638ms 0.621ms 0.658ms
4 131.111.7.82 (c-hi.b-jc.net.cam.ac.uk) 0.353ms 0.346ms 0.338ms
5 131.111.7.217 (ips-out.b-jc.net.cam.ac.uk) 0.582ms 0.441ms 0.397ms
6 146.97.41.37 (ae0.lowdss-ban1.ja.net) 2.754ms 2.648ms 2.701ms
7 146.97.35.245 (ae26.lowdss-sbr1.ja.net) 2.852ms 2.728ms 2.738ms
8 146.97.33.25 (ae30.erdiss-sbr2.ja.net) 5.412ms 5.177ms 4.474ms
9 146.97.33.21 (ae31.londpg-sbr2.ja.net) 8.408ms 8.213ms 8.293ms
10 62.40.125.57 (janet-bckp.mx1.lon2.uk.geant.net) 9.199ms 9.140ms 9.108ms
11 62.40.98.64 (ae2.mx1.lon.uk.geant.net) 10.119ms 9.818ms 9.756ms
12 62.40.124.45 (internet2-gw.mx1.lon.uk.geant.net) 95.065ms 95.962ms 95.434ms
13 163.253.1.120 (fourhundredge-0-0-0-0.4079.core2.ashb.net.internet2.edu) 152.834ms 153.562ms 154.448ms
14 163.253.1.139 (fourhundredge-0-0-0-1.4079.core2.clev.net.internet2.edu) 154.008ms 153.800ms 154.429ms
15 163.253.2.17 (fourhundredge-0-0-0-2.4079.core2.eqch.net.internet2.edu) 155.463ms 154.863ms 154.334ms
16 163.253.1.66 (fourhundredge-0-0-0-18.4079.core1.eqch.net.internet2.edu) 153.802ms 153.600ms 154.553ms
17 163.253.1.206 (fourhundredge-0-0-0-1.4079.core1.chic.net.internet2.edu) 154.783ms 154.926ms 154.796ms
18 163.253.2.29 (fourhundredge-0-0-0-1.4079.core2.kans.net.internet2.edu) 152.851ms 152.414ms 154.916ms
19 163.253.1.250 (fourhundredge-0-0-0-1.4079.core2.denv.net.internet2.edu) 155.571ms 155.047ms 154.572ms
20 163.253.1.169 (fourhundredge-0-0-0-3.4079.core2.salt.net.internet2.edu) 153.369ms 153.824ms 154.321ms
21 163.253.1.114 (fourhundredge-0-0-0-8.4079.core1.losa.net.internet2.edu) 153.786ms 153.549ms 154.839ms
22 137.164.26.200 (hpr-lax-agg10--i2.cenic.net) 152.552ms 153.465ms 152.493ms
23 137.164.25.89 (hpr-sdg-agg4--lax-agg10-100ge.cenic.net) 154.682ms 154.604ms 154.752ms
24 137.164.26.43 (hpr-sdsc-100ge--sdg-hpr3.cenic.net) 167.094ms 154.553ms 154.627ms
25 192.12.207.46 (medusa-mx960.sdsc.edu) 154.854ms 154.646ms 156.379ms
26 192.172.226.122 (proxy.caida.org) 154.581ms 154.390ms 154.477ms
A little more interesting because each hop resolves to a name (caida is in San Diego)

## Slide 99: Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 100: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 101: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other.

## Slide 102: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., Verizon, Sprint, AT&T, Cable and Wireless), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately

## Slide 103: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
….
…
…
…
POP: point-of-presence
Notes: Switched Private Network Telecommunications
South Pacific Railway
-=-=-
End of lecture 23rd Jan 2012

## Slide 104: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers
Each packet travels independently
No link resources are reserved in advance. Instead packet switching uses statistical multiplexing
  allows efficient use of resources
  but introduces queues and queuing delays
Notes: Restart here 23-1-23

## Slide 105: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Packet switching may (does!) allow more users to use network
N users
1 Mbps link
Q: how did we get value 0.0004?

## Slide 106: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Q: how did we get value 0.0004?

## Slide 107: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Q: how did we get value 0.0004?
Let U be number of users active
N the total users
P is 0.1 in our example to get 0.0004

## Slide 108: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Q: how did we get value 0.0004?
Let U be number of users active
N the total users
P is 0.1 in our example to get 0.0004
Notes: (check this)

## Slide 110: Circuit switching: pros and cons
Pros
  guaranteed performance
  fast transfers (once circuit is established)
Cons
  wastes bandwidth if traffic is “bursty”
  connection setup adds delay
  recovery from failure is slow

## Slide 111: Packet switching: pros and cons
Pros
  efficient use of bandwidth (stat. muxing)
  no overhead due to connection setup
  resilient -- can `route around trouble’
Cons
  no guaranteed performance
  header overhead per packet
  queues and queuing delays

## Slide 112: Summary
A sense of how the basic `plumbing’ works
  links and switches
  packet delays= transmission + propagation + queuing + (negligible) per-switch processing
  statistical multiplexing and queues
  circuit vs. packet switching
Notes: 21 Jan 2019