## Slide 1: XORs in The Air: Practical Wireless Network Coding
Sachin Katti, Dina Katabi, Wenjun Hu, Jon Crowcroft et al.
Presented by Jon Crowcroft
Slides borrowed from MIT Collaborators including Yan Gao

## Slide 2: Capacity of Multi-hop Wireless Networks
Gupta/Kumar limit (for 1/r^2 far field)
  Based on geometry/receiver interference
Grossglauser/Tse improvement
  Requires (random) mobility
Tse co-operative MIMO improvement
  Requires smart antennae and v. accurate clocks
Net Coding - originally for broadcast
  Aswelde result for rateless code/cast

## Slide 3: Problem
Network Coding

## Slide 4: Background
Bob and Alice
Relay
Require 4 transmissions

## Slide 5: Background
Bob and Alice
Relay
Require 3 transmissions
XOR
XOR
XOR
Notes: Bridge the gap between theory of network coding and practical network design

## Slide 6: Outline
COPE Overview
Design
Performance

## Slide 7: COPE (Coding Opportunistically)
Consider multiple unicast flows
  Generalize Alice-Bob scenario
Exploits Shared Nature of Wireless Medium
  Store Overheard Packets for Short Time
  These packets are used for decoding perspective packets
First implement Wireless Network Coding in the real world

## Slide 8: Opportunistic Coding
Overhear neighbors’ transmissions
Store these packets in a buffer Packet Pool for a short time
Report the packet pool info. to neighbors
Determine what packets to code based on the info.
Send encoded packets

## Slide 9: Opportunistic Coding

## Slide 10: Opportunistic Coding
Three ways to get neighbor state
  Reception report
  Guess
    Based on ETX metric (delivery probability)
    Estimate the probability that packets are overheard
  The neighbor is the previous hop of the packet
Notes: But how does a node know what packets its neighbors have?
Report to its neighbors the packets it stores.
However, at times of severe congestion, report may get lost in collisions. They also may arrive too late after the coding decision
The first way and the third way are reliable.

## Slide 11: COPE’s Gain
Coding Gain
  Alice-and-Bob example gains 4/3 (maximum is 2)
Coding+MAC Gain
  Due to Mac allocation, relay node is the bottleneck and throughput is ½
  With COPE, throughput is 1
  Coding+Mac Gain = 2

## Slide 12: Outline
COPE Overview
Design
Performance

## Slide 13: COPE Design
Coding Algorithm
  Take the packet at the head of its output queue
  Never delay packets (if can not code, simply send it)
  Categorize larger packets and small packets
  Code packets headed for the different nexthops
    Two virtual queues for each neighbor: large and small
    M neighbors  2M virtual queues

## Slide 14: COPE Design
Coding Algorithm
Packet_1
Packet_2
Packet_3
Virtual QA
Virtual QB
Virtual QC
A
B
C
P1b
P1c
P2a
P2c
P3a
P3b
P2a
P1b
P2a
×P3a
P1b
×P3b
P1c
×P2c
0.8

## Slide 15: COPE Design
Decoding
  Packet id: A 32-bit hash of src IP and Seq. no.
  XOR the encoded packet with the corresponding stored packets to get native packet
  Store the native packet in packet pool

## Slide 16: COPE Design
Pseudo Broadcast
  Cons of broadcast
    Unreliable due to no ACK
    Lack of backoff
  Piggy back on unicast
    Set one of intended node as Mac address
    List all others in COPE header (between MAC and IP header)
    Receiver: if it is on the list, decode the packet, else store the packet in its pool

## Slide 17: COPE Design
Hop by hop ACKs
  Asynchronous Acks
  Each of native packet schedules an event for retransmission
  Re-enqueue the packet if no Ack within Ta seconds.
  Acks added in COPE header

## Slide 18: COPE Design
COPE header
  Indicate what packets are encoded
  Report sender’s packet pool info.
  Acknowledge what packets the sender received

## Slide 19: Outline
COPE Overview
Design
Performance

## Slide 20: Performance
Alice and Bob (TCP)

## Slide 21: Performance
Alice and Bob (UDP)

## Slide 22: Performance
Large Scale Experiment
  20 nodes
  2 floors
  Pick sender and receiver randomly
  Packet size based on actual measurement
  Flow arrival are Possion

## Slide 23: Large Scale Exp.
Offered load in Mb/s

## Slide 24: Conclusion
COPE: a new approach to wireless
Large throughput increase
First implement network coding to wireless networks
Simple

## Slide 25: Problems
The experiment runs on a hidden node free network
  Almost no gain due to hidden terminal
More general (3+ packets coded together)
  Very hard (np) to figure out schedule
Better (e.g. Luby) codes
  Computationally expensive
  counter indicated for wireless nodes:-)

## Slide 26: Future work
CoCo: Bjorn Scheuermann/Wenjun Hu
  Combine hop-by-hop Congestion control & coding
  achieves near optimal coding advantage
  Rate target is set to incorporate coding improvement
Code Casting: Gkantsidis/Hu et al
  Multipath (e.g. VRR) routing + coding
  Again near optimal
Optimal MAC would be “simpler”/better
  but nearly impossible to design

## Slide 27: Questions?
Any questions….please e-mail me and I can forward &
Acknowlegements to my colleagues, collaborators and students in
  Cambridge, MIT and Microsoft research
  N.b. some work was funded by the Cambridge MIT Institute (DTI+BT) and some by MSR