## Slide 1
Herding Cats, Mice and Elephants – Network resource implications for the GRID
Jon Crowcroft
Jon.Crowcroft@cl.cam.ac.uk
http://www.cl.cam.ac.uk/homes/jac22
10.30am, July 25, 2002
HPDC-11, Edinburgh

## Slide 2
Acknowledgements
Funding by PPARC +EPSRC
At UCL: Prof. Pete Clark. Department of Physics +
Dr. Saleem Bhatti, Soren Sorenson, Computer Science.
http://www.cs.ucl.ac.uk/staff/S.Bhatti/grs/
http://www.cs.ucl.ac.uk/staff/jon/mbng/
Res:.
Integrating GRID tools to build a computing resource broker: activities of DataGrid WP1, Authors M. Ruda et al
http://web.datagrid.cnr.it/pls/portal30/GRID.RPT ATAGRIDPAPERS
http://www.cs.nwu.edu/ jms/sched-wg/

## Slide 3
Abstract, continued
Grid Applications make use of significant quantities of resources, whether it be CPU cycles, number of CPUs (whether clustered or distributed over a wide area), storage (whether local, remote, structured or at, central or distributed), and network capacity. Historically, there has been research into scheduling in distributed systems, but often the assumption has been that a network is largely in the local area, and is dedicated to the task in hand. Even in that constrained environment, scheduling is an NP-hard problem.
In the GRID, the resources are almost all shared, including the network. This talk is about the work in the GRS project which is trying to provide an ”application cradle” into which the range of different GRID middleware can sit, that gives a simple API to requesting, and being granted, or denied access to a set of distributed resources, including networking resources.
Think Supply Chain Economics.

## Slide 4
History
What is the GRID?
“The Grid : Blueprint for a New Computing Infrastructure”, by Ian Foster (Editor), Carl Kesselman (Editor) Morgan Kaufmann Publishers; (November 1998) ISBN: 1558604758
It’s a metaphor - you plug in a toaster or a matter transmitter to a 13Amp socket on the wall. You don’t care how the electricity is generated or distributed.

## Slide 5: What’s a GRID For? The idea is you have some scientific problem to solve, for example: • Where is the Dark Matter? • How does this protein fold? • Is there a likely causal link between MMR and Autism? • Is the average temperature of the sea or atmosphere increasing? • Will this shape wing lift this much mass? • When does turbulence break bits off this turbine blade?

## Slide 6
What’s hard about these GRID Problems?
These are all computationally expensive, and may even require large amounts of storage for intermediate stages (or rely on large amounts of telemmetry data). They may benefit from enlisting computers and people from many places in many organisations (distributed virtual information societies, formed on an ad hoc basis to solve urgent, or important problems).
The GRID is to this what the Web is to sharing documents (in fact, the web is just a component of the GRID).

## Slide 7
So you want to use MY computer?
Client/Server, Systolic Array, P2P – Patterns… … …
So there are lots of peer2peer systems out there (Yes, LOTS) napster, gnutella, kazaa, morpheus, fastraqck, directconnect, edonkey, freenet But these all just do file sharing.
Then there’s: SETI@home....versus real work:-)
What do we have in the Open Source world?
Well, right now, we have ssh. While this is ok for closed communities it is just that: it relies on a at user id space, and a single accounting domain.What about sharing CPU cycles across multiple administrative domains?
It’s a hard problem, entailing, authorisation, access control, authentication, accounting, and so far we’ve only got as far as the letter ’A’ :-)

## Slide 8
Problem definition
One size doesn’t fit all e.g. PPARC problems different from NERC, BBSRC etc
10 Tera op machines versus 1 million 100MIPS PCs
Brittle, High Cost, High Availability v. Highly Organised Tolerance
Monopoly, verus broker/bourse/market organisation
Guiding principal: KISS

## Slide 9
Desired Properties
Protection of existing re sources
Incentive to offer resources to other organisations
“Guarantees” that if I pay for resources, I get them

## Slide 10
System Components
Pace: OGSA - define these in terms of WSDL/Grid
Services! TBD! (Think: Schedule factories etc)
API
job description
user interfaces
Push versus Pull
exceptions
re-negotiation
Co-allocation
group naming
membership management
application layer multicast
VPNs/MBNG
Accounting

## Slide 11
More System Components
Schedulers
Turing’s Halting Problem reminder!
CPU schedulers
pre-emption
constraints
priority
elastic
heuristics
etc (see pp 291 on in
ftp://cs.ucl.ac.uk/darpa/ods.ps.Z

## Slide 12
Yet More System Components - IDEA!!
Maybe system schedulers could be like network Shedulers?
Network Schedulers
FCFS
Int-serv - WFQ
Diff-serv - CBQ
Priority
DRR
Pragmatic: CAR etc
Has nice property that we think of process as throughput and latency - other properties (locality to data or I/O, also natural).
Has undesirable property that one can schedule for other resources (memory) - perhaps these really should be constraints only though, rather than parameters

## Slide 13
Policy/Mechanism
• Economics - maybe a market is a way to do distributed management?
List resources on a bourse. Users ”bid”- run an online auctioning system (maybe blind vickrey auction to avoid nasty games).
Users choose which parameter (cpu, storage, i/o, network) - could be like different commodity markets -3.
Users are allocated tokens by funding agencies, or their institution.

## Slide 14
Policy/Mechanism continued
• Service Level agreements (SLAs):
SLA’s need to be announced (might include availability, including MTBF (e.g. windows is typically 6.5 hours, linux 65 days etc)
Need refund mechanism (like railtrack:-)
Long term statistics published (like internet weather service, need GRID weather service).

## Slide 15
Policy/Mechanism continued
User can choose to pay spot or futures, or brokered
price.
Need to worry about stability, of course. But scale of
system can help!
Markets in bundled services might emerge.
Need tariff distribution mechanism (c.f. Grid event
notification service is part of OGSA).
Need to think about CPU and memory and I/O
Congestion (and signaling - a bit like ECN in
Networking!).

## Slide 16
Remarks…
In a complex heteroegeneous system with many organisations, the only current model we have for organisation is a market
It works for the Internet (a thousand ISPs per country!)
It is highly optimised and robust, but built out of sloppy components (see work by John Doyle at Caltech on control theoretic analysis of such systems, often biologically inspired)

## Slide 17: So what does this mean for the Network:- The GRID promises several novel traffic patterns: Data from the large hadron collider(elephants), Distributed computation from genomics(cats) General web+acess grid traffic (mice). we are trying to characterise these from 20,000 feet, and discuss some of the resource management consequences for this complex ecosystem. Why?

## Slide 18
Why we need Traffic Characteristics.
The Internet does not offer protection of one user from another. (hence term “best effort”). If the net is overloaded, and there are some legitimate reason to give some users decent performance rather than others, we would like to have some mechanisms for this.
On a road system, this is like having the California ”Car Pool Lane” or the London Bus Lane.
In some cases, we need to - e.g. tele-surgery, etc, this is clear. In others (e.g. voice over IP, video conference) it may be necessary too. In others, more ”elastic” behaviour (i.e. adaptation and tolerance) may suffice.
In the past, we had a network based on ATM (Asynchronous Transfer Mode switches) which could dynamically be programmed (managed/configured) to partition the network capacity into such separate chunks. Now we do not have this capability in the underlying transmission system; we have to re-implement it in the Internet Protocol Layer.
MBNG is looking at how to do this using a technology called Differentiated Services and MPLS, with help from a small company called Cisco...
See “Sojourn-time aware dynamic online routing” (Su/Veciana) for more…

## Slide 19
Realities: Measurements
But what we really want to know is ”what are the real traffic patterns” and what are the real requirements? Right now, net traffic is mainly made up out of two types of traffic, known colloquially as mice and elephants.
Mice are your typical web browser - small (<<14 packets total exchanged) and interactive, but fairly delay tolerant (most userid can stand about 1 second web download delay)
Elephants are your large downloads - FTP of a new Redhat release....many megabytes (therefore thousands of packets) - these are very delay tolerant - we don’t really care if the rate or delay vary even by orders of magnitude during the download so long as the FTP completes with in some broadly reasonable timeframe.
Mice and Elephants co-exist quite nicely, as typically there are millions of mice, and only a handful of elephants, and the collective behaviour of many mice looks pretty much like an elephant (central limit theorem, or even statistical thermodynamics math can be used to show this). The behaviour of many humans driving the mice, and a few FTP servers have well behaved long term stability due to a mix of luck, economics, network structures and the design of the TCP congestion avoidance algorithms.
Here is some data from Sprint, courtesy Dina Papagiannaki

## Slide 20: Lets look at some data
Dina Papagiannaki at SPrintLabs with Christophe Diot, looked at the Sprint core inter-pop traffic
Represents about 10 years effort
Goal:provisioning/prediction/protection
Xun Su, G. de Veciana, ``Dynamic multi-path routing: Asymptotic approximation and simulations'', ACM Sigmetrics 2001.
Xun Su, G. de Veciana, `` Sojourn-time aware dynamic online routing: Aflow perspective '', submitted review.http://www.ece.utexas.edu/%7Exsu/publication.html

## Slide 25: Try to find mice/elephants
First try simple thrreshold (byte/packet rate from/to prefix pair about a certain amount)
Next try Markov Model
Its actually quite tricky, but in the end can get a reasonable match
Why? Allows automatic placement of mice on low delay and elephants on high capacity paths (or MPLS FEC or DiffServe Queues)

## Slide 33: So what might we do with this?
We want separation of traffic types so that we can provide protection
E.g. latency/jitter for interaction
Minimum throughput for bulk txfer
Responsiveness for cats
Need source characteristics as well as traffic matrix…then can provide virtual pipes

## Slide 34
Win Win - Controls
The GRID may be introducing a third type which is a tad trickier to comprehend, which I have termed “cats”, after the famous quote about the difficulty of herding cats:-)
Cat’s eat mice. They are not scared of elephants (note elephants are famously scared of mice, which leads to some rather lame jokes ... ... ...)
Cat’s are medium term, do need care and feeding (i.e. live on the edge, need low latency) and come and go as they please.
Cat’s are a luxury.
IMHO, the only way to accommodate cats is through economics. We have a mechanism due to Kelly et all, called Congestion Pricing.
A Cat must pay its way. (finally)

## Slide 35
Justice for Mice
If the presence of a cat means that a mouse dies, or an elephant forgets, then the cat must learn guilt.
This is done through
Explicit Congestion Notification (a.k.a packet shadow pricing)
ECN counting is done by the edge devices.
A Cat accrues an ECN Bill. It is sent to their project or their institute (or their tutor:-)
Non-payment of bills leads to being blocked for prowling, but ALSO for mice and elephant like mimicry.

## Slide 36
Practicalities
To Do
ECN needs deployment
ECN billing needs a AAA environment.
Also MUST have user route choice (RON?)
GRS is deploying such an environment.
Thus we have the pieces. But cats make it harder!

## Slide 37
Questions???