## Slide 1: Mob Handed: Realworld Human Mobility Model driven design of forwarding algorithms for Opportunistic Networking
Jon.Crowcroft@cl.cam.ac.uk
http://www.cl.cam.ac.uk/~jac22
+ Pan Hui
Computer Laboratory
University of Cambridge

## Slide 2: Outline
Multiple levels human social heterogeneity
  Local community structures
  Diversity of centrality on different scales
  Four categories of human relationship
Heterogeneous forwarding algorithms
  Design space
  RANK (centrality based forwarding)
  LABEL (community based forwarding)
  BUBBLE RAP (centrality meets community)
Approximation and predictability
  Decentralized approximation of centrality
  Human predictability

## Slide 3: The first goal of this research is to move to a third generation of human mobility models, understanding heterogeneity at multiple levels of detail.
Understanding multiple levels of heterogeneity

## Slide 4: Social Structures Vs Network Structures
Community structures
  Social communities, i.e. affiliations
  Topologically cohesive groups or modules
Centralities
  Social hubs, celebrities and postmen
  Betweenness, closeness, inference power, centrality

## Slide 5: Experimental setup
iMotes
  ARM processor
  Bluetooth radio
  64k flash memory
Bluetooth Inquiries
  5 seconds every 2 minutes
  Log contact tuples:
    {MAC address, start time, end time}
Notes: To study the human mobility we setup a series of iMote experiment. iMotes are some tiny embeded sensor produced by intel research. iMotes use Bluetooth as communciation media, this is different from the berkeley motes which use RF radio. This is one reason why we choose iMote as our experiment devices since nowaday many portable devices have BT and usually go with the user so can be a good indication of human mobility.So we programmed the motes and distributed to the people participating in the experiment to carry around. The motes are programed to do to do BT Inqueries for every 2 minutes for the other BT devices in the environment. For the BT devices seen, it will recored the mac address of that device, and the time start see the device and the time the deviced disappear.

## Slide 6: Experimental devices
Notes: Here showes the imotes. The left hand figure shows the imote without packaging. We can see that the imote is very small, around 2.5cm without the battery. This is a advantage so we can ask people to carry around with them. The right photo shows two packaging of the imotes. One is inside the dental fossil box, this package is water proof, transparent and can see the LED shinning inside it. The people can put it inside their pockage or handbags. Another package is the keychain, people are encourgae to put it onto their keys. This is good since that people usually will carry their keys together with them so can prevent the problem that the iMotes will be left at home for a whole day.

## Slide 7: So we did a lot of experiments
Mix of ours and other research groups:
  Infocom conferences 05 and 06 (miami, barcelona)
  In Cambridge (with 1st & 2nd yr undergrds)
  Hong Kong (with High School, and random [people on street)
  Plus others’ data
    from crawdad dbase @dartmouth, ucsd, toronto
    From MIT Reality Mining dataset
Typical data set involves:
  54 iMotes distributed, Experiment duration: 3 days
  41 yielded useful data
  11 with battery or packaging problem, 2 not returned
Notes: 54 iMotes were distributed to the students attending the workshop on the first day or the conference and was required to return back at the end of the conference. We put a collection box at the conference place. Most of the iMotes were returned, only 2 were taken away as suverniors.

## Slide 8: K-clique Community Definition
Union of k-cliques reachable through a series of adjacent k-cliques [Palla et al]
Adjacent k-cliques share k-1 nodes
Members in a community reachable through well-connected well subsets
Examples
  2-clique (connected components)
  3-clique (overlapping triangles)
Overlapping feature
Percolation threshold
pc (k)= 1/[(k-1)N]^(1/(k-1))

## Slide 9: K-clique Communities in Infocom06 Dataset
Barcelona Group
Paris Group A
Paris Group B
Lausanne Group
Paris Groups
Barcelona Group
Lausanne Group
K=3

## Slide 10: K-clique Communities in Infocom06 Dataset
Barcelona Group
Paris Group A
Paris Group B
Lausanne Group
Paris Groups
Barcelona Group
Lausanne Group
K=4

## Slide 11: K-clique Communities in Infocom06 Dataset
Barcelona Group (Spanish)
Paris Group A (French)
Paris Group B (French)
Italian
K=5

## Slide 12: Other Community Detection Methodologies
Betweenness [Newman04]
Modularity [Newman06]
Information theory[Rosvall06]
  Most literature is in social anthropology
  Some in physics (AS level topology and web interconnect topology)
  Future is to look at social net (myspace, linkedin, orkut, yahoo groups, facebook)
  And user contributed tags (del.icio.us, etc)

## Slide 13: Centrality in Temporal Network
Simulate flooding over the temporal graph
Uniform source/destination and temporal traffic distribution
  Count number of times each node is on shortest delay deliveries
  Higher the count, more central node
  Analogue to Freeman centrality
Need to threshold over lifespan of “link” in temporal graph

## Slide 14: In-Group Centrality (Reality)
Group A
Group D
Group C
Group B

## Slide 15: Heterogeneous Forwarding
The second goal of this research is to devise efficient forwarding algorithms for PSNs which take advantage of both a priori and learned knowledge of the structure of human mobility.

## Slide 16
Give it to me, I have 1G bytes phone flash.
I have 100M bytes of data, who can carry for me?
I can also carry for you!
Thank you but you are in the opposite direction!
Don’t give to me! I am running out of storage.
Reach an access point.
Internet
Finally, it arrive…
Search La Bonheme.mp3 for me
Search La Bonheme.mp3 for me
Search La Bonheme.mp3 for me
There is one in my pocket…

## Slide 17: Interaction and Forwarding
Third generation human interaction model
  Categories of human contact patterns
  Clique and community
  Popularity/Centrality
Dual natures of mobile network
  Social network
  Physical network
Benchmark Forwarding strategies
  Flooding, Wait, and Multiple-copy-multiple-hop (MCP)

## Slide 18: Design Space
Explicit Social Structure
Structure in Degree
Structure in Cohesive Group
Label
Rank, Degree
Clique Label
Bubble
Network Plane
Human Dimension

## Slide 19: Greedy Ranking Algorithm (RANK)
Use pre-calculated centrality/rank
Push traffic to nodes have higher rank
Good performance in small and homogeneous

## Slide 20: Problem with RANK
Heterogeneous at multiple levels
Best node for the whole system may not be best node for a specific community
D
A
E
D
C
B

## Slide 21: Label Strategy (LABEL)
A Priori label, e.g. affiliation
Correlated interaction
Forward to nodes have same label as the destination
Good performance in conference mixing environment
Infocom06

## Slide 22: Problem with LABEL
In a less mixing environment (e.g. Reality)
A person in one group may not meet members in another group so often
Wait for destination group not efficient

## Slide 23: Centrality meets Community
Population divided into communities
Node has a global and local ranking
Global popular node like a postman, or politician in a city
Local popular node like Christophe Diot in SIGCOMM
BUBBLE-A
BUBBLE-B

## Slide 24
Ranking
Source
Destination
Global Community
Sub community
Sub community
Subsub community

## Slide 25: Centrality meets Community
Notes: Bubble Reality single group

## Slide 26: Distributed Community Detection
The third goal of this research IS to devise practical ways to implement forwarding based on community in a decentralised (ad hoc or DTN)/PSN network, where offline analysis of traces is not feasible, so online, decentralised/distributed community detection has to be used. We show that online community detection can be both practical, and achieve a reasonable approximation to offline analysis of long-term traces.
Notes: <number>

## Slide 27: General Frame Work
SIMPLE, K-CLIQUE, MODULARITY
Terminology : Familiar Set (F), Local Community (C)
Update and exchange local information during encounter
Build up Familiar Set and Local Community
CommunityAccept,MergeCommunities
Notes: <number>

## Slide 28: Results and Evaluations
Data Set | SIMPLE | K-CLIQUE | MODULARITY
Reality | 0.79/0.81 | 0.87 | 0.89
UCSD | 0.47/0.56 | 0.55 | 0.65
Cambridge | 0.85/0.85 | 0.85 | 0.87
Complexity | O(n) | O(n2) | O(n4)/O(n2k2)
Newman weighted analysis
Palla et al, k-Clique
Notes: <number>

## Slide 29: Results and Evaluations
UCSD
MIT
Distributions
of
Local Community Views
Notes: <number>

## Slide 30: Conclusion and Future Woks
Forwarding using a priori label or social structure inferred through observation
Distributed k-clique building through gossiping
Why per-6-hour?
Weighted version of k-clique detection
Third generation modeling

## Slide 31: More Future Work…
Privacy and trust (including incentives forwarding).
Absolute location based, versus co-location based forwarding
Other layer social network based forwarding, e.g.
Content (url distance, or meta, e.g. del.icio.us tag) based forwarding
Myspace, Orkut, etc

## Slide 32: Jon.Crowcroft@cl.cam.ac.uk

## Slide 33: Regularity and Familiarity
Regularity
Familiarity
IV
I
II
III
I: Community II. Familiar Strangers III. Strangers IV. Friends
Correlation Coefficient = 0.9026

## Slide 34
Reality
Infocom05
Infocom06
HK
c: 0.6604
c: 0.5817
c: 0.8325
c: 0.7927

## Slide 35: K-clique Communities in Cambridge Dataset

## Slide 36: SIMPLE
CommunityAccept ( vi)
MergeCommunities ( Co, Ci)
Notes: <number>

## Slide 37: K-CLIQUE
CommunityAccept ( vi) :
MergeCommunities( Co, Ci):
CommunityAccept ( vi)
Notes: <number>

## Slide 38: MODULARITY
Boundary Set
Local Modularity
Measure of the sharpness of local community
Notes: <number>

## Slide 39: MODULARITY
CommunityAccept ( vi ) :
MergeCommunities( Co , Ci ): for each vk in set K,
or
or
Notes: <number>

## Slide 40: Greedy Ranking Algorithm
Hierarchical organization
Hierarchical paths [Trusina et al]
High percentage in most dataset

## Slide 41: Problem with RANK
Hop distribution and rank at dead-end for HK dataset