## Slide 1: Mobile QoS:Can we provide predictable services for unpredictably mobile users?
Jon Crowcroft
Jon.Crowcroft@cl.cam.ac.uk

## Slide 2: Rationale
QoS is most wanted when it is least present
Wireless networks are the last frontier of scarce resource, and will remain so for some time
The Big Challenge appears to be coping with uncertainty
Predictable service is what the subscriber and provider both want.
What lessons are there from QoS Architectures from Wired Networks, and What is Missing???

## Slide 3: What becomes a Wired Internet QoS Architecture
Timescale decomposition (short to longest):
    Packet
      Scheduling
      Shaping
      Dropping
    Flow
      Admission Control
      Rate adaption
    Aggregate
      Traffic Engineering
      Link Provisioning
      Node and Link Placement

## Slide 4: A Priori Knowledge
How Much do we know or learn?
  Source Model
    e.g. TCP Padhye Equantion
    e.g. RTP VOIP/on-off speech
    e.g. Poisson Arrival of sessions
    e.g. VOIP – Erlang stats?
  Traffic Matrix
    Mice/Elephant aggregates
    Route logs
    POP level source/destination flows

## Slide 5: What’s similar for mobile?
Cellular/Wireless Access Network
  Backhaul capacity known
  Cell capacity known
Ad Hoc
  No backhaul
  May have spine
Hybrid
  depends

## Slide 6: What’s different for mobile?
“Link” capacity not necessarily constant
  Depends on spectrum allocation policy
  Depends (less usually) on noise
Source model may be affected by variation
  in cell, distance from base station
  In ad hoc, route capacity
  if feedback, e.g. TCP adapts (or proxy/splice etc)
Matrix is more rapidly time varying
  If aggregate behaviour is really random…so…

## Slide 7: Can we still use traditional tools?
Depends on what we believe about randomness
In real world, we know about the disposition of
  Buildings
  Walkways
  Roads
  Have RF propagation models for these
Users do not move randomly
  Along architected and planned routes
  Do not use communication randomly

## Slide 8: Is ad hoc/hybrid case specially hard?
Depends on why you use ad hoc.
  Meeting networks- small, not multi-hop
    Rendezvous,
    Find infrastructure
    Don\t need high capacity (unless to reach printer/backup)
  Vehicle networks – take a different approach:
    Design network in space
    Vehicle constellation simply swap through cells in space
    Could use multi-hop, but, eventually, reach roadside.
    Plenty of power
    Metal in vehicle makes spectrum re-use efficient even in flash crowd
    Near true random movement between vehicles

## Slide 9: Consequences for MAC
Need to have power/distance aware MACs (trend in 802.11* and Blue Tooth is to hide this information)
Need to think about information theory in regard to application:
E.g. vehicle network, for real time monitor and control:
  Somewhere between Gupta/Kumar , and Grossglauser/Tse  result
  Could design to be at the good end…

## Slide 10: Application Adaption v. Guarantee
Same old chestnut – can always do adaptation, but users (particularly humans) don’t like it.
So need admission control (Yes, I agree with Jim Roberts!).
Needs to be policed down to the MAC/physical layer, and included in spectrum allocation.
We suggest spectrum allocation by economic measures.
Substitute surprising price for surprising QoS

## Slide 11: Mobileman (ostring/gibbens/kelly/crowroft)
System Optimisation:
  Each user has a utility function to optimise;
  Goal is optimise the aggregate utility;
Primal Algorithm:
  Users adapt their transmission rates (c.f. TCP);
  Node prices set by aggregate traffic;
Dual Algorithm:
  Network nodes adapt prices (c.f. ATM);
  Transmission rates are set by route prices.
Prices are used to guide a system to its optimum operating point.

## Slide 12: System Model
Network of N nodes: node S has R routes to send traffic to D:
  Must select particular route(s) to use;
Nodes are equipped with one directional transceiver:
  Nodes cannot send/receive simultaneously;
Traffic sent, received or forwarded (received & sent) is constrained by C:
  maximum speed of wireless card;
Maximum power consumption at a node is constrained by :
  Energy consumed by transmitting/receiving/forwarding traffic.

## Slide 13: Rate Control, Price Adaptation
Each node has a willingness-to-pay parameter ws(t):
  Depends on node’s credit balance;
Node S determines the route with minimum price:
  Routes discovered by, e.g. DSR.
Algorithm for sending rate:
Route price is the cumulative cost of sending traffic on each hop along the route;
  Transmission cost & receiving cost
  Costs include power costs and capacity costs
Nodes adapt bandwidth and power prices:
  measure local total traffic load and power consumption.

## Slide 14: Credit Balance
Provide incentives for users to forward traffic:
  Users receive credit for forwarding traffic;
  Amount of credit received is dependent on the node prices and the magnitude of the flow.
Users receive an initial credit balance of 1;
Willingness-to-pay is proportional to credit balance;
Credit is lost when users leave the system:
  Amount of credit lost depends on credit accrued by the user during its stay in the network;
Introduce a discount factor :

## Slide 15: Simulation Design
Randomly placed nodes in a 100mx100m grid;
All nodes within range of a node’s radio are its neighbours;
Users are ON-OFF sources:
  ON/OFF periods are exponentially distributed;
  Destinations for traffic during ON period are uniformly distributed;
Route costs are determined when a connection is initiated:
  Minimum cost route is selected;
Route not changed during connection;
  Reduces routing information being distributed within the network;
  Avoids route flapping;
System optimum not achieved, but reflects routing in actual networks.

## Slide 16: Random Static Network

## Slide 17: Static Nodes: Power Prices
Power prices are strongly dependent on location;
N8 has the highest power price:
It is often used by other nodes to forward traffic;
It’s location requires higher energy to transmit to neighbouring nodes.
N1 has very low power price.

## Slide 18: Static Nodes: Bandwidth Prices
N8 does not have the highest bandwidth price:
Traffic can be routed around edge of the network;
Extreme edge nodes (N1 and N7) carry minimal traffic:
bandwidth prices rapidly head to zero.

## Slide 19: Static Nodes: Credit Balances
Credit balances are strongly dependent on location;
N8 has the highest power price:
It accumulates the most credit by forwarding traffic for other nodes;
N1 has non-negligible credit replenished

## Slide 20: Dynamic Network Simulation
Nodes arrive according to a Poisson process;
  Nodes are geographically placed according to a uniform distribution.
Nodes’ stay in the network is exponentially distributed;
  Routes must be updated within the network for ongoing connections;
How does the total credit evolve...

## Slide 21: Total Credit Balance
An arrival of a user always increases the total credit by 1.0;
The change in total credit, due to a departure of a user, varies depending on the credit the user has accumulated;
Total credit in the system decays to the number of users;
Rate of decay depends on .

## Slide 22: Path of Mobile Node

## Slide 23: Mobility: Node Power Prices
Power price of N1 increases as it moves towards the centre of the network:
Routes are increasingly chosen with N1 as a forwarding node;
Power price of N8 decreases:
N1 provides competition for N8;
Less energy is required to transmit to N1 as it moves closer.

## Slide 24: Mobility: Bandwidth Prices
Bandwidth price of N1 increases:
Overall increase in traffic in the network
Bandwidth price of N8 also increases:
Greater flow of traffic between N1 and N8 as they move closer together;
Overall increase in traffic in the network;
Bandwidth Price of N4 increases:
Stability?

## Slide 25: Individual Node Throughputs
Throughputs of both N1 and N8 increase:
More traffic between the nodes;
Both nodes have more credit to send traffic;
Throughput of N4 increases:
N4 is the node most often used to forward traffic to N1;
Traffic transmitted from N4 to N1 is relatively cheap.

## Slide 26: Total Network Throughput
Total network throughput increases:
Increased throughput for N1 has not been at the expense of the overall network throughput;
Mobility (in an appropriate direction) has increased the performance of the system;
Total Credit in system is constant.

## Slide 27: In summary...
Developed a system model for the interaction between nodes in a mobile ad hoc network;
Introduced price mechanisms and credit balance to provide framework for cooperation;
Simulations demonstrated:
  Stability
  Dynamics of total credit
  Throughput increases with mobility

## Slide 28: Future
To do:
  Evaluate our scheme further
    Do timescale decomposition properly
  Need to stop people working on pure ad hoc
    Yes we know its fun, but it makes no sense…
  Try in practice
    Persuade Intel to build some chips
    Persuade FCC to let us do this
  Trust Mechanisms
    Identifier denial,theft,witnesses…
    eCash (double spend/forge)
    Algorithm signatures (trust h/w – e.g. ARM)

## Slide 29: All done!
Thanks for listening!
Questions?