## Slide 1: Communications and Transport – synergies and lessons
Jon Crowcroft
http://www.thecii.org
http://www.cl.cam.ac.uk
Jon.crowcroft@cl.cam.ac.uk

## Slide 2: Location, location, location!
When designing networks, one needs
  Source model (individual’s behaviour)
    E.g. greedy, elastic, etc
  Traffic Matrix (collective demand)
    E.g. source/destination and route preferences/policies
  Network Topology Cost model
    (e.g. cost of a link, hub/router/switch)
Mobile/Wireless networks add the need for data on
Mobility models and location preferences…

## Slide 3: Network design for mobility
Recently, we designed a multi-hop radio network for a taxi-dispatch system
Instead of centralized broadcasting dispatcher, we had users radio the nearest taxi (expanding search), which then forwards requests, hop by hop to neighbours.
Cost saving can be large (35k per year if we use unlicensed spectrum, just on radio rental)
But we needed a lot of data
Needed RF propagation model for the city, plus the route statistics for the taxi company (3000 taxis in Cambridge), plus the road traffic data for all other vehicles (which, being metal, get in the way of radio, but actually that’s a good thing, surprisingly)

## Slide 4: Network design mobility data needs
So we needed aggregate flow data at roads by time of day, decision statistics at junctions, and data on taxi preferred routes
Managed to abstract from DfT data for flow on roads
Got route preferences from taxi dispatchers logs.
Built a model (ran for simulated period of 1 day for whole city of Cambridge with 3000 taxis and 50,000 other cars – quite computationally expensive)
Showed ad hoc net provides 98% coverage at any time with relatively short (~1 minute) outages fairly uniformaly distributed
Viable alternative (and far more optimal and fair in getting right taxi to right customer!)

## Slide 5: So roads (and transport in general) not so different
Well, obviously costs/timescales radically different
Can deploy 1M broadband users/year in the UK
Roughly 100£ per person to do fiber to everywhere
Clearly, equivalent (zero congestion transport) slightly more complex and expensive!
However, common area of need is for data about the usage pattern
And another area to learn from is interaction of choices

## Slide 6: Even 10 years ago, 1 ISDN line=1 Commuter
We trialed ISDN access for researchers at UCL in 1992
Discovered that 1 hours use cost about same as difference in peak time ticket and off peak!
Allowed us to move researchers travel to more pleasant and cost effective time, at no cost to social interaction or work effectiveness
The Web makes this very easy to do in a much more general way!

## Slide 7: The general virtualized commuter
can drive to supermarket to get weeks shopping, or can use Internet to tell supermarket to deliver shopping
direction of value of networks and transport systems is always interesting.
Understanding how people and vehicles move is essential to planning and pricing of roads
but also essential to planning and pricing of wireless networks for mobile users.
feedback between pricing and user behaviour means that pricing and provisioning are complex problems
both for transport and for communications systems
Rest of this talk illustrates that life is even more complex for the planner when there are two or more systems (e.g. communications and transport) which have price senstive users who can trade off their behaviours in each domain against the other.

## Slide 8: Willingness to pay/risk aversion etc
Both transport and communications networking researchers lack data on users behaviour
Dynamic pricing (congestion charge that actually reflects traffic) can be very effective in theory
Practice is that price could be quite unpredictable
Not clear what user preference is – neither much-touted experiments: INDEX project, nor London Congestion Charge tell us this works
In fact, both argue strongly for fairly fixed charge, but need a LOT of market research to set the right charge

## Slide 9: Spot price + broker?
Could one have a market for road and Internet use?
Maybe mitigate users’ fear of unexpected bill by use of brokers?
Would need careful regulation, otherwise subject to arbitrage (futures markets and so on)
Could be very complex when we include choice between two, possibly seperately regulated markets
Should I take car, train, or should I use network for next 2 hours?

## Slide 10: Conclusions and Outlook
There are a lot of synergies between communications networks and transport systems research
Two areas suggest themselves for more work
  Sharing of monitoring data in large scale
  Understanding human behaviour/non-rational choices when confronted with different tariff structures in areas one can choose between
The first of these needs some modest investment – ESRC+Department should get a decent transport monitoring Grid Data Service up as soon as possible – industry should jump at the chance to help fund this if they can get at the data (road haulage, Internet shopping delivery systems, etc)
The second requires reasonable scale real trials with users and is pretty subtle, but, in my opinion, essential
Thank you – any questions?