## Slide 1: Pocket Switched Networks: Real-world Mobility and its Consequences for Opportunistic Forwarding
Jon Crowcroft ,Pan Hui (Ben)
Augustin Chaintreau, James Scott,
Richard Gass, Christophe Diot
University of Cambridge
Intel Research Cambridge
Notes: Good morning, today I will present our work on pocket switched networks. It is a co-work with augustin chaintreau…and christophe diot done in UCam and Intel research Cam

## Slide 2: Pocket Switched Networks Is there a packet in your pocket or are you pleased to see me?
Notes: Pocket Switched Networks is a term shows a vivid picture of our application. A package swtich from a mobile phone in your pocket to a PDA in other people’s pocket. So when you meet a person, you may think is there a packet in your pocket that you want me to carry for you or are you just pleased to see me?

## Slide 3: Pocket switched networks motivations
Not always connected, “internet connectivity islands”
Huge amount of untapped resources in portable devices
  Local wireless bandwidth
  Storages
  CPUs
A packet can reach destination using network connectivity or user mobility
MANET/DTN [Fall]
Notes: Not connected, internet end-to-end connection not working. Scenario 100M of data, need to send to the people but there is no internet connection so you look around and ask people to carry for you. Oliver pass by and he has a mobile phone of 1 G storage and with Wimax. Portable devices contains a human amount of data. HK 7 million ppl, each person has two mobile phone.

## Slide 4
Give it to me, I have 1G bytes phone flash.
I have 100M bytes of data, who can carry for me?
I can also carry for you!
Thank you but you are in the opposite direction!
Don’t give to me! I am running out of storage.
Reach an access point.
Internet
Finally, it arrive…
Search La Bonheme.mp3 for me
Search La Bonheme.mp3 for me
Search La Bonheme.mp3 for me
There is one in my pocket…

## Slide 5: Applications
Asynchronous, local messaging
Automatic address book or calendar updates
Ad-hoc Google
File sharing, bulletin board
Commercial transactions
Alerting, tracking or finding people
Notes: Ad hoc Google is a quite interesting application. Google provide a very effective directory services on the internet but actually there are many mobile devices containing interesting data. Can we have a method to browsing on the ad hoc devices? That are huge amount of mobile devices and hence huge amount of interesting data on them.

## Slide 6: Measuring Human Mobility Mobility is a double-edged sword, it potentially increases the bandwidth, but also provides challenges for communication.

## Slide 7: Why measure human mobility?
Mobility increases capacity of dense mobile network [tse/grossglauser]
Also create dis-connectivities
Human mobility patterns determine communication opportunities
Notes: Mobility provide physical way to carry a large bunch of data from one place to another place, some research actually also shows that mobility increase the capacity of dense network. But moblity at the same time creat the challenge for communication, it creats disconnectivities and make end to end communications less possible. In pocket swich network, mobility has another important role, the mobility patterns determine the next commnication opportunities. Human mobility is so important so worth us to spend sometimes to study it.

## Slide 8: Experimental setup
iMotes
  ARM processor
  Bluetooth radio
  64k flash memory
Bluetooth Inquiries
  5 seconds every 2 minutes
  Log {MAC address, start time, end time} tuple of each contact
Notes: To study the human mobility we setup a series of iMote experiment. iMotes are some tiny embeded sensor produced by intel research. iMotes use Bluetooth as communciation media, this is different from the berkeley motes which use RF radio. This is one reason why we choose iMote as our experiment devices since nowaday many portable devices have BT and usually go with the user so can be a good indication of human mobility.So we programmed the motes and distributed to the people participating in the experiment to carry around. The motes are programed to do to do BT Inqueries for every 2 minutes for the other BT devices in the environment. For the BT devices seen, it will recored the mac address of that device, and the time start see the device and the time the deviced disappear.

## Slide 9: Experimental devices
Notes: Here showes the imotes. The left hand figure shows the imote without packaging. We can see that the imote is very small, around 2.5cm without the battery. This is a advantage so we can ask people to carry around with them. The right photo shows two packaging of the imotes. One is inside the dental fossil box, this package is water proof, transparent and can see the LED shinning inside it. The people can put it inside their pockage or handbags. Another package is the keychain, people are encourgae to put it onto their keys. This is good since that people usually will carry their keys together with them so can prevent the problem that the iMotes will be left at home for a whole day.

## Slide 10: Infocom 2005 experiment
54 iMotes distributed
Experiment duration: 3 days
41 yielded useful data
11 with battery or packaging problem
2 not returned
Notes: 54 iMotes were distributed to the students attending the workshop on the first day or the conference and was required to return back at the end of the conference. We put a collection box at the conference place. Most of the iMotes were returned, only 2 were taken away as suverniors.

## Slide 11: Brief summary of data
41 iMotes
182 external devices
22459 contacts between iMotes
5791 contacts between iMote/external device
External devices are non-iMote devices in the environment, e.g. BT mobile phone, Laptop.
Notes: Before the explaining of the data, I want to first explain the term external address. As we know the iMotes will record the devices in the environment includes both iMotes address and other address. So these addresses except iMote are classified as external address, they maybe BT mobile phones and Laptop. And we can see that there are much more contact between iMotes than between iMotes and external addresses.

## Slide 12: Contacts seen by an iMote
iMoites
External Devices
Notes: We have mentioned that a imote will record the contact information of (Mac address, start time, end time). Let’s go into an iMote and see what is actually inside it. We extract the data from one imote and plot it on a graph. The x-axis of the graph shows the time of the day and the y-axis shows the node ID, since we have promised the participants to keep all information anormous so we will not plot out the Mac addresses of the devices and motes discovered, we give each device a number for indication. On the graph, each blue dot representate a contact. We can see the contacts are quite sparsely distributed, with more contact between the motes than the external devices. One the left figure, we have an interesting observation. The mote see node 28 every night and they stay together the whole night. We can say that these two persons share the same room or live in the next door.

## Slide 13: Analysis of Conference Mobility Patterns

## Slide 14: Contact and Inter-contact time
Inter-contact is important
  Affect the feasibility of opportunistic network
  Nature of distribution affects choice of forwarding algorithm
  Rarely studied
Notes: Let’s zoom in the picture on page 13, we can see that the contacts between two nodes are sparsely distributed. The solid line in the above plot represent the blue dots in the previous contacts diagram. Between the solid lines are some empty spaces. So we say in the daily life, two persons may meet each other then go away and then meet again some other time. The time they can see each other, or we say within a contact range, is called the contact time. Contact time determine how much data two devices can transfer between each other, but which is also heavily depend on the bandwidth of transmission. Inter contact time is the time between two contact, it detemine how often a communication is possible. Shorter inter contact time means that the two people see each other quite often. If two person with short inter-contact time, then means that we can wait for next contact and send the data directly. If longer inter-contact time is observed, then need to rely on other media to transfer the data instead of waiting forever. In previous reseach, inter-contact is rarely studies. But we think this is a important parameter need to be seriously studied.

## Slide 15: Contact and Inter-contact Distribution
Contacts
Inter-contacts
Notes: These two graphs are the log-log distribution of time and probability. The x-axis shows the time in log scale and the y-axis show the probablity in log sclae. Let look at the point of (10 mins, 0.1), it means that the probability of contact time larger 10 minutes is 0.1 Both graph has a green line and a red line. The green line shows the distribution for an iMote and the red line shows the distribution for a external address. We can see that both the contact time and the inter-contacts time follow a heavy tail log-log distribution, or we can call it a approximate power law distribution. Let’s look at the figure on the right handside, both the imote and exernal address has a power law coefficient of 0.4 as show by the blue line. One day, two day, three day, the cut-off is limited by the duration of experiment.

## Slide 16: What do we see?
Power law distribution for contact and Inter-contact time
Both iMotes and external nodes
Does not agree with currently used mobility model, e.g. random way point
Power law coefficient < 1
Notes: Our observation here does not agree with the currently used mobility model such as the random way point, which assume an exponential decay for the inter-contact time. This make the human mobility behaviour very different.

## Slide 17: Implication of Power Law Coefficient
Large coefficient => Smaller delay
Consider 2-hops relaying [tse/grossglauser] analysis [TechRep]
Denote power law coefficient as 
For > 2
    Any stateless algorithm achieves a finite expected delay.
For > (m+1)/m and #{nodes} ≥2m :
    There exist a forwarding algorithm with m copies and a finite expected delay.
For < 1
    No stateless algorithm (even flooding) achieve a bounded delay (Orey’s theorem).
Notes: Now we know that human inter-contact time follows an approximate power law. But how the power law coefficient affect the forwarding algorithm? In general, we can say, the larger the coefficient, the smaller the delay. But if we consider a more detail sceneria, we can look at a 2-hops relaying algorithm as analysised in our technical report. The detail of the two relay scheme can be find in [tse/grossglauser] or in our technical report.

## Slide 18: Frequency of sightings and pairwise contact

## Slide 19: What do we see?
Nodes are not equal, some active and some not
  Does not agree with current mobility model, equally distributed.
iMotes are seen more often than external address
More iMotes pair contact
  Identify Sharing Communities to improve forwarding algorithm

## Slide 20: Influence of time of day

## Slide 21: What do we see?
Still a power law distribution for any three-hour period of the day
Different power law coefficient for different time
  Maybe different forwarding algorithm for different time of the day

## Slide 22: Consequences for mobile networking
Mobility models needs to be redesigned
  Exponential decay of inter contact is wrong
  Mechanisms tested with that model need to be analyzed with new mobility assumptions
Stateless forwarding does not work
  Can we benefit from heterogeneity to forward by communities ?
  Should we consider different algorithm for different time of the day?

## Slide 23: Future Work
Continue mobility measurement in different network environments
Continue mathematical analysis
Create representative mobility models
Design and evaluate forwarding algorithms for PSN
Prototyping PSN applications, e.g. distributed file sharing and newsgroups

## Slide 24: Thank You Jon.Crowcroft@cl.acm.ac.uk Pan.Hui@cl.acm.ac.uk

## Slide 25: Inter-contact for Workplace and University Environment

## Slide 26: Inter-contact time for WiFi traces

## Slide 27: Any-contact and inter-any-contact
Any-contact : the duration of staying with at least one node
Inter-any-contact : the duration between two any-contact
Contact
Contact
Contact
Any-contact

## Slide 28: Any-contact and Inter-any-contact distribution

## Slide 29: Pocket switched networks
Make use of global, local network connectivity and user mobility
Under more general
  MANET
  DTN [Fall]
Notes: Idea case is the package can jump from UK to HK