## Slide 1: Building Trusted Systems with Protected Modules
Bryan Parno
Microsoft Research

## Slide 2: Collaborators
Michael Reiter
Arvind Seshadri
Adrian Perrig
Jonathan McCune
Jacob R. Lorch
James Mickens
Microsoft Research
Carnegie Mellon University
John R. Douceur

## Slide 3: The Perils of Digital Data
X
Chart: 
| Clean | Infected
Sales | 75 | 25
Infected
[OECD ‘08]
[Holz et al. ‘08]
[Anderson & Kuhn ‘95]
HW
Violation!

## Slide 4: My Goal: Security & Features
Feature-rich
Low-cost
Quickly evolving
Secrecy
Integrity
Isolation
Availability
And

## Slide 5: My Research: Trust Extension
Bootstrapping Trust
[IEEE S&P’10] [Springer’11]
Fully Trusted
HW & SW
Minimal Trust
in Endhosts
Extension to the Network
[SIGCOMM ‘07]
Verifiable Computing
[Crypto’10]
Fully Untrusted
HW & SW
Minimal Trust
in HW & SW
OS
Hardware
App
1
App
N
…
Secure Code Execution
[IEEE S&P’07,’11] [EuroSys’08] [ASPLOS’08]
Notes: Explain color scheme.
For example, Alice might check that the computer in the Internet café is not running a keylogger.
Emphasize “outsourcing” aspect of VC.

## Slide 6
Talk Overview
Introduction
Securely Executing Code On Demand
Practical State Continuity for Protected Modules
Conclusions
Notes: Investigation of how to provide a secure environment on-demand

## Slide 7: Problem Overview
OS
App
App
…
S
S
DMA Devices
(Ex: Network, Disk, USB)
CPU, RAM,
Chipset
Notes: Emphasize that this is an overview!

## Slide 8: Problem Overview
OS
App
App
…
DMA Devices
(Ex: Network, Disk, USB)
CPU, RAM,
Chipset
Run arbitrary code with maximum privileges
Subvert devices
Perform limited hardware attacks
  E.g., Power cycle the machine
  Excludes physically monitoring CPU-to-RAM communication
S
Adversary Capabilities
Notes: Emphasize that this models a remote/software attacker, which is most common by far.

## Slide 9: Previous Work: Persistent Security Layers
OS
App
App
…
S
Security Kernel
Virtual Machine Monitor
Hardware
S
Hardware
  [Gold et al. ‘84], [Shockley et al. ‘88], [Karger et al. ‘91], [England et al. ‘03], [Garfinkel et al. ‘03], …
Notes: Once VMM takes over, it never gives up control
KVM/370 in Retrospect – Gold, Linde, Cudney
An Overview of the GEMSOS class A1 technology and application experience – Shockley, Tao, Thompson
A Retrospective on the VAX VMM Security Kernel – Karger, Zurko, Bonin, Mason, Kahn
Terra: A virtual machine-based platform for trusted computing – Garﬁnkel, Pfaff, Chow, Rosenblum, and Boneh.
Reducing TCB complexity for security-sensitive applications: Three case studies – Singaravelu, Pu, Haertig, and Helmuth.
A trusted open platform - England, B. Lampson, J. Manferdelli, M. Peinado, and B. Willman.

## Slide 10: Previous Work: Persistent Security Layers
OS
New CPU instruction
Designed to securely start a VMM
Atomically protects and executes code
Late Launch Support
DMA Devices
(Ex: Network, Disk, USB)
CPU, RAM,
Chipset
Late
Launch
VMM
Virtual Machine Monitor
OS
App
App
…
S
  [Gold et al. ‘84], [Shockley et al. ‘88], [Karger et al. ‘91], [England et al. ‘03], [Garfinkel et al. ‘03], …
Notes: VMM or Hypervisor

## Slide 11: Previous Work: Persistent Security Layers
  [Gold et al. ‘84], [Shockley et al. ‘88], [Karger et al. ‘91], [England et al. ‘03], [Garfinkel et al. ‘03], …
DMA Devices
(Ex: Network, Disk, USB)
CPU, RAM,
Chipset
Allow?
OS
App
App
…
S
Virtual Machine Monitor
Performance reduction
Feature elimination
Increased attack exposure
Additional complexity
Drawbacks:
Key Insight:
All avoided with
security on demand!
Observation:
All result from persistence
Notes: VMM or Hypervisor
Question: What causes these drawbacks?
Observation: Cause is Persistance, i.e., VMM is present even when not performing security-sensitive operations!
Insight: Avoid w/ security on-demand.

## Slide 12: Flicker Overview: On-Demand Security
Hardware
OS
App
App
…
OS
Hardware
App
App
…
Flicker
S
[IEEE S&P ‘07], [EuroSys ‘08], [ASPLOS ‘08]

## Slide 13: Flicker: An On-Demand Secure Environment
OS
Full HW access
Full performance
Hardware
App
1
App
…
[IEEE S&P ‘07], [EuroSys ‘08], [ASPLOS ‘08]
Insecure
OS
Hardware
App
App
…
Flicker
S
Full secrecy
Full isolation
Minimal trust
Minimal complexity
Secure
Notes: Of course, by design, the Flicker environment is quite spartan. This means you can include exactly the code you need for your app and nothing else. Applications this work well for include computational tasks (e.g., crypto), those that require minimal UI, e.g., password entry, etc.

## Slide 14: Challenges of On-Demand Security
Insecure
Secure
1. Secure Context Switching
3. Secure Data Preservation
4. Leverage
Insecure Features
2. Evidence of Security
Notes: Emphasize why these are hard!
Example for #4: Use the network without including a network driver in the set of trusted code

## Slide 15: Secure Context Switching
CPU
RAM
Flicker
OS
Module
RAM
App
…
CPU
App
S
Allow?
S
Late
Launch
App
Module
OS
App
…
Module
App
CPU
Late
Launch
S
Inputs
S
Flicker
Flicker
S
Outputs
Module
Request Flicker
Late Launch
Application Code Execution
Resume OS
Steps:
✓
Notes: Module makes the decision, which prevents a malicious module from being run. Of course, the tradeoff is availability. A malicious OS may choose not to run Flicker. Fortunately, as I describe later, the user can detect this.

## Slide 16: Challenges of On-Demand Security
Insecure
Secure
1. Secure Context Switching
3. Secure Data Preservation
4. Leverage
Insecure Features
2. Evidence of Security

## Slide 17
OS
App
…
Module
App
CPU
RAM
Module

## Slide 18
Flicker
Late
Launch
S
Inputs
Outputs
Must be unforgeable
Prevents
Additions
Must be tamper-proof
How can we convey the log to Alice?
Notes: Mention that this log is what prevents (via later detection) the adversary from providing bad input

## Slide 19: Hardware-Supported Logging
Provides integrity for append-only logs
Can digitally sign logs
Equipped with a certificate of authenticity
Can authenticate that a Late Launch took place
Trusted Platform Module (TPM)
✓
Late
Launch
✓
John
Hancock
Late
Launch
Notes: Mention that logs don’t persist through reboot

## Slide 20: We Do Not Use the TPM to:
Take over your machine
Force you to run Windows (or Linux)
Enforce Digital-Rights Management (DRM)
Notes: Using the TPM to benefit the user
Mention TPM not tamper-proof, so ill-suited to DRM

## Slide 21
Flicker
Late
Launch
S
Inputs
Outputs

## Slide 22: Attestation
random #
✓
random #
John
Hancock
John
Hancock
Guarantees freshness
Guarantees real TPM
Guarantees actual TPM logs
Trustworthy!
Notes: Alice trusts her phone. Attestation is a protocol that allows Alice to extend the trust she has in her phone to allow her to trust the software on her computer.
Random # is “given” to the TPM
Allows Alice to conclude that the log is accurate, and hence she can trust that the code described did indeed execute in a secure environment.

## Slide 23: Comparison With “Traditional” Attestation
Flicker
Late
Launch
S
Input
Output
Flicker
Traditional
BIOS
OS
Bootloader
Drivers 1…N
App 1…N
Key Insight:
Late Launch + Fine-Grained Attestations
Fine-Grained Attestations Improve Privacy
Fine-Grained Attestations Simplify Verification
  [Gasser et al. ‘89], [Arbaugh et al. ‘97], [Sailer et al. ‘04], [Marchesini et al. ‘04]
Notes: Digital Distributed System Security Architecture – Gasser, Goldstein, Kaufman, Lampson
A Reliable Bootstrap Architecture- Arbaugh, Farber, Smith
Design and Implementation of a TCG-based Integrity Measurement Architecture - Sailer, Zhang, Jaeger, van Doorn
Open-Source Applications of TCPA hardware - Marchesini, Smith, Wild, Stabiner, Barsamian

## Slide 24: Application: Verifiable Malware Scanning
OS
Hardware
App
1
App
N
…
Run Detector
OS
Hardware
App
1
App
N
…
OS
Hardware
App
1
App
N
…
No Malware
Detected!
Flicker
D
John
Hancock
Notes: Let’s say Alice has noticed her computer is running slower than usual, and she wants to check if her computer is infected. Or suppose she wants to check her email using a computer in an Internet café.
Verifiably learns about software. Doesn’t tell her about modified hardware.

## Slide 25: Application: Verifiable Malware Scanning
OS
Hardware
App
1
App
N
…
John
Hancock
Run Detector
Flicker
D
Flicker
Late
Launch
D
Inputs
Outputs
John
Hancock
OS
Hardware
App
1
App
N
…
✓

## Slide 26: Additional Applications
Improved SSH password handling
Distributed computing
Protected CA keys

## Slide 27: Implementation
Open-source versions for AMD & Intel
Linux and Windows kernel modules
Many implementation challenges:
  Hardware bugs, incomplete/incorrect vendor implementations, labyrinthine spec, etc.
http://flickertcb.sourceforge.net/
Notes: Jon!

## Slide 28: Performance: Context Switches
Chipset Modifications [ASPLOS ‘08]
Insecure
Secure
Late
Launch
14 ms
Retrieve Data
905 ms
Total
929 ms
Store Data
20 ms
20 ms
34 ms
<1 ms
TPM Encryption
TPM Storage ACLs
0.0005 ms
0.0005 ms
0.0005 ms
Notes: Might be tough to do every keystroke, but acceptable for entering a password, signing an email, etc.

## Slide 29: Related Approaches
Persistent security layers
  KVM [Gold et al. ‘84], GEMSOS [Shockley et al. ‘88], VAX VMM [Karger et al. ‘91], Terra [Garfinkel et al. ‘03], NGSCB [England et al. ‘03], Proxos [Ta-Min et al. ‘06]
System-wide attestation
  DDSSA [Gasser et al. ‘89], Secure Boot [Arbaugh et al. ‘97], IMA [Sailer et al. ‘04], Enforcer [Marchesini et al. ‘04]
Secure co-processors
  Dyad [Yee ‘94], IBM 4758 [Jiang et al. ‘01]
Notes: KVM/370 in Retrospect – Gold, Linde, Cudney
An Overview of the GEMSOS class A1 technology and application experience – Shockley, Tao, Thompson
A Retrospective on the VAX VMM Security Kernel – Karger, Zurko, Bonin, Mason, Kahn
Terra: A virtual machine-based platform for trusted computing – Garﬁnkel, Pfaff, Chow, Rosenblum, and Boneh.
Reducing TCB complexity for security-sensitive applications: Three case studies – Singaravelu, Pu, Haertig, and Helmuth.
Splitting Interfaces: Making trust between applications and operating systems configurable – Ta-Min, Litty, Lie
Digital Distributed System Security Architecture – Gasser, Goldstein, Kaufman, Lampson
A Reliable Bootstrap Architecture- Arbaugh, Farber, Smith
Design and Implementation of a TCG-based Integrity Measurement Architecture - Sailer, Zhang, Jaeger, van Doorn
Open-Source Applications of TCPA hardware - Marchesini, Smith, Wild, Stabiner, Barsamian
Using Secure CoProcessors – Bennet Yee
Securing Web Servers Against Insider Attack - Jiang, Smith, Minami

## Slide 30
New paradigm: On-Demand Security
New challenges:
  Secure context switches
  Evidence of security
  State preservation
New properties: Fine-grained attestations
Flicker Summary
[IEEE S&P ‘07], [EuroSys ‘08], [ASPLOS ‘08]
OS
Hardware
App
App
…
Flicker
S

## Slide 31: Limitations
Current systems only support one Flicker session at a time
Flicker environment is spartan (by design!)
Flicker does not guarantee availability
Flicker is vulnerable to sophisticated HW attacks
Notes: 1st one is engineering. Next two are fundamental.

## Slide 32
Talk Overview
Introduction
Securely Executing Code On Demand
Practical State Continuity for Protected Modules
  Defining protected modules
  Problems with naïve solutions
  Design of Memoir
  Implementation and evaluation
Conclusions
Notes: Investigation of how to provide a secure environment on-demand

## Slide 33: Protected Module: Data that’s only accessible via a small piece of code.
Code
Data

## Slide 34: Protected modules are enabled by isolation architectures.
Flicker
Secure execution infrastructure
Secure coprocessor
Trusted hypervisor
Small trusted computing base
Minimal code
Few devices
Trusted system
Untrusted system
Code
Storage

## Slide 35: Isolation architectures have limited trusted storage.
Small trusted computing base
Minimal code
Few devices
Trusted system
Untrusted system
Code
Storage
TPM
Disk device drivers
1,280 bytes of NVRAM

## Slide 36: Protected modules must leverage untrusted storage for their data.
Trusted system
Untrusted system
Code
Data
Storage
Bjcx
Signature
Confidentiality
Data
Integrity
Data

## Slide 37: Cryptography is insufficient to prevent a rollback attack.
Trusted system
Untrusted system
Code
Storage
Bjcx
Signature
Kebz
Signature
Saved from 2008:

## Slide 38: Encryption key protector illustrates the importance of rollback resistance.
Guess PIN
Recover
Key protector
User | PIN | Recovery key | Disk key | # wrong
parno lorch johndo mickens mccune | 1111 0905 8034 9999 7654 | 90928389234 82378912837 29812982309 40954353458 32234528981 | A0FF23849083 B58890AD38E1 8293808E20CD 003827878EE3 C4358C380102 | 0 2 0 0 0
lorch: 1234?
3
Wrong
lorch: 1235?
Rolling back wrong-guess count allows dictionary attack.

## Slide 39: Rollback resistance is important for almost any stateful protected module.
Protected module | Consequences of rollback
Encryption key protector | Rolling back wrong-guess count allows a dictionary attack.
Privacy-preserving database using differential privacy | Rolling back privacy budget expenditure allows privacy safeguards to be subverted.
Monotonic counter | Rolling back counter updates makes the counter go backward.
Audit log | Rolling back the log tail subverts the append-only property of the log.
Game monitor | Rolling back recent activity lets player react to another player’s move after seeing it.
Access control list | Rolling back the removal of a user from a group restores access to the disallowed user.
… | …

## Slide 40: Naive approach to rollback resilience creates problems.
Monotonic counter prevents rollback
But, it introduces new problems
  Potential for permanent unavailability after non-adversarial crash event
    OS crash or power failure
  Limited lifespan and slow operation
    due to trusted non-volatile write on each request

## Slide 41: Memoir demonstrates how to make rollback resistance practical.
Memoir achieves rollback resistance yet still has...
  Crash resilience
  Long lifespan and fast operation, by avoiding writes to trusted NV storage
Adversarial attacks on availability are out of scope.
Non-adversarial crashes only

## Slide 42
Talk Overview
Introduction
Securely Executing Code On Demand
Practical State Continuity for Protected Modules
  Defining protected modules
  Problems with naïve solutions
  Design of Memoir
  Implementation and evaluation
Conclusions
Notes: Investigation of how to provide a secure environment on-demand

## Slide 43: A monotonic counter can provide rollback resistance.
Code
Data
Initialize
Hwpb
NV
Tag: 1
Signature
1
1

## Slide 44: A monotonic counter can provide rollback resistance.
Code
NV
Hwpb
Tag: 1
Signature
1

## Slide 45: A monotonic counter can provide rollback resistance.
Code
Data
Request
Hwpb
1
Tag: 1
Signature

## Slide 46: A monotonic counter can provide rollback resistance.
Code
Data
1
2
Tag: 2
Data’
Yzqr’
Signature
2

## Slide 47: Problem 1: The monotonic-counter solution is not crash-resilient.
Code
1
2
Tag: 2
Yzqr’
Signature
2

## Slide 49: Problem 1: The monotonic-counter solution is not crash-resilient.
Code
2
Request
Yzqr
Tag: 1
Signature
Module permanently unusable
Window of vulnerability includes time to exit isolated environment, restore OS, write to disk.

## Slide 50: Problem 2: Monotonic-counter frequently writes trusted NV storage.
an extra 30-80 ms per request
100,000 write-cycle limit
only 100,000 requests, ever!
lasts only 28 hours at
one request per sec

## Slide 51: Two-phase commit also doesn’t work.
Performance problems
  Every request requires two invocations of isolation architecture, trusted randomness, an NV write
Fundamental security problem
  Adversary can observe side channels of request without performing it
For details, see paper.

## Slide 52
Talk Overview
Introduction
Securely Executing Code On Demand
Practical State Continuity for Protected Modules
  Defining protected modules
  Problems with naïve solutions
  Design of Memoir
  Implementation and evaluation
Conclusions
Notes: Investigation of how to provide a secure environment on-demand

## Slide 53: For crash resilience, Memoir requires request execution be deterministic.
Source of non-determinism | How to avoid it
Random numbers | Seed secure PRNG with random data during initialization
Multi-thread scheduling | Apply others’ research to make deterministic (future work)
Time | Exchange messages with a trusted time source

## Slide 54: Memoir achieves crash resilience by storing a secure history summary.
Deterministic code
5
h
h
Request1
Request2
= Hash(Hash(Hash( ) || ) || ) …
Request3
Request
Ewfg
Tag: h
Signature

## Slide 55: Memoir achieves crash resilience by storing a secure history summary.
Deterministic code
5
h
Request
Data
h’
Tag: h’
Data’
Urvi’
Signature
h’
h
Request
= Hash( || )
h’

## Slide 57: Memoir achieves crash resilience by storing a secure history summary.
Deterministic code
h’
Request
Ewfg
Tag: h
Signature
Since request execution is deterministic, replaying will produce the same output.
Thus, it is safe to replay the last request.
h
Request
= Hash( || )
h’

## Slide 58: Memoir avoids non-volatile writes by using trusted volatile storage.
TPM
Platform
Configuration
Registers
PCR
PCR
PCR
PCR
= Hash( || )
p
p’
h
or by rebooting, causing it to be zeroed.
A PCR can only be modified by extending it:

## Slide 59: Memoir avoids NV writes by using two-part history summaries.
Deterministic code
n
p
h
n’
p
0
Written twice per boot
Updated on every request
Before reboot, a checkpoint routine must run, to incorporate trusted volatile state into trusted NV state.
At 1 reboot per day, 1 request per sec, module can last
136 years instead of the monotonic counter’s 28 hours.
= Hash( || )
p
n
n’

## Slide 60: Memoir must ensure correctness if an adversary doesn’t checkpoint.
Adversary can clear PCR without running checkpoint routine
  Guard bit in trusted NV storage indicates whether PCR should be non-zero
Adversary can extend PCR
  Extension secret used on each extension
For details, see paper.

## Slide 61: Checkpoint routine must run before a non-adversarial reboot.
System Management Interrupt Handler
Checkpoint routine
For OS crashes:
For power failures:

## Slide 62: Memoir improves dramatically on the monotonic-counter solution.
Monotonic counter | Memoir
OS crash or power failure can make module permanently unusable | Non-adversarial crashes not a problem
Lasts only 28 hours at one request per sec | Lasts 136 years even with one reboot per day
Spends 30-80 ms per request to write NVRAM | Spends 15-25 ms per request to access a PCR

## Slide 63: Also in the paper:
Proof of correctness of Memoir protocols
  Machine-checked TLA+
  Full details in 390-page tech report
Supporting unlimited modules with constant NVRAM and one PCR
Suggestion for minor TPM modification to solve NVRAM issue
Obviating trusted randomness in execution
CONSTANT InputType, OutputType, PublicStateType, PrivateStateType
ServiceResultType 
[ newPublicState : PublicStateType; newPrivateState : PrivateStateType; output : OutputType ]
CONSTANT Service(_, _, _)
CONSTANT InitialAvailableInputs, InitialPublicState, InitialPrivateState
VARIABLE AvailableInputs, ObservedOutputs, PublicState, PrivateState
MakeInputAvailable 
 input  InputType :
 input  AvailableInputs
 AvailableInputs' = AvailableInputs  {input}
 UNCHANGED ObservedOutputs
 UNCHANGED PublicState
 UNCHANGED PrivateState
AdvanceService 
 input  AvailableInputs :
LET
sResult 
Service(PublicState, PrivateState, input)
IN
 PublicState' = sResult.newPublicState
 PrivateState' = sResult.newPrivateState
 ObservedOutputs' =
ObservedOutputs  {sResult.output}
 UNCHANGED AvailableInputs
Init 
 AvailableInputs = InitialAvailableInputs
 ObservedOutputs = {}
 PublicState = InitialPublicState
 PrivateState = InitialPrivateState
Next  MakeInputAvailable  AdvanceService
Spec  Init  □[Next]AvailableInputs, ObservedOutputs, PublicState, PrivateState
TLA+ High-Level Memoir Spec

## Slide 64
Talk Overview
Introduction
Securely Executing Code On Demand
Practical State Continuity for Protected Modules
  Defining protected modules
  Problems with naïve solutions
  Design of Memoir
  Implementation and evaluation
Conclusions
Notes: Investigation of how to provide a secure environment on-demand

## Slide 65: Implementation is a framework for making and using protected modules.
Untrusted system
Client
Trusted system, isolated by Flicker
Protected module
MemoirLib
Service
n
p
Pseudo-random
numbers
Memoir tools
create_module.exe
exec_request.
exe
Service
initialize_state
handle_request
serialize_state
deserialize_state
Memoir ensures confidentiality, integrity, rollback resilience, crash resilience, and NV avoidance.
Memoir makes it easy to write protected modules.
Available at http://research.microsoft.com/memoir

## Slide 66: Future implementation work
System management interrupt handler
Module management module
  Enables multiple modules to use constant NVRAM and one PCR

## Slide 67: Our evaluation results answer three main questions.
How much does Memoir increase TCB size?
How fast can modules run with Memoir?
In particular, how useful is NVRAM avoidance?

## Slide 68: Our experimental platform is a standard PC supported by Flicker.
Isolation mechanism: Flicker 0.5 secure execution infrastructure
HP Compaq 6005 Pro PC
  3.0 GHz AMD Athlon II X2 CPU with AMD-V
  2.0 GB memory, 160 GB SATA disk, Infineon TPM
Linux 2.6.31
Only one core enabled since Flicker doesn’t support multiprocessors

## Slide 69: Memoir contribution to TCB
Chart: SLOC
| Memoir tools | MemoirLib
Crypto code | 2819 | 4695
Other code | 1055 | 1831
Safety depends on this code.
Bugs can only lead to liveness violations.
TCB increase is modest, much smaller than disk drivers.
Most of the code is well-tested cryptography code publicly and widely available.
Only some of this code is safety-critical. Bugs in the tools can only hamper availability.

## Slide 70: Execution time of no-op module
Chart: Execution time (ms)
| No protection | + confidentiality and integrity | "+ rollback resistance and crash resilience" | "+ NV avoidance"
Flicker | 47.8472 | 52.2477 | 52.4036 | 48.3101
Other Memoir | 0.19591 | 1.0726 | 1.0675 | 1.0546
Extend PCR | 0 | 0 | 0 | 5.7336
Read PCR | 0 | 0 | 0 | 9.8874
Write NVRAM | 0 | 0 | 33.0498 | 0
Read NVRAM | 0 | 6.7613 | 6.8016 | 6.8316
Sync. disk write | 0 | 0 | 43.1095 | 39.9722
On this architecture, Flicker takes about 50 ms, mostly for late-launch.
Flicker
baseline
+ confidentiality
and integrity
+ crash
resilience
and rollback
resistance
+ avoiding
trusted
NV writes
Encrypting and signing adds about 7 ms.
Crash resilience adds about 43 ms, due to synchronous disk write before executing request.
Rollback resistance adds about 33 ms, to write trusted NVRAM.
Avoiding NVRAM writes saves 17 ms (and also increases module lifespan).

## Slide 71: Execution time of other modules
Chart: Execution time (ms)
| EKP | PPD | TrInc | EKP | PPD | TrInc
Flicker | 52.5936 | 52.4087 | 48.4238 | 48.3326 | 48.1261 | 48.4143
Other Memoir | 0.99557 | 0.9413 | 0.99071 | 0.99238 | 0.94422 | 0.99253
Extend PCR | 0 | 0 | 0 | 5.7328 | 5.7316 | 5.7338
Read PCR | 0 | 0 | 0 | 9.8857 | 9.8889 | 9.8856
Write NVRAM | 33.0734 | 33.082 | 33.0964 | 0 | 0 | 0
Read NVRAM | 6.801 | 6.8013 | 6.799 | 6.8359 | 6.8368 | 6.8368
Execute request | 0.060503 | 0.060427 | 5.5551 | 0.060996 | 0.061005 | 4.9114
Sync. disk write | 42.6775 | 15.7908 | 43.5989 | 38.8724 | 20.6662 | 43.7588
Without NV avoidance
With NV avoidance
We built several prototype protected modules with Memoir.
Encryption key protector
Privacy-preserving database
Trusted monotonic counter
Similar performance to no-op service, except different amounts of time to write state to disk.

## Slide 72: Additional Research
Improved application security on client computers
  Eliminating manifests and pop-ups
  Eliminating the need for software updates
Privacy-preserving personalized online services
  Protected modules + fuzzed client requests
  New models for Oblivious RAM
Verifiable computation
  More efficient constructions
  Connections to attribute-based encryption

## Slide 73: Conclusions
    Flicker provides an on-demand secure execution environment with minimal trust assumptions
Protected modules with rollback resistance are a powerful, general tool
Memoir is a practical framework for building protected modules with state continuity
Thank you!
parno@microsoft.com
http://flickertcb.sourceforge.net/
http://research.microsoft.com/memoir
Notes: Emphasize: Flicker uses a new, on-demand security architecture to provide strong properties and avoid drawbacks of previous accepted architecture
Emphasize: VC achievable via the counter-intuitive use of secrecy to achieve integrity.

## Slide 74: Application: SSH Passwords
K
Flicker
S
Generate
{K, K-1}
Flicker
S
K-1
EncryptK(passwd)
Start
Start
EncryptK(passwd)
Flicker
S
K-1
Flicker
S
K-1
EncryptK(
)
passwd
✓
K
John
Hancock
Used for Encryption
Used for Decryption
Notes: Combine attestation with sealed storage to create a secure channel.

## Slide 75: Application: Distributed Computing
Trustworthy!
Flicker
S
Inputs
…
Outputs
Prevents software-based cheating!

## Slide 76: Default Functionality
Shim can execute arbitrary x86 code but provides very limited functionality
Fortunately, many security-sensitive functions do not require much
  E.g., key generation, encryption/decryption, FFT
Functionality can be added to support a particular security-sensitive operation
We have partially automated the extraction of support code for security-sensitive code

## Slide 77: Existing Flicker Modules
OS Protection Memory protection, ring 3 execution
Crypto Crypto ops (RSA, SHA-1, etc.)
Memory Alloc. Malloc/free/realloc
Secure Channel Secure remote communication
TPM Driver Communicate with TPM
TPM Utilities Perform TPM operations

## Slide 78: Developing With Flicker
Sensitive code linked against the Flicker library
Customized linker script lays out binary
Application interacts with Flicker via a Flicker kernel module
#include “flicker.h”
void flicker_main(void *inputs) {
}
const char* msg = “Hello, world”;
for(int i=0;i<13;i++)
OUTPUT[i] = msg[i];
Made available at:
/sysfs/flicker/output
Notes: If we want developers to use Flicker, it must be easy to deploy

## Slide 79: Flicker’s Impact on Suspended OS
User I/O ceases during Flicker session
Network can recover from dropped packets
In experiments with long-running Flicker sessions (~8 seconds):
  Copied files from CD to Disk to USB Drive
    No I/O errors reported
    File integrity unaffected
Conclusion: OS is resilient to Flicker sessions

## Slide 80: TPM Microbenchmarks
Significant variation by TPM model
Notes: Be concise. Mention that each color of bar is for a different TPM model.

## Slide 81: SKINIT (Secure Kernel Init)
Accepts address of Secure Loader Block (SLB)
  Memory region up to 64 KB (more on next slide)
SKINIT executes atomically
  Sets CPU state similar to INIT (soft reset)
  Enables DMA protection for entire 64 KB SLB
  Disables interrupts
  Causes TPM to reset locality-specific PCRs to 0
  Extends a measurement of the SLB into PCR 17
  Begins executing at SLB’s entry point

## Slide 82: Secure Loader Block Layout
SL Stack
Length
SL Header
EP Offset
SL Code and
Static Data
64 KB
SL Runtime
Data Area
SL Image
(hash area)
Length
ESP
EAX
SL Entry Point

## Slide 83: TPM Microbenchmarks
Significant variation by TPM model
Notes: Be concise. Mention that each color of bar is for a different TPM model.

## Slide 84: Overheads and Recommendations
O1 Late launch and TPM sealed storage overhead on every context switch
R1 Secure context switch between sensitive applications without TPM
O2 Other cores must halt to enable late launch
R2 Secure execution on multiple CPUs concurrently
O3 TPM equipped to store records from only one late launch
R3 TPM support for concurrent Flicker sessions
Notes: Motivation: Minimize changes to existing arch.
HOW, not just should. Inspired by our system, but not particular to it. Don’t blame TPM for being inadequate for a non-existent architecture.
Summary: 1 CPU in secure mode, (n-1) CPUs keep going

## Slide 85: Late Launch Performance
Late launch requires extra processors to stop execution
  More cores => more expensive
CPU
Memory Controller
TPM
CPU
Memory Controller
CPU
Memory Controller
CPU
Memory Controller
CPU
Memory Controller
Other CPUs I/O Devices
Other CPUs I/O Devices
TPM
RAM
RAM
…
STOP
Notes: Emphasize colored memory region is protected.

## Slide 86: New States for Memory Pages
CPU i
None
All
Launch
Suspend
Resume
Exit
Sensitive
Application
Avoid TPM for short-term data protection
Memory Controller supports DMA protection vector
Memory
Notes: Avoid TPM because it is slow (would be a waste of power even if it is fast) Emphasize ONLU CPI I can touch memory

## Slide 87: Concurrent Flicker Sessions
Other CPUs continue to perform useful work
Memory Controllers isolate secure state
CPU
Memory Controller
CPU
Memory Controller
Other CPUs I/O Devices
Other CPUs I/O Devices
TPM
RAM
Notes: Not actually a large divergence from today’s systems since cache coherence is already maintained.
Summary: 1 CPU in secure mode, (n-1) CPUs keep going

## Slide 88: Add Secure Execution PCRs to TPM
TPM
Each SE PCR holds state for one Flicker session
Bounds number of concurrent Flicker sessions
Static PCRs
Dynamic PCRs
Secure Execution PCRs

## Slide 89: Anticipated Improvement
Late launch cost only incurred when Flicker session launches
TPM (Un)Seal only used for long-term storage
Multicore systems remain interactive
Context switch overheads (common case) resemble VM switches today
Notes: Reminder: We’re better than VMMs due to our improved security properties
We care about VMMs because they are a common alternative for providing isolation
Our recommendations are designed to be similar to existing functionalities. The closest thing to a secure execution context switch is a VM context switch.

## Slide 90: Challenges of On-Demand Security
Insecure
Secure
1. Secure Context Switching
3. Secure Data Preservation
4. Leverage
Insecure Features
2. Evidence of Security

## Slide 91: Securely Preserving State
OS
Seal data under code, inputs, and/or outputs
Time
Flicker
S
Flicker
S
Flicker
S
Data
Flicker
S
Data
Flicker
S
Flicker
S
Flicker
S
Data

## Slide 92
Insecure
Secure
Securely Preserving State
Flicker
S
Data
A
Data
A
Flicker
S
Data
B
Data
B
Key Insight: Only possible via Code Identity

## Slide 93: Another naive solution, two-phase commit, also doesn’t work.
Performance problems: Every request requires...
  Two invocations of the isolation architecture
  Write to trusted non-volatile storage
  Trusted randomness
Fundamental security problem
  Adversary can observe phase 1, then decide whether to do phase 2
    Can tentatively perform request, observe side channels like output size and execution time, then decide whether to actually commit
  Example: dictionary attack on encryption key protector
    Guess a PIN, observe that output is too small to contain a key, don’t commit to prevent increment of wrong-guess count

## Slide 94: Other Memoir operations
Chart: Operation time (ms)
| Create module | Get public key and attestation | Checkpoint routine
Execution Time | 372.0639 | 429.8952 | 101.7463

## Slide 95: Preventing equivocation in distributed systems
Update counter
TrInc (trusted incrementer)
Monotonic counter ID | Value
1 2 3 4 5 | 17 243 0 1 19,012
ID 2 => 244, hash 90F357
244
SignK(ID 2, 243=>244,
hash 90F357)
Key: K

## Slide 96: Privacy-preserving database
Insert datum
Query
Differential-privacy database
Database
Privacy budget remaining
Asymmetric key pair
Health record
Cancer rate?
Answer + noise

## Slide 97: Privacy-preserving database
Privacy-preserving database
Insert datum
244
Key: K
Date range | Privacy budget spent
1/1/2011 – 1/31/2011 2/1/2011 – 2/28/2011 3/1/2011 – 3/31/2011 | 0.75 0.50 0.25
Current query
Range: 3/1/2011 – 3/31/2011
Last item: 3/3/2011
Privacy budget to spend: 0.25
Query state: S
ID 2 => 244, hash 90F357
SignK(ID 2, 243=>244,
hash 90F357)
Start query