## Slide 1: Infocom 2000 Tutorial Integrated services
Jon Crowcroft, thanks to Saleem Bhatti...
e-mail: jon@cs.ucl.ac.uk
phone: +44 20 7 679 7296
room: Jon – 212
Reading:
  S. Keshav, “An Engineering Approach to Computer Networking”, chapters 6, 9 and 14
  http://www.cs.ucl.ac.uk/staff/jon

## Slide 2: Objectives
Learn and understand about:
Support for real-time applications:
  network-layer and transport-layer
Quality of service (QoS):
  the needs of real-time applications
  the provision of QoS support in the network
Many-to-many communication - multicast
Integrated Services Network (ISN)
Notes: During the 1990’s, applications have become increasingly reliant on the use of the Internet protocols to provide data communications facilities. The use of the Internet protocols seems likely to increase at an extremely rapid rate and the Internet Protocol (IP) will be the dominant data communications protocol in the next decade. IP is being used for a huge variety of “traditional” applications, including e-mail, file transfer and other general non-real-time communication. However, IP is now being used for real-time applications that have quality of service (QoS) sensitive data flows. A flow is a stream of semantically related packets which may have special QoS requirements, e.g. an audio stream or a video stream. Applications such as conferencing (many-to-many communication based on IP multicast), telephony – voice-over-IP (VoIP) – as well as streaming audio and video are being developed using Internet protocols. The Internet and IP was never designed to handle such traffic and so the Internet community must evolve the network and enhance the Internet protocols in order to cater for the needs of these new and demanding applications. Users wish to have access to a whole plethora of telecommunication and data communication services via the Internet; users wish to access an Integrated Services Network (ISN).
In this set of lectures, we try to understand about QoS for IP-based applications and how the network must be changed to support these new applications.

## Slide 3: Support for real-time applications
Support in the network:
  routers, routing
Support at the end-systems:
  transport protocols
Support at the application level:
  user-network signalling
  application-level signalling and control
(Link & physical layers?)
Z10
Z11
7 application
6 presentation
5 session
4 transport
3 network
2 data link
1 physical
application layer protocol
Internet
upper
layer(s)
Notes: To provide support for real-time applications, we need to introduce mechanisms at many different parts of the communication stack.
At the network layer, we need to modify router behaviour so that packets belonging to QoS sensitive flows receive some kind of preferential treatment, compared to “normal” data packets. We also need to modify the behaviour of routing protocols in order to support multicast communication and QoS-based routing metrics.
At the transport layer, recall that we only have two general protocols: TCP for traditional applications that require an ordered by-stream delivery, and UDP for applications that build in specific control mechanisms at the application layer. For real-time flows, we can identify some general requirements, which we will see can be implemented by extending UDP as in the Real-time Transport Protocol (RTP).
At the application layer, we may identify other mechanisms that are required for specific real-time applications: floor control for conference applications; transcoding for audio and video flows; security mechanisms such as authentication. Although it is possible to identify some general requirements, such higher-layer mechanisms tend to specific to particular applications.
In this set of lectures, we consider the support that we have in the network and at the transport layer, as well as some general issues concerning the interface between the application and the network.
Why do we not consider the link layer and physical layer? Surely these have a fairly vital role in QoS as they provide the transmission capability? Remember that IP tries to hide the lower layers, so although we will se there are important issues concerning the lower layers, we concentrate on the network layer and transport layer.

## Slide 4: Real-time flows and the current Internet protocols

## Slide 5: The “problem” with IP [1]
Data transfer:
  datagrams: individual packets
  no recognition of flows
  connectionless: no signalling
Forwarding:
  based on per-datagram forwarding table look-ups
  no examination of “type” of traffic – no priority traffic
Routing:
  dynamic routing changes
  no “fixed-paths”  no fixed QoS
Traffic patterns
Notes: Let us first examine the service that IP offers. IP offers a connectionless datagram service, giving no guarantees with respect to delivery of data: no assumptions can be made about the delay, jitter or loss that any individual IP datagrams may experience. As IP is a connectionless, datagram service, it does not have the notion of flows of datagrams, where many datagrams form a sequence that has some meaning to an applications. For example, an audio application may take 40ms “time-slices” of audio and send them in individual datagrams. The correct sequence and timeliness of datagrams has meaning to the application, but the IP network treats them as individual datagrams with no relationship between them. There is no signalling at the IP-level: there is no way to inform the network that it is about to receive traffic with particular handling requirements and no way for IP to tell signal users to back-off when there is congestion.
At IP routers, the forwarding of individual datagrams is based on forwarding tables using simple metrics and (network) destination addresses. There is no examination of the type of traffic that each datagram may contain – all data is treated with equal priority. There is no recognition of datagrams that may be carrying data that is sensitive to delay or loss, such as audio and video.
One of the goals of IP was to be robust to network failure. That is why it is a datagram-based system that uses dynamic routing to change network paths in event of router overloads or router failures. This means that there are no fixed paths through the network. It is possible that during a communication session, the IP packets for that session may traverse different network paths. The absence of a fixed path for traffic means that, in practice, it can not be guaranteed that the QoS offered through the network will remain consistent during a communication session.
Even if the path does remain stable, because IP is a totally connectionless datagram traffic, there is no protection of the packets of one flow, from the packets of another. So, the traffic patterns of a particular user’s traffic affects traffic of other users that share some or all of the same network path (and perhaps even traffic that does not share the same network path!).

## Slide 6: The “problem” with IP [2]
Scheduling in the routers:
  first come, first serve (FCFS)
  no examination of “type” of traffic
No priority traffic:
  how to mark packets to indicate priority
  IPv4 ToS not widely used across Internet
Traffic aggregation:
  destination address
(QoS: pricing?)
Notes: At the individual routers, the process of forwarding a packet involves, taking an incoming packet, evaluating its forwarding path, and then sending it to the correct output queue. Packets in output queues are serviced in a simple first-come first-serve (FCFS) order, i.e. the packet at the front of the queue is transmitted first. The ordering of packets for transmission takes the general term on scheduling, and we can see FCFS is a very simple scheduling mechanism.
FCFS assumes that all packets have equal priority. However, there is a strong case to instruct the router to give some traffic higher priority than other traffic. For example, it would be useful to give priority to traffic carrying real-time video or voice. How do we distinguish such priority traffic from non-priority traffic, such as, say e-mail traffic. The IPv4 type of service (ToS) do offer a very rudimentary form of marking traffic, but the semantics of the ToS markings are not very well defined. Subsequently, the ToS field is not widely used across the Internet. However, it can be used effectively across corporate Intranets.
Also, in dealing with traffic that has been marked, we need to be wary of the extra processing a marking scheme may introduce in the core of the network where there is very high aggregation of network traffic. With FCFGS, effectively, aggregation is by use of the destination IP address.
Even if we could offer some sort of QoS control mechanism, with prioritisation or traffic differentiation, there is then the issue of pricing. How do we charge for use of network resources for a particular treatment of traffic for a particular customer?

## Slide 7: Questions
Can we do better than best-effort?
What support do real-time flows need in the network?
What support can we provide in the network?
Alternatives to FCFS?
Many-to-many communication?
Application-level interfaces?
Scalability?
Notes: So we can ask ourselves several questions.
Firstly, can we provide a better service that that which IP currently provides – the so-called best-effort?
The answer to this is actually, “yes”, but we need to find out what it is we really want to provide! We have to establish which parameters of a real-time packet flow are important and how we might control them. Once we have established our requirements, we must look at new mechanisms to provide support for these needs in the network itself. We are essentially asking trying to establish alternatives of FCFS for providing better control of packet handling in the network as well as trying to support multi-party (many-to-many) communication.
We also need to consider how the applications gain access to such mechanisms, so we must consider any application-level interface issues, e.g. is there any interaction between the application and the network and if so, how will this be achieved.
In all our considerations, one of the key points is that of scalability – how would our proposals affect (and be affected by) use on a global scale across the Internet as a whole.

## Slide 8: Requirements for an ISN [1]
Today’s Internet
IPv4: QoS not specified
TCP: elastic applications
Many network technologies:
  different capabilities
  no common layer 2
No support for QoS:
  ToS in IPv4 – limited use
QoS requirements:
  not well understood
Integrated Services Packet Network (ISPN)
QoS service-level:
  service type descriptions
Service interface:
  signalling
Admission control:
  access to resources
Scheduling:
  prioritisation and differentiation of traffic
Notes: The Internet was never designed to cope with such a sophisticated demand for services [Cla88] [RFC1958]. Today’s Internet is built upon many different underlying network technologies, of different age, capability and complexity. Most of these technologies are unable to cope with such QoS demands. Also, the Internet protocols themselves are not designed to support the wide range of QoS profiles required by the huge plethora of current (and future) applications.
In [CSZ92], the authors speak of the Internet evolving to an integrated services packet network (ISPN), and identify four key components for an Integrated Services architecture for the Internet:
service-level: the nature of the commitment made, e.g. the INTSERV WG has defined guaranteed and controlled-load service-levels (these are discussed later) and a set of control parameters to describe traffic patterns, which we examine later
service interface: a set of parameters passed between the application and the network in order to invoke a particular QoS service-level, i.e. some sort of signalling protocol plus a set of parameter definitions
admission control: for establishing whether or not a service commitment can be honoured before allowing the flow to proceed
scheduling mechanisms within the network: the network must be able to handle packets in accordance with the QoS service requested
A key component that is required here is signalling – talking to the network. Signalling is essential in connection-oriented networks (used for connection control), but datagram network typically need no signalling. No signalling mechanism exists in the IP world – it is not possible to talk to the network, one simply uses the service it provides. The signalling part of a CO network communication offers a natural point at which information about the particular requirements of a connection can be transmitted to the network. As IP is connectionless, any signalling mechanism should that is compatible with current operation of the Internet and should not constrain or change the operation of existing applications and services.

## Slide 9: Requirements for an ISN [2]
QoS service-level:
  packet handling
  traffic description
  policing
  application flow description
Service interface:
  common data structures and parameters
  signalling protocol
Admission control:
  check request can be honoured
Scheduling:
  packet classification
  prioritisation of traffic
  queue management
Notes: The simple description of the interactions between these components is as follows:
a service-level is defined (e.g. within an administrative domain or, with global scope, by the Internet community). The definition of the service-level includes all the service semantics; descriptions of how packets should be treated within the network, how the application should inject traffic into the network as well as how the service should be policed. Knowledge of the service semantics must be available within routers and within applications
an application makes a request for service invocation using the service interface and a signalling protocol. The invocation information includes specific information about the traffic characteristics required for the flow, e.g. data rate. The network will indicate if the service invocation was successful or not, and may also inform the application if there is a service violation, either by the application’s use of the service, or if there is a network failure
before the service invocation can succeed, the network must determine if it has enough resources to accept the service invocation. This is the job of admission control that uses the information in the service invocation, plus knowledge about the other service requests it is currently supporting, and determines if it can accept the new request. The admission control function will also be responsible for policing the use of the service, making sure that applications do not use more resources than they have requested. This will typically be implemented within the routers
once a service invocation has been accepted, the network must employ mechanisms that ensure that the packets within the flow receive the service that has been requested for that flow. This requires the use of scheduling mechanisms and queue management for flows within the routers
Imagine a video application. The application or user would select a service level and note the traffic characteristics required for the video flow. Information such as required data rate would be encapsulated in a data structure (service interface) that is passed to the network (signalling). The network would make an assessment of the request made by the application and consider if the requirements of the flow can be met (admission control). If they can be met routers would ensure that the flow receives the correct handling in the network (scheduling and queue management).

## Slide 10: Traffic and QoS parameters

## Slide 11: Network structure [1]
access
distribution
Network hierarchy
Access network:
  low multiplexing
  low volume of traffic
Distribution network:
  interconnectivity at local level
  medium volume of traffic
  low multiplexing
Core network – backbone:
  high volume of traffic
  high multiplexing
core
Notes: Let us first examine the problem of traffic. The network consists of several layers of hierarchy with respect to traffic volume and traffic multiplexing.
The outer layer is the access network, and can also be considered the edge of the network – closest to the users (applications) which generate the traffic. Here, there is typically a dedicated link to the end-system (for example Ethernet over UTP or residential dial-up). On these links, the level of multiplexing is low and the volume of traffic is comparatively low. If we consider a corporate network, with respect to the Internet, the site network and the corporate’s ISP is seen as the access network. For residential users, the ISP network is seen as the access network.
The access network passes on traffic to a distribution network. The distribution network may also be called a transit network. This network has the job of connecting the access network to the main core or backbone networks. Typically, end users do no transmit traffic directly onto the distribution network. The distribution network has higher levels of multiplexing and higher volumes of traffic than the access network. However, the level of multiplexing may not be much more than the access network. As an example, several ISPs may use the same transit network (to access the same backbone provider, perhaps). Distribution networks may have a scale that covers a large geographical region, may be as much as a whole country.
The core or backbone network is the part of the network that provides international/global interconnectivity. There are in fact many backbone network providers, and the have peering agreements to interconnect their networks. Here, there are very high volumes of traffic and very high levels of multiplexing – traffic from millions of users.
This diversity in the volume of traffic and its level of multiplexing has serious implications for any kind of traffic control mechanisms we may wish to apply. We have to remember that if we choose mechanisms that act on a per-packet basis to control traffic, these mechanisms must be scalable in order to maintain performance.

## Slide 12: Network structure [2]
AS1
AS3
AS2
Administrative boundaries
Autonomous system (AS):
  intra-domain routing
  internal policy
  routing metric?
  protocols: RIPv2, OSPFv2
Interconnection of ASs:
  inter-domain routing
  interconnectivity information
  protocols: BGP
border router
intra-domain routing exchanges
inter-domain routing exchanges
Notes: This is not the only way of viewing the network. The Internet was formed from the interconnection of many other networks. Today it consists of many network technologies and many network providers all using a standard set of protocols and mechanisms for internetworking. However, each network operator wishes to have control of the construction, operation, management and maintenance of their own network. Indeed the way that routing is organised for the Internet acknowledges these administrative boundaries between networks that run as autonomous systems.
Within an AS, an operator can choose to run their network how they like. They will use an intra-domain routing protocol such as RIPv2 or OSPFv2. They will have their own policy for administering the day to day operation of the network, and this policy may well be confidential. The routing metrics that they use may not make sense outside the AS boundary.
Between ASs, different routing protocols – inter-domain routing protocols - are used, such as BGP. In fact, no routing metrics are passed between ASs using BGP. rather, interconnectivity information is passed,using (effectively) discovery messages to determine connectivity paths with respect to ASs.
Given this autonomy of network operators, and the usage of diverse routing information and routing protocols, it is not realistic to agree on common routing metrics and polices for handling traffic on a global basis.

## Slide 13: Mixed traffic in the network [1]
Different applications:
  traffic (generation) profiles
  traffic timing constraints
Routers use FCFS queues:
  no knowledge of application
  no knowledge of traffic patterns
Different traffic types share same network path
Consider three different applications …
WWW
FTP
real-time audio
time
Notes: Different applications generate different kinds of traffic. The traffic has different requirements with respect to a series or flow of chunks of data; the size of data chunks that are created, the inter-chunk spacing with respect to time, and the timeliness of delivery of the chunks across the network. These different traffic types are mixed together when transmitted across the network. Remember that routers traditionally use first-come-first-served (FCFS) queuing mechanisms. That is, the packets are forwarded by the router in an order determined only by their arrival at router’s input lines, and no consideration is made about the type of traffic or the requirements of the application. Remember that datagram forwarding considers each datagram (IPv4 packet) as a separate entity and there is no notion of a flow of packets in IPv4. This means that where an application does have a flow of packets, they will not be treated in any special way by the network. We will have a look at some simple (fictional) example applications to demonstrate what happens when the traffic traverses a network.
Firstly, consider a real-time audio application. This may produce a stream of evenly spaced packets, each of which represents, say, a 40ms time slice of audio. The spacing of the audio packets should be maintained at the receiver so that the playout of the audio stream is not “jerky”. Also, we would prefer packets not to be reordered or lost. The whole of the IP packet may be no more than about 100bytes in size.
Secondly, let us consider a large file transfer. This will typically create large packets, up to the size of the path MTU (e.g. 1500bytes),in order to make most efficient use of the available network capacity. The packets will be generated as a steady stream by the sender of the file. Although loss of packets could be a problem to the application, reordering and disruption of the packet spacing will not have nay adverse affects to the application.
Thirdly, let us consider someone browsing the web. The traffic generated by the server will depend on the actions of the users of the clients (browsers). There may be relatively large silent periods (no transmissions) while the user is reading a page and the bursts of activities during browsing and download of pages from server to client. The chunks of data are of very variable size, from a few 10’s of bytes to several hundred bytes.
A representation of the traffic profiles of these three types of applications is given above. We see that, pictorially, they look very different. Let use consider what happens as these flows pass along parts of the same network path.

## Slide 14: Mixed traffic in the network [2]
Router:
  3 input lines: serviced round-robin at router
  1 output line (1 output buffer)
5
4
3
1
3
4
5
1
1
1
1
1
2
2
2
2
2
2
Notes: Let us examine the processing of our example flows in a very simple router. Let us assume that these three flows arrive at the router on three separate interfaces and will all be forwarded by the route onto the same outgoing link. We assume that the router performs a very simple round-robin servicing of the input queues, taking on packet from each input queue and sending it to the output. We can see how the traffic patterns of our flows are disrupted when the flows are aggregated. This picture may be slightly misleading in that we do not show the relative speeds of the incoming lines and outgoing lines, but if we assume that they all run at the same speed, we see that there disruption to the traffic flow.

## Slide 15: Mixed traffic in the network [3]
Different traffic patterns:
  different applications
  many uses of an application
  different requirements
Traffic aggregation:
  core: higher aggregation
  many different sources
  hard to model
Routing/forwarding:
  destination-based
  single metric for all traffic
  queuing effects
Large packet size:
  good for general data
  “router friendly”
  “slows” real-time traffic
Small packet size:
  good for real-time data
  less end-to-end delay
  better tolerance to loss
  (less jitter?)
  less efficient (overhead)
  “not router-friendly”
Notes: The mix of traffic is inevitable. There are many different types of applications, all with different requirements for how they might like their packets to be treated within the network. Indeed, a single application may be used differently by different users, so different instances of the same application may produce different traffic flows.
As traffic moves towards the core of the network, there is much higher multiplexing and so a much higher mix and aggregation of traffic. The huge number of sources and the extremely varied patterns of traffic, not only due to the sources but also due to the accumulated queuing effects due to upstream routers, makes it very hard to model traffic on the Internet. (See [PF97] and [WP98].) Remember in the traditional IP-based network, all traffic is treated in the same way, destination-based forwarding, all packets for the same destination pretty much sharing the same forwarding path and all routing information using a single metric.
One thing that does seem evident from the previous slide is that the differences in packet size of the different traffic types play an important role in how mixing of traffic affects individual flows. Large packets are efficient for non-real-time applications. For example, file transfer applications are happy with larger packet sizes, e.g. 1500bytes. However, large packets add delay to smaller packets from other sources (such as real-time audio flows) that they share queues with inside the network.
Smaller packets are much more suited to real-time applications, e.g. a real-time audio application may generate a packet that is of size 100bytes or less. This means that the the packet should have smaller transmission delay and so that flow as a whole has a smaller end-to-end delay. Also, losing a small packet – a small amount of data – is generally better than losing a large packet for a real-time application.
Also recall that the main “cost” of forwarding within an IP-based network is the per-packet cost of making a forwarding decision and then queuing a packet to the output at each router hop, so large packets that transfer lots of data per packet can, in this context, be considered more “router-friendly” than many small packets.

## Slide 16: Delay [1]
End-to-end delay
Propagation:
  speed-of-light
Transmission:
  data rate
Network elements:
  buffering (queuing)
  processing
End-system processing:
  application specific
Delay bounds?
Internet paths:
  “unknown” paths
  dynamic routing
Other traffic:
  traffic patterns
  localised traffic
  “time-of-day” effects
Deterministic delay:
  impractical but not impossible
Notes: On factor of great importance to interactive applications is end-to-end delay. This is certainly true for real-time applications using voice or video streams. Across a network such as the Internet, the end-to-end delay is made up of many components.
propagation delay: this is also called “speed-of-light” delay, and is a physical constraint that is linked to the propagation of a physical signal. In general, the speed of light, c, is taken to be approximately 3.0108m/s, and this is often used in calculations. However, it should be noted that in copper the propagation speed of an electrical signal is nearer 2.5108m/s, whilst in fibre the propagation speed of an optical signal is nearer 2.0108m/s.
transmission delay: this is the delay in getting bits onto the wire due to the speed of the link. Do not confuse this with propagation delay. A 1000byte packet is transmitted “faster” on a 10Mb/s line than on a 64Kb/s link, i.e. the bits are placed onto the wire quicker, but the electrical signal is subject to the same propagation delay in both cases.
network element processing delay: a packet arriving at a network element may be queued a an input buffer, then it will be read and processed (e.g. forwarding decisions made at routers), and finally queued to an output buffer while it waits to be transmitted.
end-system delay: delay may be introduced at the sender or receiver for various reasons. The input may not be processed immediately or transmitted immediately at the sender, for example due to end-system load. At the receiver, delay may be introduced in order to compensate for network affects, e.g. the use of de-jitter buffers in real-time audio tools.
The end-to-end path that traffic follows across the Internet is never fixed for any application. In general, the application neither knows or cares about the actual end-to-end path. Changes to the the path occur due to the dynamic nature of the IP routing protocols, and do not forget that paths may not be symmetric delay may be asymmetric. Traffic patterns may be observed to have effects that are localised, e.g. localised congestion, as well as “time-of-day” effects.
(See [PF97a] and [PF97b] for a discussion of observed effects of routing and packet dynamics.)

## Slide 17: Delay [2] #picture#

## Slide 18: Jitter (delay jitter) [1]
End-to-end jitter
Variation in delay:
  per-packet delay changes
Effects at receiver:
  variable packet arrival rate
  variable data rate for flow
Non-real-time:
  no problem
Real-time:
  need jitter compensation
Causes of jitter
Media access (LAN)
FIFO queuing:
  no notion of a flow
  (non-FIFO queuing)
Traffic aggregation:
  different applications
Load on routers:
  busy routers
  localised load/congestion
Routing:
  dynamic path changes
Notes: Jitter is the delay variation observed at the receiver. Packets do not arrive with constant delay so the timing of packet generation at the sender is perturbed and timing needs to be re-constructed at the receiver – this is called synchronisation. The effects at the receiver are application dependent, but what is visible is a variable packet arrival rate, and therefore a variable data rate for the flow. This is not suitable for application such as audio which produce flows that may have a constant data rate. For non-real-time applications, jitter is typically not an issue. For real-time applications, jitter compensation needs to be applied at the receiver.
Jitter is caused by a number of factors. At the sender, use of LAN technology like Ethernet may lead to packet transmissions being unevenly spaced. In routers, the use of FIFO queuing and traffic aggregation may lead to packet spacing being perturbed. Some routers may also use non-FIFO techniques, perhaps prioritising certain traffic (e.g. policy-based, using source address), and so disrupting the normal spacing of other flows. Traffic aggregation, with many different size packets sharing the same buffers/output-link may also cause jitter.
As router load increases, buffers/queues in routers may start to fill up, adding queuing delay. Very busy routers may lead to (localised) congestion, and this may lead to further delay. Where congestion or router failure leads to dynamic routing changes, packets may find themselves traversing different network paths between the same source and destination. This causes delay variation. Congestion in the network can lead to routing instability, and route flapping – dynamic changes routes from A  B  A – may occur.

## Slide 19: Jitter (delay jitter) [2] #picture#

## Slide 20: Loss [1]
End-to-end loss
Non-real-time:
  re-transmission, e.g.: TCP
Real-time:
  forward error correction and redundant encoding
  media specific “fill-in” at receiver
Adaptive applications:
  adjust flow construction
Causes of loss
Packet-drop at routers:
  congestion
Traffic violations:
  mis-behaving sources
  source synchronisation
Excessive load due to:
  failure in another part of the network
  abnormal traffic patterns, e.g. “new download”
Packet re-ordering may be seen as loss
Notes: Loss generally occurs because of congestion somewhere in the network. Congestion at an individual router occurs when it does not have enough resources to deal with the number if incoming packets and so has to discard packets. For non-real-time applications, loss is normally not a problem. For example, applications using TCP rely on TCP’s re-transmission mechanisms and congestion control to ensure that data does get through. However, retransmission schemes are generally unsuitable for real-time traffic, and receiver-side mechanisms (such as forward error correction, redundant encoding and “fill-in” schemes) are used (more about this in Z11).
Loss is caused by packet drop ate routers, Router do not have enough input-buffer space or output-buffer space to deal with the number of packets they have received and some must discard some packets. Such congestion can occur at at traffic aggregation points (perhaps due to insufficient provisioning) or at the ingress to “busy” network/server sites. Traffic violations from sources may cause congestion, if traffic ingress is not policed. In some cases, even with well behaving, policed sources, there may still be congestion if many sources go to “peak” load at the same time – source synchronisation.
Excessive load at a point in the network maybe due to under-provisioning, traffic being re-routed because of a failure elsewhere in the network or sometimes due to abnormal traffic patterns, for example due to many people downloading the latest piece of software from a popular server.
Another important effect to note is that, as viewed from the receiver, certain modes of packet re-ordering may seem like loss to the user. For example, consider an application that is waiting to receive packets A, B and C. A and C arrive, and B has not been lost but just re-ordered and will arrive shortly. However, the application can not wait and so perhaps will “fill-in” or correct fro the absence of B in an application-specific manner.

## Slide 21: Loss [2] #picture#

## Slide 22: Data rate [1]
End-to-end data rate
Short-term changes:
  during the life-time of a flow, seconds
Long-term changes:
  during the course of a day, hours
Protocol behaviour:
  e.g. TCP congestion control (and flow control)
Data-rate changes
Network path:
  different connectivity
Routing:
  dynamic routing
Congestion:
  network load – loss
  correlation with loss and/or delay?
Traffic aggregation:
  other users
  (time of day)
Notes: The end-to-end data rate across the Internet varies tremendously. Changes are observable at just about every timescale, from second to hours. There are absolutely no guarantees with respect to data rate, and fluctuations can occur at any time. These fluctuations are typically as the result of the complex interaction of network elements and traffic. At the application-level they may also be seen due to the action of transport protocols (or application-specific control), for example TCP congestion control. (note that in TCP, although flow control also affects the end-to-end data rate, this is due to the action of the receiver and not the network, so we do not consider it here.)
Data rate changes are due to similar reasons as for delay and loss: network connectivity, dynamic changes in routing resulting in a change of the end-to-end path, changes network traffic leading to generally higher network load and congestion. The change in value of the end-to-end data rate may often be closely correlated with the changes in end-to-end delay and/or observed loss, but this is not a general rule.
Data rate changes can be highly visible as time-of-day effects due the the network usage of other users. For example, from the UK try browsing a WWW server on the west coast of the US early on a Sunday morning and you should see a good data rate. Try the same server again at 3.00pm on a Monday afternoon and you will notice a huge difference in the end-to-end data rate.

## Slide 23: Data rate [2] #picture#

## Slide 24: Network probing: a quick note
Can use probes to detect:
  delay
  jitter
  loss
  data rate
Use of network probes:
  ping
  traceroute
  pathchar
Probes load the network, i.e the affect the system being measured
Measurement is tricky!
See:
  www.caida.org
  www.nlanr.net
Notes: It is possible to using probe techniques to determine the value of certain parameters on an end-to-end path. Probing techniques work by an application generating, transmitting and receiving specially formatted packets, e.g. ICMP packets as used by ping, traceroute and pathchar. These specially formatted packets are sometimes called probes. They travel along the network path and the application can determine the values of certain parameters by looking the the response to the probe from the network. Note that in order to do this, the application is actually loading the network – it introduces additional traffic onto the network – in order to determine what is happening. Measuring performance and QoS in IP-based networks and on the Internet as a whole is stil a research issue. Many other tools and techniques are available, and you can find information about some of them at:
Cooperative Association for Internet Data Analysis: http://www.caida.org/
National Laboratory for Applied Network Research: http://www.nlanr.net/

## Slide 25: Elastic applications
Elastic
Interactive
e.g. Telnet, X-windows
Interactive bulk
e.g. FTP, HTTP
Asynchronous
e.g. E-mail, voice-mail
Notes: Elastic applications are those applications that can tolerate relatively large delay variance – essentially the traditional data applications. They work best with low delays but they do not become unusable when delays increase or vary somewhat. Throughput may or may not be an issue. The basic requirement for these applications generally is that that they receive a reliable, ordered end-to-end data delivery service.
Interactive applications require near real-time, human interaction and ideally would like to have delays of 200ms or less, but could possibly tolerate slightly more.
Interactive bulk applications will also have similar requirements for delay, but they may also have high throughput requirements. Generally, the user is willing to tolerate a delay that is roughly proportional to the volume of data being transferred.
Asynchronous applications may or may not involve bulk data (e.g. e-mail), but they are prepared to tolerate much greater delay as they are generally store-and-forward type applications and the user does not expect anything close to real-time interaction.

## Slide 26: Examples of elastic applications
E-mail:
  asynchronous
  message is not real-time
  delivery in several minutes is acceptable
File transfer:
  interactive service
  require “quick” transfer
  “slow” transfer acceptable
Network file service:
  interactive service
  similar to file transfer
  fast response required
  (usually over LAN)
WWW:
  interactive
  file access mechanism(!)
  fast response required
  QoS sensitive content on WWW pages
Notes: Examples of “traditional” datacomms services are e-mail, file transfer, network file services and WWW.
E-mail is the least demanding of these services in terms of timeliness and interaction. E-mail messages can be read and prepared off-line (without a network connection). The network connection is required only when sending or receiving messages. When sending messages, it is sufficient that the e-mail service manages to delver your mail “sometime soon”. Typically this is the order of several minutes (or less). However, in many cases, even a delivery time of several hours is sufficient. Asynchronous means (literally) that there is no synchronisation between the sender and receiver of an e-mail message.
With file transfer, what is required is that you can retrieve or send files to a remote server. Generally, the user must somehow interact with the server so some timeliness of response to commands is required. When a file is transferred, the user would like to have the transfer take place “as quickly as possible” but the user’s value in use of the service is not severely depreciated if the transfer happens to be slightly “slower”.
Network file service can be though of as an enhanced version of file transfer. Here, files that are on a remote server are manipulated as if they were local to the end-system at the which the user is physically situated. Of course, a fast response to commands and fast file transfer are vital to this service. This is typically not a problem as network file services are normally run within an office environment where there is a high data rate available. Again, “slower” transfers may be acceptable but the service would still perform a useful function.
The WWW is essentially an interactive, non-real-time service. Web pages are documents that can be access from a remote server. In some ways, there are elements similar to file transfer and network file service here. However, the interaction is very important here – web pages should appear quickly and hyperlinks that are selected (“clicked”) should be responded to quickly also. Web pages often now contain links to other content such as streaming audio and video. This is not really interactive but may have fairly strict requirements with respect to QoS (e.g. loss, available data rates, etc.).

## Slide 27: Inelastic applications
Inelastic
(real-time)
Tolerant
In-tolerant
Rate Adaptive
Non-adaptive
Adaptive
Non-adaptive
Delay adaptive
Rate Adaptive
traditional
real-time
applications
newer
real-time
applications
Notes: Inelastic applications are comparatively intolerant to delay, delay variance, throughput variance and errors. If QoS is not sufficiently well controlled, the applications become unusable.
Tolerant applications can be adaptive or non-adaptive. Tolerant adaptive applications may be able to:
adapt to delay variation: a voice application might adapt to a decrease in the average delay by dropping a few packets to allow the transmitter to catch up with the receiver.
adapt to data rate variation: a video application may be able to adjust the encoding and trade quality against throughput.
Tolerant non-adaptive applications cannot adapt – but can still tolerate – some QoS variation. A voice application may still be usable with a measure of packet loss.
Intolerant applications cannot tolerate QoS variation – for example real-time control of a robot arm. Some may be rate-adaptive being able to adjust to detected changes in throughput, but others are totally non-adaptive.

## Slide 28: Examples of inelastic applications
Streaming voice:
  not interactive
  end-to-end delay not important
  end-to-end jitter not important
  data rate and loss very important
Real-time voice:
  person-to-person
  interactive
Important to control:
  end-to-end delay
  end-to-end jitter
  end-to-end loss
  end-to-end data rate
Notes: Inelastic applications are generally those that involve some sort of QoS sensitive media, such as voice.
If we have a look first at non-real-time voice, e.g. streaming audio. Here, large end-to-end delay and delay variation – jitter – does not matter greatly as the media flow is not interactive. There are well-known mechanisms that can adjust for jitter at the application-level. What is important is that a certain data rate is maintained that there is relatively low packet loss.
For real-time audio, e.g. person-to-person, the data rate and packet loss remain important but the end-to-end delay and end-to-end jitter are now quite important. There should be a constant and flowing dialogue in order for human voice interaction to work. If the delay is large (e.g. over half a second), conversation becomes difficult. (You may have experienced this sometimes on very-long distance phone calls, e.g. to Asia or Australasia from the UK.)
In fact, there are similar requirements for streaming and real-time video, respectively, as the are for streaming and real-time voice. However, humans tend to be much less tolerant to packet loss and variations in data rate in video traffic than in voice traffic.
Notice also that the requirements for real-time voice and video are different from those of streaming voice/video. For real-time voice and video, we assume that the media streams are being created in real-time and are being used in an interactive manner, e.g. a conversation. Applications that are providing conversational services have more stringent QoS constraints than applications that are processing streaming media (e.g. voice/video playback). The latter can cope (to some extent) with variations in data rate, packet loss rates and delay.

## Slide 29: QoS parameters for the Internet [1]
Delay
Not possible to request maximum delay value
No control over end-to-end network path
Possible to find actual values for:
  maximum end-to-end delay, DMAX
  minimum end-to-end delay, DMIN
Jitter
Not possible to request end-to-end jitter value
Approximate maximum jitter:
  DMAX – DMIN
  evaluate DMIN dynamically
  DMAX? 99th percentile?
Jitter value:
  transport-level info
  application-level info
Notes: In general, requests for particular delay and jitter constraints by an application are not parameters that can be honoured across the Internet. That is not to say they could not be honoured by an IP-based network, e.g. it might be possible to arrange for such mechanisms in an IP-based corporate VPN. As we have noted, there are many autonomous systems that are linked together to form the Internet and it is not possible implement a homogenous environment across them. So, typically, it may be possible for an application to request “low delay” and “low jitter” and it may be possible for the network to give an indication of what the delay/jitter is along a particular network path, e.g. a value for maximum end-to-end delay can be found with the use of RSVP/INTSERV as we will see later.
So, it may be possible to find the maximum possible delay bound by querying network elements along a certain end-to-end path, and it should be possible to evaluate current (and mean) delay by using network probes (a “ping”-type of scheme). However, jitter is very much harder to evaluate. This, once again, is because the end-to-end path may consist of concatenation of various network technologies and routers with different behaviour. However, with an upper bound for the delay, DMAX, and a lower bound for delay, DMIN, it could be argued that a reasonable estimate for the jitter is DMAX – DMIN. DMIN can be evaluated dynamically during the operation of the flow, perhaps from application-level header information or from protocol headers as in RTP/RTCP (we look at RTP/RTCP later).
DMAX may also be evaluated dynamically, form the same measurements used to determine DMIN, however, it may be that such an estimate for DMAX results in an estimate that is too conservative. Other summaries may be used, e.g. the 99th percentile for the measured delay values. Evaluations of both DMIN and DMAX are likely to be application specific.

## Slide 30: QoS parameters for the Internet [2]
Loss
Not really a QoS parameter for IP networks
How does router honour request?
Linked to data rate:
  hard guarantee?
  probabilistic?
  best effort?
(Traffic management and congestion control)
Packet size
Restriction: path MTU
May be used by routers:
  buffer allocation
  delay evaluation
Notes: It should be possible to specify loss characteristics as QoS parameters. However, it may not be practical to ask for a particular numerical value for loss, e.g. asking for 10-4 packet loss rate. Note that packet loss decreases the end-to-end data rate. So, specification of loss may be linked to the specification of how a data rate quest if honoured. For example, one could ask for a data rate to be guaranteed (no loss), have “low” loss (low probability of packet loss) or best effort. One reason for not using loss rates is that monitoring per-flow loss rates is taken to be a computationally expensive exercise for routers to perform in practise. So, in IP-based networks such as the Internet, packet loss rate is not usually specified numerically. (In ATM networks, or Frame Relay networks, numerical values for cell loss rates and frame loss rates may be specified, respectively.)
Although packet size may not be considered specifically as a QoS parameter, the maximum (and perhaps the minimum) packet size that an application will generate may be specified. Of course the maximum packet size will be restricted by the path MTU, and real-time applications generally do not exceed the path MTU as IP-packet fragmentation is normally considered harmful for real-time applications. Routers may find the specification of maximum and minimum packet size useful, e.g. for the Guaranteed Service in INTSERV as we will see later.

## Slide 31: QoS parameters for the Internet [3]
Data rate:
  how to specify?
Data applications are bursty:
Specify mean data rate?
  peak traffic?
Specify peak data rate?
  waste resources?
Real-time flows:
  may be constant bit rate
  can be variable bit rate
Application-level flow:
  application data unit (ADU)
Data rate specification:
  application-friendly
  technology neutral
Notes: For many IP-based application, the most precious resource is data rate. So, specification of data rate as a QoS parameter is essential. However, how is data rate to be specified? remember that traditional data applications may produce a very varied traffic profile. Also, while we have generally considered real-time applications as producing constant bit-rate flows, more sophisticated audio and video coding techniques produce variable bit rates. So do we specify mean rates, and then lose data when there are peaks above the mean? Or do we specify peak rates, and then make inefficient use of the network resources when we operate below the peak rate?
As you will see in Z11, multimedia applications generate a lump of data that can be considered as an application data unit (ADU). We need to have a specification mechanism can reflect the way that the application may generate data. It should also be something that is technology neutral, as IP itself is. That is, the specification should not rely on any particular mechanisms or functions in levels 1 (physical) and 2 (data link).

## Slide 32: Leaky bucket
Two parameters:
  B: bucket size [Bytes]
  L: leak rate [B/s or b/s]
Data pours into the bucket and is leaked out
B/L is maximum latency at transmission
Traffic always constrained to rate L
data
B
rate, L
Notes: A traffic control mechanism used by ATM is leaky bucket. Here, there is a fixed data rate, effectively the peak rate of transmission, which is L. However, to cope with bursts of data, a bucket size, B, is also defined. The model is that data arrives in the bucket and is drained from the bucket at the rate L. Bursts of traffic that result in an overflow of the bucket are discarded.
Note that the bucket may be filled in ADU sized lumps, so it is probably sensible to arrange for the B to be a a multiple of the transmitted ADU size. The maximum latency introduced by the bucket is B/L. Note that the traffic is always constrained to rate L by the leaky bucket, even if greater capacity is available, i.e. a higher peak rate may be possible at a given time. Leaky bucket is used in ATM, where B and L be specified in units of cells and cells per second, respectively.

## Slide 33: Token bucket
Token bucket
Three parameters:
  b: bucket size [B]
  r: bucket rate [B/s or b/s]
  p: peak rate [B/s or b/s]
Bucket fills with tokens at rate r, starts full
Presence of tokens allow data transmission
Burst allowed at rate p
data sent < rt + b
data
tokens, rate r
b
peak rate, p
Notes: There is a subtle, and very important, difference between a leaky bucket and a token bucket. The token bucket also has a bucket size, b, and a bucket rate, r, but it allows traffic bursts to be transmitted at peak rate, p, under certain conditions. In this case, the bucket does not “fill with data” as it does in the leaky bucket, but it fills with tokens, that that allow data to be transmitted. Data can only be transmitted when there are enough token to allow transmission to take place. Transmission can then take place at a peak rate of p. Nominally, data is transmitted at a rate r, the same rate at which the bucket is filled with tokens. However, it can be seen that bursts of traffic, up to the bucket size, can be transmitted at the peak rate, p.

## Slide 34: Real-time media flows

## Slide 35: Interactive, real-time media flows
Audio/video flows:
  streaming audio/video
  use buffering at receiver
Interactive real-time:
  only limited receiver buffering
  delay <200ms
  jitter <200ms
  keep loss low
Effects of loss:
  depend on application, media, and user
Audio:
  humans tolerant of “bad” audio for speech
  humans like “good” audio for entertainment
Video:
  humans tolerant of “low” quality video for business
  humans like “high” quality video for entertainment
Audio – video sync:
  separate flows?
Notes: People often think of real-time flows as “audio and video”. We must make a distinction between streamed audio and video flows and real-time, interactive audio and video flows. For streamed audio and video, while low delay, low jitter, low loss and high data rate are desirable for playback of the flow, under normal circumstances, only the latter (data rate) is significantly important that it might be considered a QoS issue. We do require large amounts of capacity to transmit high quality streamed audio and video. However, end-to-end delay is not an issue, even if this may be in the order of a few seconds but for one –way transmission - playback - it should not matter. Jitter and loss can be compensated having a large buffer at the receiver for delaying playback at the receiver to allow time for smoothing unevenly spaced packet arrival as well as dealing with re-transmissions of lost data as required. This scenario may be complicated in a multicast scenario (reliable multicast is a tricky issue as we will see later). (More information about dealing with audio and video in Z11.)
Real-time audio and video normally involves humans as the subjects of audio/video flows. Humans use applications that generate audio and video flows to interact across a network. Small “timeslices” of audio/video are placed into packets and then sent across a network. Generally, for human interaction to continue in a “conversational” manner, delay and jitter must be kept to around 200ms each, i.e. the maximum end delay should be no more than around 400ms. The rules for loss are less easy to specify so easily, as loss effects tend to be application-specific, media-specific and user-specific. For example, let us consider a fictitious video-telephone (VT) application being used by a human on a laptop machine, ad the user is travelling away from home. That user may find it appropriate to use only low quality audio when talking to someone back at the office to check on deliveries, then use high quality audio (and perhaps some video) when giving a report to his/her boss, and use high quality and use high quality video and audio when talking to his family. Also, hu,mans are generally tolerant of low quality audio and video for “normal” (business or domestic) usage, but for entertainment, they generally want high quality audio and video. Some other applications, e.g. medical applications, may require high quality audio and video at all times.
Also, if audio and video flows are transmitted separately, then the receiver may need to re-synchronise the flows for playback. (More about this in Z11.)

## Slide 36: Audio
QoS requirements
Delay < 400ms:
  including jitter
Low loss preferable:
  loss tolerant encodings exist
Data rates:
  speech  64Kb/s
  “good” music  128Kb/s
Time domain sampling
Example – packet voice:
  64Kb/s PCM encoding
  8-bit samples
  8000 samples per second
  40ms time slices of audio
  320 bytes audio per packet
  48 bytes overhead (20 bytes IP header) (8 bytes UDP header) (20 bytes RTP header)
  73.6Kb/s
Notes: We discuss briefly the QoS requirements for real-time audio. You will receive more information in Z11.
For audio, we normally require that delay is less than 400ms end-to-end for any packet, and this includes any jitter. It is preferable to have low loss, but there are mechanisms to compensate for loss, either by use of special audio encoding techniques, or by “fill-in” techniques at the receiver. Telephone quality speech is achievable in audio encodings of 64Kb/s or less. Reasonable quality music (for entertainment) may require at least twice this rate.
Audio is taken to be a single dimensioned variable, and is normally sampled in the time domain.
When it is transmitted as packet voice over IP, a typical dat rate required for the application may be approximately 74Kb/s.

## Slide 37: Example audio encoding techniques
G.711
PCM (non-linear)
4KHz bandwidth
64Kb/s
G.722
SB-ADPCM
48/56/64Kb/s
4-8KHz bandwidth
G.728
LD-CELP
4KHz bandwidth
16Kb/s
G.729
CS-ACELP
4KHz bandwidth
8Kb/s
G.723.1
MP-MLQ
5.3/6.3Kb/s
4KHz bandwidth
GSM
RPE/LTP
4KHz
13Kb/s
Notes: LD-CELP: low delay code excited linear prediction
CS-ACELP: conjugate structure algebraic excited linear prediction
ML-MLQ: multi-pulse maximum likelihood quantisation
PCM: pulse code modulation
RPE/LTP: residual pulse excitation/long term prediction
SB-ADPCM: sub-band adaptive differential pulse code modulation

## Slide 38: Video
QoS requirements
Delay < 400ms:
  including jitter
  same as audio
  inter-flow sync
Loss must be low
Data rate – depends on:
  frame size
  colour depth
  frame rate
  encoding
Frequency domain:
  discrete cosine transform (DCT)
Example - packet video:
  ###
Notes: We discuss briefly the QoS requirements for video. You will receive more information in Z11.
Loss and delay on video has a much more significant affect than on audio, especially if there is significant compression. Remember that compression removes redundancy, the very thing that we need for robustness in the face of loss. Typically, a whole screen of data may not fit into a single packet and so multiple packets may be required to make up a single frame of video. This means that it is possible for part of a picture to go missing. However, burst errors (loss of several packets close in sequence) may mean that several parts of the same picture could go missing.

## Slide 39: Example video encoding techniques
MPEG1
upto 1.5Mb/s
MPEG2
upto 10Mb/s (HDTV quality)
MPEG4
5-64Kb/s (mobile, PSTN)
2Mb/s (TV quality)
MPEG7, MPEG21
H.261 and H.263
n  64Kb/s, 1 n  30
Notes: MPEG moving pictures expert group
Commonly used picture sizes are given below.
Picture format Image size
sub-QCIF 128x96
QCIF 176x144
CIF 352x288
4CIF 702x576 (full screen)
16CIF 1408x1152
CIF common intermediate format
QCIF quarter CIF

## Slide 40: Summary
IPv4 and current Internet:
  not designed for QoS support
Need to add support for ISN:
  service definitions
  signalling
  update routers
Need to describe traffic:
  QoS parameters
Audio and video have different requirements

## Slide 41: Routing for Integrated Services

## Slide 42: New routing requirements
Multiparty communication:
  conferencing (audio, video, whiteboard)
  remote teaching
  multi-user games
  networked entertainment – “live broadcasts”
  (distributed simulations)
  (software distribution)
  (news distribution)
Support for QoS in routing
Notes: As we have already discussed, there are a whole new range of applications that will support Integrated Services – one network all services. However, in order for Integrated Services to be possible on an IP-based network we need additional support – things that were not specified in the original IPv4 specification.
One aspect of communication that is increasing rapidly is that of multiparty communication. This is the ability to have a communication session that is not just one-to-one, but perhaps one-to-many or many-to-many. Such application including multimedia conferencing, remote teaching and multi-user games. These may demanding have QoS requirements as well as the requirement for many-to-many communication. (Other multi-party communication applications distributed simulation, software distribution and news distribution whose main requirement may be reliable multiparty communication.)
Let us also consider the current mechanisms for routing and forwarding. These are built around the use of destination addresses for building routing tables, and not other constraints are applied. Traditionally, there is only one route between a source and destination. However, what if we would like to perform routing specifying QoS criteria, allowing alternative route selection based on, for example, the requirement for low-end-to-end delay and loss? Traditionally, the use of such QoS constraints are not used generally in constructing routing information.

## Slide 43: Questions
How can we support multiparty communication?
How can we provide QoS support in routing?
Notes: So we would like to answer two questions in this section:
How can we support many-to-many communication? This is not a simple case of having O(N2) point-to-point unicast connections for our N end-points. Such a nave solution is not practical – it will not scale.
Also, how can we provide QoS-based decision making for constructing and selecting routes? Again, this is not a simple case of adding extra information about QoS parameters to routing updates as we must consider carefully the implications for the operation of the routing algorithms and protocols, especially the intra-domain and inter-domain interactions.

## Slide 44: Many-to-many communication: IP multicast

## Slide 45: Group communication using IP
Many-to-many:
  many senders and receivers
  host group or multicast group
One transmission, many receivers
Optimise transmissions:
  e.g. reduce duplication
Class D IP address:
  224.0.0.0 - 239.255.255.255
  not a single host interface
  some addresses reserved
Applications:
  conferencing
  software update/distribution
  news distribution
  mutli-player games
  distributed simulations
Network support:
  LAN
  WAN (Internet routers)
  scoped transmission: IP TTL header field
Notes: Multicast can be defined, loosely, as the ability to logically connect a group of hosts in a network in order that they perform many-to-many communication. This group of hosts is called a multicast group or a host group. In a an IP network, multicast is the process whereby a source host or protocol entity sends a packet to multiple destinations simultaneously using a single ‘transit’ operation which implies that the packet transit only takes place once from sender to all destinations in the group rather than once for each destination. The connectionless nature of packet switched network means that the packet sender is not necessarily in the multicast group. A packet switched network is said to provide a multicast service if it can deliver a packet to a set of destinations (a multicast group), rather than to just a single destination. Basically, a multicast service can offer many benefits to network applications in terms of reducing the transmission overhead on the sender, reducing the overhead on the network and time taken for all destinations to receive all the information when an application must send the same information to more than one destinations. The key to efficient multicast is to optimise the duplication of the transmitted data in some sense. Normally, this means keeping the duplication of the transmitted information to a minimum.
IP multicast uses Class D IP addresses in the range 224.0.0.0 – l 239.255.255.255. These addresses do not identify a single host interface as unicast IP addresses do, but a group of hosts that may be widely, geographically dispersed. This means that special routing procedures are required in the wide-area to enable multicast connectivity. Some of these are reserved, e.g. 224.0.0.1 is the “all systems” address which all hosts must listen to. To contain the scope of IP multicast packets, the TTL field in the IP header is used to limit the maximum number router hops that a multicast packet can traverse before it should be silently discarded.
Multicast has many benefits over unicast communication in certain areas, e.g. conferencing, software distribution/updates and news distribution. To enable multicast communication, support is needed in the end-systems (hosts and LANs) as well as in the wide-area Internet.

## Slide 46: IP multicast and IGMP
Features of IP multicast:
  group of hosts
  Class D address
  leaf nodes (hosts) and intermediate nodes (routers)
  dynamic membership, leaf-initiated join
  non-group member can send to group
  multicast capable routers
  local delivery mechanism
IGMP: group membership control
network
A
B
C
C wishes to join group X, so sends
IGMPREPORT (after random timeout)
C has sent report with destination address X so if A and B want to become members, the do not need to send an IGMPREPORT
The multicast capable router listens in
multicast promiscuous mode so that it can
pick up all mulitcast packets for relay off the LAN if required.
periodic IGMPQUERY
from router
Notes: Here we briefly introduce the fundamentals of IP multicast:
IP multicast allows efficient simultaneous communication between hosts in a logical group called the host group or multicast group. A host/multicast group which includes a set of zero or more hosts, is identified by a single IP destination address from a specially designated address space.
The group communication path is modelled as a tree network with the hosts (senders and receivers) within the group located at the leaf nodes of the tree, and the intermediate nodes representing distribution/replication points of the communication path.
The membership of a host group is dynamic; i.e., hosts may join and leave groups at any time (leaf initiated join). This is achieved using the Internet Group Management Protocol (IGMP). There are no restrictions on the physical location or the number of members in a multicast group. A host may be a member of more than one multicast group concurrently.
A host need not be a member of a group to send packets to the multicast group.
Inter-network IP multicast is supported by multicast routing mechanisms. This means that inter-network forwarding of IP multicast packets is handled by multicast routing mechanisms residing in “multicast capable routers”. The intermediate nodes of the communication path should be multicast capable routers.
IP multicast relies on the existence of an underlying multicast delivery system to forward data from a sender to all the intended receivers within a sub-network.
IGMP is a very simple protocol with only to messages, IGMPQUERY (sent by a router to see if there are any members of a particular group) and IGMPREPORT (sent by a node to indicate it is leaving or joining a group). Each message refers to a single multicast group, i.e. a single IP multicast address. For Internet-wide connectivity every LAN must have at least one multicast router that can listen out for hosts that send group membership reports. If at least one group member exists, then the router should forward multicast packets for that group. To minimise traffic, hosts set random timers and do not send a IGMPREPORT for joining groups until a random timer has expired. IGMP messages are only used in the local area.

## Slide 47: Multicast: LAN
Need to translate to MAC address
Algorithmic resolution:
  quick, easy, distributed
MAC address format:
  IANA MAC address allocation
  last 23-bits of Class D
  not 1-1 mapping
Host filtering required at IP layer
Final Ethernet multicast address
0000 0001 0000 0000 0101 1110 0100 0000 0101 0000 0001
IANA MAC ADDRESS PREFIX
0000 0001 0000 0000 0101 1110 0--- ---- ---- ---- ----
IPv4 multicast address
224.20.5.1  1110 0000 0001 0100 0000 0101 0000 0001
Notes: Single LAN multicast is possible without the need for a multicast router. However, LANs do not understand IP addresses they understand MAC addresses. We need address resolution.
MAC multicast addresses cannot be hardwired into LAN adaptor cards in the same way as ordinary MAC addresses. They need to be configured at run-time, i.e. the host must tell its LAN adaptor which multicast MAC addresses to listen for. This must be done the first time a process on the host expresses interest in joining a particular IP multicast group. At this point, the host needs to map the IP multicast group address to a MAC multicast address which it can pass to the adaptor. The mapping must be identical in all hosts and in the router since all participants in the group must end up listening to the same MAC multicast address. This could be done through consultation with a server or, perhaps, a broadcast address resolution protocol could be devised. In fact, the decision made was that the mapping should be algorithmic.
IANA owns a block of Ethernet addresses in the range 00:00:5e:00:00:00 to 00:00:5e:ff:ff:ff and allocates the lower half of these for multicast. The Ethernet convention is that the first byte must be set to 01 to indicate a multicast address. Therefore the range we can use for multicast is 01:00:5e:00:00:00 to 01:00:5e:7f:ff:ff . This means we have 23 bits to play with. These bits are set to the low-order 23 bits of the IP multicast group address to generate the MAC address. So, the address 224.20.5.1, which is e0.14.05.01 in hex, will map to the MAC address 01:00:5e:14:05:01. This is shown in binary below. (We have shown the bit ordering in the conventional way so that 0x01 appears as 00000001. In fact the bits are inserted into the Ethernet frame fields with each byte reversed - so, for example, that the first byte goes out on the wire as 10000000.)
Now, this is obviously not a 1-1 mapping and it is possible that we end up with two IP multicast groups on a LAN mapped to the same MAC multicast address. This is unfortunate, but not disastrous. It means that a host which has joined the group with address 224.20.5.1 will also receive datagrams intended for (say) 224.148.5.1 and will have to filter these out in software. However, many LAN interface cards do not filter multicast traffic efficiently, so this software filtering will need to be present in any case.

## Slide 48: Multicast routing [1]
S
B
C
E
F
RS
RB
RC
RE
RF
RD
Starting point: flood
  creates looping
First refinement
  reverse path broadcast (RPB)
  duplication
RS
RB
RC
RE
RF
RD
Notes: IGMP allows routers to determine which multicast group addresses are of interest in the LAN. We now need a routing mechanism which ensures that all transmissions to a multicast address reaches the correct set of routers and hence the correct set of LANs. Therefore, we need an efficient dynamic multicast routing protocol. This turns out to be a hard problem to crack and is still the subject of much research. In this section we look at the problem and examine some of the protocols which have been developed to date.
The host S is transmitting to a multicast group address. Hosts B and E have joined the group and have announced the fact to RB and RE via IGMP. We need to calculate a spanning tree which interconnects the relevant routers. We can approach a solution through a series of refinements:
Starting point: Flood a multicast datagram to all neighbours except the one which sent it.
The problem with this is that we will get loops; RC will forward to RD, RD to RE and RE to RC. One way of solving this problem would be for each router to keep a list of the datagrams it has seen, check this each time it receives a datagram, and delete it if it is in the list. This is clearly not feasible for a multicast which might last several hours and involve millions of datagrams.
First refinement: Reverse Path Broadcasting
It turns out that routers already have quite a lot of the information they need in order to calculate a spanning tree simply from the operation of normal unicast routing protocols. In particular, each node will have a notion of the shortest path from itself to RS - at the very least, they will know the length of this path and the identity of the first hop on it. This is true irrespective of which unicast routing protocol they are using. We can adopt the following rule - “flood a datagram that comes from the first-hop (on the path back to the source),but delete all others”. Now, when RC forwards to RD, RD will delete the datagram because it did not arrive from its “first-hop to source” (which, for RD, is RS itself). This technique is called reverse path broadcasting (RPB).

## Slide 49: Multicast routing [2]
Second refinement
  eliminate duplicates
  need routing information
RS
RB
RC
RE
RF
RD
Distance vector:
  need next hop information
  (or use poisoned reverse)
Link state:
  construction of all SP trees for all nodes possible
  “tie-break” rules required
Notes: Second refinement: Duplicate elimination
As things stand, even with RPB, both RC and RD will forward a multicast datagram to RE. RE will delete one of these on the basis of the RPB rule. However, we have still wasted effort with a useless transmission to RE. If RC and RD knew that RE’s path to RS was via RD (say) then RC need not forward to RE. How can RC and RD learn about RE’s paths? There are two cases to consider:
1) distance-vector routing: the distance-vectors RE sends will contain distances but no indication of first-hop. One possibility is to modify the protocol to include this information. A second possibility is to make use of the poisoned reverse rule – send a hop count of “infinity” (i.e. value 16) back to the first hop on the route.
2) link state routing: link-state algorithms flood link-state information to all other nodes in the network. By this means, each node ends up with a complete picture of the state of every link in the network. In a unicast link-state algorithm, a node now proceeds to calculate a shortest path tree from itself to every other node in the network. In fact, each node has enough information to calculate shortest path trees for every node in the network. All the routers shown can calculate shortest-path trees with RS as source. If we ensure that they all perform precisely the same calculation, they will all end up with the same result. This means that the calculation algorithm has to be formally part of the protocol and needs to specify unambiguous “tie-breaking” rules to select between equal length routes. For example, there are clearly two equal-length routes from RE back to RS – we must ensure that all routers make the same choice between them. This can be done, for example, by choosing the router with the numerically higher IP address.

## Slide 50: Multicast routing [3]
Networks with no group members pruned from tree
Must somehow allow tree to re-grow
Soft-state:
  timeout – re-flood
  downstream nodes prune again
Explicit graft:
  downstream nodes join tree
Third refinement:
  pruning
  need to refresh tree – soft-state
  reverse path multicasting (RPM)
RS
RB
RC
RE
RD
a)
RS
RB
RC
RE
b)
RPM:
  used in many multicast protocols
  per-sender, per-group state
Notes: Third refinement: Pruning
By careful application of rules such as those above, it is possible for the routers to agree on a spanning-tree for the whole network. However, we are still wasting effort in forwarding datagrams to RF when it has no group members. The solution is to introduce special prune messages.
When a router such as RF receives a datagram for a multicast group which has no members on its attached LAN, it sends a prune message back to the router which forwarded the datagram. This router (RD in this case) now adjusts its routing database to remove RF from the tree. If we are in the situation of b), RD will now know it has no-one to forward to, in which case it can, itself, send a prune message to RS. With the addition of pruning, RPB becomes reverse path multicasting (RPM). We need to have a method of restoring pruned links in case a host the other side of the link joins the group. We can either let prunes time-out (at which point the flow is restored and then, maybe, pruned again) or we can add explicit graft messages to the protocol. The former mechanism is a use of soft-state which is applied extensively in Internet protocols. Anticipating that state information is perishable in this way and building in mechanisms to restore it is fundamental to the operation of the Internet. It is key concept in making the Internet robust.
By using all these refinements, we can arrive at a reasonably efficient spanning tree. The two possibilities are shown. Both of these use shortest path routes from the source router (RS) to RB and RE. On the face of it, the tree in diagram b) is more efficient since it involves one fewer transmission hop. However, this is not necessarily so since the network cloud might might be a LAN. If it is, then RS can reach RB and RC with one transmission. We may then prefer diagram b) since it shares the forwarding load between the two routers.

## Slide 51: DVMRP and the MBONE
DVMRP:
  RPM
  used on MBONE
MBONE:
  virtual overlay network
  distance vector routing
MBONE Visualisation Tools
http://www.caida.org/Tools/Manta/
http://www.caida.org/Tools/Otter/Mbone/
Notes: The Internet’s first multicast routing protocol - Distance Vector Multicast Routing Protocol (DVMRP) [RFC1075] – is a RPM protocol. It is based on RIP includes all the refinements outlined above, including the poisoned reverse trick. However, it suffers all the well-known problems of distance-vector algorithms and is regarded very much as a simple, interim solution intended to get Internet multicasting off the ground (in which it succeeded mightily). DVMRP has been used extensively in the MBONE (multicast backbone).

## Slide 52: MBONE configuration
Routers not multicast aware:
  use virtual network
Multicast islands:
  connected by virtual links
  can not use normal routing info – use multicast hops
IP tunnelling:
  software runs on a host
  ad hoc topology
Use TTL for scope:
  TTL expiry: silent discard
  administrative scope possible
G
G
G
router
to MBONE
IP-in-IP tunnel
M
M
M
M
multicast routing software
Notes: The MBONE is a multicast network that spans the Internet, but consists of multicast islands connected together. It is a virtual network that is overlaid on the existing Internet unicast infrastructure. This approach was adopted in order to get experience of multicasting at a time when very few Internet routers actually supported it. The links between the multicast routers are virtual links. In order to send multicast datagrams along these links, they must be encapsulated within an ordinary (non-multicast) IP datagram with the destination address being the IP address of the multicast router at the end of the virtual link. This is called IP-in-IP encapsulation or IP tunneling [RFC1853]. This datagram is then forwarded by the normal routers in the ordinary way. On arrival, the multicast router extracts the multicast datagram and routes it according to the multicast group address it contains – it will have to re-encapsulate it in order to send it along the next virtual link. This arrangement is necessary because most "normal" routers do not yet understand multicast group addresses. In practice, the multicast routers are usually instances of the freely available mrouted program which runs on Sun workstations. The topology of the MBONE is ad hoc. To become part of the MBONE you simply negotiate the establishment of an IP tunnel between your site and a site that is already connected to the MBONE.
Unfortunately, when operating in an overlay network like the MBONE, we cannot use normal RIP distance-vectors directly. Normal RIP distance vectors will refer to the real nodes and links and not to the multicast nodes and virtual links. Therefore, DVMRP has to send its own distance-vectors containing information related to the MBONE itself. The poisoned reverse rule (which is optional in RIP) is used. In typical Internet fashion, DVMRP uses soft-state (explicit prunes) to maintain the tree.
To control the scope of transmission (how far they are transmitted on the network), the time-to-live (TTL) in the IPv4 header is used. The TTL is set by the transmitter to indicate how many MBONE router hops this packet should “live” for. When the TTL becomes zero, the packet is subject to silent discard – no ICMP TIME EXCEEDED message is generated to avoid packet implosion to the sender. The use of administrative scope by controlling the use of multicast addresses and controlling forwarding policy at multicast routers is also possible.

## Slide 53: MOSPF
Link-state algorithm
RPM
Intended for larger networks
Soft-state:
  router advertisement sent on group join
  tree evaluated as routing update for a group arrives
Still suffers from scaling problems:
  a lot of state-required at each router
  per-group, per-link information required
Notes: A link-state based algorithm called Multicast Extensions to Open Shortest Path First (MOSPF) [RFC1584] is also available. MOSPF ends up being quite complex since it has to deal with OSPF’s concepts of Areas and Autonomous Systems. It is designed to cope with large networks, however it still has some scaling problems. In larger networks, there could be hundreds of multicast groups in existence at any time. Only a few of these will pass through any particular node. Therefore it makes no sense for each node to pre-calculate trees for every possible source and every possible group. Instead, trees are calculated on the fly when a multicast datagram is received. Like DVMRP, MOSPF uses a soft-state approach, but does not need to use flood-and-prune (as DVMRP does). This is because when a router detects a group join from a leaf node, it send a routing update to the network to let other MOSPF routers know of the new group member. However, this is also MOSPF’s short-coming: it needs to send many routing updates and holding routing information on a per-group, per-link basis, resulting in a large database of information. Also, it needs to evaluate the shortest-path algorithm for every source in the group, which is computationally expensive if there are many senders.

## Slide 54: CBT
Core router(s):
  core distribution point for group
Leaf sends IGMP request
Local router sends join request to core
Join request routed to core via normal unicast
Intermediate routers note only incoming i/f and outgoing i/f per group
Explicit join and leave:
  no pruning
  no flooding
Distribution tree may be sub-optimal
Core is bottleneck and single-point-of-failure:
  additional core maybe possible
Careful core placement required
Notes: In Core Based Trees (CBT) [RFC2201] routers are explicitly designated as core routers for the group – in the simplest case, there will be a single core router. When a host wishes to join the group, it informs its local multicast router via IGMP. This router then forwards an explicit join message towards a core router. This is contained in a perfectly ordinary unicast IP datagram and so follows a route which has been established by unicast routing protocols in the normal way. Eventually a single shared tree results; we no longer require routers to be able to calculate different trees for each source as they had to for DVMRP and MOSPF. In fact, the state information retained by the on-tree routers is little more than the identity of the parent and child routers in the tree. Intermediate routers need only to maintain information about which interface a packet came in on, and which interface it was forwarded on. This information need is per group only, so the amount of information is O(G) for multicast, as opposed to O(G.S) for DVMRP and OSPF (where G is the number of groups and S is the number of senders). Also, join and leave request in CBT are explicit, and so CBT is quite well suited to sparsely populated groups.
The disadvantages with CBT are:
that a tree may be sub-optimal and is heavily influenced by the location of the core; careful core location may be required
the core router becomes a single point of failure, though a recovery mechanism is being added

## Slide 55: PIM
PIM:
  can use any unicast routing protocol info
  two modes: dense mode and sparse mode
Dense mode:
  RPM
  flood-and-prune with explicit join
Sparse mode:
  similar to CBT
  core (rendezvous point) or shortest-path possible
  rendezvous point sends keep-alive
  explicit graft to tree
Notes: An important observation is that some groups are quite dense - heavily populated and in a relatively small geographical area. Other groups are sparse - lightly populated and spread right around the globe. For dense trees there is a lot of scope for link-sharing and it is worth exchanging state information frequently and expending computational effort to achieve this. For sparse trees there is unlikely to be much link-sharing. This has serious implications for a global Internet in which thousands of multicast groups might exist concurrently. The Protocol Independent Multicast (PIM) protocol incorporates these concepts having both dense and sparse modes - in fact it is really two protocols. PIM dense mode is a RPM algorithm. PIM sparse mode [RFC2362] uses an explicit graft mechanism to allow addition to a tree, similar to CBT.

## Slide 56: Multicast address management
Some addresses are reserved:
  224.0.0.1 all systems on this sub-net 224.0.0.2 all routers on this sub-net 224.0.0.4 all DVMRP routers (plus many others)
No central control as in unicast addresses
Others generated pseudo-randomly:
  28-bit multicast ID (last 28 bits of Class D address)
Notes: Unlike the unicast address space in which address allocation is controlled, the multicast address space is (almost) a free-for-all. Some addresses have been reserved and there are certain allocations of ranges of addresses for particular use. However, within these constraints, if a multicast addresses are chosen on an ad hoc basis. To help avoid clashes of different addresses, suggestion have been made as to how readily available information (such as time of day, IP address of the host initiating the group, etc.) might be used to produce the last 28 bits – the multicast ID – of a Class D address in a pseudo-random fashion.

## Slide 57: Multimedia conferencing [1]
Multimedia applications:
  voice - RAT
  video - VIC
  text - NTE
  whiteboard - WBD
Support:
  session directory - SDR
  gateway - UTG
All use IP multicast:
  local – direct
  wide area – MBONE
RTP/RTCP
IP multicast:
  224.2.0.0 - 224.2.255.255
  different address per application per session
Scoping:
  IP TTL header field: 16 local (site) 47 UK 63 Europe 127 world
  administrative
Notes: UCL have been heavily involved with networked multimedia, especially multimedia conferencing. The standards for such applications are still developing. Example applications can be found at:
http://www-mice.cs.ucl.ac.uk/multimedia/
which include an audio tool (RAT), a video tool (VIC), a text editor (NTE) and a whiteboard (WBD). All these applications can run as standalone applications or can be run together within an integrated user interface. All are designed to operate over IP multicast for group communication (on a single LAN or across the MBONE), but unicast (one-to-one) communication is possible. Two additional support applications are a session directory (SDR) for a allowing advertisements multicast sessions on the MBONE and a transcoding gateway (UTG) for supporting dial-up users and allowing receiver heterogeneity.
All the applications use RTP and RTCP.
When used on the MBONE, the IP multicast addresses used are in the range 224.2.0.0 - 224.2.255.255. These have been designated by IANA for MBONE use by conferencing applications. Each application uses a different multicast address for each multicast session.
To restrict the extent of the transmission of the multicast traffic - its scope - the TTL field of the IPv4 header is used. This currently the most common mechanism used as it is simple to implement but there is a move to adopt a more administratively controlled approach, based on the actual values of multicast addresses being used.
A multicast conference may consist of the use of one or more of the user applications. The support applications may be required for configuration (SDR) and supporting LAN users (UTG).

## Slide 58: Multimedia conferencing [2]
Two multicast channels per application per session:
  RTCP and RTCP
Stand-alone - ad hoc:
  individual applications
Advertised conference:
  SDR
  configuration information
multicast-capable
routers
MBONE (Internet)
Notes: Each application establishes a multicast session. This consists of two logical channels for multicast traffic, one for RTP traffic (the application data) and one for RTCP traffic (signalling and control). These two channels share the same multicast address but have different port numbers. The convention is that a multicast address, D, and an even port number greater than 5000, K, is chosen by the application user. The session then consists of two channels at D/K for the RTP traffic and D/(K+1) for the RTCP traffic.
This configuration is true whether or not the multicast session is to be local or to be sent across the MBONE. If the MBONE is to be used, the LAN requires a multicast capable router to distribute the local traffic and to act as a relay for any traffic from remote group members. The applications default to use local scope but this can be overridden through a command line option or via a configuration menu to change the TTL field as required (unless administrative scoping is being used).
Applications can be started individually as required. However, if the session is to be used on the MBONE, the Session Directory Rendezvous (SDR), can be used to advertise the session beforehand, along with configuration parameters. SDR listens on some well-known multicast addresses and ports designated for SDR to pick up advertisements for other multicast sessions. SDR can be seen as the equivalent of a TV guide for the MBONE. When a session is advertised, it may include timing information (when the session is to be executed) as well as information about the media flows to be used. SDR can be configured to launch particular applications in order to process certain media types, e.g. RAT for audio.

## Slide 59: Multimedia conferencing [3]
Inter-flow synchronisation:
  e.g. audio-video (lip-synch)
  RTP/RCTP time-stamps
  e.g. RAT+VIC: synch to RAT flow
Inter-application communication:
  conference bus
  local communication (e.g. pipes)
Heterogeneity:
  data rates
  (QoS)
Gateway:
  transcoding
  multicast-to-unicast
  supports dial-up users via BR-ISDN
  (similar to H.323 Gatekeeper)
Notes: When several applications are used together to process different media flows, there my be a requirement to have inter-flow synchronisation, e.g. to achieve lip-synchronisation between audio and video in a virtual meeting. On the MBONE, as there is no timing signals from the network itself (unlike say, ISDN), the timing information for synchronisation must be built into higher layers. In fact, the timing information is carried in RTP packets and RTCP packets. NTP timestamps give the absolute time, and media-specific timestamps give the intra-flow synchronisation. By comparing the flow-specific timestamp with the NTP timetsamp, it is possible to achieve inter-flow synchronisation. Inter-process communication is required between the application instances on a particular host. This is typically achieved by the use of pipes (for example) and the use of a a well-defined set of message on a conference bus. The bus is a mechanism for allowing the transfer of control and configuration information between application instances. It can be seen as a signalling channel.
When many different users exist in a large multicast group, there is likely to be some heterogeneity in the capability of the end-systems and their connectivity. We have also seen that the MBONE leaf-nodes are assumed to be on a LAN. What if the end-user is a dial-up user, with lower data rates than a LAN and no multicast relay? To support such users, transcoding gateways can be used to transform the data in multicast flows and redistribute as required. Transcoding the is process of converting a media flow encoding into a different format, e.g. reducing the audio data rate by converting from PCM (64Kb/s) to ADPCM (32Kb/s). A transcoding gateway may perform such flow transformations, as well as act as a relay between a multicast-capable network and users not connected to multicast network, for example users connecting to an office network using BR-ISDN.
(Transcoding and providing relay services between connection-oriented and connectionless networks are two of the functions that are performed by the Gatekeeper function that is described in H.323.)

## Slide 60: Multimedia conferencing [4]
UTG server:
  performs transcoding and relay
  UTG clients register with server
Dial-up users:
  unicast to UTG client
  local multicast at remote (client) host
RAT, VIC,
WBD, NTE,
SDR
UTG client
UTG server
MBONE (Internet)
ISDN
not multicast
capable
Notes: In the UCL toolkit, the transcoding functionality is provided by the UCL Transcoding Gateway (UTG). The UTG consists of a client and a server. The server is a central point of contact for users wishing to have a transcoding and relaying service. The user executes the normal MBONE applications locally on their workstation. The workstation must be multicast capable. The user also executes a UTG client process that liases with the UTG server. The client registers with the server and provides information about its capability, e.g. data rate of the link, whether it requires a relay service, which audio and video formats it can support. It can also register which multicast groups the user wishes to join or it can use SDR via the UTG to dynamically join groups. The UTG server then provides the services requested.
For example, consider a dial-up user connecting using BR-ISDN (128Kb/s). This user would like to connect to a conference that will audio and video flows but knows that it will not be able see the full video rate as well as receive good quality audio. The UTG client at the remote site registers with the UG server at the main site (which could be, for example, a main office site for a teleworker, or an ISP PoP site). The UTG client asks that the UTG server provide a 32Kb/s audio flow and a 96Kb/s video flow. (Video flow data-rate reduction can be achieved by reducing the number of colours used, the frame refresh rate, the size of the picture, etc.) The actual multicast conference may be using 64Kb/s audio and 384Kb/s video. The UTG server joins the relevant multicast groups, transcodes the data audio flow and video flow, and the sends them to the UTG client using IP-in-IP tunnelling. The UTG client, on receiving the tunnelled packets, removes the inner multicast packet and redistributes locally.

## Slide 61: Multimedia conferencing [5]
RAT:
  packet audio: time-slices
  numerous audio coding schemes
  redundant audio for repair
  unicast or multicast
  data-rate configurable
VIC:
  packet-video: frames
  numerous video coding schemes
  unicast or multicast
  data-rate configurable
Notes: RAT and VIC are both multicast tools that use RTP to transport audio and video (respectively) across IP networks.
RAT sends time-slices of audio in 20ms, 40ms, 80ms or 160ms chunks (configurable). Larger time-slices are preferable, but packet loss then leaves larger gaps in the audio flow at the receiver. Numerous audio encoding techniques allow use of lower data-rate channels:
linear: 16-bit linear, 128Kb/s
PCM: -law companded Pulse Code Modulation, 64Kb/s
DVI: Digital Video Interactive (Intel), 32Kb/s
GSM: Global System for Mobile communication, 13.2Kb/s
LPC: Linear Predictive Coding, 5.8Kb/s
as we go down this list, quality decreases, as does required data-rate, and computational cost increases. All use 8KHz sampling. Typically, linear or PCM is used on the LAN, PCM or DVI over the Internet and GSM or LPC over a modem.
RAT also uses redundant encoding to allow repair of the audio stream to counter packet loss.
VIC sends single time-slices - single frames (not to be confused with link-level frames) - of video at anywhere between 1 frame per second (fps) and 30 fps (which is suitable for full motion video). It supports the following video encodings at various image sizes:
raw: 24-bit frame-by-frame dumps
JPEG: motion JPEG
MPEG: MPEG1
H.261: intra-frame H.261
H.263: intra-frame H.263
CellB: Sun Microsystems proprietary encoding
NV: Xerox PARC Network Video encoding
The frame rate and overall data rate can be adjusted independently for fine-grained control of the video transmission rate.

## Slide 62: Multimedia conferencing [6]

## Slide 63: Multicast conferencing [7]
Floor control:
  who speaks?
  chairman control?
  distributed control?
Loose control:
  one person speaks, grabs channel
Strict control:
  application specific, e.g.: lecture
Resource reservation:
  not supported on the MBONE(!)
  ~500Kb/s per conference (using video)
Per-flow reservation:
  audio only
  video only
  audio and video
Notes: In a conference, discussion or seminar, there is normally an orderly way that humans conduct themselves. This has to be available in multimedia conferencing tools and is called floor control. Floor controls requires communication between the humans using the applications as well as some automatic communication between the applications themselves. This latter communication is sometimes also referred to as application-level signalling. The floor control models are currently an area of research but two basic concepts exist:
loose floor control: when anyone who speaks grabs the floor. This model is suitable for discussions or ad hoc meetings
strict floor control: a chairman has explicit control controls which participants speak. This model is suitable for conferences or lectures.
To enable such control, the applications in the multicast groups must be able communicate. This is enabled through signalling between the applications based on the chose floor control model.
Resource reservation may also be required in a conference in order to allow adequate capacity for audio and video flows. A typical conference with several several tens of participants using audio and head-and-shoulders 8fps video may require around 500Kb/s for operation. The MBONE does not currently support resource reservation, so it may not be possible to have an audio and video conference across the MBONE (remember that the MBINE is an overlay network across the Internet so sees the same QoS as other Internet applications.) Typically, it may be required that some sites in the conference remove the video stream in order to allow continued participation in the conference. Within a LAN environment, if there is a light load on the network then a single-LAN conference is possible without requiring resource reservation (as loss, delay and jitter are likely to be low). Indeed it is often not possible to make resource reservations in a LAN environment based on certain network technology (e.g. Ethernet).
If reservation is used, it could be applied independently to each of the audio video and data flows. For example, human users are fare more intolerant to loss in video flows than audio flows so a reservation could be made for the video flow and the audio (with its relatively modest data rate requirements) could continue operation at “best-effort” service.

## Slide 64: QoS-based routing

## Slide 65: What is QoS-based routing?
Traditional routing:
  destination address chooses path/route
  routers have one “optimal” path to destination
  routing metrics are single values
QoS routing:
  multiple paths possible
  alternative paths have different QoS properties
  routing updates include QoS parameter information
  use destination address, source address, ToS, etc.
RSVP/INTSERV/DIFFSERV:
  signalling may still be required
Notes: Traditionally, routing involves routers exchanging information about connectivity/reachability with a single metric to indicate some kind of “cost” that makes sense to the routing table algorithm. This metric may be hop count (e.g. RIP/DVMRP) or link cost (e.g. OSPF/MOSPF). The router uses this single metric to create a single “optimal” path to a destination. The path is optimal with respect to the single metric being used. Other, sub-optimal paths may exist, but they are not used.
With QoS-based routing (also called constraint-based routing), multiple paths are possible between sender and destination, and the choice of which path is followed is based on policy criteria selected by looking at packet header information such as source address, the ToS/DIFFSERV byte, etc. This requires that the router hold information about multiple paths per destination, running its routing algorithm multiple times to set up this information, and to include various QoS-related metrics in its routing updates. This is a non-trivial change to the operation of the router and the network as a whole.
A good overview of the issues in QoS-based routing is presented in [RFC2386].
Note that the aim of QoS routing is to indicate that paths with suitable QoS characteristics are available, but other mechanisms (such as RSVP and/or INTSERV and/or DIFFSERV) may still be required in order to ensure that resources along that path remain for the duration of the flow.

## Slide 66: IPv4 ToS byte
IPv4 header – ToS byte:
  3-bit precedence, P
  4-bit ToS
Precedence:
  000: lowest
  111: highest
ToS – flags:
  1xxx: minimise delay
  x1xx: maximise throughput
  xx1x: maximise reliability
  xxx1: minimise cost (£)
  0000: “normal” service
Not widely used:
  no global
RFC1349 – now historic:
  superseded by DIFFSERV
VER
IHL
ToS byte
Total length
0
3
7
15
31
P
0
ToS
0
2
6
7
Notes: In [RFC1349] is documented as way of using the 8-bit Type of Service (ToS) byte in the IPv4 header to provide a class of service indicator. The byte is plit into two fields, a precedence indicator, P, and a set of flags indicating the type of service (ToS) required for the packet. P takes values from 0 – 7, with 0 being the lowest precedence and 7 being the highest. The ToS flags indicate whether the packet requires minimum delay, maximum throughput, maximum reliability (low loss) or minimum (monetary) cost. The terms “maximum” and “minimum” are not that well defined.
This system was not widely use across the Internet, but found its way into use in some intra-domain (intra-AS) routing mechanisms. Although [RFC1349] is now historic (superseded by the DIFFSERV work), it serves to illustrate how we might perform QoS routing by indicating, in a packet, some simple handling requirements.

## Slide 67: Multi-metric routing
Use multiple metrics:
  minimum delay path
  maximum throughput path
  maximum reliability path
  minimum cost path
Example – OSPF:
  QoS parameters passed in link-state packets
  ToS byte used in IPv4
  multiple executions of shortest-path algorithm
Sequential filtering:
  filter paths using metrics
Granularity of QoS:
  can be per-flow, but requires much state in routers
Router overhead:
  more per packet processing
  larger router updates
  more state at routers
  possibility of instability during routing updates
Notes: Multiple metrics can be used to establish multiple paths based on QoS parameter criteria. For example, OSPF [RFC2328] allows the use of delay, throughput loss and cost information to establish routes. Information about these parameters is included in link-state packets emitted by OSPF routers. When routing tables are evaluated, the the SP algorithm is run multiple times, once for each metric and the resulting routes are stored. When a packet arrives with a ToS marking, say, for “maximum reliability” in its ToS markings, the router makes a path selection based on the routing table evaluated using the loss/reliability information.
In general, where multiple selection criteria are specified, sequential filtering can be used to select a path. For example, if “high throughput” and “low delay” are selected, initially some candidate paths are selected by applying the “high throughput” criteria only. Then, these candidate paths are filtered based on the “low delay” criteria so selecting the path(s) with both “high throughput” and “low delay”. This allows flexibility but requires extra processing, compared to using a single metric to describe/summarise both “high throughput” and “low delay”. The added processing could increase the latency of transmission, at least for the first packet in a flow, before the selected path is cached to the routers forwarding table.
The granularity of such an approach is generally kept quite coarse in order to keep processing overhead low. It could be possible to define polices that select packets based on header information down to a per-flow level, but this would introduce a large amount of extra processing and storage of state at the routers.
General disadvantages of multi-metric routing are that there is an increased overhead on the router, in terms of per-packet processing, generating and processing router updates, holding state for paths. There is also the possibility on instability and routing loops during updates, or if inconsistent implementation of routing policy causing conflicts in routing behaviour, e.g. routers in the same domain find they have different routing tables even though they have seen the same routing updates.

## Slide 68: Route pinning and path pinning
Dynamic routing:
  path change  QoS change
Keep route fixed for flow?
Route pinning
Ensure that route is fixed while packet forwarding in progress
Disrupts normal routing behaviour
May cause congestion conditions
Path pinning
Allow route to change:
  existing flows remain on fixed path
  new flows use new route
Allow different paths for different flows:
  pin separate flows to separate paths
Inconsistency:
  could affect stability if flow is long lived
(Use of RSVP?)
Notes: We have already noted that changes in QoS for a flow can occur due to the changes in the network path being followed by the packets in the flow. This is a natural consequence of the dynamic routing changes that give IP its robustness. However, routing changes can often occur when a the existing route is still serviceable, but just not “optimal”. Remember that, traditionally, routers only compute one optimal route based on the routing metric. This itself could cause instability as much traffic may be re-routed, but also this will normally result in an observable QoS change. Holding a routes constant – pinning routes – for the duration of a flow (e.g. based on some caching/time-out criteria) might help to alleviate this. However, this could disrupt the network stability, as routers with active flows may not change their routing tables, whilst other routers in the domain do, and routing loops and congestion effects could result.
An alternative is to use path pinning, allowing the routing table to be updated as normal but keeping knowledge of the current path for exiting flows. So, any existing flows continue to use the same path but new flows would use a different path. This could still lead to instability and consistency in the network if there are many long-lived flows that hold paths pinned for a long time.
Another proposal is to use RSVP to signal path pinning for some flows, and where paths really do have to change, to try and use RSVP to establish provide some likeness of QoS one the new path as was present on the old path.
These are still research areas.

## Slide 69: Intra-domain
Can use agreed single/multiple metrics
Allow autonomy in domains to remain
Should indicate disruptions to QoS along a path
Must accommodate best-effort traffic:
  no modification to existing, best-effort applications
Optionally support multicast:
  allow receiver heterogeneity and shared reservations
Still a research issue
Notes: Intra-domain QoS routing may be achievable by using mechanisms such as OSPF with ToS or DIFFSERV or traffic engineering in the underlying network. Multi-metric routing is possible with OSPF as we have already said.
The requirements listed in [RFC2386] for intra-domain QoS routing include:
allow autonomy of operation within domains, as exist at the current time
flow must be routed along a path with QoS requested or requested/indicated or a notification must be generated to say that such QoS capability can not provided at this time
indications of QoS disruption should be signalled during the lifetime of a flow if disruption is due topological changes
must accommodate best-effort flows without requiring changes to the applications that generate them
optionally support multicast and allow receiver heterogeneity and shared reservations
A QoS routing protocol that fulfils alls these criteria does not exist … yet.

## Slide 70: Inter-domain
Must be scaleable
QoS-routing should not be highly dynamic:
  few router updates, relatively small amounts of information
  may have to rely on traffic engineering and capacity planning
Must not constrain intra-domain routing mechanisms
Allow QoS information aggregation
Optionally support multicast
Notes: For inter-domain routing the key property that any QoS-based routing mechanism must possess is scalability. As there are large amounts of traffic between AS boundaries and the stability of the boundary routers is key to connectivity, we must ensure that such nodes are not subject to excessive load/processing due to the QoS-based routing mechanisms. To ensure this, [RFC2386] lists the following requirements:
QoS routing mechanisms must not be highly dynamic, there must be relatively few routing updates with small amounts of information. So, there may be a need to rely on more traditional forms of engineering, such as capacity planning, in order to ensure that border routers are kept lightly loaded
metrics should be agreed and consistent. Internal AS/domain specific metrics may need to be mapped to metrics that have global semantics
path computation should not be constrained, and be allowed to use QoS request for flows, path metrics, local policy, heuristics as well as other reachability information available from normal operation
flow aggregation should be supported as it will not be practical to maintain state for thousands of individual flows. Mechanisms must be defined to ensure that aggregate flow descriptions for QoS are consistent with the combined requirements of the individual flows so composition and comparison rules for QoS metrics must be established
optionally support multicast

## Slide 71: QoS-based routing for multicast
Reliable multicast:
  retransmissions from sender does not scale
  research issue
QoS for multicast:
  need to support widely/sparsely dispersed groups
  dynamic membership changes
  must scale across domains (across AS boundaries)
  should allow heterogeneity in group
  support for shared reservations
  research issue
Notes: QoS for multicast is still a research issue.
For the moment, there is work in progress to develop reliable multicast, for example the Reliable Multicast Transport (RMT) WG of the IETF. Normal, sender-based based retransmissions coupled with acknowledgements form the receiver does not scale to the multicast environment.
RSVP/INTSERV was designed with multicast very much in mind but we have already seen it has scaling problems and does not support receiver heterogeneity very well. Also, reservation merging is inflexible. So, [RFC2386] lists these key requirements for QoS-based multicast routing:
support widely and sparsely dispersed groups
allow dynamic membership changes for groups
scale across domains
allow heterogeneity within groups
support shared reservation styles
Needless to say, this is still a research issue.

## Slide 72: Summary
Many-to-many communication:
  IP multicast
  DVMRP, MOSPF, CBT, PIM
  conferencing example
QoS-based routing:
  multi-metric
  route/path pinning
  intra-domain and inter-domain
  QoS-based routing for multicast

## Slide 73: Scheduling and queue management

## Slide 74: Traditional queuing behaviour in routers
Data transfer:
  datagrams: individual packets
  no recognition of flows
  connectionless: no signalling
Forwarding:
  based on per-datagram, forwarding table look-ups
  no examination of “type” of traffic – no priority traffic
Traffic patterns
Notes: Let us first examine the service that IP offers. IP offers a connectionless datagram service, giving no guarantees with respect to delivery of data: no assumptions can be made about the delay, jitter or loss that any individual IP datagrams may experience. As IP is a connectionless, datagram service, it does not have the notion of flows of datagrams, where many datagrams form a sequence that has some meaning to an applications. For example, an audio application may take 40ms “time-slices” of audio and send them in individual datagrams. The correct sequence and timeliness of datagrams has meaning to the application, but the IP network treats them as individual datagrams with no relationship between them. There is no signalling at the IP-level: there is no way to inform the network that it is about to receive traffic with particular handling requirements and no way for IP to tell signal users to back-off when there is congestion.
At IP routers, the forwarding of individual datagrams is based on forwarding tables using simple metrics and (network) destination addresses. There is no examination of the type of traffic that each datagram may contain – all data is treated with equal priority. There is no recognition of datagrams that may be carrying data that is sensitive to delay or loss, such as audio and video.
As IP is a totally connectionless datagram traffic, there is no protection of the packets of one flow, from the packets of another. So, the traffic patterns of one particular user’s traffic affects traffic of other users that share some part or of, or all of, the network path (and perhaps even traffic that does not share the same network path!).

## Slide 75: Questions
How do we modify router scheduling behaviour to support QoS?
What are the alternatives to FCFS?
How do we deal with congestion?
Notes: So we can ask ourselves several questions.
Firstly, can we provide a better service that that which IP currently provides – the so-called best-effort?
The answer to this is actually, “yes”, but we need to find out what it is we really want to provide! We have to establish which parameters of a real-time packet flow are important and how we might control them. Once we have established our requirements, we must look at new mechanisms to provide support for these needs in the network itself. here are many functional elements required in order to provide QoS in the network, some of which we will look at later. Here, we are essentially trying to establish alternatives to FCFS for providing better control of packet handling in the network.
We also need to consider how the applications gain access to such mechanisms, so we must consider any application-level interface issues, e.g. is there any interaction between the application and the network and if so, how will this be achieved.
In all our considerations, one of the key points is that of scalability – how would our proposals affect (and be affected by) use of IP on a global scale, across the Internet as a whole. Also, we must try to adhere, as much as possible, to the current service interface, i.e. a connectionless datagram delivery.

## Slide 76: Scheduling mechanisms

## Slide 77: Scheduling [1]
Service request at server:
  e.g. packet at router inputs
Service order:
  which service request (packet) to service first?
Scheduler:
  decides service order (based on policy/algorithm)
  manages service (output) queues
Router (network packet handling server):
  service: packet forwarding
  scheduled resource: output queues
  service requests: packets arriving on input lines
Notes: In general, the job a a scheduler is to control access to resources at some kind of server. The server offer a service and receives service requests. the way in which the scheduler determines which service request is dealt with next is subject to some well-defined policy or algorithm.
The main job of a scheduler is to make decisions regarding the order in which service request should be allowed access to resources. It has a secondary job which is to manage the service queues. This secondary roles reflects that fact that, in the face of excessive service requests, the finite resources of the server must be managed in a way that is consistent with the policy that is established at the server.
For a router (a network packet handling server), the service being offered is a packet forwarding service; the resource which is under the control of the scheduler is (are) the output queue(s) of the router; service requests are packets that need forwarding arriving on input line(s).

## Slide 78: Scheduling [2]
Simple router schematic
Input lines:
  no input buffering
Packet classifier:
  policy-based classification
Correct output queue:
  forwarding/routing tables
  switching fabric
  output buffer (queue)
Scheduler:
  which output queue serviced next
switching fabric
forwarding / routing tables
output buffer(s)
packet classifier(s)
forwarding / routing policy
scheduler
Notes: In a model of a simple router, we have the following functional elements.
forwarding/routing policy: this is part of the decision making process that is set-up by a network administrator. The policy includes information about how to classify packets as well as any constraints on routing an forwarding.
forwarding/routing tables: these are constructed by the normal operation of the routing protocols and algorithms that run in the router.
input lines: as packets arrive interrupts are generated to indicate that an input should be processed. We assume that for a QoS sensitive network, router do not perform input buffering. Although input buffering is possible, packets may have their QoS requirements violated as they wait in input buffers, so we assume that packets are processed at line speed.
packet classifier: this makes some policy-based decision in order to classify the packets. The packet classification will allow the scheduler to make decisions about the order in which packets are serviced.
switching fabric: this moves a packet in an input queue to the appropriate output queue.
output queue: hold packets awaiting transmission.
scheduler: makes decisions as to which output queue should be serviced next.
More information router design and scheduling can be found in [KS98] and [KLS98].

## Slide 79: FCFS scheduling
Null packet classifier
Packets queued to outputs in order they arrive
Do packet differentiation
No notion of flows of packets
Anytime a packet arrives, it is serviced as soon as possible:
  FCFS is a work-conserving scheduler
Notes: In first-come first-served (FCFS) scheduling, the packets are scheduled in the order they arrive at the router. No other packet differentiation is performed. The router has no notion of flows of packets. In fact, FCFS scheduling is a very function and the main concern of most FCFS scheduled routers is queue management – coping with excessive bursts of packets with finite buffer space. We look at key management techniques and congestion control later.
There is one very important aspect of FCFS which we will examine before we go on to discuss other scheduling disciplines, and that is that it is a work-conserving scheduling disciple. That is, the router is never idle when there are packets waiting to be serviced.

## Slide 80: Conservation law [1]
FCFS is work-conserving:
  not idle if packets waiting
Reduce delay of one flow, increase the delay of one or more others
We can not give all flows a lower delay than they would get under FCFS
Notes: An important theorem due to Kleinrock (p.117 in [Kle75]) helps us in analysing scheduling disciplines. This theorem is The Conservation Law. Consider N flows arriving at a scheduler, so that the traffic rate of connection n (1  n  N) is n. If we assume that flow n has a mean service rate of n. So, the mean utilisation of a link by flow n, n, is n n. Let the mean waiting time due to the scheduler for the packets of flow n be qn. According to the Conservation Law, the scheduler is then work conserving if:
 n qn= C where C is a constant value
n
This expression is important as it makes no reference to any particular scheduling disciplines. This expression also says that for any work conserving scheduling discipline, if one of the flows is given a lower delay by the scheduler, then it must be by increasing the delay for one or more of the other flows. This is a fundamental result.

## Slide 81: Conservation law [2]
Example
n : 0.1ms/p (fixed)
Flow f1:
  1 : 10p/s
  q1 : 0.1ms
  1 q1 = 10-7s
Flow f2:
  2 : 10p/s
  q2 : 0.1ms
  2 q2 = 10-7s
C = 210-7s
Change f1:
  1 : 15p/s
  q1 : 0.1s
  1 q1 = 1.510-7s
For f2 this means:
  decrease 2?
  decrease q2?
Note the trade-off for f2:
  delay vs. throughput
Change service rate (n):
  change service priority
Notes: Let us demonstrate this using an example. Assume we have two equal flows, initially, f1 and f2. We assume that packet service rate is a function of the hardware/software of the router (though it is possible it is also a function of the average packet size in the flow) and is therefore fixed and equal for all flows. For the initial situation shown ab0ve, we can use the conservation law to evaluate C. If we now change the attributes f flow 1, so that we would like it to have a higher data rate, we find that the Conservation Law tells us that we must either decrease the data rate of f2 to maintain its data rate, or decrease its data rate to maintain the delay.
It is possible to change the service rate of each flow by changing the priority of the flow. Here, we have assumed that both flows have the same, i.e. FCFS scheduling is being used.

## Slide 82: Non-work-conserving schedulers
Non-work conserving disciplines:
  can be idle even if packets waiting
  allows “smoothing” of packet flows
Do not serve packet as soon as it arrives:
  what until packet is eligible for transmission
Eligibility:
  fixed time per router, or
  fixed time across network
Less jitter
Makes downstream traffic more predictable:
  output flow is controlled
  less bursty traffic
Less buffer space:
  router: output queues
  end-system: de-jitter buffers
Higher end-to-end delay
Complex in practise
  may require time synchronisation at routers
Notes: We have defined a work-conserving scheduler as one that is never idle if there are packets waiting. So what is a non-work conserving scheduler and why might they be useful? In a non-work-conserving scheduler, the scheduler can be idle even though there are packets waiting for transmission. The reason it remains idle is that waits for packets to become eligible for transmission. It is a bit like a clever set of traffic lights at a junction – not only does it know where you are going, it also knows how fast you should be going and only lets you move on when the time is right, even if there is no other traffic going through at other junctions. (Continuing the analogy, a work-conserving discipline is more like a junction with stop signs – as soon as there is a chance for you to go through, then you do.)
The eligibility of a packet can be determined in different ways. One way is to ensure that it always spends no more than a fixed time at a router. In this way the end-to-end jitter is controlled. This is equivalent to control the data rate and the jitter, and so such mechanisms are called delay-jitter regulators. Another way to determine eligibility is establish the notion of a fixed end-to-end delay for a packet. Then, routers decide a packet is eligible based on the time budget that remains for each packet. This is called a delay-jitter regulator as both the end-to-end delay and the end-to-end jitter are controlled.
The advantages of non-work conserving disciplines is that they reduce jitter, making downstream traffic more predictable. This means that there are fewer and smaller traffic burst, which reduces the buffering requirements at router and end-systems. However, we have already discussed that end-systems can de-jitter streams as required.
However, the cost of using such mechanisms is higher end-to-end delay overall. Also, such systems can be complex to build in practise. For example, delay-jitter regulators require that the network operator know the propagation on each link in the network, and that all router maintain a synchronised clock with which they can establish the eligibility of packets. Consequently, non-work-conserving disciplines are not used and are still considered a research issue.

## Slide 83: Scheduling: requirements
Ease of implementation:
  simple  fast
  high-speed networks
  low complexity/state
  implementation in hardware
Fairness and protection:
  local fairness: max-min
  local fairness  global fairness
  protect any flow from the (mis)behaviour of any other
Performance bounds:
  per-flow bounds
  deterministic (guaranteed)
  statistical/probabilistic
  data rate, delay, jitter, loss
Admission control:
  (if required)
  should be easy to implement
  should be efficient in use
Notes: There are four key requirements that can be listed for any scheduling mechanism.
ease of implementation: the mechanisms should be easy to implement. Keeping the mechanism as simple as possible makes it faster, it should be easier to implement. Also, if we can keep the amount of algorithmic complexity low, as well as minimise the amount of state information needed by the algorithm, then the mechanisms may lend itself more easily to implementation in hardware, making it suitable for high-speed networking.
fairness and protection: flows should receive fair allocation of resource, all other things being equal, they should not receive any less than any other flow also asking to use the same resources. In fact, it is possible to be much more precise about how resources should be allocated, using the max-min fairness criteria. The max-min fairness criteria allows per-hop local fairness for each flow, which results in global fairness for all of the flows. The protection requirement states that no flow should suffer due to the (mis)behaviour or characteristics of any other flow. We can see from the Conservation Law that FCFS does not provide protection as if one flow was to increase its data rate, all the other flows would suffer.
performance bounds: for supporting QoS in networks, it should be possible to specify performance bounds to describe so that we can be sure that our flow is handled appropriately by the network. The exact nature of these performance bounds depends on the kind of QoS guarantee that we need for our flow. Where a scheduler is being used to provide a guaranteed service, it would have to offer the ability to work with deterministic performance bounds. If relative priorities for flows were being specified, then the scheduler should allow the specification of performance bounds in a statistical or probabilistic way.
admission control: where deterministic performance bounds are specified, the network may need to perform admission control before it can allow a flow to start transmission. In this case the admission control mechanism should be easy to implement and efficient to operate.

## Slide 84: The max-min fair share criteria
Flows are allocated resource in order of increasing demand
Flows get no more than they need
Flows which have not been allocated as they demand get an equal share of the available resource
Weighted max-min fair share possible
If max-min fair  provides protection
Example:
C = 10, four flow with demands of 2, 2.6, 4, 5
actual resource allocations are 2, 2.6, 2.7, 2.7
Notes: In max-min fair share, resources are allocated according to some simple rules. The demands of the resource flows are ordered in increasing demand so that flows with the lowest demands are allocated resources first. This means that resources with small demands are likely to be allocated all that they ask for (as the simple example above illustrates.)
It is possible to assign weights to the resource demands so that some demands receive a greater share of the resources than others. In this case the rules of max-min fair share are modified as follows:
flows are allocated resource in order of increasing weighted demand (the demands are normalised by the weight)
no flow gets more than it needs
flows which have not been allocated as they demand get a weighted share of the available resource
Raj Jain has proposed a simple fairness metric between flows which is the sum of the rates squared over the square of the sum - this varies up to one for fair allocation.

## Slide 85: Scheduling: dimensions
Priority levels:
  how many levels?
  higher priority queues services first
  can cause starvation lower priority queues
Work-conserving or not:
  must decide if delay/jitter control required
  is cost of implementation of delay/jitter control in network acceptable?
Degree of aggregation:
  flow granularity
  per application flow?
  per user?
  per end-system?
  cost vs. control
Servicing within a queue:
  “FCFS” within queue?
  check for other parameters?
  added processing overhead
  queue management
Notes: When designing a scheduling mechanism, we have several dimensions or degrees of freedom in which we can work.
The first of these is the use of priority levels. Here we assign different priorities to different output queues. Queues with higher priorities receive service first. Queues with lower priorities are only serviced when the higher priorities queues are empty. We can decide to have an arbitrary number of priority levels to reflect our QoS policy.
We can also choose for our scheduling mechanism to be work-conserving or non-work-conserving. We have already discussed the differences between these two, and the decision boils down to two questions:
do you need to have good delay and jitter control?
if so, is the additional cost of implementing non-work-conserving schedulers acceptable?
When we design our scheduling policy, we must decide on the granularity of our flows, i.e. we must decide on the level of aggregation of traffic that we want. We can have large levels of aggregation and have relatively poor control over individual application-level flows, or we can have per-application flow state and have very fine grained control. The choice is a trade-off between the amount of control we have for our flows (with respect to individual packet sources) versus the amount of state we store for the scheduler and the processing overhead in involved with that state.
Finally, within an individual queue, we need to decide on how packets should be serviced within that queue. We can just decide to service the packets in the order in which they arrived within the queue (i.e. treat each queue as a single FCFS queue waiting for transmission) or we can examine the contents of individual packets in the queue and make fine-grained policy decisions as to which should be serviced first. Again, the trade-off is between the level of control desired and the cost of the processing required. Queue servicing may be required for queue management, which we look at later.

## Slide 86: Simple priority queuing
K queues:
  1  k  K
  queue k + 1 has greater priority than queue k
  higher priority queues serviced first
Very simple to implement
Low processing overhead
Relative priority:
  no deterministic performance bounds
Fairness and protection:
  not max-min fair: starvation of low priority queues
Notes: In priority queuing, K queues are established, numbered 1 … K. Higher numbered queues are serviced before lower numbered queues – they have higher priority. A lower priority queue will only be serviced if there are no packets awaiting service in a higher priority queue. This means that busy higher priority queues could prevent lower priority queues from being serviced – situation known as starvation. This system would need to be used with some other mechanism to police the traffic into the queues, e.g. a token bucket filter for each queue, plus admission control at the edge of the network.
Note that the queues assign relative priority, so this mechanism by itself would not be suitable for providing deterministic guarantees for performance bounds.

## Slide 87: Generalised processor sharing (GPS)
Work-conserving
Provides max-min fair share
Can provide weighted max-min fair share
Not implementable:
  used as a reference for comparing other schedulers
  serves an infinitesimally small amount of data from flow i
Visits flows round-robin
Notes: Generalised processor sharing (GPS) is a work-conserving scheduler that provide max-min fairness and protection. It can be used to provide probabilistic/statistical (relative) as well as deterministic performance bounds. Unfortunately, it is not implementable as the analysis requires that for each flow i, only an infinitesimally small amount of data is served. However, the analysis is useful in that it provides us with a reference with which we can assess other schedulers by comparison. All flows are serviced round-robin. GPS is described in [GP93] and [GP94].

## Slide 88: GPS – relative and absolute fairness
Use fairness bound to evaluate GPS emulations (GPS-like schedulers)
Relative fairness bound:
  fairness of scheduler with respect to other flows it is servicing
Absolute fairness bound:
  fairness of scheduler compared to GPS for the same flow
Notes: In [Gol94] is described two fairness bounds that can be used to assess the performance of the service, S, provides by an emulation of GPS (i.e. a scheduler that attempts to achieve a GPS-like service). The first fairness bound is the relative fairness bound (RFB), which attempts to provide evaluate how fairly resources are allocated between flows being serviced by the GPS emulation. The second fairness bound is the absolute fairness bound (AFB), which tries to make a comparison of the service provided by the GPS emulation to that which would be provided by GPS. The closer that the RFB and AFB are to zero the better. It is normally hard to obtain an evaluation of the AFB for most emulations, so the RFB is used.
In the expressions above, it is assumed that we examine the K routers along a path that serve N flows. S(.) is the service given to a flow by the GPS emulation and G(.) is the service that would be given by GPS. g(i, k) is the relative service rate given to flow i at router k along the path. g(i) is, effectively, the bottleneck rate along the path.

## Slide 89: Weighted round-robin (WRR)
Simplest attempt at GPS
Queues visited round-robin in proportion to weights assigned
Different mean packet sizes:
  weight divided by mean packet size for each queue
Mean packets size unpredictable:
  may cause unfairness
Service is fair over long timescales:
  must have more than one visit to each flow/queue
  short-lived flows?
  small weights?
  large number of flows?
Notes: The simplest emulation of GPS is weighted round-robin (WRR). Here, queues are serviced round-robin, in proportion to a weight that is assigned to each flow/queue, i.e. flows/queues with a greater weight have more service. In each round each queue is visited once. Normally, at least one packet is transmitted from each queue that is non-empty. The weight assigned to each flow/queue is normalised by dividing by the average packet size for each flow/queue. If this is not know before hand, them WRR may not be able to offer the correct service rate for the flow. For many applications, it may not be easy to evaluate the average packet size before hand. The service provided by WRR can be shown to be fair over long-lived flows but for short lived flows, flows with small weights or where there are a large number of flows, WRR may exhibit unfairness.

## Slide 90: Deficit round-robin (DRR)
DRR does not need to know mean packet size
Each queue has deficit counter (dc): initially zero
Scheduler attempts to serve one quantum of data from a non-empty queue:
  packet at head served if size  quantum + dc dc  quantum + dc – size
  else dc += quantum
Queues not served during round build up “credits”:
  only non-empty queues
Quantum normally set to max expected packet size:
  ensures one packet per round, per non-empty queue
RFB: 3T/r (T = max pkt service time, r = link rate)
Works best for:
  small packet size
  small number of flows
Notes: In deficit round-robin (DRR), an attempt is made to by-pass the requirement to know the average packet size for each flow. Each non-empty queue initially has a deficit counter (dc) which starts of at the value zero. As the scheduler visits each non-empty queue, it compares the packet at the head each of these queues and tries to serve one quantum of data. If dc is zero for a queue, then the packet is served if the size of the packet at the head of the queue is less than or equal to the quantum size. If a packet can not be served, then the value of the quantum is added to the dc for that queue. If the scheduler visits a queue with a dc > 0, the a packet from the queue is served if quantum + dc is greater than or equal to the size of the packet at the head of the queue. If the scheduler sees a queue with a non-zero dc, yet it is empty, then the dc is reset to zero so that it can not keep acquiring deficit. The quantum size used is normally that largest expected packet size in the network. Example, three flows A, B, C with packets of size 600, 1000, 1400 bytes. The quantum size is set to 1000 bytes. In the first round:
queue A: packet is served, dc = 1000 – 600 = 400
queue B: packet is served, dc = 1000 – 1000 = 0
queue C: packet is not served, dc = 1000
In the second round:
queue A: no packet, dc set to zero
queue B: no packet, dc set to zero
queue C: packet is served, dc = 1000 + 1000 – 1400 = 600
In third round:
queue A: not served
queue B: not served
queue C: no packet, dc set to zero
If weights are assigned to the queues, then the quantum size applied for each queue is multiplied by the assigned weight.
DRR works best for small packets sizes and a small number of flows, suffering similar unfairness behaviour to that for WRR.

## Slide 91: Weighted Fair Queuing (WFQ) [1]
Based on GPS:
  GPS emulation to produce finish-numbers for packets in queue
  Simplification: GPS emulation serves packets bit-by-bit round-robin
Finish-number:
  the time packet would have completed service under (bit-by-bit) GPS
  packets tagged with finish-number
  smallest finish-number across queues served first
Round-number:
  execution of round by bit-by-bit round-robin server
  finish-number calculated from round number
If queue is empty:
  finish-number is: number of bits in packet + round-number
If queue non-empty:
  finish-number is: highest current finish number for queue + number of bits in packet
Notes: WFQ is an emulation of GPS that actually uses a GPS computations to control its behaviour. In fact it runs a GPS computations and uses these to tag packets in flows to indicate the time the would have finished being served had they been subject to GPS scheduling. WFQ itself approximates GPS by using a model of bit-by-bit round robin service, i.e. for a packet of size N bits at the head of a queue, it will have complete service after the scheduler has performed N rounds of visiting all the other queues. This is bit-by-bit fair. However, we can not actually transmit packets one bit at a time from multiple queues, so instead the packets are tagged with a finish-number, which indicates when they would have completed service if served bit-by-bit. So, we can see that packets with the smallest finish number are the ones that should be transmitted first. Let us take the simple case that the queue is empty and a packet of size 50 bits arrives in the queue. As it is served bit-by-bit round robin, it will be serviced in 50 rounds. So its finish number will simply be the current round-number plus its own size in bits. So if the round number is 20, the finish-number for our packet is 70. If the queue is non-empty, then packets already in the queue will be served first. So the finish number of this new packet, which is at the back of the queue, will be the finish number for the packet in front of it plus its own size in bits. When the round-number is equal to (or greater than) the finish-number of the packet, it should be served immediately.
The closest analogy (at least that I can think of at this time!) is probably that of using a number system when you go to the delicatessen counter at the supermarket. All the people (packets) are of unit size, so this simplifies things. They are served one at a time (unit-by-unit) and people can appear at the delicatessen counter from any of a number of aisles in the supermarket. A person takes a piece of paper with a number on it from the from the counter. This is your finish-number and is one more than the person in front of you. It does not matter where you are physically, but when your number comes up on the big counter display (the round-number), it is your turn to be served.

## Slide 92: Weighted Fair Queuing (WFQ) [2]
Rate of change of R(t) depends on number of active flows (and their weights)
As R(t) changes, so packets will be served at different rates
Flow completes (empty queue):
  one less flow in round, so
  R increases more quickly
  so, more flows complete
  R increases more quickly
  etc. …
  iterated deletion problem
WFQ needs to evaluate R each time packet arrives or leaves:
  processing overhead
Notes: More formally, the evaluation of the finish-number, F, is as shown above.
The ‘W’ in WFQ comes from applying weights to evaluation of the finish-number, as shown in the expression for F.
We can see here that the finish time is depended on R. Also, F and R are both functions of absolute time t. As the number of flows change, so does the rate of change of R. As more flows become active, so the rate of change of R decreases. As the number flows decreases, so the rate of change of R increases. This latter property leads to a problem know as iterated deletion. A flow is deleted if it has completed, i.e. the queue becomes empty. When this happens, it means that R will increase at a faster rate. This means that the R will approach the finish-number of other packets, already queued, faster than originally evaluated. This may cause some of the other flows to complete also, leading to a further increase in the rate of change of R. In order to keep track of R, a WFQ system must evaluate the value of R every time a packet arrives or leaves.

## Slide 93: Weighted Fair Queuing (WFQ) [3]
Buffer drop policy:
  packet arrives at full queue
  drop packets already in queued, in order of decreasing finish-number
Can be used for:
  best-effort queuing
  providing guaranteed data rate and deterministic end-to-end delay
WFQ used in “real world”
Alternatives also available:
  self-clocked fair-queuing (SCFQ)
  worst-case fair weighted fair queuing (WF2Q)
Notes: WFQ also proposes a a buffer drop policy that is max-min fair. If a packet arrives to a full queue, enough packets are dropped to allow the new packet to be queued. Packets are dropped in order of decreasing finish-number, i.e. most recent arrivals are dropped first.
WFQ can be used for scheduling multiple best effort flows, providing protection for each flow. With a few modifications – the weighted part of WFQ which we have not examined – it can also provide services for flows that require guaranteed data rate and an upper bound on the end-to-end delay.
Even though it is computationally expensive, and need to hold per-flow state, WFQ is used by many router manufacturers. Alternatives to WFQ, such as self-clocked fair-queuing (SCFQ) and worst-case fair weighted fair queuing (WF2Q). SCFQ has similar properties to WFQ, except that it removes the expensive round-number computation but also has a higher end-to-end delay bound than WFQ. WF2Q has an AFB that more closely approaches the AFB that is lower than WFQ (i.e. it has a a better AFB than WFQ), but requires an additional implementation complexity and has higher processing overhead in operation.

## Slide 94: Class-Based Queuing
Hierarchical link sharing:
  link capacity is shared
  class-based allocation
  policy-based class selection
Class hierarchy:
  assign capacity/priority to each node
  node can “borrow” any spare capacity from parent
  fine-grained flows possible
Note: this is a queuing mechanism: requires use of a scheduler
root
(link)
X
RT
Y
Z
NRT
appN
app1
100%
RT real-time
NRT non-real-time
40%
30%
30%
30%
10%
1%
RT
NRT
25%
15%
Notes: CBQ was designed to allow sharing of link capacity within a class-based hierarchy [FJ95] [WGCJF95]. We see an example showing the link capacity as a root node in a tree at 100%. Organisations X, Y and Z that share the link are assigned 40%, 30% and 30% of the link capacity, respectively. Within their own allocations of capacity, the organisations can choose to partition the available capacity further by creating sub-classes within the tree. Organisation X decides to allocate 30% to real-time traffic and 10% to all non-real-time traffic. Within the real-time allocation, X decides to allocate capacity to individual applications. Organisation Z also divides its allocation into real-time and non-real-time, but with a different share of the available link capacity. Organisation Y decides not to further refine its allocation of link capacity. The percentages indicate the minimum share of the link capacity a node in the tree will receive. Child nodes effectively take capacity from their parent node allocation. If some sibling nodes are not using their full allocations, other siblings that might be overshooting their own allocation are allowed to “borrow” capacity by interacting with the parent node. With an appropriate scheduling mechanism, this allows support for QoS sensitive flows. Classifications could be made per application, per flow, per IP source address, etc., as dictated by the policy chosen by the individual organisations in conjunction with their Internet connectivity provider. Not shown above is that different priority levels can be assigned to each classification. For example, real-time traffic could be given priority 2 and non-real-time priority 1, where priority 2 is higher (receive better service) than priority 1.

## Slide 95: Queue management and congestion control

## Slide 96: Queue management [1]
Scheduling:
  which output queue to visit
  which packet to transmit from output queue
Queue management:
  ensuring buffers are available: memory management
  organising packets within queue
  packet dropping when queue is full
  congestion control
Notes: Schedulers are used to select which packet from which queue will receive service next. Some, such as WFQ may also suggest ways in which queues may be managed under overflow conditions, i.e when there is a scarcity of buffers. However, queue management is a topic in its own right, although it is often related closely to the operation of scheduling. Queue management may include several function, including memory management and organisation/ordering of packets within a queue. However the two functions of queue management that we will discuss are packet dropping and congestion control.

## Slide 97: Queue management [2]
Congestion:
  misbehaving sources
  source synchronisation
  routing instability
  network failure causing re-routing
  congestion could hurt many flows: aggregation
Drop packets:
  drop “new” packets until queue clears?
  admit new packets, drop existing packets in queue?
Notes: Congestion can occur for a range of reasons. Sources may be mis-behaving, generating traffic above their normal rate. Even when sources are all behaving, correctly, pathological occurrences such as source synchronisation may cause congestion. Routing instability or network path changes due to network failure close to a node may cause a temporary burst of congestion. The result of congestion could hurt many flows, and this is more so as you move towards the core of the network and find a higher aggregation of traffic.
When congestion occurs, the router has run out of buffers and must drop packets. However, which policy should the router adopt in dropping packets, and what are the effects of using one particular dropping policy over another?

## Slide 98: Packet dropping policies
Drop-from-tail:
  easy to implement
  delayed packets at within queue may “expire”
Drop-from-head:
  old packets purged first
  good for real time
  better for TCP
Random drop:
  fair if all sources behaving
  misbehaving sources more heavily penalised
Flush queue:
  drop all packets in queue
  simple
  flows should back-off
  inefficient
Intelligent drop:
  based on level 4 information
  may need a lot of state information
  should be fairer
Notes: The granularity of the drop algorithm has the same choices as for scheduling. We can decide to drop packets from individual application-level flows, or have a courser grain of dropping. With a fine granularity, the cost, as always is the additional state to be held at the router and the overhead of maintaining and processing that state information. With a courser granularity, we have reduce the amount of state information and lose some control over which flow’s packets are dropped. If packets are queued per-flow, then we also offer some protection as a mis-behaving source will only fill and overflow its own queue and not hurt any other flows. We can decide to drop form the tail of the queue. This is easiest to implement, as it means that there is no need to adjust any pointers in any other part of the queue. However, packets already in the queue and already delayed, and their usefulness may expire while they wait in the queue, i.e. they get to the receiver too late to be used by the application. Yet the receiver may not become aware of the congestion until it sees dropped packets, i.e. until the drop packets at the end of the queue are not received. So an alternative is drop form the head of the queue. This means that older packets – packets that have been in the network longer – are purged. This is good for real-time data, as these packets would no longer be as useful anyway. This is also good for protocols like TCP, as the loss is seen sooner and so TCP’s congestion control/avoidance mechanisms can operate. However drop from head typically has a higher processing overhead than drop from tail. We can also drop a packet from a random place in the queue. This should be fair if all sources are behaving. If there are any mis-behaving sources, they are likely to be occupying more buffers and so are more likely have packets dropped than other flows, which is also beneficial.
Another very simple policy to implement is dropping a whole queue. This has the advantage that frees up buffers immediately, and this could be useful if the router is experiencing extreme congestion. However, this policy could be inefficient, as it may lead to many more re-transmission than are necessary, and may compound the burstiness of traffic. The exact behaviour of sources when such an event occurs may be application specific. For real-time applications, to have such a large contiguous hole in the flow may not be acceptable. This may be useful for “reprimanding” mis-behaving flows, when per-flow queuing is used.
Another alternative is intelligent dropping, where packets are dropped by knowledge of the traffic flow, for example knowledge of the level 4 protocol operation. This may require a lot of state information to be held at the router, but appears to have the potential of offer very fine-grained congestion control.

## Slide 99: End system reaction to packet drops
Non-real-time – TCP:
  packet drop  congestion  slow down transmission
  slow start  congestion avoidance
  network is happy!
Real-time – UDP:
  packet drop  fill-in at receiver  ??
  application-level congestion control required
  flow data rate adaptation not be suited to audio/video?
  real-time flows may not adapt  hurts adaptive flows
Queue management could protect adaptive flows:
  smart queue management required
Notes: We are considering packet dropping to control congestion. However, what do applications do when they see packet loss? TCP uses loss as an indicator of congestion, and slows down its transmission rate. TCP has well-defined behaviour in the form slow-start and congestion avoidance, and generally does a reasonable job of being kind to the network.
Real-time applications, however, use UDP, which has now congestion control mechanisms. The packet loss may be seen at the receiver and he receiver may perform some application-specific action, but there is unlikely to be any feedback to the sender. Some form of application-level congestion control is required. This may require, for example, adapting the flow rate by hanging audio or video coding. However, the application may not e suited to such adaptation. yet, without such adaptations, congestion events may continue to occur. Indeed, adaptive flows (such as TCP) that do back down in the face of congestion my be forced down to low data rates as unconstrained, non-adaptive real-time flows continue unabated.
However, smart queue management (coupled with an appropriate scheduling mechanism) could be used to protect adaptive flows from is-behaving flows whilst at the same time controlling congestion.

## Slide 100: RED [1]
Random Early Detection:
  spot congestion before it happens
  drop packet  pre-emptive congestion signal
  source slows down
  prevents real congestion
Which packets to drop?
  monitor flows
  cost in state and processing overhead vs. overall performance of the network
Notes: One widely implemented intelligent drop mechanism is Random Early Detection (RED) [#FJ93#]. This drops packets before congestion actually occurs by monitoring queue lengths at a router and increasing the probability of a packet drop as the queue length builds up. The drop of a packet from a flow will act as an indication of congestion and cause it to back of is transmission rate. The packet drop occurs before real congestion starts and is intended to prevent real congestion occurring.
The cost of this mechanism is the requirement to monitor flows and queue lengths, and the processing overhead of dealing with the state information being held. This increase in performance cost is seen as acceptable as the overall performance of the network is improved by avoiding real congestion.

## Slide 101: RED [2]
Probability of packet drop  queue length
Queue length value – exponential average:
  smooths reaction to small bursts
  punishes sustained heavy traffic
Packets can be dropped or marked as “offending”:
  RED-aware routers more likely to drop offending packets
Source must be adaptive:
  OK for TCP
  real-time traffic  UDP ?
Notes: RED drops a packet from a flow with probability, p, which increase linearly as the queue length increases. However, the actual value of queue length used to evaluate p is an exponentially-weighted moving average (EWMA) of the actual queue length. This is to allow small bursts of traffic to be allowed through the network, but to spot sustained, heavy traffic. The dampening effect of the EWMA also helps to stabilise the dropping mechanism, so it does not “over-react” to short-lived bursty traffic. As well as dropping packets, RED can mark IP packets as “offending”, i.e. in violation of some traffic profile, and not drop them when traffic load is light. However, offending packets can be spotted by RED-aware routers downstream and can sill be dropped if congestion appears.
While RED can control queue length regardless of end-system co-operation, as we have noted already, if the end-system does reduce its transmission rate in response to such congestion signals, this would be helpful to the health of the network as a whole. We have also noted that while dynamically adaptive behaviour does not harm non-real-time applications, real-time applications, such as voice and video applications, normally do not find such behaviour acceptable.

## Slide 102: TCP-like adaptation for real-time flows
Mechanisms like RED require adaptive sources
How to indicate congestion?
  packet drop – OK for TCP
  packet drop – hurts real-time flows
  use ECN?
Adaptation mechanisms:
  layered audio/video codecs
  TCP is unicast: real-time can be multicast
Notes: In recognition of the usefulness of mechanisms like RED, and the requirement for congestion control in real-time end-systems, there are several proposals to deal with congestions.
The first one we shall examine how to indicate congestion to end-systems. The lost packet is an effective indicator of congestion to TCP, but real-time flows may not be monitoring for packet loss in the same way. There is a proposal to provide explicit congestion notification (ECN) [RFC2481] at the IP level. This would be a single-bit flag which would normally be clear, but which would be set by a congested router and so act as an explicit signal to a receiver that this packet has passed through a part of the network that is experiencing congestion.
Other, ore complex mechanisms concentrate on building congestion control into the application-layer protocol. We have already stated that real-time flows such as video do not normally adapt well. However, by using layered-codecs we can adjust the transmission rate dynamically. A layered video codec encodes video as several separate flows, each flowing carrying different frequency (spatial) components. There is a single base-layer which must be received, but several additional layers just adder finer detail to the base layer, and can be received optionally depending on the availability of network resources. In [VRC98] is described an experiment to provide TCP-like adaptation for video.

## Slide 103: Scheduling and queue management: Discussion
Fairness and protection:
  queue overflow
  congestion feedback from router: packet drop?
Scalability:
  granularity of flow
  speed of operation
Flow adaptation:
  non-real time: TCP
  real-time?
Aggregation:
  granularity of control
  granularity of service
  amount of router state
  lack of protection
Signalling:
  set-up of router state
  inform router about a flow
  explicit congestion notification?
Notes: A good analysis of requirements for the future Internet is given in [She95].

## Slide 104: Summary
Scheduling mechanisms
  work-conserving vs. non-work-conserving
Scheduling requirements
Scheduling dimensions
Queue management
Congestion control

## Slide 105: QoS services and application-level service interfaces

## Slide 106: IP “service”
IP datagram service:
  datagrams are subject to loss, delay, jitter, mis-ordering
Performance: no guarantees
Integrated Services:
  new QoS service-levels
Differentiated Services:
  class of service (CoS)
User/application may need to signal network
User/application may need to signal other parts of application
Notes: Internet users have increasing demands to use a range of multimedia applications with QoS sensitive data flows. All these applications may require different QoS guarantees to be provided by the underlying network. An e-mail application can make do with a best-effort network service. Interactive or real-time voice and video applications require (some or all of) delay, jitter, loss and throughput guarantees in order to function. Web access can make do with a best-effort service, but typically requires low delay, and may require high throughput depending on the content being accessed. The Internet was never designed to cope with such a sophisticated demand for services. Today’s Internet is built upon many different underlying network technologies, of different age, capability and complexity. Most of these technologies are unable to cope with such QoS demands. Also, the Internet protocols themselves are not designed to support the wide range of QoS profiles required by the huge plethora of current (and future) applications.
To deal with such issues, the IETF have two working groups looking at QoS issues directly. The INTSERV WG is looking at how to extend the IP network to become an Integrated Services Network (ISN). INTSERV have been looking at the definition and support of new service-levels (other than best-effort) within an IP network. The DIFFSERV WG is looking at the provision of differentiated services within IP networks, allowing service providers to treat packets from different sources with different QoS. The source of packets is defined administratively, e.g. could be a single host or a whole organisation.
In some cases, the user or the application (or both) may need to indicate their requirements to the network by use of some sort of signalling. The notion of user-to-network signalling is not inherent in the IP networking model. At the application-level, there may be a requirement for user-to-user (application-to-application) supported as a network service.

## Slide 107: Questions
Can we do better than best-effort?
What support do real-time flows need in the network?
What support can we provide in the network?
QoS for many-to-many communication?
Application-level interfaces?
Signalling
Notes: So we can ask ourselves several questions.
Firstly, can we provide a better service that that which IP currently provides – the so-called best-effort?
The answer to this is actually, “yes”, but we need to find out what it is we really want to provide! We have to establish which parameters of a real-time packet flow are important and how we might control them. Once we have established our requirements, we must look at new mechanisms to provide support for these needs in the network itself. We are essentially asking trying to establish alternatives to FCFS for providing better control of packet handling in the network as well as trying to support QoS for multi-party (many-to-many) communication.
We also need to consider how the applications gain access to such mechanisms, so we must consider any application-level interface issues, e.g. is there any interaction between the application and the network and if so, how will this be achieved.
IP, as connectionless network protocol, involves no signalling. However, in order to allow the use of real-time applications, we need to establish a richer set of function in order to allow information about a communication session to sent into (and across) the network. So, we need signalling capability, both user-to-network and user-to-user.

## Slide 108: INTSERV

## Slide 109: Questions
What support do we need form the network to give QoS capability to the Transport layer?
How can we control congestion in the network?
How can we support legacy network protocols over the Internet?
Notes: In the last section we produced a taxonomy of applications with respect to their QoS requirements. Real-time applications need a better service that standard IP unreliable datagram delivery. We will see that there is some support available at the transport layer for real-time applications (e.g. by use of RTP), but this can not give us QoS guarantees. We need direct support form the network so we must modify the operation of the routers somehow so that they can give priority to QoS sensitive traffic.
Finally, we take a brief look at how legacy applications might be operated across an IP-based network.

## Slide 110: Integrated services
Need:
  service-levels
  service interface – signalling protocol
  admission control
  scheduling and queue management in routers
Scenario:
  application defines service-level
  tells network using signalling
  network applies admission control, checks if reservation is possible
  routers allocate and control resource in order to honour request
Notes: To provide Integrated Services for IP applications, we can envisage the following scenario:
a service-level is defined (e.g. within an administrative domain or, with global scope, by the Internet community). The definition of the service-level includes all the service semantics; descriptions of how packets should be treated within the network, how the application should inject traffic into the network as well as how the service should be policed. Knowledge of the service semantics must be available within routers and within applications
an application makes a request for service invocation using the service interface and a signalling protocol. The invocation information includes specific information about the traffic characteristics required for the flow, e.g. data rate. The network will indicate if the service invocation was successful or not, and may also inform the application if there is a service violation, either by the application’s use of the service, or if there is a network failure
before the service invocation can succeed, the network must determine if it has enough resources to accept the service invocation. This is the job of admission control that uses the information in the service invocation, plus knowledge about the other service requests it is currently supporting, and determines if it can accept the new request. The admission control function will also be responsible for policing the use of the service, making sure that applications do not use more resources than they have requested. This will typically be implemented within the routers
once a service invocation has been accepted, the network must employ mechanisms that ensure that the packets within the flow receive the service that has been requested for that flow. This requires the use of scheduling mechanisms and queue management for flows within the routers
We examine each of the highlighted components.
The Internet Integrated Services architecture is described in [RFC1633].

## Slide 111: INTSERV
http://www.ietf.org/html.charters/intserv-charter.html
Requirements for Integrated Services based on IP
QoS service-levels:
  current service: best-effort
  controlled-load service (RFC2211)
  guaranteed service (RFC2212)
  other services possible (RFC2215, RFC2216)
Signalling protocol:
  RSVP (RFC2205, RFC2210)
Notes: It is possible to identify four specific technical issues that need to be addressed in the provision of Integrated Services for IP-based networks:
service-level: the nature of the commitment made, e.g. the INTSERV WG has defined guaranteed and controlled-load service-levels and a set of control parameters to describe traffic patterns
service interface: a set of parameters passed between the application and the network in order to invoke a particular QoS service-level, i.e. some sort of signalling protocol plus a set of parameter definitions
admission control: for establishing whether or not a service commitment can be honoured before allowing the flow to proceed
scheduling mechanisms within the network: the network must be able to handle packets in accordance with the QoS service requested
The INTSERV WG addresses only the first two of these issues. However, the INTSERV work does specify the requirements for any mechanisms used to address the last two issues, with some implementation hints. With the present IP service enumerated as best-effort, currently, two service-level specifications are defined:
controlled-load service [RFC2211]: the behaviour for a network element required to offer a service that approximates the QoS received from an unloaded, best-effort network
guaranteed service [RFC2212]: the behaviour for a network element required to deliver guaranteed throughput and delay for a flow
The INTSERV signalling protocol is called RSVP (Resource Reservation Set-up Protocol, [RFC2205] [RFC2210]).

## Slide 112: INTSERV service templates
Describe service semantics
Specifies how packets with a given service should be treated by network elements along the path
General set of parameters
  <service_name>.<parameter_name>
  both in the range [1, 254]
TSpec: allowed traffic pattern
RSpec: service request specification
Notes: INTSERV have produced a set of specifications for specific QoS service-levels based on a general network service specification template [RFC2216] and some general QoS parameters [RFC2215]. The template allows the definition of how network elements should treat traffic flows, i.e. the QoS granularity here is that of a single logical flow (or session in RSVP parlance).
The service template specifies describes the semantics of the services and specifies how packets should be treated as they pass through network elements that would like to implement the service, i.e. packet handling rules.
The genral parameters are identifed using two bytes, one identifying the service name (e.g. controlled-load) and one identifying the parameter.
The use of a service requires a TSpec (Traffic Specification) to specify the allowed traffic characteristics for a session. A RSpec (Resourse Specification) may also be used during reservation establishment for service specific parameters, but its use is service specific. The service definition includes information on how admission control is applied for the service and how the service is policed within the network (how non-conformant packets should be handled).
The controlled-load service requires a TSpec but no RSpec. For the guaranteed service,, as well as a TSpec, a RSpec should be specified (which will not be discussed here).
Note that this architecture requires that all the network elements along the path, as well as the applications, and applications have semantic knowledge about the service-levels for the application flows, as specified in the service templates.

## Slide 113: Some INTSERV definitions
Token bucket (rate, bucket-size):
  token bucket filter: total data sent  (rt + b)
Admission control:
  check before allowing a new reservation
Policing:
  check TSpec is adhered to
  packet handling may change if TSpec violated (e.g. degrade service-level, drop, mark, etc.)
Characterisation parameters: local and composed
Notes: A key element of the flow description is the TSpec that describes the (expected) traffic characteristics of he flow/session. The traffic characteristic is defined in terms of a token-bucket filter which, in general has the following elements:
r: the data rate (bytes/s)
b: the bucket size (bytes)
This specifies that the flow shall have sent no more than (rt + b) bytes of data at any time t.
This information (along with other, service specific information) may be used by the network for:
admission control: to check if the requested traffic profile and service can be currently be honoured along the intended network path
policing: to ensure that the application/user does not exceed the requested traffic specification and to take action (mark/drop packets, degrade the service-level for some packets) as appropriate
The INTSERV specification allows network elements to have local value for INTSERV parameters. When a path for a flow/session is selected the composed values for a parameter are the combination of the local values for the network elements along the path. For example, network elements A, B and C form a path for a flow or session. They have path latency values of 10ms, 12ms and 8ms respectively. The composed value for the (minimum) path latency will be (10+12+8)ms = 30ms. Different parameters have different composition rules which should be defined when the parameter for a service is defined.

## Slide 114: General INTSERV parameters
NON_IS_HOP (flag): no QoS support
NUMBER_OF_IS_HOPS: QoS-aware hop count
AVAILABLE_PATH_BANDWIDTH
MINIMUM_PATH_LATENCY
PATH_MTU
TOKEN_BUCKET_TSPEC:
  r (rate), b (bucket size), p (peak rate) m (minimum policed unit), M (maximum packet size)
Notes: The service template specifies and describes the semantics of the services and specifies how packets should be treated as they pass through network elements that would like to implement the service, i.e. packet handling rules. There is a general set of parameters specified and their values can be defined for each service level, as required. The general parameters include:
a flag to indicate that a network element is not INTSERV-aware
hop-count of INTSERV-aware network elements
available path bandwidth
minimum path latency
path MTU
traffic characteristic in terms of a token bucket specification (data rate, bucket size, peak rate), minimum packet size to be policed and maximum packet size allowed
The last of these parameters is used in the TSpec. A RSpec (Resource Specification) may also be used during reservation establishment for service specific parameters.
Other, service-specific parameters may be defined. Some of the paramters (for example AVAILABLE_PATH_BANDWIDTH and MINMUM_PATH_LATENCY) are carried in a special AdSpec data structure (see later) and are filled in by the routers along the network path to form composed values, which represent the values of those parameters for the path as a whole.

## Slide 115: Controlled-load service
Best-effort under unloaded conditions:
  probabilistic guarantee
Invocation parameters:
  TSpec: TOKEN_BUCKET_TSPEC
  RSpec: none
Admission control:
  Class-Based Queuing (CBQ), priority and best-effort
Policing:
  not defined (e.g. treat as best-effort)
Notes: The controlled-load service definition [RFC2211] specifies that network elements supporting this service should provide a service that is no worse than a best-effort service that would be seen at that network element under unloaded (lightly-loaded) conditions.
To invoke the service, the TSpec must be specified and a RSpec is not required.
It is suggested that Class-Based Queuing (CBQ) could be used to implement controlled-load service in network elements, e.g. with two classes of service, priority for the controlled-load packets and a separate class for normal best-effort packets.
Policing mechanisms are not specified/defined, but it is suggested that non-conformant packets should be degraded to best-effort.

## Slide 116: Guaranteed service [1]
Assured data rate with bounded-delay
  deterministic guarantee
  no guarantees on jitter
Invocation parameters:
  TSpec: TOKEN_BUCKET_TSPEC
  RSpec: R (rate), S (delay slack term, s)
Admission control:
  Weighted Fair Queuing (WFQ)
Policing:
  drop, degrade to best-effort, reshape (delay)
Notes: The guaranteed service definition [RFC2212] specifies the network elements should treat packets so that there is an assured data rate and all packets have a bounded overall delay. However, the service makes no commitment on jitter (packet inter-arrival delay).
The invocation of the service requires a TSpec and a RSpec. The RSpec contains two parameters, R a required service rate, and S a slack-term for the delay bound. R must be greater than or equal to r (the rate defined in the TSpec token-bucket). S must be non-negative. Defining a bigger value for R helps to decrease the overall path delay. Defining a bigger value for S makes it more likely that the reservation request will succeed, but may result in a larger end-to-end delay. R is used as a suggestion and larger values of S may require routers to use a value lower than R for the reservation. The exact use of R and S are given in [RFC2212].
The suggested admission control mechanism for this service is Weighted Fair Queuing (WFQ) where the weight assignments will be a function of the required rate, R.
The suggested policing function takes one of two forms. A simple policing function (the suggested default) is for non-conformant packets to be dropped or degraded to best-effort. A more complex policing function take the form of reshaping the flow/session by delaying packets so that they conform to the requested parameters.

## Slide 117: Guaranteed Service [2]
End-to-end delay bound:
  maximum delay
  based on fluid flow model
  fluid flow model needs error terms for IP packets
Error terms:
  each router holds C and D
C [B]: packet serialisation
D [s]: transmission through node
Composed values:
  CSUM and DSUM
Notes: With the Guaranteed Service, it is possible to evaluate the exact end-to-end delay bound from the TSpec and RSpec parameters. The equations above show how to evaluate the delay, using the TSpec and RSpec parameters discussed earlier. There are also two as well as two new values, CSUM and DSUM. The equations above are based on a fluid flow model, and CSUM and DSUM provide the error terms required to correct for the effect of IP packets being of a size that deviates from the fluid flow model. CSUM and DSUM are discovered using RSVP, and constructed from individual values of C and D held at routers. Full details are given in [RFC2212].
As well as upper bound on delay, we can compute a lower bound - this is simply the delay seen when there are no other packets - I.e. the term for peak rate allocation without the term n M.

## Slide 118: RSVP

## Slide 119: INTSERV: RSVP [1]
Provides signalling:
  user-to-network
  network-to-network
Traffic information – FlowSpec:
  TSpec
  sent through network
  AdSpec (optional)
Receiver confirms reservation:
  uni-directional reservation
Notes: RSVP is a signalling protocol that provides the service invocation interface for applications. The messages are sent between applications, but are acted upon and modified by the network elements en-route, so RSVP provides both user-to-network and network-to-network signalling. Special RSVP message carry TSpec and RSpec messages that are seen by (INTSERV aware) network elements along the network path as well as by the flow recipients.
The reservation request consists of a FlowSpec identifying the traffic characteristics and service-level required. One part of the FlowSpec is a TSpec, a description of the traffic characteristic required for the reservation. So it is possible for the same traffic characteristic to be used with different service levels. This difference in QoS service-level could, for example, act as a way for offering cost differentials on the use of a particular application or service.
RSVP can be used to set-up resource reservations for multicast as well as unicast flows. The reservations are unidirectional and in fact it is the receiving application that actually confirms the reservation, i.e. this is a receiver-oriented reservation protocol. The receiver may also be made aware of composed parameter values along the route if an (optional) AdSpec is present within the FlowSpec transmitted from the sender.
Note that RSVP is a general QoS signalling protocol specified in [RFC2205]. For use in a particular QoS architecture additional specification is required. In the case of INTSERV, the additional specification is provided in [RFC2210].

## Slide 120: INTSERV: RSVP [2]
Two-pass, with soft-state:
  sender: Path message
    NEs hold soft-state until Resv, PathTear or time-out
  receiver(s): Resv message - TSpec (+RSpec)
  sender: PathTear
  receiver(s): ResvTear
  soft-state refreshed using Path and Resv
Composed QoS params:
  AdSpec for path
S
A
B
Path
Resv
merge
point
Notes: To make a resource reservation, an appropriate FlowSpec is used along with session IP destination address, the protocol number in the IP packet and – optionally – the destination port number in the service invocation. The reservation procedure is as follows. The sender transmits a Path message advertising the session QoS requirements towards the destination IP address. All RSVP routers forwarding the Path message hold soft-state – information about the resource reservation required – until one of the following happens: a PathTear is sent from the sender cancelling the reservation, a Resv message is transmitted from a receiver effectively confirming the reservation, or the soft-state times-out. A Resv message from a receiver is sent back along the same route as the Path message, establishing the reservation and then the application starts sending data packets. Path and Resv messages are sent by the sender and receiver, respectively, during the lifetime of the session to refresh the soft-state and maintain the reservation. A PathTear or ResvTear message explicitly tears down the reservation and allows resources to be freed. It is possible for the reservation to be changed dynamically during the lifetime of the session. RSVP can be used for unicast or multicast sessions. (It is assumed that routes are symmetrical and relatively stable, but this is not always true in the wide area.)
As part of the Path message, an AdSpec data structure may also be sent in a one pass with advertising (OPWA) that allow network elements along the path to indicate to the receiver the composed (combined) QoS parameter values along the path based on local QoS capabilities at each network element. The local and composed capabilities are reported as QoS parameters for each service definition.
Where multicast communication is involved for the same flow, it is possible for a router to effectively merge two reservations instead of making two separate reservations.

## Slide 121: Reservation types and merging
FilterSpec: style of reservation
Fixed-filter (FF):
  FilterSpec required
  distinct sender reservation
  explicit sender selection
Wildcard-filter (WF):
  FilterSpec not required
  shared sender reservation
  wildcard sender selection
Shared-explicit (SE):
  FilterSpec required
  shared sender reservation
  explicit sender selection
Merging reservation info:
  merging allows aggregation of reservation information
  merging not possible across styles
  merging possible for reservations of the same style – use maximum
Notes: There are three reservation styles that are permitted with RSVP/INTSERV.
fixed-filter (FF) style: this style sets up a distinct reservation per sender that requires and specifies explicitly the set of sender who can make use of this reservation specification.
wildcard-filter (WF) style: allows a shared reservation for senders, but the senders are not explicitly specified.
shared explicit (SE) style: allows the reservation to be shared amongst an explicitly specified list of senders.
Information about the list of senders for FF and SE is carried in a FilterSpec data structure that forms part of the Resv message provided by the sender.
Its is possible for the RSVP routers to merge reservations of the same style. This is effectively to allow router to pass upstream a single reservation that is a maximum of the incoming reservations. This is specifically for multicast, where many flows for the same group are merged.
FF would typically be used for unicast communication only
WF would be used for an open conference, where the number of senders and who they will be is not known a priori. It would be expected that only one person would be speaking at a time, and perhaps the reservation would be enough for two speakers just in case two people did start to speak at once.
SE would be for a similar situation to WF but the conference would be closed, with the senders known before hand and listed in the FilterSpec.

## Slide 122: Reservations about reservations
Two-pass – one reservation may “block” another:
  PathErr and ResvErr
Need to hold a lot of soft-state for each receiver
Extra traffic due to soft-state refreshes
Heterogeneity limitations:
  same service-level
Router failure:
  QoS degrades to best-effort, need to re-negotiate QoS
Applications and routers need to be RSVP aware:
  legacy applications
Charging
Notes: We summarise the main problems with RSVP below:
1. Intuitively, we can see that in a network with limited resources, which are heavily utilised (e.g. the Internet), it is likely larger reservations are probably less likely to succeed that smaller reservations. During reservation establishment if the first pass of each of two separate reservation requests are sent through the same network element, where one request is a “super-set” of the other, the lesser one may be rejected (depending on the resources available), even if the greater one eventually fails to complete (of course it is possible to re-try).
2. If the first pass does succeed, the router must then hold a considerable amount of state for each receiver that wants to join the flow (e.g. in a multicast conference)
3. The routers must communicate with receivers to refresh soft-state, generating extra traffic, otherwise the reservation will time out
4. Complete heterogeneity is not supported, i.e. in a conference everyone must share the same service-level (e.g. guaranteed or controlled-load), though heterogeneity within the service-level is supported
5. If there are router failures along the path of the reservation, this results in IP route changes, so the RSVP reservation fails and the communication carries on at best-effort service, with the other routers still holding the original reservation until an explicit tear-down or the reservation times out or the reservation can be re-established along the new path
6. The applications must be made RSVP aware, which is a non-trivial goal to realise for the many current and legacy applications that already exist, including multimedia applications with QoS sensitive flows
Resource reservation could be expensive on router resources and adaptation capability is still required within the application to cope with reservation failures or lack of end-to-end resource reservation capability. Indeed, RSVP is now recommended for use only in restricted network environments [RFC2208].
Additionally, there is as yet no agreement as to how to charge for end-to-end QoS guarantees that span the networks of multiple administrations, e.g. across multiple ISPs.

## Slide 123: DIFFSERV

## Slide 124: DIFFSERV
http://www.ietf.org/html.charters/diffserv-charter.html
Differentiated services:
  tiered service-levels
  service model (RFC2475)
  simple packet markings (RFC2474)
Packets marked by network, not by application:
  will support legacy applications
Simpler to implement than INTSERV:
  can be introduced onto current networks
Notes: Concerns about resource reservation have directed the Internet community to consider alternatives; specifically differentiated services. In fact the IETF DIFFSERV WG was spawned directly from the INTSERV WG.
This is a relatively new IETF WG and most of the work within this group is currently at the stage of discussion and the formulation of a framework and architecture for the DIFFSERV work.
The IETF charter for the workgroup is:
http://www.ietf.org/html.charters/diffserv-charter.html
Two RFC documents have been produced. RFC2474 describes special values to be used for the IPv4 ToS field or IPv6 traffic-class field when DIFFSERV is in use. RFC2475 describes the DIFFSERV architecture.
DIFFSERV hopes to offer a relatively simple, coarse-grained QoS mechanism that can be deployed in networks without needing to change the operation of the end-system applications. The QoS mechanism is based around marking packets with a small-fixed bit-pattern, which maps to certain handling and forwarding criteria at each hop. The WG seeks to identify a common set of such per-hop handling behaviours as well as packet markings to identify these behaviours.
This is a much coarser granularity of service, but reflects a well understood service model used in other commercial areas. The DIFFSERV model is different to INTSERV. A key distinction of the DIFFSERV model is that it is geared to a business model of operation, based on administrative bounds, with services allocated to users or user groups.
The DIFFSERV mechanisms should be simpler to implement than INTSERV mechanisms and will allow some QoS control for legacy applications that are not QoS aware.

## Slide 125: Service Level Agreements
Not (necessarily) per-flow:
  aggregate treatment of packets from a “source”
Service classes:
  Premium (low delay) - EF (RFC2598)
  Assured (high data rate, low loss) - AF (RFC2597)
Service level agreement (SLA):
  service level specification (SLS)
  policy between user and provider - policing at ingress
  service provided by network (end-system unaware)
Notes: Whereas RSVP can act on a per-flow basis, the DIFFSERV classes may be used by many flows. Any packets within the same class must share resources with all other packets in that class, e.g. a particular organisation could request a Premium (low delay service provided using Expedited Forwarding) quality with an Assured (low loss, using Assured Forwarding with different drop precedence assignments) service-level for all their packets at a given data rate from their provider.
The exact nature of the packet handling will be based on a policy and Service Level Specification (SLS) that forms part of a Service Level Agreement (SLA) between user and provider. The policy could be applied to all the traffic from a single user (or user group), and could be set up when subscription to the service is requested, or on a configurable profile basis. The policy implemented by the SLA may include issues other than QoS that must be met, e.g. security, time-of-day constraints, etc.
The DIFFSERV mechanisms would typically be implemented within the network itself, without requiring runtime interaction from the end-system or the user, so are particularly attractive as a means of setting up tiered services, each with a different price to the customer.

## Slide 126: Scope of DIFFSERV
IP host
IP router
Internet
INTSERV
DIFFSERV
customer premises
network
customer premises
network
Notes: The DIFFSERV-capable routers could be at the edge of the customer network or part of the provider’s network. If the DIFFSERV-marking is performed within the customer network, then policing is required at the ingress router at the provider network in order to ensure that customer does not try to use more resources than allowed by the SLA.
The INTSERV mechanism seeks to introduce well-defined, end-to-end, per-flow QoS guarantees by use of a sophisticated signalling procedure. The DIFFSERV work seeks to provide a “virtual pipe” with given properties in which the user may require adaptation capability or further traffic control if there are multiple flows competing for the same “virtual pipe” capacity.
Additionally, the DIFFSERV architecture means that different instances of the same application throughout the Internet could receive different QoS, as different users may have different SLAs with their subscriber. So the application needs to be dynamically adaptable.

## Slide 127: DIFFSERV classification
Packet marking:
  IPv4 ToS byte or IPv6 traffic-class byte
  DS byte
Traffic classifiers:
  multi-field (MF): DS byte + other header fields
  behaviour aggregate (BA): DS field only
  DS codepoint: values for the DS byte
Aggregate per-hop behaviour (PHB):
  aggregate treatment within network
Notes: The DIFFSERV work is aimed at providing a way of setting up QoS using policy statements that form part of a service level agreement between service user and service provider. The policy may use several packet header fields to classify the packet, but the classification marking can also be a simple identifier – currently a single byte, the DS (differentiated services) byte – within the packet header. The DS (differentiated services) byte will be used in place of the ToS (Type of Service) field in IPv4 packets or the traffic-class field in IPv6 packets. The DS byte will have the same syntax and semantics in both IPv4 and IPv6. There are likely to be some global values – DS codepoints – agreed for the DS field within the IETF but the intention is that the exact policy governing the interpretation of the DS codepoints and the handling of the packets is subject to some locally agreed SLA. SLAs could exist between customer and Internet Service Provider (ISP) as well as between ISPs. The DS codepoints are used to identify packets that should have the same aggregate per-hop behaviour (PHB) with respect to how they are treated by individual network elements within the network. The PHB definitions and the DS codepoints used may differ between ISPs, so there will be need for translation mechanisms between ISPs.
A traffic classifier selects packets based either on the on DS codepoint or on some (policy-based) combination header fields from the packet header and directs them to an appropriate traffic conditioner. When the DS codepoint is used to classify traffic, the classifier is called a Behaviour Aggregate (BA) classifier. When other packet header fields are used we have a Multi-Field (MF) classifier. And MF classifier may use information such as the port numbers, IP addresses protocol types, as well as the DS byte to make classification decisions.
Although there will be scope for changes to the SLA by agreement between customer and provider, the kind of dynamic, flexible, host-to-host resource reservation that is possible with the INTSERV model using RSVP is not envisaged for DIFFSERV.

## Slide 128: DIFFSERV PHBs
Specify rate/delay in SLS
Expedited Forwarding (EF) (RFC2598):
  virtual leased line (VLL) service
  data rate specified in SLS
  low delay, low jitter, low loss
Assured Forwarding (AF) (RFC2597):
  4 classes (1-4)
  3 levels of drop precedence per class (1-3)
  AF11 - “best”, AF43 - “worst”
Notes: Recently (June 1999), the DIFFSERV WG have defined two PHBs, both of which are proposed standards. Both require that the SLS contain information such as delay, data rates (e.g. token bucket filters), and the scope over which the SLS applies (e.g. between ingress and all end-points, between ingress and specific end-points, etc.), as well as actions to take if the traffic is found to be violating the SLS.
The Expedited Forwarding (EF) PHB is used to provide a low loss, low delay, low jitter end-to-end service across DS domains. The service if provides is likened to that of a virtual leased line (VLL). Suggested implementation mechanisms include weighted round robin scheduling and class based queuing (CBQ). If simple priority queuing is used (the EF queue is always serviced before any other traffic) then the implementation must ensure that other traffic is not locked out (e.g. by using rate limiting via a token bucket filter). Violating traffic can be dropped. A single DS codepoint is defined for EF.
The Assured Forwarding (AF) PHB will allow a DS domain to provide different levels of assurance for forwarding of IP packets. Currently, 4 AF classes are defined with 3 drop precedence levels in each. An AF class mark is indicated by the lexeme AFcd where c is the AF class and d is the drop precedence within that class. An example usage is that each class represents a higher level of service (e.g. 1= platinum, 2=gold, 3=silver, 4=bronze), with low, medium and high (1, 2, 3 respectively) drop precedence levels in each class. So, AF11 would be the “best” AF mark and AF43 the “worst”. Implementation might be using weighted queuing/scheduling with violating traffic being dropped or re-marked to lower classes, higher drop precedence or best effort.

## Slide 129: DIFFSERV traffic conditioning
Traffic conditioners:
  meter
  marker
  shaper/dropper
Metering of traffic:
  in-profile
  out-of profile
Re-marking:
  new DS codepoint
Shape/drop packets
meter
marker
dropper/shaper
traffic conditioners
packet
classifier
meter
marker
dropper/shaper
packets
control information
Notes: A DS domain contains DS boundary nodes at its edge and DS interior nodes within the domain. DS boundary nodes act as traffic conditioners. Traffic conditioners implement the Traffic Conditioning Agreement (TCA) part of a SLA. A schematic diagram showing how streams are treated is shown in .
Part of the SLA is the definition of a traffic profile for a packet stream. This may, for example, be specified as a token bucket, limiting the way that packets are transmitted into the DS domain. When packets in a stream from a user exceed the negotiated traffic profile, they are said to be out-of-profile, else packets are in-profile.
After passing through a classifier, information about the packet is passed to a meter that provides control information to other parts of the conditioner. This information includes whether or not the packet is in-profile or out-of-profile. Within the conditioner, the packets follow a path through a marking function and a policing function:
marker: may change the DS codepoint of the packet – re-mark the packet
shaper: delays out-of-profile packets in order to enforce the traffic profile for a stream
dropper: drops out-of-profile packets in order to enforce the traffic profile for a stream
Note that a dropper can be implemented by using a shaper with the buffering reduced to zero packets (or a few packets).
DS interior nodes may perform limited BA traffic conditioning, but the intention is that the main traffic conditioning function is performed at the edges of DS domain (as the DS boundary nodes), close to where the packets enter the domain.

## Slide 130: DIFFSERV service invocation
At subscription:
  per user/user-group/site/customer
  multi-field, policy-based
Within organisation:
  per application/user/user-group
  use ad hoc tools or network management system
  behaviour aggregate or multi-field possible
Dynamically using RSVP: IETF work in progress
Notes: It is intended that the DIFFSERV work will offer a subscription-time mechanism for defining coarse-grained QoS requirements for an organisation. The exact nature of the service level agreement will be left as a matter of negotiation between user and provider. However, DIFFSERV offers an architecture and definitions that will allow an SLA to be defined. The policy for controlling traffic could be based on applications, individual users or user-groups.
It may even be possible to have control of traffic within an organisation, providing the network elements can be persuaded to be DIFFSERV aware. The network elements could be configured, for example, to control the amount of traffic form a particular application appearing on certain segments of the network, e.g. off-site WWW traffic.
It may even be possible to control or invoke SLAs more dynamically using RSVP (with suitable additional specifications) but this is currently work in progress.

## Slide 131: Problems with DIFFSERV
No standard for SLAs:
  same DS codepoints could be used for different services by different providers
  different providers using the same PHBs may have different behaviour
  need edge-to-edge semantics
Lack of symmetry:
  protocols such as TCP (ideally) require symmetric QoS
Multicast:
  support for multi-party, symmetric communication
Notes: DIFFSERV is not without its own problems, however.
Firstly, there is a problem with service definitions. Only DS-codepoints have been defined, and not end-to-end semantics (though two standard track PHB documents do exit). This means that it will be possible for service providers to implement different services using the same DS codepoints. So, provider must co-operate and ensure that mappings between DS codepoints at network boundaries results in semantically correct service translation as packets go from one network to another.
For the current standard-track PHB documents, it is possible that different provider may implement different behaviour across their networks for the same DS codepoints, though this is likely to be more so with AF than with EF. Edge-to-edge semantics are required, so that network boundaries can still be honoured but handling of packets is consistent.
Secondly, note that the SLA/SLS is between a user and their service provider. If that user accesses a server which is connected using a link that has a different, perhaps “worse”, SLA/SLS with its provider then our user would not see the service they expect when paying for the “better” service. This is because the return traffic from the server is treated differently – worse – than the initial request to the server. So, for whizzy web-browsing you need to ensure that the server site has a “good” SLA/SLS as well as getting a “good” SLA/SLS yourself. This lack of symmetry in DIFFSERV connectivity would affect protocols such as TCP which rely on a a two way exchange for reliability.
There is also the issue of support for multicast. DIFFSERV is not as dynamic invocation of services as is INTSERV/RSVP. DIFFSERV, at least currently, I based on the notion of a subscription. Work is in progress to allow dynamic establishment of SLAs/SLS using RSVP. However, many end-to-edn signalling issues remain unresolved.

## Slide 132: INTSERV and DIFFSERV [1]
Complimentary:
  DIFFSERV: aggregate, per customer/user/user-group/application
  INTSERV: per flow
For example:
  INTSERV reservations within DIFFSERV flows
DIFFSERV class identified by DS codepoint
individual application flows
using INTSERV
Notes: The big gain with DIFFSERV is that the end-to-end signalling and the maintenance of per-flow soft-state within the routers that is required with RSVP is no longer required. This makes DIFFSERV easier to deploy and more scaleable than using RSVP and INTSERV services. However, this does not mean that INTSERV and DIFFSERV services are mutually exclusive. Indeed, it is likely that DIFFSERV SLAs will be set-up between customer and provider for general use, and then RSVP-based per-flow reservations may be used for certain applications as required, e.g. for instance an important video conference within an organisation.

## Slide 133: INTSERV and DIFFSERV [2]

## Slide 134: RTP

## Slide 135: UDP
Connectionless, unreliable, unordered, datagram service
No error control
No flow control
No congestion control
Port numbers
Must be used for real-time data:
  TCP automatic congestion control and flow control behaviour is unsuitable
0
8
16
24
(31)
data
source port
destination port
length
checksum
Notes: UDP provides an unreliable, connectionless datagram service. It does not guarantee delivery or ordering, and individual packets may be duplicated within the network. Exactly how “unreliable” the service is depends very much on the network environment. In a lightly loaded LAN, it is unlikely that you will observe much packet loss. Across a wide area backbone, however, there may be significant packet loss, especially over paths involving large numbers of routers or heavily loaded routes.
UDP is very simple to implement, and this is reflected in the packet header for UDP. The port number work in a similar way to those for TCP, identifying a local UDP end-point.

## Slide 136: RTP
RFC1889: general message format
  specific formats for media types in other RFCs
Carried in UDP packets:
  application must implement reliability (if required)
  supports multicast and point-to-point
RTCP - Real Time Control Protocol:
  application-level information (simple signalling)
RTP and RTCP provide no QoS guarantees:
  QoS mechanisms are separate
Notes: The Real time Transport Protocol (RTP) is an Internet Proposed Standard and is widely used for multimedia applications (including voice and video) within the Internet community. Its use as the underlying transport mechanism for packetised voice and video is specified in H.323.
RTP carries “time-slices” of audio and video flows in UDP packets, with synchronisation information and application-specific identifiers, QoS parameter information and user information. RTP itself is a general mechanism and the are specific RTP usage profiles available for different media types, each described in their own RFC document, e.g.
RFC2032 for H.261
RFC2038 for MPEG1 and MPEG2
RFC2190 for H.263
RFC2198 for redundant (fault tolerant) audio
and many others. RTP is designed to support multicast and unicast communication.
RTP has an associated with it a simple application-level signalling protocol, the Real Time Control Protocol (RTCP) that allows application using RTP to pass resource usage information, flow QoS parameters and other information between senders and receivers.
RTP and RTCP themselves do not provide QoS control or resources reservation - they are protocols that enable the transport of real-time media flows.

## Slide 137: RTP header information
SSRC = mixer
CSRC1 = s1
CSRC2 = s2
CSRC3 = s3
SSRC = s1
SSRC = s2
SSRC = s3
s1
s2
s3
mixer
SSRC = s1
s1
SSRC = s1
translator
V 2-bits, version number (=2)
P 1-bit, indicates padding
X 1-bit, indicates extension header present
CC 4-bits, number of CSRCs (CSRC count)
M 1-bit, profile specific marker (defined elsewhere)
PT 7-bits, payload type, profile specific (defined elsewhere)
SSRC synchronisation source
CSRC contributing source
timestamp has profile/flow-specific units
V
P
X
M
31
16
0
added
by mixer
CC
SSRC
PT
sequence number
CSRC
timestamp
IP header
UDP header
RTP header
app. data
Notes: RFC1889, the RTP specification, defines some general header information that is used by all RTP applications.
All RTP packets carry a sequence number to allow detection of loss and misordering at the receiver.
There is an application-specific timestamp indicates where in the flow this packet should be with respect to the rest of the flow. This allows synchronisation of the flow playback at the receiver, and also allows packets to be disregarded if they are delayed beyond the point that they have far exceeded their playout time.
RTP uses unique identifiers - SSRC (synchronisation source) and CSRC (contributing source) to identify originators of flows within and RTP session. Any IP address, SSRC pair must be unique so that multiple flows from the same host can be distinguished. The SSRC is randomly generated.
An end-station will generate an SSRC to be carried in the RTP header. The packets in a flow may pass through a translator or a mixer. When passing through a translator, the flow may be altered, e.g. transcoded, but this is transparent to the receiver. When a flow passes through a mixer, the mixer may decide to merge and/or translate flows. When flows are merged (mixed) the mixer identifies itself as the SSRC, but also identifies the original sources of the mixed flows by putting their respective SSRC IDs into the CSRC list of the packet header. (A maximum of 15 flows can be mixed.)
Media specific header extensions are defined in the relevant RFC documents.

## Slide 138: RTCP - Real time Control Protocol
Provides feedback to senders/receivers
QoS info for flow:
  packet info: loss, delay, jitter
  end-system info: user info
  application-specific or flow-specific info
RTCP message types:
  RR and SR: Receiver Report and Sender Report
  SDES: Source DEScription
  BYE: leave a RTP session
  APP: application-specific
Notes: RTCP provides simple information about the flow. Reports are sent by senders and receivers. The RTCP messages defined in RFC1889 carry information about the loss, delay and jitter for a flow, as well as some end-system user information. Additionally, application-specific information is defined for particular media-flows in he relevant RFC documents.
The generation of control message is controlled by an algorithm that seeks to limit the amount of RTCP traffic to around 5% the available network capacity.

## Slide 139: SR and RR messages
V
P
31
16
0
RC
NTP timestamp, hi-word
PT=SR
length
NTP timestamp, lo-word
SSRC of sender
RTP timestamp
sender’s packet count
sender’s octet count
cum. no. of pkts lost
ext. highest seq. n. recv’d
inter-arrival jitter
frac. lost
SSRC1 (SSRC of source 1)
last SR NTP timestamp (part)
delay since last SR
multiple instances
of this report block
possible in a single
report
V
P
31
16
0
RC
PT=RR
length
SSRC of sender
cum. no. of pkts lost
ext. highest seq. n. recv’d
inter-arrival jitter
frac. lost
SSRC1 (SSRC of source 1)
last SR NTP timestamp (part)
delay since last SR
Notes: The Receiver Report and Sender Report are used to convey information about the flow throughout the lifetime of the flow.
The SSRC is used to identify the sender of the RR/SR and then the rest of the message consists of Report Blocks. Each report block identifies the source using an SSRC and the gives the following information for each:
fraction of lost packets for the flow
cumulative number of lost packets
the last received sequence number, and also the number of times the sequence number has cycled (wrapped)
estimate of the variance of inter-packet arrival time
part of the last NTP timestamp sent in the SR as received by this SSRC
the delay since the last SR was received
The SR also has:
NTP timestamp
RTP timestamp (flow-specific)
sender’s packet count
sender’s octet count
This information allows the applications to evaluate the QoS being received by particular flows from particular senders. This may allow the application to co-ordinate adjustments to the flow based on the QoS information.
NTP is the Network Time Protocol. The RTP timestamp provides application/flow specific timing information whilst the NTP timestamp provides a measure of global time.
Both the RR and SR can be extended with profile specific information.

## Slide 140: SDES
Source DEScription: all ASCII strings
Information types from RFC1889:
  CNAME: canonical identifier (mandatory)
  NAME: name of user
  EMAIL: address user
  PHONE: number for user
  LOC: location of user, application specific
  TOOL: name of application/tool
  NOTE: transient messages from user
  PRIV: application-specific/experimental use
Notes: SDES message are simple ASCII strings that contain information that is typically application-specific. RFC1889 defines 8 types that can be carried in the SDES message, most of which will have application-specific values:
CNAME: this is the only mandatory type and is used to uniquely identify a participant in a conference. It is normally generated automatically by the application and usually takes the form: user@host (or just host on single user systems), e.g. saleem@darhu.cs.ucl.ac.uk
NAME: the real name of the user (or any other identifying string, e.g. nickname, etc.)
EMAIL: RFC822 e-mail address of the user, e.g. s.bhatti@cs.ucl.ac.uk (this value could also be used for CNAME)
PHONE: international format phone number, e.g. “+44 20 7679 3249”
LOC: physical location of the user (application-specific detail required here)
TOOL: identifies the name of the application/tool e.g. “blob-talk audio tool v42”
NOTE: for transient message from the user, e.g. “out to lunch”
PRIV: to allow application-specific SDES contents and for experimental use

## Slide 141: BYE and APP
BYE - leave RTP session:
  SSRC (or SSRC and CSRC list if mixer)
  reason for leaving
APP - application-specific packets:
  SSRC (or SSRC and CSRC list if mixer)
  ASCII string for name of element
  application-specific data
Notes: The BYE message allows end-points to signal that they are leaving a session. The packet can contain a SSRC if sent by a single system or an SSRC and CSRC list if sent by a mixer. Optionally, a string giving the reason for leaving may be included.
If a mixer receives a BYE message, it should forward it unchanged. If the mixer itself shuts down, then it should send a BYE message with itself as the SSRC and CSRC for all its contributing sources.
The APP message is a mechanism that can be used for application specific messages. This mechanism is also intended for use in development and testing of a new media flow or application before making specific RTP/RTCP modifications that may be documented a separate RFC.

## Slide 142: Application-level signalling

## Slide 143: User-to-network
Telco network:
  common channel signalling (CCS)
  separate data path and signalling path
  equipment designed to handle data and signalling separate
IP:
  RSVP carried in IP packets along data path
  scaling issues (RFC2208)
  need aggregated signalling towards the core (use INTSERV with DIFFSERV?)
Notes: Telco networks use common channel signalling (CCS), which provides physically separate channels for signalling. Telco equipment is designed to have separate data paths and signalling paths. Signalling also allows the switching of channels to be aggregated. IP has none of these facilities, and these of signalling is relatively new to the IP world. While level-4 protocols such as TCP do have handshaking, and there are application-specific session information exchanges, these are all carried as IP packets along the same path that will eventually carry the data. This means that routers must look for signalling packets as they handle data, a function that slows down the processing of data packets. Also, signalling such as RSVP can not be aggregated in the same way as can telco signalling. Indeed we have already seen that [RFC2208] points out the scaling limitations of RSVP, as used in its current form. Perhaps the solution would be to use RSVP as an edge-system mechanism, and map flows into DIFFSERV pipes, e.g. map Guaranteed service-level request to EF PHB pipes, and Controlled-load service level to AF11 PHB pipes.

## Slide 144: User-to-user signalling
Call/session set-up
Capabilities exchange
Directory services
PBX-like facilities
Application-level signalling supported by network
MMUSIC IETF WG:
  application architecture
  SDP
  SIP
H.323:
  umbrella document for existing standards
  uses ITU and IETF standards
  currently more mature than MMUSIC work
  wide support available (e.g. Microsoft NetMeeting)
  IMTC: www.imtc.org
Notes: There is also a need for application-specific signalling in establishing multimedia sessions. The kind of information that is required is typically configuration and control information to allow a session to take place, e.g. multicast address, time and duration of session, audio and video profile to use, etc. Additional signalling mechanisms can be envisaged that allow capabilities negotiation (allowing terminals to establish negotiate use of various audio and video codecs), and directory services allowing location of users to be determined. Also, there is the desire to build in more traditional PBX-like functions into the software environment, such as call forwarding, call waiting etc. While this is application-level signalling, the transmission of the this signalling information may need to be supported by service providers for Internet-wide use, but of course as with telco PBXs, virtual private networks (VPNs) are possible.
Within the Internet community, the Multi-party Multimedia Session Control (MMUSIC) workgroup of the IETF is defining an architecture for multimedia applications as well as protocols for describing sessions (Session Description Protocol – SDP) and initiating calls or session (Session Initiation Protocol – SIP). SIP supports functions such as call waiting, call forwarding etc. SIP is designed to be very compatible with HTTP and other existing Internet standards.
The ITU world has documented a similar infrastructure in the Recommendation H.323. This umbrella document from the ITU describes how existing ITU and Internet protocols can be used together to offer build multimedia terminal equipment as well as control infrastructure such as Gatekeepers for call control, multi-point control units (MCUs) for conferencing as well as resource control. The H.323. work is more mature than the MMUSIC work, with H.323v1 (1996) and H.323.v2 (1998) now fairly widely accepted and implemented. More information about H.323 and related standards can be found at the WWW site of the Internet Multimedia Technical Consortium (IMTC) which is an industry forum promoting the use of H.323 and related standards.

## Slide 145: Summary
Need QoS mechanisms for IP
Per flow:
  INTSERV
  RSVP
  does not scale well, hard to provision
Customer/provider services:
  DIFFSERV
  still maturing
Support for application: RTP and signalling

## Slide 146: Miscellania: objectives
Broader Considerations for real-time applications:
  Systems Questions:
    Scaling & Stability
    Mobility
    Management
Non-technical Questions
  economic and user aspects
    Pricing and Provisioning
  implementation context:
    Active Networks
    MPLS/”Circuits”
Notes: The Internet is a complex machine - probably now the most complex machine that human’s have built to date, now that it has outgrown the telephone network in capacity and complexity. A number of things are impacted when we try to make the Internet service at the network layer more rich. Firstly, we have to consider the impact on scaling of any such a refinement. The Internet scales well - this is evidenced by the fact that it is growing at roughly 100% per annum in terms of numbers of end systems, numbers of end to end services, and raw backbone capacity to accommodate all of this. This ability to scale is all due to the decentralized nature of the control systems for the network (naming, addressing, routing, caching), and the lack of more than very simple peering rules between user and provider, and between access and core, and core and core network service provider.
Adding QoS will affect this scaling. Similarly, the Internet is relatively stable - the protocols in use have been subject to some refinements over the past 15 years which have included factoring in control theoretic results to improve stability.
The facilities used to access the Internet are evolving even more rapidly right now than the services, and mobile access is one area that most pundits expect to see massive growth over the next 5 years - to date there are some 250M Internet users, and some 250M mobile phone users -the demographics of these groups are quite similar - there’s certainly a massive overlap - wireless link technology brings interesting problems for basic IP performance (well, for TCP and RTP anyhow) without having to start worrying about QoS.
Payment is always a thorny question - the Internet appears to make economic sense, although the models for funding the infrastructure continually evolve. Service discrimination will require more complex payment options.

## Slide 147: Scaling and Stability
References
Vern Paxson, End-to-end Routing Behavior in the Internet
ACM CCR, vol. 26, no. 4, pp. 25-38, Oct. 1996.
http://www.acm.org/sigcomm/ccr/archive/1996/conf/paxson.html
Floyd, S., and Jacobson, V.,
The Synchronization of Periodic Routing Messages
IEEE/ACM ToN, V.2 N.2, p. 122-136, April 1994.
href="http://www.aciri.org/floyd/papers/sync_94.ps.Z
~
Notes: The first part of the net subject to control to avoid instability was the end-to-end protocol area. TCP uses a congestion avoidance and control strategy that is now part of general requirements from many ISPs for baseline source behaviour in the best effort arena. Other protocols (e.g. reliable multicast transport, and even some rate adaptive audio and video sources, e.g. from Real Networks) now follow this design goal. Given careful implementation, this leads to a network sharing model that approximates to weighted fair share on a single ISP service.
The routing systems are also dynamic, and as such could under high event loads potentially become unstable - this would be exactly when least wanted (e.g. when there are correlated outages) - work has been done to try to understand stabilising this part of the network control system too..

## Slide 148: Scaling (or Complexity) - 1
All mechanisms that we add to IP Have some cost - we would like ideally, this cost to be O(C) (Order constant) - I.e. if we add QoS, the cost in terms of messages, router and end system memory, router and end system CPU should just be a constant, ideally! In practice though…
Its likely that some mechanisms will be O(n), where n is the number of…
end systems or routers - or can we do better?
Diff-serve versus Int-serve is based around this...
Notes: Many Internet papers and articles use the term “scalable” when describing a protocol or a part of the architecture.
What they actually mean is that this component makes sense economically in terms of its computational complexity with regard to related inter-dependant components. For example,
the capacity of the backbone scales as linear or better in the number of end systems, and the routing table in the Internet as it currently operates scales with the number of end systems, n, as better than ln(n) - this means that as we add end systems and gain revenue, we can afford to deploy more capacity, and the routers’ memory in the core do not need continually upgrading at more than this rate. Address aggregation means that routing updates do not grow rapidly either.
If we add new services in the IP layer, how will they affect this scaling?

## Slide 149: Scaling (or Complexity) - 2
So per flow-queues are at least going to have a data structure in a router per active pair (tree) of sender/receiver(s)
Whereas per class queues have some data structure per class although edge systems may have to do per source policing and/or shaping - which implies that overall, we may have O(ln(n))
Need tostate overall architecture to see overall system costs!
Notes: Current routing tables reflect the address hierarchy and to some extent nowadays due to address allocation policies , topological hierarchy (at least in some providers).
Flow based forwarding may require state in the routers for packet scheduling that grows beyond this rate depending on the approach.
Integrated services can be naively implemented with per source/destination state - this would mean for example on the UK-US academic link (2 OC3 links, operating at 300Mbps), some 4000 entries at the busy hour (assuming that the number of flows requiring QoS was the same as the number of TCP Flows currently seen there). This is not necessarily difficult to implement, but would require quite fast memor for per packet lookup, and would be required on all routers on any Int-serv capable path.
Diff-serve might more easily be implemented with priority queues (at least for low utilisation of higher priority levels) in the core routers, although edge devices would need more per-flow specific state - however, edge devices would also handle far less flows- so while overall across an entire ISP, the state might grow, the additional memory per router is potentially a lot less.
Of course, if accounting is needed per flow (for billing, or for trend analysis and provisioning), then we may be back to the same position as int-serve.

## Slide 150: Stability - 1
Ideally, Traffic, whether user or management (e.g. signaling, routing updates etc) should be stable.
Conditions for stability complex - basically need to do control theoretic analaysis
Even if oscillatory, should converge or be bounded, not diverge….
Reasons for instability or divergence:
  Positive Feedback
  Correlation/phase effects...
Notes: Oscillation is not necessarily a bad thing (maybe ought to see if John Harrison said anything about this:-)
However, in networks, traffic that oscillates (e.g. alternates routers, alternates between low and high rate) causes knock-on effects - for example to accommodate a delay, we would need to provision for the higher rate (on multiple links). Oscillations tend to synchronise - this may lead to divergence of load, in which case we will get a service failure.

## Slide 151: Stability - 2
End-to-end congestion control systems are designed to be stable - damped feedback
Routing systems are designed to be stable -randomized timers
QoS systems (especially call admision and QoS routing) need to be stable too.
Needs careful thought and smart engineering…
e.g. don’t want to do alternate path routing and admission control on same timescales.
Notes: So schemes are put in place to damp out oscillations
avoid positive feedback
damp delayed feedback
randomize timers to remove phase locking
etc etc
As the system gets larger, higher level synchronisation effects become possible - e.g. web page announcement on bulletin board or TV or radio program causes a number of users to direct browsers towards the same server in a loosely synchronised fashion familiar in telephone networks as the flash-call or mothers day (or 11.59:31/12/1999) problem.

## Slide 152: Mobility
Reference:
  Anup Kumar Talukdar, B. R. Badrinath and Arup Acharya, "Integratedservices packet networks with mobile hosts: architecture and performance",Wireless Networks, vol. 5, no. 2, 1999
  Jarkko Sevanto, Mika Liljeberg, and Kimmo Raatikainen, "Introducingquality-of-service and traffic classes into wireless mobile networks",Proceedings of first ACM international workshop on Wireless mobile multimedia, October 25-30, 1998, Dallas, TX USA
Links…
Patterns…
Resources...
Notes: Two common wireless networks:
wavelan - wireless ethernet
GSM/GPRS - mobile telephones
Both offer IP. Neither offers IP QoS yet. Problem is that they are shared media - the appropriate solutions are link level combined with IP level.

## Slide 153: Mobile 1 - Wireless Links
Wireless links can have variable characteristics, e.g. delay, throughput, loss
Offering hard QoS is hard
GPRS and other wireless links offer shared media
May be able to coordinate QoS via shared media MAC layer management and handoff management (see ISSLL work in IETF) - requires cooperation
Opposite of trend on fixed nets (e.g. shared media LANs moving to switched approaches!)
Notes: IETF has working group called
Integrated Services over Specific Link Layers
working on how to map QoS from IP level services onto link layers.
In the point to point case it is fairly simple and works well at the pure IP level provided there is no link layer multiplexing of other services in an unknown way. On shared media links, it is less simple, and depends on adding facilities to the MAC layer. In the IEEE 802 committee there are working groups doing this for int-serve like QoS (q) and diff-serve type Class of Service (p).
For wavelan the appropriate solution may be the Subnet Bandwidth Manager
For GSM, the IP level sees a fixed telephony link so there is no special problem (apart from those associated with low speed links) but for GPRS the problem is complex, and handover makes life even harder

## Slide 154: Mobile 2 - Patterns
Mobile access patterns may be quite different from fixed ones
Simply don’t know yet, but may entail lots more state refresh (e.g. re-sending RSVP path/resv triggered by moves)
Mobiel multicast with source or sink moving may be complex (involve re-building tree)
Notes: Building predictable QoS is not just a matter of implementing the signalling, call admission and scheduling - the user doesn’t want to be told “no” too often! So we need to provision the network - this relies on some idea of the traffic pattern and its dynamics. Unfortunately, we have practically no idea of what this will look like for mobile, wireless IP ! However, since a large amount of wireless access will be confined to access networks (whether wireless ethernet or wireless telephony) it is likely that initially, we will not have to deal with the wireless end-to-end QoS problem in the Internet.

## Slide 155: Mobile 3 - Resources
Some QoS approaches are based on the netwrk running largely underloaded
e.g. EF and AF may only work for IP telephony if it constitutes a small part of traffic
This is not the case on many wireless links today.
Need to look at hard QoS schemes - particularly for low latency (e.g. interactive voice/games) - even down to the level of limited frame/packet sizes - leads to interleave problems...
Notes: Wireless links are generally slower than their fixed counterparts due to physics- in the extreme this means that there is no choice - capacity is a genuine scarce resource.
The first place that this impacts is on packet headers and packet sizes and their effect on delay - at 10Kbps, a 40 byte header (TCP/IP or RTP/UDP/IP) is a serious liability. Luckily, this problem has been tackled, at least partly, already on low bandwidth fixed network links of the past, by applying hop-by-hop header compression. Typically, this reduces the header size by just over 1 order of magnitude, down to around 3 octets, at the cost of some state in the routers at each end of a wireless hop. The state is soft (I.e. if the route changes or the state is otherwise lost, it is recovered at some delay cost, on the next packet exchange.
Some approximations to QoS work by assuming that a link runs very underloaded, clearly these will not work well in many wireless domains.

## Slide 156: Management
All this needs managing by someone, at the very least the policies need configuration…..

## Slide 157: Management-1
User account management
QoS auditing
MIBs for queues, signalling protocols, etc
risk analysis and trend prediction tools
security (authentication and privacy aspects of payment for qos - see next)
Notes: Each new QoS component needs a management information base. This adds cost to the network management systems.The inter-relationship of some management information is also stressed by adding QoS - for example, one would like to relate usage to topology, and call rejections to network faults and errors.

## Slide 158: Pricing and Provisioning
Reference: http://www.statslab.cam.ac.uk/~richard/PRICE
Notes: It is often said that the Internet needs pricing. This is clearly a rather naïve statement - the Internet is priced - typcially users pay commercial ISPs for access per month at the rate appropriate to their access link. The traditional model then has been a flat lease fee for the right to access anywhere in the Internet, only limited at the ISP ingress by the speed of ones access line. Of course, traffic conditions and server performance would also cause ones “mileage to vary”.
Recently (particularly in the UK with massive de-regulation of the telecommunications industry), a number of ISPs have emerged who have been referred to as “free”. This is again rather a misnomer - there are two main ways that such ISPs have raised revenue:
1. For dial up users, some ISPs get a fraction of the telephone call charge - this is part of normal inter-LATA arrangements n some countries, particularly where local calls are not free, this is a very effective partnership between ISP and local telephony company since the access phone company gets more calls for IP access (and therefore more revenue) and the ISP gets to avoid having to build a billing system. It does usually require call-line-identification to match the $$$ to the account.
2. The server side pays - typically gaining revenue from advertising - this model mimics commercial television and suits highly commercial content providers.

## Slide 159: Pricing 1
If you don’t charge for QoS, won’t everyone just ask for first-class?
What are the users paying for?
What are they prepared to pay?
If you do charge, how to stop arbitrage (rich buy all the bandwidth and then re-sell at different price).
Notes: Costs:
Capacity is non linear priced in line rate, distance, and time!
Routers are non-linear priced in CPUI, Memory, Line Cards, performance (over time too)
Access network has been slowest to change (either academic LAN + router based, or domestic/small office, dial-up based) - this has been stabilised in price by the near monopolies -its now changing due to use of other technologies like fast wireless, DSL replacement of dumb modems, and cable modem use over terrestrial TV network plant. The cost of these networks is lower than the original phone net, and offers instead of a maximimum of 56kbps, somewhere in the range 10kbps (GSM) to 20Mbps (VDSL).
We live in “interesting times”

## Slide 160: Pricing 2
Typically, access fee can cover actual cost of infrastructure
Bill is often just an incentive scheme (to stop users hogging capacity in a class)
Parameters:
  time of day and duration
  distance (geographic, provider hops, AS-count?)
  capacity
  delay (iff possible) and jitter control
  Loss (possibly)
Notes: Bills for QoS are rarely to pay for actual costs. Typically they are used as part of marketing and control, at least in much of the economics of networks literature. The normal way to set a tariff is to calculate (dynamically) what percentage of users will pay how much for the capacity an ISP does have, and offer the rest as best effort.
If an ISP offers VNP (or virtual leased line like services) then a simpler scheme is to offer pro-rata tariff based on actual costs - since the ISP buys wholesale, but is offering this serive retail, this will more than cover real costs.
However, to make life seem more palatable, it is usual in the networking literature to consider a set of plausible parameters for a QoS based bill:
  time-of-day
  duration
  capacity
  delay, jitter
  loss
  priority (for pre-emption)

## Slide 161: Pricing 3
Can price by effective capacity
Do we want to vary price with network conditions? (optimal in theory but complex - too complex for user - in practice) - congestion pricing
security associated with payment and policing necessary
Predictable bills are often more important than cheapest fare (c.g. mobile phones).
Notes: In many dynamic shared systems (e.g. road transport) congestion pricing and e-payment are offered as a mechanism for achieving an optimal market. At the extreme, this can be an auction per packet for capacity on offer. At a lesser extreme, this might be done in a bourse on a daily or weekly or monthly basis by ISPs who then offer a tarrif for their QoS bill-of-fare for the end user to pick from.
This has been seen in ts latter form to work for international and mobile telephony in the last few years. It remains to be seen if it will work for IP. Note that telephony only offers 1 service (just like standard IP) and not really a QoS range. Adding in consideration of the user and the users’ understanding of the price and performance may undermine such approaches - the INDEX Project at Berkeley in the US has been studying this recently, but we don’t have any really widely applicable solid results yet.

## Slide 162: Provisioning
Users don’t like being refused access (prefer degraded service, but…)
Need to dimension network for the user satisfaction and revenue levels
Base on traffic measured. Look at frequency of overload or call rejection for RSVP…
IP telephony - can (if pricing and patterns match) base on Erlang models…traditional - may not apply - e.g. either or both of call and packet arrival independence may be wrong...
Notes: Once an ISP offers per-flow QoS, they have to compete with other such ISPs on the basis of call-blocking probability. This is calculated by looking at the set of source traffic models, and the traffic matrix (and its evolution over the working day and over time), and computing where to allocate more capacity.
Problems for IP exist here:
  Traffic ource model of TCP is understood to some extent, but not in the large
  Traffic model for RTP is not obvious
  Traffic matrix is not at all obvious
  Correlated calls seem much more likely than in telephone networks
  aggregate traffic behaviour is not analytically understood.
Current solutions to provisioning often are based on monitoring the churn in the customer base and triggering acquisition and deployment of more capacity whenever that exceeds some threshold.

## Slide 163: Implementation Novelties
Active Networks &
MPLS

## Slide 164: Active Networks
Reference: D. L. Tennenhouse, J. M. Smith, W. D. Sincoskie, D. J. Wetherall, G. J.Minden, "A Survey of Active Network Research, IEEE Communications Mag.,Vol. 35, No. 1, pp 80-86. January 1997
Active networks subject of large DARPA program, and quite a few european projects.
Interpose processing of user data in network path by dynamically moving code there….radical idea based in strong distributed computation
Originated in observation that it has become very hard in telephony and IP networks to deploy new services of any kind due to scale (and inflexibility) of the infrastructure.
Notes: Active Networks includes quite a wide range of ideas now, ranging from servlets, through packet headers containing insutrvtions and not just data, through to agents.
It’s a “hot research topic”, but not without controversy and critics.

## Slide 165: Active Networks 2
Weak model just puts code in place at application level points -either call handling (e.g. dynamic singlaing protocol code -switchware, switchlets IEEE programmable networks work) or at application level relays (e.g. non transparent caches)
Strong model - re-programs switches on the fly possibly per packet - packet header is now code for VM in switch instead of data for fixed program in switch.

## Slide 166: Active Networks 3
Jury is out on AN
Looks like at least some ideas will make it through to prime time though….
Main problems
  with strong AN is code performance, safety and liveness
  with weak AN is management - could be very useful for generalized VPNs though...

## Slide 167: MPLS
Datagrams Meets Circuits
Based on strong idea of “flow”

## Slide 168: Performance
Getting data from source to destination(s) as fast as possible
Higher data rates required for:
  large files …
  multimedia data
  real-time data (video)
Fast forwarding
Not the same as QoS provisioning, but closely linked
Notes: Multi-Protocol Label Switching (MPLS) is a technology that is currently being developed within the IETF to allow fast-forwarding of IP-packets. The IETF charter for the workgroup is:
http://www.ietf.org/html.charters/mpls-charter.html
There is now a high performance demands from network users with the use of large files, multimedia applications and real-time flows.
MPLS is a label-based scheme that allows packets to be forwarded based on short, fixed-length labels rather than using the normal IP-routing table lookups. This is not to say that MPLS is a replacement for routing, indeed it relies on the normal routing protocols to allow the correct assignment and distribution of labels. Essentially, the mechanism attaches a label to an IP packet and uses this to make hop-by-hop forwarding decisions, bypassing the normal destination-based, longest-prefix match IP-forwarding mechanism at a router.
The aim of MPLS is to provide a fats forwarding mechanism. This should also help in provisioning of QoS capability in an IP network.

## Slide 169: Forwarding vs. Routing
Routers have to:
  maintain routes
  forward packets based on routing information
Forwarding:
  moving a packet from an input port to an output port
  make a forwarding decision based on route information
  get the packet to an output port (or output queue) fast
Routing:
  knowing how to get packets from source to destination
Notes: IP routers have to perform a number of tasks, including maintaining routes. This is achieved by the exchange of routing information using routing protocols like OSPF (Open Shortest Path First) and BGP (Border Gateway Protocol). Based on this routing information, the router makes forwarding decision, i.e decides which of its output ports a packet must be sent to.
The problem of making fast forwarding decisions is inherent in any datagram network, such as IP networks. A description of the task is quite simple – to move a packet from an input port to an output port as fast as possible. However, there is a process involved in making the forwarding decision that is a major factor in determining the overall performance of the router.
The task of routing is a more far-reaching task in that it is achieved by the interaction between and involvement of all the routers in a network, whereas the task of forwarding is specific to an individual router.

## Slide 170: IP forwarding
Packet arrives (input buffer?)
Check destination address
Look up candidate routing table entries:
  destination address
  routing entry
  address mask
Select entry:
  longest prefix match selects next hop
Queue packet to output port (buffer)
Notes: To make a forwarding decision for an IP packet the following steps take place at a router:
1. a packet arrives at an input port and the packet may need to be buffered
2. the router must read the destination address of the packet
3. based on the destination address, the router selects candidate routing table entries, and for each candidate entry, saves the next hop address, the address mask for the address and the output port for that entry
4. after all the candidate entries have been found an entry must be selected by using the longest prefix match using the routing entry address mask and the destination address in the packet
5. when the appropriate candidate entry has been selected, the packet is placed on the appropriate output queue
Steps 3 and 4 in this process may require the consideration of other information such as routing metrics, policy-based routing, security information, etc. In general, this may slow down the forwarding process, although clever caching and recent developments in table-lookups and packet classification can help.

## Slide 171: Flows
A sequence of IP packets that are semantically related:
  packet inter-arrival delay less than 60s
Flows may be carrying QoS sensitive traffic
Many thousands of flows could exist when you get to the backbone
Detect flows and use label-based routing:
  make forwarding decisions easier
  make forwarding decisions faster
Notes: A packet flow (or stream) can be thought of as a sequence of packets that are semantically related. the relationship is application specific, e.g. it could be all packets with the same source and destination address. A flow exists if there are at least two packets that are semantically related and their inter-arrival delay is 60s or less.
Flows may be carrying traffic that is QoS sensitive, e.g. audio or video data, or has other real-time constraints.
When identifying flows, it must be appreciated that there may be a need to have aggregation capability for flows, else in the backbone there may be many thousands of flows that need to be monitored and maintained.
If flows can be identified then it seems that the forwarding decision process need only be executed once, for the first packet in the flow, as all packets for the same flow/stream will be subject to the same forwarding decision. So, the impetus for MPLS is that if the forwarding decision is initially executed using normal routing mechanisms and then identified with a short, fixed-length label, the much simpler task of matching labels enables faster and easier forwarding for subsequent packets in the stream/flow.
There are several names for such mechanisms including:
cut-through routing
short-cut routing
layer-3 switching
and specific vendors have their own names for proprietary schemes.

## Slide 172: MPLS
Multi-protocol label switching:
  fast forwarding
  IETF WG
MPLS is an enabling technology:
  helps scaling
  increases performance
  forwarding still distinct from routing
Intended for use on NBMA networks:
  e.g. ATM, frame-relay
Notes: The Multi-Protocol label Switching (MPLS) WG of the IETF is seeking to define a standard that will support fast-forwarding mechanisms.
It is intended that the use of MPLS in place of traditional IP forwarding will allow better performance and scaling in certain IP network scenarios. Its is intended that such mechanisms will help scaling an and performance of IP networks in certain environments, i.e. where it is likely that the layer-2 technology will offer a faster forwarding mechanism than the layer-3 forwarding of IP.
MPLS is designed to be complementary to existing routing mechanisms. Indeed, routing information is used to establish the forwarding entries used by MPLS.
Although independent of any particular bearer technology and any particular layer-3 technology, there is particular interest in finding MPLS solutions tailored to provide IP-over-ATM and IP-over-FR (Frame Relay).

## Slide 173: MPLS architecture [1]
IETF work in progress - requirements:
  integrate with existing routing protocols
  support unicast, multicast, QoS, source routing
MPLS uses label-swapping
Flows are labelled:
  special shim header
  can use existing labels in bearer technology (e.g. VCI)
LSR (Label Switching Router):
  simple, fast link-level forwarding
Notes: The MPLS WG work is still in progress. No RFC documents had been produced at the time of writing. The main requirements for MPLS are that:
it can be integrated with existing level-3 routing protocols
will support unicast and multicast
has the potential to be used as a QoS control mechanism
will enable traffic engineering mechanisms such as source routing and hierarchical routing
The MPLS architecture is based around the label-swapping paradigm that is used in virtual circuit (VC) networks. Flows are labelled with a short, fixed-length label that is used for identifying flows. The label value can be part of a generic shim header (defined by the MPLS WG), or could be inserted into existing header fields in various technologies, e.g. the VPI/VCI in ATM cells.
The main network element that allows MPLS use is the Label Switching Router. This is a MPLS-capable IP router that can effectively perform link-level forwarding of IP packets.

## Slide 174: MPLS architecture [2]
LSR1
LSR2
LSR3
LSR4
LSR5
LSR6
LSR11
LSR8
LSR Label Switching Router
MPLS Multi-Protocol Label Switching
LSR7
MPLS domain
MPLS-capable IP router
LSR10
LSR9
ingress LSR
egress LSR
Notes: The MPLS enabled network consists of Label Switching Routers (LSRs) that use label-swapping to perform packet forwarding. A LSR is a MPLS-capable IP router. An IP packet flow/stream enters the MPLS network – MPLS domain – via an ingress LSR. Generally, this is where the IP packet is given a label, but the MPLS work does not preclude direct labelling by individual hosts. Once the packet is labelled, it is forwarded to the next LSR along the Label Switched Path (LSP). At the point where the packet leaves the MPLS network, the final router, the egress LSR, forwards the packet towards its final destination. The label may be removed at the egress LSR, or it maybe removed by the penultimate hop LSR, and this is a matter for local configuration. If the packet is being forwarded to another MPLS domain at the egress router, then another label value may be assigned. In , we see an example of an MPLS network, with a packet flow/stream marked by arrows. All packets in the same flow/stream are forwarded along the same path. LSR1 is the ingress LSR and LSR11 is the egress LSR. The LSP for the flow/stream is given by the concatenation of the LSRs through the MPLS network, i.e. {LSR1, LSR2, LSR4, LSR7, LSR11}.
With respect to the forwarding direction, LSRs have upstream and downstream relationships, e.g. LSR2 is upstream from LSR4 and LSR7, and LSR4 and LSR7 are downstream from LSR2.

## Slide 175: Label switching
Packet enters ingress router
  lookup label: Forwarding Equivalency Class (FEC)
  packet forwarded with label
At next hop (next LSR):
  label used in table lookup: LIB and NHLFE
  new label assigned
  packet forwarded with new label
Saves on conventional look-up at layer 3
Need label distribution mechanism
Notes: As the packet passes to the ingress router, a normal IP forwarding lookup is performed for that packet. However, the result of the lookup is to identify:
the Forwarding Equivalency Class (FEC) for the packet
the label that is associated with the FEC
The label is then attached to the IP packet and forwarded to the next LSR in the LSP. At the next LSR, the label is used in an exact-match table lookup to identify:
the next LSR in the LSP
the new label value
The new label is written to the packet and the packet is forwarded along the LSP. This process continues until the egress LSR (or the penultimate hop LSR) where the label is completely removed and the packet continues on its journey (unless forwarding to another MPLS domain). Within the MPLS network, the overhead of the normal IP-level lookup (using longest-prefix matching) is avoided and this should improve performance. The key to this mechanism is the efficient allocation, distribution and maintenance of labels.
LSRs maintain a Label Information Base (LIB) containing label-FEC bindings and a table of Next Hop Label Forwarding Entries (NHLFEs) that are indexed using the label value.

## Slide 176: Labels [1]
Label:
  short
  fixed-length
  local significance
  exact match for forwarding
Forwarding equivalency class (FEC):
  packets that share the same next hop share the same label (locally)
  packets with the same FEC and same route: streams
Notes: Labels are short, fixed-length identifiers used to identify packets that will receive the same forwarding treatment. Their value has only local significance and they are used in exact-match lookups to identify how a packet should be forwarded. Labels effectively identify Forwarding Equivalency Classes (FECs). Packets belonging to the same FEC will receive the same forwarding treatment. Label-based forwarding uses a simple exact match mechanism for making forwarding decisions.
The labels identify packets with the same FEC. Its is possible for packets from different flows/streams to share the same FEC for part of their journey, i.e. an FEC does not map one-to-one with a flow/stream. For example, packets from different sources headed from the same destination might share the same FEC for some of the last hops of their journey.
The MPLS terminology is to use the word stream for identifying packets in transit that have the same FEC.

## Slide 177: Labels [2]: shim header
Generic: can be used over any NBMA network
Inserted between layer-2 and layer-3 header
label: 20 bits
Exp: 3 bits (use not yet fully defined - CoS)
S: 1 bit stack flag (1 indicates last in stack)
TTL: 8 bits
label
Exp
S
TTL
0
20
23
24
31
Notes: The shim header sits between the IP header and level 2 header. The shim header is 32 bits in order to aid fast processing in modern hardware platforms. The Experimental bits may be used as Class of Service (CoS) identifiers, but this is for further study. Labels can be stacked (explained below) and the S bit is set when this label is the final one in the stack. The TTL identifier is copied from the IP packet header at the when the label is added and its value is decremented at each LSR, as the TTL would be decremented in a normal IP packet at each router hop. When the label is removed, the TTL value in the label is copied to the IP packet header.
Specific technologies, such as ATM and FR, will have different label encodings mechanisms that take advantage of existing header fields, e.g. the FR DLCI or the ATM VCI/VPI.

## Slide 178: Label granularity
IP prefix:
  aggregation of several routes
Egress router:
  all IP destinations with common egress router for LSP
Application flow:
  per-flow, end-to-end
Others possible:
  e.g. host pairs, source tree (multicast)
Notes: The label identifies a FEC and the label may have a granularity that is chosen to suit particular needs of a particular administration. In fact, the way the semantics of a label (effectively the description of the description of the FEC) is chosen may reflect some policy controlled by requirements based on, Quality of Services (QoS), traffic engineering, cost or any other administartion specific criteria. The granularity chosen could be:
destination IP-prefix: effectively each routing table entry has a FEC and so its own unique LSP. This may be an easy policy to implement based on information gained from the normal routing information carried in IP routing protocols. This may not scale where the label-space is limited or where there are large numbers of routes.
egress router: all packets heading for the same egress router of an MPLS network might be given the same FEC. This may allow aggregation of several routes and would scale better than using the destination IP-prefix, but is a much more coarse-grained FEC, and offers less control of individual traffic streams/flows.
application flow: this level of granularity could be used in conjunction with a resource reservation protocol or other QoS control mechanism.
MPLS does not constrain any policy-based definition of the FEC or the label granularity, and indeed the current documents specify other granularities such as host-address pairs, network-address pairs, source specific tree and shared tree, where the latter two are applicable to multicast.

## Slide 179: Label distribution [1]
Routing information used to distribute labels:
  piggy-back label info on existing protocols?
Performed by downstream nodes
Each MPLS node:
  receives outgoing label mapping from downstream peer
  allocates/distributes incoming labels to upstream peers
Label Distribution Protocol (LDP):
  LDP peers (LDP adjacency)
Notes: Genrally, the label distribution mechanism for a flow starts at the egress router and is passed upstream, i.e. the distrbution is perfomed by the action of downstream nodes.
Each LSR receives a lebl fromdown stream with information about the FEC to which that label is bound. For that label, it allocates and distributes its own label upstream and maintains the incoming-outgoing labels mapping.
To allow distribution of the label information, in general, there are several options. The information about label values and FECs could be piggy-backed onto messages generated by existing routing protocols. This would mean that no new protocol is required. However, there may be a large difference in the operation of the level 3 network and the level 2 network, especially with respect to the timescales over which forwarding decisions or routing changes are made. So, a Label Distribution Protocol (LDP) is also being designed to allow label information to be distributed between LSRs. LSRs are said to engage in LDP peering and have LDP adjacency when they are using the LDP to communicate.

## Slide 180: Label distribution [2]
Distribution of label info from LSR only if:
  egress LSR
  LSR has an outgoing label
Downstream: LSR allocates and distributes
Downstream-on-demand: upstream LSR requests allocation from a downstream node
Address prefix-based FEC/forwarding:
  independent distribution: any node in LSP
  ordered distribution: egress LSR
Notes: Generally, label distribution can occur in two ways:
downstream-on-demand: a LSR recognises a packet for a FEC and asks its next hop to provide a label binding for the FEC before assigning its own label binding
downstream: a LSR recognises a FEC assigns a label binding and advertises this label binding to its peers
Where FECs correspond to address prefixes that are used by IP-routing, LSP control can occur in two ways.
ordered distribution: an LSR can only distribute a label binding if it is the egress router for the stream, or if it already has a downstream label binding for a FEC.
independent distribution: an LSR recognises that a stream belongs to a particular FEC, starts MPLS forwarding, and advertises its label binding to its peers, even though it may not have received a label binding from a downstream LSR.
Note that for label-based forwarding to work across the entire domain, all the downstream nodes must be aware of the stream and the relevant FECs, and have a label binding for the FEC. So, to ensure that downstream nodes have this information, it is advisable for label distribution to begin from the egress node, and this would ensure that a packet is never forwarded from an upstream LSR unless a downstream LSP exists. So, ordered distribution is preferred, in general. Although it may have a higher latency in some cases, it is more robust to looping, and can be more easily configured for QoS-based or policy-based forwarding. Independent distribution follows the conventional IP-forwarding model, but relies on the fact that the LDP algorithm must allow fast convergence.

## Slide 181: Label stacking [1]
Two mechanisms:
  equivalent to IP source routing
  hierarchical routing
Multiple labels are stacked by the ingress LSR
LSRs along the route can pop the stack:
  makes forwarding even faster

## Slide 182: Label stacking [2]
LSR1
LSR2
LSR3
LSR4
LSR5
LSR6
LSR11
LSR8
LSR Label Switching Router
MPLS Multi-Protocol Label Switching
LSR7
MPLS domain B
MPLS-capable IP router
LSR10
LSR9
MPLS domain A
MPLS domain C
Notes: Labels can be stacked to allow hierarchical forwarding or mechanisms akin to source routing. Multiple labels are used. The label nearest the IP-header is at the bottom of the stack, and is said to be the lowest level label. The label that is used is always the one at the top of the stack.
Here, we have several MPLS domains (these may be coincident with administrative domains such as IP autonomous systems). In this example, packets from two different streams arrive at LSR1 with labels, L1 and L2, respectively, and are identified all to be destined for LSR11. However, LSR1 may be configured to offer separate paths to each stream through MPLS domain B (the solid arrows and the dotted arrows). It does this by using different labels for each stream. It adds another label, L3, in front of L1 for one LSP and a separate label, L4, for the other LSP, i.e. a new label is said to be pushed on to the stack. In domain B, this top-level label is used to forward packets through domain B. When the packets from each stream arrive at LSR11, it pops the top-level labels in each stream and makes its forwarding decision based on the original labels (L1 and L2) for each stream (respectively). This provides fast forwarding at the inter-domain level (using L1 and L2) and at the intra-domain level (using L3 and L4).
Label stacking could be a useful mechanism for enabling QoS-based or policy-based forwarding, providing VPN functionality and traffic engineering.

## Slide 183: MPLS-like implementations
Control-based:
  tag-switching: cisco
  ARIS (Aggregated Routing and IP Switching): IBM
  IP-Navigator (Ascend)
Request-based: RSVP
Traffic-based:
  IP switching: Ipsilon
  CSR (cell switch router): Toshiba
Many others …
Notes: Currently, there are three broad strategies in label assignment:
control traffic driven (topology-based): here control traffic such as routing information is used to identify FECs. Generally, labels are pre-assigned based on network routes. ARIS (Aggregated Routing and IP Switching - IBM), Tag-switching (Cisco) and IP-Navigator (Ascend) use this strategy.
request driven: explicit requests from control protocols (application-level or via management tools) that pass through a LSR may result in that LSR assigning a forwarding entry for a particular stream. Such explicit requests might be from a resource reservation mechanism like RSVP.
data traffic driven: as streams/flows are “detected” by and LSR by examination of the data traffic, the LSR initiates the label assignment process and an LSP is established. IP switching (Ipsilon) and Cell Switch Router (Toshiba) are examples of the use of this strategy.
Each strategy has its pros and cons, which are highlighted in the MPLS documents.

## Slide 184: Other performance issues
Router architectures
Fast route-table lookup
Fast packet-classification (QoS)
Better address aggregation (e.g. CIDR, IPv6)
Traffic engineering (differentiated services)
Faster boxes or smarter software?
Notes: MPLS is not a panacea for fast, QoS-capable IP networks. Indeed the MPLS WG recognises that in some cases MPLS will not be suitable. MPLS is seen as a complement to “traditional” IP-routing.
However, “traditional” IP-routing is being re-though and re-engineered. Not only are developers and manufacturers giving ploughing more resources into hardware solutions for IP routers and equipment, but the Internet community has ongoing research into faster table-lookup and packet classification algorithms.
Additionally, mechanism like CIDR (Classless Inter-Domain Routing) help address aggregation allowing better scaling of IP routing/forwarding information. A range of novel algorithms in the literate in the last 5 years show that it is possible to do classication of very large numbers of types of flow in near or equal to O(C) time.
Also, IPv6, which is fast approaching stability and ratification within the IETF, has a much simpler, less cluttered header, has the potential for direct flow identification (unlike IPv4) as well as being more amenable than IPv4 to hardware processing.Having said this, some of the QoS scheduling schemes are now affordable in router hardware. Coming from the other direction, novel switch-router platforms are making “full metal jacket” WFQ affordable too!
Issues regarding traffic engineering are at the fore. Internet service providers see the market in offering differentiated services, policy-based traffic handling and establishing service-level-agreements (SLAs) that are more than the simple “best-effort” offered through much of today’s Internet.
The current thinking is that they key to providing flexible, QoS-capable, customer tailored services in the future is the integration of hardware with smart software, and not just making the hardware platform faster to run the same old software.

## Slide 185: Summary
Reference: Scott Shenker, "Fundamental design issues for the future Internet",IEEE J. Selected Areas Comm, 13 (1996), pp 1176-1188
QoS isn’t that simple!
Push something out of one part of the architecture, it will show up somewhere else
e.g. if you remove statelessness by ading RSVP, you need to do congestion control of signaling
e.g. if you remove adaption by adding connection admission (e.g. for TCP), users start adapting.
Notes: Reading List
Items marked * should be read.
[Cla88] D. D. Clark, “The Design Philosophy of the DARPA Internet Protocols”, Proc. ACM SIGCOMM’88, pp106-114, August 1988. *
[CSZ92] D. D. Clark, S. Shenker, L. Zhang, “Supporting Real-Time Applications in an Integrated Services Packet Network: Architecture and Mechanism”, Proc. ACM SIGCOMM’92, pp14-26, August 1992. *
[FJ93] S. Floyd, V. Jacobson , “Random Early Detection Gateways for Congestion Avoidance”, IEEE/ACM Transactions on Networking, vol. 1, no. 4, August 1993, pp. 397-413
[FJ95] S. Floyd, V. Jacobson, V., “Link-sharing and Resource Management Models for Packet Networks”, IEEE/ACM Transactions on Networking, vol. 3, no. 4, pp. 365-386, August 1995
[Gol94] S. J. Golestani, “A Self-Clocked Fair Queuing Scheme for Broadband Application”, Proc. IEEE INFOCOM’94, Toronto, June 1994, pages 636-646
[GP93] Abhay K.Parekh, and Robert G.Gallager , “A generalized processor sharing approach to flow control in integrated services networks: the single-node case”, IEEE/ACM Transactions on Networking vol. 1, no. 3 (1993), pages 344-357
[GP94] Abhay K.Parekh, and Robert G.Gallagher , “A generalized processor sharing approach to flow control in integrated services networks: the multiple node case”, IEEE/ACM Transactions on Networking, Volume 2, Issue 2 (1994), pages 137-150
[Kle75] L. Kleinrock, “Queuing Systems, Volume 2: Computer Applications”, Wiley Interscience, 1975

## Slide 186
Notes: [KLS98] V. P. Kumar, T. V. Lakshman, D. Stiliadis, “Beyond Best Effort: Router Arhcitectures for the Differentiated Services of Tomorrow’s Internet”, IEEE Communications, vol. 36, no. 5, May 1998, pp. 152-163 *
[KS98] S. Keshav, R. Sharma, “Issues and Trends in Router Design”, IEEE Communications, vol. 36, no. 5, May 1998, pp. 144-151 *
[Pax97a] V. Paxson , “End to End Internet Packet Dynamics”, Proc. SIGCOMM’97, September 1997.
[Pax97b] Vern Paxson, “End-to-End Routing Behavior in the Internet”, IEEE/ACM Transactions on Networking, vol. 5. no. 5, October 1997
[PF95] V. Paxson, S. Floyd, “Wide-Area Traffic: The Failure of Poisson Modeling”, IEEE/ACM Transactions on Networking, vol. 3, no. 3, pp. 226-244, June 1995
[PF97] V. Paxson, S. Floyd, “Why we don't know how to simulate the Internet”, Proc. 1997 Winter Simulation Conference *

## Slide 187
Notes: [RFC1075] D. Waitzman, C. Partridge, S.E. Deering, “Distance Vector Multicast Routing Protocol”, November 1988
[RFC1581] G. Meyer , “Protocol Analysis for Extensions to RIP to Support Demand Circuits”, February 1994
[RFC1584] J. Moy, “Multicast Extensions to OSPF”, March 1994.
[RFC1633] R. Braden, D. Clark, S. Shenker, “Integrated Services in the Internet Architecture: an Overview”, June 1994 *
[RFC1853] W. Simpson, “IP in IP Tunneling”, October 1995
[RFC1958] B. Carpenter, “Architectural Principles of the Internet”, June 1996. *
[RFC2201] A. Ballardie, “Core Based Trees (CBT) Multicast Routing Architecture”, September 1997
[RFC2205] R. Braden, Ed., L. Zhang, S. Berson, S. Herzog, S. Jamin, “Resource ReSerVation Protocol (RSVP) -- Version 1 Functional Specification”, September 1997
[RFC2208] A. Mankin, Ed., F. Baker, B. Braden, S. Bradner, M. O’Dell, A. Romanow, A. Weinrib, L. Zhang, “Resource ReSerVation Protocol (RSVP) -- Version 1 Applicability Statement Some Guidelines on Deployment”, September 1997

## Slide 188
Notes: [RFC2210] J. Wroclawski, “The Use of RSVP with IETF Integrated Services”, September 1997
[RFC2211] J. Wroclawski, “Specification of the Controlled-Load Network Element Service”, September 1997
[RFC2212] S. Shenker, C. Partridge, R. Guerin, “Specification of Guaranteed Quality of Service”, September 1997
[RFC2215] S. Shenker, J. Wroclawski, “General Characterization Parameters for Integrated Service Network Elements”, September 1997
[RFC2216] S. Shenker, J. Wroclawski. , “Network Element Service Specification Template”, September 1997
[RFC2328] J. Moy, “OSPF Version 2”, April 1998.
[RFC2362] D. Estrin, D. Farinacci, A. Helmy, D. Thaler, S. Deering, M. Handley, V. Jacobson, C. Liu, P. Sharma, L. Wei, “Protocol Independent Multicast-Sparse Mode (PIM-SM): Protocol Specification”, June 1998.
[RFC2386] E. Crawley, R. Nair, B. Rajagopalan, H. Sandick, “A Framework for QoS-based Routing in the Internet”, August 1998
[RFC2474] K. Nichols, S. Blake, F. Baker, D. Black, “Definition of the Differentiated Services Field (DS Field) in the IPv4 and IPv6 Headers”, December 1998
[RFC2475] S. Blake, D. Black, M. Carlson, E. Davies, Z. Wang, W. Weiss, “An Architecture for Differentiated Service”, December 1998
[RFC2481] K. Ramakrishnan, S. Floyd , “A Proposal to add Explicit Congestion Notification (ECN) to IP”, January 1999.
[RFC2597] J. Heinanen, F. Baker, W. Weiss, J. Wroclawski, “Assured Forwarding PHB Group”, June 1999

## Slide 189
Notes: [RFC2598] V. Jacobson, K. Nichols, K. Poduri, “An Expedited Forwarding PHB”, June 1999
[She95] S. Shenker, “Fundamental Design Issues for the Future Internet”, IEEE Journal of Selected areas in Communication, no.13, pp1141-1149, 1995 *
[VRC98] L. Vicisano, L. Rizzo, J. Crowcroft, “TCP-like congestion control for layered multicast data transfer”, Proc. IEEE INFOCOM’98, San Francisco, USA, 29 March 1998 – 2 April 1998
[WGCJF95] I. Wakeman, A. Ghosh, J. Crowcroft, V. Jacobson, S. Floyd, “Implementing Real Time Packet Forwarding Policies using Streams”, Proc. USENIX’95, new Orelans, Louisiana, USA pp71-82, Jan 1995
[WP98] W. Willinger and V. Paxson,, “Where Mathematics meets the Internet”, Notices of the American Mathematical Society, 45(8), August 1998.