## Slide 1: Rethinking Incentives for Mobile Ad Hoc Networks
By
E Huang, J Crowcroft & I Wassell
Laboratory of Communication Engineering
&
Computer Laboratory
University of Cambridge

## Slide 2: Mobile Ad Hoc Networks (MANETs)
Consist of a set of self-organized, decentralized, mobile hosts that roam at will and communicate directly with each other
A mobile host has to work as a router and cooperate with other hosts to find routes and relay messages
If battery power, bandwidth, and other resources are scarce, selfish users may not wish to forward packets for other users

## Slide 3: Incentives
Encourage users to cooperate
  Token Based Incentive Systems
  Trust Management Systems
Incentive systems have inherent flaws that make them difficult and undesirable to implement in practice
Some may backfire by offering an incentive to cheat the incentives system

## Slide 4: Token Based Incentive Systems
Use notional credit to pay off users for congestion costs; earn credit by forwarding for other users
Limits amount of data that can be sent at any given time. Buffering only works if buffer is large enough and no delay constraints on packets. Hence somewhat inefficient for real time communications
Users on outskirts of network put at a disadvantage

## Slide 5: Token Based Incentive Systems
Estimation of hop number takes up resources. If done incorrectly results in dropped packets, wasted credit and wasted energy
Balance of token levels
Using real money as credit provides more incentive to cheat and requires centralisation or tamper proof hardware
Who pays?
Adds complexity

## Slide 6: Trust Management Systems
Nodes within network exchange reputation information
Takes up resources
Relying on second hand information can lead to false accusations or cheating via collusion
Obtaining authentication and trust information about accusing node is very hard to achieve; may not be possible for dynamic short lived networks

## Slide 7: Transparency vs. Choice
Incentives seek to induce cooperation
We want users to choose to forward and keep devices on
The more choice there is, the more complex for user
Given that incentives system makes forwarding mandatory there is little point of giving users a choice in the matter

## Slide 8: Are incentives really necessary?
Cooperation is only an issue when resources are scarce
Chicken and egg
MANETs require phased deployments and are unlikely to be used for generic applications in early stages
Vital that overly complex incentive systems do not cause early adopters to shun MANETs
MANETs vs. P2P
Decentralised allocation of identifiers and unforgeable tokens is generally an unsolved technical problem

## Slide 9: A Phased Out Solution
Pioneers are enthusiastic users, more interested in exploring technology than benefiting from it
Visionaries see the potential in new technology and are willing to help to get a head start in reaping the benefits
Pragmatists want a complete solution that works
Conservatives want products that are cheap and simple. They hop onto the bandwagon only when they have no choice
Only at later points in the cycle do incentive systems make sense. At this point it is better understood how people use and abuse systems. Even then incentives can stem from common interest.
Pioneers
Visionaries
  Pragmatists
  Conservatives
Early Market
Mainstream Market
Adoption Cycle for Mobile Ad Hoc Networks

## Slide 10: Why We Don’t Need Incentive Systems Anyway
Main need for incentives vs. hardwired behaviour is to prevent tampering
But majority of users will only cheat when it is beneficial to them and easy to do
Playstation has fallen victim to large scale tampering
With PS there are compelling reasons for consumers to pay for modification and criminal organisations to provide these services
Benefit from modifying ad hoc devices is mainly battery power savings

## Slide 11: Why We Don’t Need Incentive Systems Anyway
Unclear that users would go out of their way to modify devices vs. buying a spare battery
Different devices for different applications will need unique modifications
It would be an expensive and complex task to reverse engineer all these devices
Without a ready market, criminal organisations have no incentive to offer modifications
Modifying ad hoc devices is not sustainable. The less nodes cooperate the worse the network performance

## Slide 12: Conclusion
Incentive systems may be better left till ad hoc networks enter mainstream markets
They should be tailored to the needs of individual applications rather than generic solutions
There is no perfect solution; it is more important at this time to allow ad hoc networks to grow and develop than to stifle it with overly complex solutions