## Slide 1
Mobile/Wireless RDMA CAAP, Cluster As Application Platform
Opens new realm, beyond Internet
Run distributed apps on the cluster, not PAAS (Platform As A Service), but native, CAAP
New protocol-free networking schemes
Yitzhak Bar Geva, Prof. Jon Crowcroft Sept. 2015

## Slide 2: Introduction Wireless Device Clusters Overview of RDMA and RoCE The RDMA model mapped over Wireless InfiniBand RoCE, Soft-RoCE iWARP, Soft-iWARP OFED, ULPs - Upper Layer Protocols Programmability with verbs Freedom from Protocols Upcomming RDMA Technologies Use Cases Implementation and Challenges Resources
Contents

## Slide 3: Up Front Notes
Some basic familiarity with InfiniBand and RDMA is assumed. Tutorials on the Internet. See resources
With a concerted effort by an academic/industrial consortium, this vision can become realized in time for 5G Cellular

## Slide 4: Introduction
D2D in 5G cellular can turn mobile/wireless device clusters into the next generation application platform.
Development of distributed apps over on-the-fly clusters is rapidly gaining popularity, but today’s networking strata is sorely lacking for the job.
The widely used RDMA clustering model with verbs programming has been a standard in HPC data centers for decades. RDMA on mobile clusters is ideal for writing distributed applications with their own custom protocol-free networking schemes.

## Slide 5: 5G standards must take a close look at RDMA networking, particularly D2D to avoid IP lockin. RDMA is faster, more efficient. Zero-copy and lower cpu usage in the (extremely slim) RDMA network stack are more important in the mobile environment. Furthermore, it lends naturally to clustering, user programmable networking.
5G Standards

## Slide 6: Computing Platform Evolution
Today’s networks and clouds are remotely provided services, like computing once was
Each Wave Dwarfs its Predecessor

## Slide 7: Following the Analogy… Device Clusters open a vastly wider Application Space with an order of magnitude more clusters than devices
Pooled Mobile Device Clusters

## Slide 8
See Pooled Device Clusters as Powerful Application Platforms
App
App
App
App
App
App

## Slide 9: For illustration, imagine if computing had not evolved outward from a monolithic core but from
personal computers
with only close-proximity wireless communications,
performance necessitated clustering of nearby machines,
that conformance was unheard-of and
gave rise to a myriad of Open Source clustering schemes

## Slide 10: Powerful over and beyond sheer horsepower
The RDMA cluster model today is limited to High Power Computing, which like networking, is beyond the reach of most developers and users.
User-programmable RDMA can potentially realize an untold number of new messaging and distributed programming paradigms.
See Wireless RDMA first and foremost as a people-power revolution whose impact can be grasped by likening it to the PC revolution which:
    Made computing resources universally accessible and
    Opened programming, the legacy of a select few, to the world.
    The PC’s feeble processing power was no issue over time as has been the case with the smartphone as well.

## Slide 11: Advantages
HPC apps run unchanged
Write distributed apps in popular languages
Devices pool their cores and storage
Devices can belong to multiple clusters and the Internet
New networking paradigms by RDMA verbs programming.
Dynamic reconfiguration. Configuration can be volatile, according to optimization requirements, devices popping in and out. See volley ball slides.

## Slide 12
A cooperative distributed programming platform in an era of friendly concurrent programming languages
Networking and clouds in‑hand, no longer externally supplied services
Freely configurable, dynamically reconfigurable IOT‑type pooled‑device clouds, on a common platform

## Slide 15
Remote Direct Memory Access
Remote
  data transfers between nodes in a network
Direct
  no Operating System Kernel involvement in transfers
  everything about a transfer offloaded onto Interface Card
Memory
  transfers between user space application virtual memory
  no extra copying or buffering
Access
  send, receive, read, write, atomic operations

## Slide 16
RDMA Benefits
High throughput
Low latency
High messaging rate
Low CPU utilization
Low memory bus contention
Message boundaries preserved
Asynchronous operation

## Slide 17
RDMA Technologies
InfiniBand – (41.8% of top 500 supercomputers)
  SDR 4x – 8 Gbps
  DDR 4x – 16 Gbps
  QDR 4x – 32 Gbps
  FDR 4x – 54 Gbps
iWarp – internet Wide Area RDMA Protocol
  10 Gbps
RoCE – RDMA over Converged Ethernet
  10 Gbps
  40 Gbps

## Slide 18
RDMA Architecture Layering
User Application
OFA Verbs API
Physical
Data Link
Network
Transport
IWARP “RNIC”
RoCE “NIC”
InfiniBand “HCA”
RDMAP
DDP
MPA
TCP
IP
IB Transport API
IB Transport
IB Network
Ethernet MAC & LLC
IB Link
Ethernet PHY
IB PHY
OSI
Layers
CA
Notes: Note: InfiniBand transport in h/w (on the NIC)

## Slide 19
Multi-Instance.
    Membership in a cluster is seen as a single instance in the device
Multi-Cluster
    Device may be member of multiple clusters simultaneously
Multi-App
    Cluster itself may be multi-instance, multi-process
Flexible message‑passing network schemes
    RDMA verbs (or newer, MPI optimized PSM) facilitate user‑programmable, protocol-free NIC behavior
RDMA Model Flexibility

## Slide 20: Kernel Bypass

## Slide 21
RDMA
User Space programmable

## Slide 22
If only we had an InfiniBand wireless chip…

## Slide 23
RDMA Mapped Over Wireless
Wireless Channel Adapter
Mobile Clusters

## Slide 24
RDMA
Mapped Over Wireless Cluster

## Slide 25
Becomes Wireless HPC
where these are mobile devices

## Slide 26: InfiniBand
Notes: High speed communications link for data flow between processors and I/O devices with support for up to 64,000 addressable devices. Scalable, supports quality of service (QoS) and failover. Widely used as a server connect in HPC environments. InfiniBand is at the core of this presentation. Familiarity with IB is assumed.

## Slide 27
InfiniBand
Notes: InfiBand is evolving, becoming more efficient, utilizing hardware advancements

## Slide 28
RoCE useful in our humble opinion only in the interim. InfiniBand over wireless is the prime choice

## Slide 29
ROCE

## Slide 30
RoCE

## Slide 32
Soft-RoCE

## Slide 33
iWARP

## Slide 34: iWARP - Internet Wide Area RDMA Protocol

## Slide 35
Software RDMA Drivers
Softiwarp
  www.zurich.ibm.com/sys/rdma
  open source kernel module that implements iWARP protocols on top of ordinary kernel TCP sockets
  interoperates with hardware iWARP at other end of wire
Soft RoCE
  www.systemfabricworks.com/downloads/roce
  open source IB transport and network layers in software over ordinary Ethernet
  interoperates with hardware RoCE at other end of wire

## Slide 36: Means that…
Clusters can be made from geographically disparate nodes
Run smoothly over the Internet (TCP/IP)
Mobile/Wireless clusters can cluster-up together with enormously powerful HPC clusters
World wide multi-million node clusters, each its own Internet or cloud

## Slide 37: OFED - OpenFabrics Enterprise Distribution
Available for Linux and Windows. Includes kernel-level drivers, channel-oriented RDMA and send/receive ops, kernel bypass, kernel and user-level API, MPI, sockets data exchange(RDS, SDP), NAS and SAN storage (iSER, NFS-RDMA, SRP) and File Systems/DB systems. RDMA network and fabric technologies for: legacy 10 GB Ethernet, iWARP for Ethernet, RoCE, and 10/20/40 Gigabit InfiniBand.
Notes: Open Source software provided by the OpenFabrics Alliance. Provides legacy services over InfiniBand through APIs to Upper Layer Protocol (ULP) (annotated by yellow marker) kernel modules.
Not what we want. The ULP route is not programable.

## Slide 39
Legacy services through Upper Level Protocol kernel modules.
Not Programmable
Notes: Following the previous slide, the left hand side shows applications interfaced through APIs to Upper Layer Protocols (ULPs) to legacy service emulation. Not Programmable!

## Slide 40: Programmability with RDMA verbs (or newer PSM)
We’ll see how any agreed upon networking code loaded on all the nodes becomes a so-called, protocol.
Here we program RDMA verbs.

## Slide 41
Programmable

## Slide 42: Verbs
Notes: Here we see the comparison between inflexible protocols in the kernel (previous slide on the right) and programmable RDMA verbs. Still a tricky art without a yet-to-be developed verbs compiler. Not trivial, but the payoff is enormous since the verb-programming code is application code, could be incorporated with the app.

## Slide 43: Java 7 VM over verbs
Notes: Here’s a fine example of what we’re striving for languages and services over verbs (or newer technology, PSM etc.). This is Java 7. We want additional concurrent languages like GoLang, Erlang/Elixir, etc. over verbs.

## Slide 44: Custom Networking Schemes
Network management, switching and routing, programmed verbs or PSM all provided by the devices as user-space loadable software.
Freedom from rigid protocols is the logical next step.

## Slide 45
and began writing their own protocols

## Slide 46
Protocols, essential where needed

## Slide 47: Imagine if Software had to be Protocol Conformant
but a hindrance where not needed

## Slide 48: Painstaking, Meticulous Only one language Ran on only one type of machine
Network protocols are like software before compilers

## Slide 49: Talk about protocols
Loadable networking code is application code
Want to switch or update the so-called, eh, protocol?
Just

## Slide 50: pushing code instead of data onto all the nodes
SDN
Like an
to run alternate network schemes

## Slide 51: Escape the protocol‑bound gravitational field

## Slide 52: If programming RDMA verbs is so
then why is hardly anyone doing it?
Because it ain’t easy yet. That it’s programmable is remarkable in itself, but it's still like assembly coding. We need a compiler (on the checklist)

## Slide 53: Upcoming RDMA technologies RDMA transfers between GPUs

## Slide 54: Upcoming RDMA technologies Virtualized RDMA

## Slide 55: A few Use Cases
Realtime statistical data mining or data mashing which produce visual outputs in a close region, like say, a visual realtime picture of crowd behavior patterns in a shopping mall or train station.
Apps which today have to be manually installed, could be seeded and run. No need for web sites, uploads to the Internet, fixed IP addresses, run as easily as a local GUI app.
Cooperative coding in realtime. Developers/users hacking together on the same running app platform.
Internet of Things - infinitely more flexible

## Slide 56: Such a Simple Conceptual Model
must be easy to implement

## Slide 57: Sorry, not quite
There are Formidable Challenges,
But…

## Slide 58: Nothing we don’t know how to do

## Slide 59
On-the-fly clustering of mobile devices
On-the-fly D2D clusters of close proximity cars.
Wireless InfiniBand Fabric Manager
Wireless InfiniBand chips. SoftROCE over Wi-Fi for the interim
Android virtualized RDMA or container D2D apps
Networking Meta Language or DSL over RDMA verbs
Challenges we can meet
Partial list

## Slide 60
Partial list of challenges, cont’d
Lacking external switching devices, switching and routing have to be done by the devices themselves.
Seeding - bootstrapping the app/cluster
  Isolation between overlapping app/clusters
  Mixing and merging overlapping app/clusters
Member registration, volatile resource allocation manager
etc., etc….

## Slide 61: Take note…
As opposed to present-day networking, in a protocol-free, all-software (or nearly all-software) realm, not all problems have to be solved in advance. The challenge is less in doing than it is in enabling to be done. The consortium’s challenge is to build the so-called launchpad, the necessary prerequisites for the developers to begin their work. From there, it becomes an evolutionary process.

## Slide 62
Volleyball Fabric Manager
Players come and go but the ball stays in the air
Redundancy and distributed juggling keeps the cluster app in the air as devices join and leave

## Slide 63: Resources
Introduction to InfiniBand
InfiniBand Technology Overview
vVerbs A Paravirtual Subsystem for RDMA