## Slide 1: Network Architecture Research Considerations Based on Haggle
Jon Crowcroft (University of Cambridge)
Jon.crowcroft@cl.cam.ac.uk
http://www.cl.cam.ac.uk/~jac22

## Slide 2: Why we shouldn’t do network arch?
Liberally borrowed slides from Mothy Roscoe and Steven Hand & Wenjun Hu, Experiments and Analysis from Pan (Ben) Hui.
First, general Arguments
Then specific (Haggle) example…

## Slide 3: What is a Network Architecture?
Choose Paradigm
  Given Physical constraint
    Packet/circuit/new(e.g. multihop radio)?
  Fundamentally is net a “graph”?
  Are protocols/services “layered”?
Choose Functional Decomposition
  Trade between packet header and node
    Choose stateless or stateful (e2e v. hbh)
    (e.g. change trade to include transport:
    can do NAT, Header Compression and QoS/Flows)
  Are nodes different (host v. router)?
  Choose Packet Format(s)

## Slide 4: One (incremental) view: Internet choices ok: Don’t Panic!
Congestion collapse!
  TCP congestion control
The backbone won’t scale!
  Traffic Engineering, DWDM
We’ll run out of address space!
  CIDR, NAT (and IPNL, 4+4, Triad, …)
Long fat pipes are under-used!
  Scalable TCP, HSTCP
Protocol stacks can’t keep up!
  Zero-copy I/O, TSO, …
TCP doesn’t work on wireless!
  Split-TCP, i-TCP
But what about security!
  Firewalls, Application-level filtering

## Slide 5: So everything’s ok then?
Well, no…
Many solutions are kludges
Many solutions are stop-gaps
  NAT for a billion cellular devices? a trillion sensors?
No management story whatsoever… and security really is a problem
In a nutshell:
  “The Internet: Just-in-time Engineering” (Anon)
  “The Internet has always just been saved from catastrophic failure” (M Handley)
  “The Internet is a triumph of human ingenuity over common sense” (S Hand)
That isn’t architecture, it’s sloppy building repairs!
Notes: Management – as 3rd speaker (TaeSaeng Choi, ETRI) mentioned – is pretty shit today.
Maybe move to autonomic stuff of some kind.

## Slide 6: One (purist?) view of network architecture
“Network Architecture”
Email
IM
Unreal Tournament
Email
IM
Unreal Tournament

## Slide 7: One (pluralist) view of network architecture
“Network Architecture”
Voice over GSM mobile phone
Skype P2P voice over IP

## Slide 8: Different (separatist/corrosive/layered) view of network architecture
“Network Architecture”
“Networking people”
“Systems people”

## Slide 9: A third way…post internet arch (“post” can bind to net or arch:)
Sidestep the whole purist/pluralist debate
Avoid an architecture completely
  It’s unnecessary
  It doesn’t address any problems
  It may be counterproductive
Let me give a detailed worked example from the Haggle Project :- IST-4-027918-IP
Post-modernism
  No to FIND/GENI?
  Experience: Architectures emerge (ANSA/Herbert)
  Papers about them are usually post-hoc rationalisations

## Slide 10: Example: Haggle, a Human DTN
Clean slate design of networking subsystem for mobile devices
Haggle: a layerless, but modular network architecture
  designed around the needs of mobile users
Aims:
  Allow applications to take advantage of all types of data transfer (neighborhood, infrastructure, mobility)
  Allow networking endpoints to be specified by user-level naming schemes rather than node-specific network addresses,
  Allow limited resources to be used efficiently by mobile devices, taking into account user-level priorities for tasks

## Slide 11
Give it to me, I have 1G bytes phone flash.
I have 100M bytes of data, who can carry for me?
I can also carry for you!
Thank you but you are in the opposite direction!
Don’t give to me! I am running out of storage.
Reach an access point.
Internet
Finally, it arrive…
Search La Bonheme.mp3 for me
Search La Bonheme.mp3 for me
Search La Bonheme.mp3 for me
There is one in my pocket…

## Slide 12: Can we Generalize From Haggle?
Wireline Networks: Solid
MANET: Liquid
Haggle: Gas
Manage Phase Changes between these – reality of wireless is that we need to move from
  Gas -> Solid
  Gas -> Liquid
More often than we previously realized
Maybe actually a new architecture … … …

## Slide 13: Design principles for Haggle (not an architecture, no no no:-)
Forward using application layer information
  De-layer
Asynchronous operation
  Do not assume path
Empower intermediate nodes
  Do not separate host from router
All user data kept network-visible, and req/resp
  Tx==rx==store - all equal class functions
Exploit all data transfer methods
  Greed is good
Take advantage of brief connection opportunities
  Impatience is good
Empowered and informed resource management
  Know and tell what it costs

## Slide 14: Current device software framework
Interfaces
Delivery (IP)
Protocol
App logic + GUI
User Data
Application
Networking
File System
Synchronous, node-centric API
Isolated from network
App has two orthogonal parts
Delivery uses anonymous IP
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Haggle Overview
Clean-slate redesign of mobile node
Spans MAC to application layers (inclusive), but is itself layerless – uses six “managers”
API is asynchronous and data-centric
Store-and-forward architecture with data persisting inside Haggle not separate file sys
App-layer protocols (SMTP, HTTP, etc) moved into Haggle rather than apps themselves
Naming/addressing done in graphs instead of stacks
Resource management built-in
Haggle Application Interface
Applications (messaging, web, etc)
Protocol
Resource
Data
Name
Connectivity
Forwarding
Connectivities (WiFi, BT, GPRS, etc)

## Slide 16: Data Objects (DOs)
DO = set of attributes = {type, value} pairs
  Exposing metadata facilitates search
Can link to other DOs
  To structure data that should be kept together
  To allow apps to categorise/organise
Apps/Haggle managers can “claim” DOs to assert ownership
DO-Type | Data
Content-Type | message/rfc822
From | James Scott
To | Richard Gass
Subject | Check this photo out!
Body | [text]
DO-Type | Data
Content-Type | image/jpeg
Keywords | Sunset, London
Creation time | 05/06/06 2015 GMT
Data | [binary]
Message
Attachment

## Slide 17: Protocols
Protocols are methods for communicating with other nodes, including Haggle-specific protocols as well as legacy protocols (e.g. email)
Example: protocol to send an ADU over an ad-hoc WiFi connection given a neighbour’s MAC address
Example: protocol using keywords as addresses via Google – e.g. satisfy a query for “world news”
Legacy example: encapsulate an ADU in an email and send it using SMTP to an email address

## Slide 18: Delivery uses user-level names(ANA)
Plutarch, IPNL, RSIP etc etc etc
Names come from:
  Network, e.g. using neighbour discovery (12:AB:23:98:BE:FF)
  Applications, e.g. Jon Crowcroft » jon.crowcroft@cl.cam.ac.uk
Some names are also “addresses” i.e. data can be delivered to that name using one of the protocols available
Delivery engine needs to:
  Sense “nearby” addresses (e.g. Bluetooth inquiry gives MAC addresses, Internet connectivity means all email addresses are deliverable)
  Known-sender: Map between ADU’s destination name(s) and addresses of suitable next-hop nodes
  Known-recipient: Determine suitable nearby nodes which may be sources or help find sources for requested data
  Describe these potential transfers and their benefits to the resource manager

## Slide 19: Resource management using tasks
Task is a network activity
Resource management uses a list of tasks mainly provided by delivery engine
  E.g. perform discovery on interface I
  E.g. send ADU X to neighbour Y on interface Z
Each task has an associated benefit and cost
  Benefit is specified by task provider. May be time-dependent (i.e. using a pointer-to-function)
  To get cost, resource use is estimated, and then the “cost” is a function of the resource use * the resource scarcity
  Resource manager then schedules execution of tasks in order of highest benefit/cost ratio.

## Slide 20: So where are we?
Problem definition and some idea of solution
NOT architecture:- framework for others to use(Sourceforge)
  Others develop use cases
  Architecture will emerge from common uses
Other work we’ve done:
  Measurement/analysis of human connectivity patterns
  Measurement of in-motion wireless networking properties
  Community detection and Community based forwarding
Ongoing work in European project
  More measurement and analysis of possible data paths
  Implementation of modular software framework
  Addressing challenges of naming/addressing, forwarding, security/trust, usability, legacy compatibility

## Slide 21: Community detection&forwarding
Community structures
  Social communities, i.e. affiliations/explicit labels
  Topological cohesive groups or modules
Centralities
  Social hubs, celebrities and postman
  Betweenness, closeness, inference power centrality
Experiments
  Traces of human xco-mobilty on/from Crawdad
  Haggle own Cambridge, Hong Kong, Infocom
  MIT Reality Mining, Dartmouth, UCSD

## Slide 22: Communities in Infocom06 Dataset: Union of k-cliques reachable via series of adjacent k-cliques [Palla et al]
Barcelona Group
Paris Group A
Paris Group B
Lausanne Group
Paris Groups
Barcelona Group
Lausanne Group
K=3

## Slide 23: K-clique Communities in Infocom06 Dataset
Barcelona Group
Paris Group A
Paris Group B
Lausanne Group
Paris Groups
Barcelona Group
Lausanne Group
K=4

## Slide 24: K-clique Communities in Infocom06 Dataset
Barcelona Group (Spanish)
Paris Group A (French)
Paris Group B (French)
Italian
K=5

## Slide 25: Centrality Cambridge Dataset: times node is on shortest delay path
Group A
Group B

## Slide 26: Interaction and Forwarding
Third generation human interaction model
  Categories of human contact patterns
  Clique and community
  Popularity/Centrality
Dual natures of mobile network
  Social network
  Physical network
Benchmark Forwarding strategies
  Flooding, Wait, and Multiple-copy-multiple-hop (MCP)

## Slide 27: Design Space
Explicit Social Structure
Structure in Degree
Structure in Cohesive Group
Label
Rank, Degree
Clique Label
Bubble
Network Plane
Human Dimension

## Slide 28: Problem with RANK
Hop distribution and rank at dead-end for HK dataset

## Slide 29: Problem with LABEL
In a less mixing environment (e.g. Reality)
A person in one group may not meet members in another group so often
Wait for destination group not efficient

## Slide 30: Centrality meets Community
Population divided into communities
Node has a global and local ranking
Global popular node like a postman, or politician in a city
Local popular node like Christophe Diot in SIGCOMM
BUBBLE-A
BUBBLE-B

## Slide 31
Ranking
Source
Destination
Global Community
Sub community
Sub community
Subsub community

## Slide 32: Centrality meets Community
Notes: Bubble Reality single group

## Slide 33: Making Centrality Practical
How can each node know its own centrality in decentralised way? How well does past centrality predict the future?

## Slide 34: Approximating Centrality
Total degree, per-6-hour degree
Correlation coefficients, 0.7401 and 0.9511

## Slide 35: Using decentralised Approximating Centrality

## Slide 36: Predictability of Human Mobility
Three sessions of Reality dataset
Two sessions using the ranking calculated from the first session: Almost same performance

## Slide 37: By way of example: Haggle (== DTN bis): A framework for Networking Mobile Users
Wireline Networks: Solid
MANET: Liquid
Haggle: Gas
Manage Phase Changes between these – reality of wireless is that we need to move from
  Gas -> Solid
  Gas -> Liquid
More often than we previously realized
Maybe actually a new architecture … … …

## Slide 38: Questions?
Please e-mail me: Jon.Crowcroft@cl.cam.ac.uk
Papers availabl!