## Slide 1
International Technology Alliance
In Network & Information Sciences
Mobile Ad-hoc Inter-domain Networking
Jon Crowcroft, Computer Laboratory, University of Cambridge
http://www.cl.cam.ac.uk/~jac22

## Slide 2: A Future with Many MANETs
One day we’ll want to inter-manet
  Not talking about a cloud of manets clustered around the fixed internet
  Actual inter-domain manet - traversing different routing schemes
  Is a very hard problem
Not even clear that one solution is sensible

## Slide 3: Quick Drying Gloss
MANET=Mobile Ad-hoc NETwork
  Al qaeda, swarm of bees, Man United
IGP = Interior Gateway Protocol
  E.g. OLSR, DLR, AODV,GPSR
EGP= Exterior Gateway Protocol
  E.g. BGP, IDPR, IDRP, as yet don’t know
AS = Autonomous System
  BiCi, ETH, 18.0.0.0
Nimrod
  http://ana-3.lcs.mit.edu/~jnc/nimrod/docs.html

## Slide 4: Definitely a MAD distributed system!
Each domain has own goals
  Routing on geo- or topo-, on demand or reactive, optimized for capacity, delay, loss, power, etc
Policies (ingress, egress, transit) are coloured
  Interconnection is not just at “edges”
Synchronization of IGP and EGP non trivial
  Does data follow control traffic (in space and time)
Heterogeneity of Addressing
  Do we add level of hierarchy or translate?

## Slide 5: 1. IGP to EGP interface
Reactive:Proactive?
  Pro- trumps re-
    can cause route and act as hello in same breath).
Geographic versus Topological?
  Topo- trumps Geo-
    Can map one way not the other
Distribute route or reachability (AS maps)?
  AS Map (like nimrod) trumps route
    Nodes associate in a MANET longer than route stability

## Slide 6: 2. Torrents of Policy
Each MANET is a community
  Each has own incentive & recommendation & reputation mechanism
Can we map these between different systems?
  Or do we have separation of ingress/egress/transit policy from intra-manet routing?
Seems like separation is required for technical reasons too (see previous and next slides)

## Slide 7: 3. IGP to EGP Synchronization
IGP may not actually converge
  Geo- and gradient- protocols don’t need to
EGP offer of probability of reachability
  Should be output of EGP computation
Like UDLR and other asymmetric schemes (IP over x.25:-)…
  AS map&reachability exchange control traverse more stable paths than users’ data

## Slide 8: 4. Heterogeneous Addresses
Each MANET will assign addresses (identifiers for routing and end system) dynamically
Need to report these in EGP as part of reachability
Do we “re-prefix” them (like IPv6) or assume AS level uniqueness, or translate?
TBD!

## Slide 9: Conclusion/future
We’re looking at using metarouting work
  New postdoc looking at approach
And further plutarch work
  Collaborate on composable networks
But first we have to have a clear problem statement
  Strawman proposed - next: evaluate - criteria/topology/mobility/dynamics?!