## Slide 1
ATM Inter Network Interface Vinai Sirkay John Drake Ted Tedijanto

## Slide 2
What do Service Providers want ?
Service Providers want to provide global ATM network connectivity
  Provide their customers with connectivty to
  any customer on
  any public ATM network
  anywhere in the world
So whats the problem ?

## Slide 3
What is the problem ?
There are multiple
  routing protocols
    PNNI based on OSPF dynamic routing
    BISUP based on static routing
  signaling protocols
    PNNI based UNI signaling
    BISUP based on ISUP signaling
  Multiple address formats
    4 different type - ICD, DCC, NSAP E.164 and native E.164
What a mess ?

## Slide 4
Present Day Model for BISUP- BISUP
SP- A
SP- A
P1
P2
BISUP
BISUP
Public
UNI
Public
UNI
B-ICI
Service Providers that run BISUP use BICI as network to network interface
BISUP Network use E.164 address formats

## Slide 5
Present Day Model for PNNI - PNNI
SP- B
SP- C
P1
P2
PNNI
PNNI
Public
UNI
Public
UNI
PNNI
Service Providers that run PNNI use PNNI as net to net interface
Problems with this model

## Slide 6
PNNI is a link state protocol that requires the exchange of
  network topology
  network state
    Hiding sate and topology information would require carrier to aggregate nodes into higher levels in a hierarchy
      Leading to problems with QoS aggregation
  explicit policy information
Service Provider network do not want to provide their competitors with network state, network topology and policy information
PNNI as a AINI - Not a good idea

## Slide 7
What can be done today ?
BICI
SP- C
SP- A
SP- B
BISUP
BISUP
SP- D
PNNI
PNNI
PNNI to BICI
Signaling
Interworking
PNNI to BICI
Signaling
Interworking
PNNI to BICI
Signaling
Interworking
BICI
BICI
BICI
PNNI to BICI interworking not specified
  Need an interface that more than interworking PNNI to BICI signaling

## Slide 8
Whats needed ?
A new interface that
  defines a signaling superset of features supported by both PNNI and BISUP
    define a set of error code in the case of mixed network types
    define interworking functions from PNNI and BISUP to new signaling protocols
  defines a new information exchange model
    via routing protocols
    via database exchanges

## Slide 9
Information Exchange Model
What information are carrier networks willing to exchange ?
  Reachability
  Estimate of Delay
  Estimate of available bandwidth
  Policy
This information needs to be quasi- static and will be updated in a minimal fashion

## Slide 10
Information Model Elements
Reachability
  A set of ATM network address or prefixes that may be reached via the advertising network
Estimate of delay
  The advertising network needs to specify the upperbound on available bandwidth through the network
Estimate of bandwidth
  available bandwidth through the network

## Slide 11
Information Model Elements
Policy
  Aggregation
    A set of component prefixes which must be present in order to create and advertise the aggregate
  Import
    Routes that a network can learn from a peer
  Export
    Routes that a network can learn from a peer

## Slide 12
AINI as a Service Provider NNI
AINI
SP- C
SP- A
SP- B
BISUP
BISUP
SP- D
PNNI
PNNI
BISUP to AINI
Signaling
Interworking
BISUP to AINI
Signaling
Interworking
BISUP to AINI
Signaling
Interworking
BISUP to AINI
Signaling
Interworking
PNNI to AINI
Signaling
Interworking
PNNI to AINI
Signaling
Interworking
PNNI to AINI
Signaling
Interworking
PNNI to AINI
Signaling
Interworking
AINI
AINI
AINI

## Slide 13
Future Service Provider Networks
AINI
AINI
AINI
AINI
AINI
AINI
Public
UNI
Public
UNI
Public
UNI
AINI
AINI
Public
UNI
SP- C
SP- B
SP- A
BISUP
BISUP
SP- D
PNNI
PNNI
P1
P1
P1
P1
EPN
PNNI
EPN
PNNI
EPN
PNNI

## Slide 14
Conclusion
AINI will be the network to network interface between
  service providers and
  extended public network and service providers
AINI will provide signaling interworking among the various signaling protocols
AINI will define the new information exchange model among service providers