## Slide 1
Put a NetFPGA into a PC to build hardware-accelerated, gigabit-speed network appliance.
Features:
Wire-speed packet processing
Cost-Effective
Can be programmed as:
  Any-protocol Router, Ethernet Switch, NIC,…
Interfaces:
  Four Gigabit Ethernet ports
  Standard PCI host interface
  Gigabit serial I/O
The NetFPGA platform provides a flexible teaching and research tool – permitting instrumentation and prototyping of real router functionality at real network speeds.
NetFPGA – Programmable Hardware for high-speed network prototypes
An open network hardware platform implemented with Field Programmable Gate Array (FPGA) logic.
Using the NetFPGA follows Cambridge Computer Laboratory tradition of working with both hardware and software.
Past networking projects have included the original Cambridge Ring, the Cambridge Fast Ring, the Fairisle ATM switch, the Desk Area Network and the Home Area Network.
Programmable network hardware allows students and researchers to do practical prototyping at real-world line-speeds.
http://www.netfpga.org
Support for the NetFPGA project has been provided by the following companies and institutions
NetFPGA platform
1GE
MAC
1GE
MAC
1GE
MAC
1GE
MAC
Your hardware specified
in Verilog source code
connected to components
of the Reference Router
circuits and cores.
-
18Mb
SRAM
1GE
PHY
1GE
PHY
1GE
PHY
1GE
PHY
V2-Pro50 FPGA w/ infrastructure
64MB
DDR2
SDRAM
Linux OS
-
NetFPGA Kernel driver
Host
computer
User
-
defined software networking applications
Four Gigabit Ethernet Interfaces
18Mb
SRAM
FIFO
packet
buffers
Control, PCI
Interface
3
Gb
SATA
Board
-
Board Interconnect
Current Projects and Plans:
Test novel ideas for control mechanisms (buffer management, scheduling) in Optical PCI Networks
Build an accurate, fast, network emulation
Hardware implementations of behavioural classifier
Hardware supporting virtual routers/hosts
Provable routers as an F#/Kiwi target
Provable routing through Metarouting