## Slide 1
POP to POP Zero Hop Routing Vinai Sirkay Lou Berger John Drake Rob Coltun

## Slide 2
Approach
Four building blocks for scaleable networking:
ATM overlay networks
Data and control driven short-cut regions
  With different levels of traffic aggregation and multiple types of short-cut triggers
Multi-point to point VC merging for large networks
Improved network operations through ATM
Building blocks combined as needed to meet the specific requirements of each network

## Slide 3
What Are Short-Cuts?
Eliminate intermediate L3 devices from control and data path
Establish pathways (VCs) independent from L3 topology
  May follow completely different switch paths
Provide different levels of traffic aggregation, multiple types of short-cut triggers:
  Data driven short-cut at the network edge
  Control driven short-cut in the core providing accelerated default forwarding paths
  Short-cuts for QoS and other critical traffic

## Slide 4
Short-Cut Aggregation
Short-cuts may support different levels of traffic aggregation
Some examples:
  Application specific flow
    No aggregation
  Traffic destined to a specific address
    Host aggregation
  Traffic destined to a specific network
    Network aggregation
  Traffic destined to a specific edge device
    Egress aggregation

## Slide 5
Short-Cut Triggers
Triggers result in creation of short-cut VCs
Triggers may be located in
  the network or
  the ATM edge device
Triggers may be
  Data driven
    N packets to destination address/network
    Data packets matching a specific application flow
  Control driven
    Based on routing traffic
    May be network or egress/ingress based

## Slide 6
Data Driven Short-Cuts
Data Driven Short-Cut
  Data driven short-cuts at the network edge
  Bypasses L3 forwarders
  Short-cut types
    Per QoS application flow
    Per unicast destination
    Per destination network prefix
    Per multicast destination
  Short-cut triggered by data flow
    Configured QoS data
    N packets per second
    Hop-by-hop path
    Short-cut path

## Slide 7
Control Driven Short-Cuts
  Provides accelerated default forwarding paths in the core
  Bypasses L3 forwarders
  Short-cut types
    Per egress device
    Configured QoS per ingress/egress pair
    Per multicast ingress
  Short-cut triggered by routing traffic
    When new egress/ingress advertised
Control Driven Short-Cut
    Hop-by-hop path
    Short-cut path

## Slide 8
Combined Short-Cut Picture
Data
Driven
Regions
Hop-by-hop
  For control data
  Some L3 forwarding
Intra-region short-cuts
  Within data and control driven regions
Cross region short-cuts
  For QoS and critical traffic
Control Driven Region

## Slide 9
FOREs Solution
Scaleable building blocks: Appropriate technology for each network
10s 100,000s
Number of supported hosts
Full Mesh
Data Driven
Short-Cuts
Control Driven
Short-Cuts
Number of sites (WAN Links)
100s
1s
VC Merging

## Slide 10
FDDI
Router POP
ATM POP
Accelerated default forwarding
    Control and distributed forwarding
    Hop-by-hop paths
      For control and initial data forwarding
    Control driven short-cuts
Backbone / Service Provider
ATM Core Backbone
Route Servers

## Slide 11
Backbone Network Flows
Ingress route server performs IP routing functions and pushes forwarding information to the ATM forwarders
  Based of control flow, setup VC from ATM forwarder to ATM forwarder
  If ingress ATM forwarder has forwarding entry then send data on short -cut to egress ATM forwarder
  else sends data to default router
ATM port to ATM port QoS short-cuts
Default Path
Control driven short-cut
Traffic engineered short cut
ATM Core

## Slide 12
Scaling the backbone
    Reduced VC requirements
    Improved scalability
Multi-Point to Point VC Merging
ATM Switch WAN Backbone
622 Mbps
Shared VC
Notes: Key points:
In VERY large networks, additional efficiencies can be gained by using a multi-point-to-point connection for all the traffic destined for a particular edge device/destination.
In very large networks with lots of random traffic patterns (a corporate intranet backbone, or the Internet backbone) every edge forwarder talks to every other. This means that for a network of N edge devices, the VC requirement increases by N x N. In large nets, this very quickly becomes a very large number of VCs. Our LIJ-MPP solution solves this problem by reducing the VC count to 1 MPP VC per edge device. For details, see below.
The MPP connection is essentially a VC ‘funnel” in which all sources sending data to a given destination share a single VC id.
The sources autonomously join the funnel, or tree, via the standard “leaf initiated join” which was standardized for doing efficient multicasts. In this case, the flow of information is reversed. The leaves join the tree to send information to a common point, rather than to receive from that point.
Note: For this to work, cells from different VCs must not be intermixed at the merge points, or data corruption will result..
In a ForeThought/ForeRunner network, this re-assembly will occur in hardware on the netmods. It draws on our EPD/PPD technology which manages cell that are associated with a single AAL5 PDU (packet).

## Slide 13
Backbone Network Flows
Ingress route server performs IP functions and pushes forwarding information to the ATM forwarder
Based on forwarding information ATM forwarder will join a multi-point-to-point ATM connection
Switches in ATM core will have VC merging capabilities
  AAL 5 sequence integrity is maintained at these switches
ATM Core

## Slide 14
Scaling Short-Cuts
Why traditional short-cuts don’t scale
  Traditionally data driven
    Requires per flow traffic analysis
    Not feasible in network cores
Solved by control driven shortcuts
  Traditionally edge device or host based
    Low aggregation of users/traffic flows per short-cut
    Leads to very large number of VCs in core of large networks
Solved by different levels of aggregation and VC merging in the ATM core

## Slide 15
Scaling Short-Cuts: FOREs Solution
Different types of short-cuts in different parts of network
Short-cut regions
  Limits any-to-any VCs to region, limits total VCs in core
Control driven short-cuts in the core
  Removes traffic analysis burden where there are many flows
  Provides improved, egress based aggregation
Cross region VCs
  Provides best service for QoS and critical uses
Multi-point to point VC merging
  For VC conservation in the very largest networks

## Slide 16
Multi-Point to Point VC Merging
Controlled via UNI and NHRP
Uses UNI4.x Point-to-Multi-Point procedures
  Root controlled (ADDPARTY)
  and Leaf initiated (LIJ)
Route servers exchange needed information via NHRP
  Ingress route server request to be added by egress route server or Get egress’ CID for use with LIJ

## Slide 17
Conclusion
ATM at the core of every ISP
Provide different levels of
  traffic aggregation
    Per egress device
    Configured QoS per ingress/egress pair
    Per multicast ingress
  multiple types of short-cuts
    Data driven short-cut regions at the network edge
    Control driven region providing accelerated default forwarding paths in the core