## Slide 1
Cell Switch Router Label Switching Router for ATM / SONET interfaces
Hiroshi ESAKI
TOSHIBA CORPORATION

## Slide 2
Features of Cell Switch Router
Interoperability with Standard ATM interface
  ATM Switch as L2 switching hub
  ATM links for L2 WAN links
Supporting both Flow Driven and Topology Driven
  Scaling Property
  Exclusive resource allocation (i.e., fair-share, QoS)
  Reduce of Required Bandwidth

## Slide 3
Issues of Intranet and Internet
Insufficient Processing Power with Router
based on Software Processing
Beyond Best-Effort Service
High Speed IP Service Over ATM Links

## Slide 4
Requirements for Intranet and Internet
High throughput and small latency
Realtime (Multimedia) packet transmission
Scalability
  Internetworking of Heterogeneous AS’s
  Processing large amount of packets
  Unreliable node (host/router) behavior
Multicast service

## Slide 5
CSR Design Policy
High throughput small latency
Realtime packet forwarding
Multiprotocol
Unreliable node behavior
Multicast packet forwarding
Flow Aggregation
Interoperability
=> ATM-SW gear
=> RSVP over ATM
=> L2&L3 Multiprotocol
=> Soft-state policy
=> M-Bone with IP
=> Address Prefix Forwarding
=> Standard Interface
(ATM, legacy)

## Slide 6
CSR Implementation Image ° Label Switching Using VPI/VCI °
IP Processing,
FANP Process
& SW control
ATM switch
(i.e., hardware)

## Slide 7
TCP/IP with Cell Switch Router
Host 1
Cell Switch
Router
Host 2
FDDI
FDDI
CPCS
SAR
AAL
IP
TCP
ATM
PHY
CPCS
SAR
IP
ATM
PHY
CPCS
SAR
IP
ATM
PHY
CPCS
SAR
IP
ATM
PHY
CPCS
SAR
IP
ATM
PHY
CPCS
SAR
IP
TCP
ATM
PHY
AAL
ATM net.
ATM net.
ATM net.
ATM net.
ATM net.
ATM net.
ATM net.
ATM net.
ATM net.
Host 1
Cell Switch Router
Cell Switch Router
Host 2

## Slide 8
CSR Theoretical Throughput
CSR System Throughput
OC3-I/F 8 ports
OC3-I/F 16 ports
OC12-I/F 8 ports
Bit Level
Packet Level
64B packets
100B packets
(*) MPPS; Million Packets Per Second
1.2 Gbps
2.4 Gbps
4.8 Gbps
2.4 MPPS
4.8 MPPS
9.6 MPPS
1.5 MPPS
3.1 MPPS
6.1 MPPS

## Slide 9
CSR Operation Principle - Flow Driven -
MODE
SW Engine
Processing
Life-Time
Application
Cut-thru
Hop-Hop
ATM
Packet
Hardware
Software
Long
Short
telnet,web
DNS query
+ Cut-thru Path Establishment/Release Trigger
- Establishment ; TCP/UDP Port-ID
- Release ; Activity of Packet Flow
(*) Cut-thru path is managed by FANP(Flow Attribute
Notification Protocol). Management (establish/release)
of cut-thru path is each CSR’s local decision.

## Slide 10
IP Forwarding with CSR
CSR
IP processing
ATM switching
CSR
CSR
<< Hop-by-Hop Packet Forwarding >>

## Slide 11
IP Forwarding with CSR
CSR
IP processing
ATM switching
CSR
CSR
<< Hop-Hop Mode => Cut-thru Mode >>
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message

## Slide 12
IP Forwarding with CSR
CSR
IP processing
ATM switching
CSR
CSR
<< Cut-thru packet forwarding mode >>

## Slide 13
IP Forwarding with CSR
CSR
IP processing
ATM switching
CSR
CSR
<< Cut-thru mode => Hop-Hop mode >>
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message
‚e‚`‚m‚o Message

## Slide 14
IP Forwarding with CSR
CSR
IP processing
ATM switching
CSR
CSR
<< Hop-by-Hop packet forwarding >>

## Slide 15
Functions and VC Management
Cut-thru Path Establishment (with local decision)
UNI Functionalities (i.e.,client functions)
FANP(Flow Attribute Notification Protocol)
Flow Driven and Topology Driven
IP process
IP process
Host X.1
CSR 1
CSR 2
Host Z.1
IP Subnet X
IP Subnet Y
IP Subnet Z
Default-VC
Dedicated-VC
Coupling of dedicated-VCs

## Slide 16
Internetworking With Cell Switch Router
MPOA
network
ATM Cloud
IP switch network
on SDH cloud
MPOA
network
RFC1577
network

## Slide 17
FANP Specifications
Mutiprotocol (network layer, e.g., IP, IPX)
Connection Oriented Datalinks (e.g., FR, STM)
Flexible Flow Definition
  mandatory: Destination address information
  wildcard or specific: dst port-id, src address/port-id
  address granularity: individual and prefix
Flexible Cut-thru Operation
  Automatic : for individual application flow
  Configured : for (address) aggregated flow
Soft-state Management

## Slide 18
Topology Driven Cut-thru
Advantage
  Small Number of VCs (especially for ISP router)
  Small Cut-thru Establishment Latency
  All packets can be cut-thru
Disadvantage
  Sharing communication resources
    exclusive QoS / resource-allocation
    QoS degradation due to mis-behaved nodes
  Conventional packet processing at edge-nodes
  Firewall function

## Slide 19
Topology Driven Cut-thru (cont’)
Disadvantage (cont’)
  Full-mesh VC configuration for the best throughput
    N-square VC problem for large scale routing domain
  Simultaneous Cut-thru Path establishment according to node appearance
    new node
    recovered node from failure

## Slide 20
Flow Driven Cut-thru
Advantage
  Exclusive communication resource allocation
    exclusive QoS / resource-allocation
    QoS provision even with mis-behaved nodes
  Cut-thru packet processing even at edge-nodes
  On demand resource Allocation
Disadvantage
  Large Number of VCs (especially for ISP)
  Cut-thru Establishment Latency => Stand-by Dedicated-VC
  All packets can not be cut-thru

## Slide 21
Benefits of Dual Mode Operation
Contribution by Flow Driven
  Reduce of Required Total Bandwidth by On-demand bandwidth Allocation
  QOS Provision Without Resource Reservation Protocol (e.g., RSVP)
  Cut-thru Forwarding Across Subnet Boundary
  Exclusive Resource Allocation
Contribution by Topology Driven
  Reduce of Required VC Numbers
  Reduce of Control Overhead

## Slide 22
Cut-thru Path Life-time
< Gateway Router; Digital Equipment Corp. >
Web
telnet
ftp
nntp
# of sessions
Average Life-Time
Traffic Volume
Session
130
16
100
130
161
22
144
139
324.73 sec.
1131.90 sec.
407.28 sec.
1058.33 sec.
13.41 %
0.43 %
32.91 %
39.94 %
Total 276 430 86.69% 481.05 sec.
Ave. Max.
Traffic volume of ftp,telnet,web and nntp generate more than 85% of total traffic. Average life-time for these sessions is more than 8 minutes and these sessions are appropriate to cut-thru forwarding.

## Slide 23
Cut-thru Path Life-Time (2)
<Back-bone router at R&D Center of Toshiba Corp.>
Web
telnet
ftp
nntp
# of sessions
Average Life-Time
Traffic Volume
Session
63
15
4
4
98
27
19
12
504.2 sec.
897.0 sec.
238.5 sec.
260.5 sec.
8.88 %
12.50 %
14.15 %
34.81 %
Total 86 115 70.34 % 515.2 sec.
Ave. Max.
Traffic volume of ftp,telnet,web,nntp generate more than 70% of total traffic. Average life-time for these sessions is more than 8 minutes and these sessions are appropriate to cut-thru forwarding.

## Slide 24
Label Switching Architectures
Standard
ATM Switch
Multiprotocol
TAG Switch
IP Switch
ARIS
SITA
IP Navigator
CSR
L2
L3
CL link
Availability
NO
NO
NO
NO
YES
NO
YES
YES
NO
?
?
?
NO
?
NO
NO
NO
?
?
YES
YES*:Not Supported, but will be supported soon
YES
YES*
YES*
TBD

## Slide 25
: Control channel (VC)
: Cut-thru channel (VC)
(
ATM cloud
IP Switch A
IP Switch B
ATM-SW
ATM-SW
Why IP Switch does not work on standard ATM links ?
I have a availavle channel VPI=2, VCI=5
I am gonna use VPI=2,VCI=5
channel for hot-line !!
VPI=2,
VCI=5
VPI=9,
VCI=3
VPI=6,
VCI=7
I do not have any VPI=2,
VCI=5 channel ?????
Which is his/her offering
VPI=2,VCI=5 channel ?

## Slide 26
VCID Negotiation Mechanism in CSR
FANP ver.1.0
- Interworking with Standard ATM Switch
- Internetworking through Standard ATM Links

## Slide 27
: Control channel (Default-VC)
ATM cloud
CSR_A
CSR_B
ATM-SW
ATM-SW
I have got a packet to be cut-thru !!
Let me establish a VC for cut-thu.
VPI=2,
VCI=5
VPI=9,
VCI=3
VPI=6,
VCI=7
(
: Cut-thru channel (Dedicated-VC)

## Slide 28
: Control channel (Default-VC)
ATM cloud
CSR_A
CSR_B
ATM-SW
ATM-SW
VPI=2,
VCI=5
VPI=9,
VCI=3
VPI=6,
VCI=7
(
: Cut-thru channel (Dedicated-VC)
I have got a VC with VPI=2,VPI=5.
I am gonna indicate CSR_B following
message through this VC.
(Node-ID of CSR_A, SN=7)

## Slide 29
: Control channel (Default-VC)
ATM cloud
CSR_A
CSR_B
ATM-SW
ATM-SW
VPI=2,
VCI=5
VPI=9,
VCI=3
VPI=6,
VCI=7
(
: Cut-thru channel (Dedicated-VC)
I have got a VC with VPI=2,VPI=5.
I am gonna indicatet CSR_B following
messge through this VC.
(Node-ID of CSR_A, SN=7)
I have got a cut-thu request from
CSR_A with SN=7 !!
Let me try to respond CSR_A !

## Slide 30
OK, he/she is ready to receive
through the cut-thru VC :-)
: Control channel (Default-VC)
ATM cloud
CSR_A
CSR_B
ATM-SW
ATM-SW
Hey, I an ready to receive
message through VC with
CSR_A with SN=7

## Slide 31
OK, let me send hot-line message to
CSR_B through the cut-thru VC :-)
I love you :-)
ATM cloud
CSR_A
CSR_B
ATM-SW
ATM-SW
VPI=2,
VCI=5
VPI=9,
VCI=3
VPI=6,
VCI=7
: Cut-thru channel (Dedicated-VC)

## Slide 32
‚`TM Switch
CSR
CSR
CSR
ISP network
CSR
CSR
CSR
CSR
‚`TM Switch
ATM Switch
STM net.
ATM net.
ATM net.

## Slide 33
Introduction of CSR to ISP Network
Dial-up Net.
Frame Relay
Dial-up
link
FR link
Campus Network
SONET Network

## Slide 34
Introduction of CSR to ISP Network
Dial-up Net.
Frame Relay
Dial-up
link
FR link
Campus Network
Ethernet link
ATM / SONET Network
ATM / SONET link

## Slide 35
WIDE Project Introduces Cell Switch Router Technology in their Test Beds
Experimental Operation at Test Beds
=> Nine Test Beds (WAN & campus)

## Slide 36
Cell Switch Router Materials
Material available
  White Paper
  RFC, Internet-Draft
  Papers
Servers Available through the Net
  ftp server
    ftp://ftp.wide.toshiba.co.jp/pub/csr
  web server
    http://www.toshiba.com
    http://www.toshiba.co.jp