## Slide 1
Computer Networking
Lent Term M/W/F 11-midday
LT1 in Gates Building
Slide Set 1
Andrew W. Moore
andrew.moore@cl.cam.ac.uk
January 2013

## Slide 2: Topic 1 Foundation
Administrivia
Multiplexing
Abstraction
Layering
Layers and Communications
Entities and Peers
Channels
The Internet
What is a protocol?
Network edge; hosts, access net, physical media
Network core: packet/circuit switching, Internet structure
Performance: loss, delay, throughput

## Slide 3
Course Administration
Commonly Available Texts
Computer Networking: A Top-Down Approach
  Kurose and Ross, 6th edition 2013, Addison-Wesley
  (5th edition is also commonly available)
Computer Networks: A Systems Approach
  Peterson and Davie, 5th edition 2011, Morgan-Kaufman
Other Selected Texts (non-representative)
Internetworking with TCP/IP, vol. I + II
Comer & Stevens, Prentice Hall
UNIX Network Programming, Vol. I
Stevens, Fenner & Rudoff, Prentice Hall

## Slide 4: Thanks
Slides are a fusion of material from
  Ian Leslie, Richard Black, Jim Kurose, Keith Ross, Larry Peterson, Bruce Davie, Jen Rexford, Ion Stoica, Vern Paxson, Scott Shenker, Frank Kelly, Stefan Savage, Jon Crowcroft , Mark Handley and Adam Greenhalgh (and to those others I’ve forgotten, sorry.)
Supervision material is largely drawn from
  Stephen Kell, Andy Rice
Practical material remains Beta for this year
  But would be impossible without Nick McKeown, David Underhill, Andrew Ryrie and Antanas Uršulis
Finally thanks to the Part 1b students past and Andrew Rice for all the tremendous feedback.

## Slide 5: Multiplexing
Sharing makes things efficient (cost less)
One airplane/train for 100 people
One telephone for many calls
One lecture theatre for many classes
One computer for many tasks
One network for many users

## Slide 6: Multiplexing
Disadvantages of Multiplexing?
Might have to wait
Might not know how long you have to wait
Might never get served
Multiplexing is the action of sharing of resources
in contrast
Concurrency is all about how resources are shared

## Slide 7: Abstraction
A mechanism for breaking down a problem
what not how
eg Specification versus implementation
eg Modules in programs
Allows replacement of implementations without affecting system behavior
Vertical versus Horizontal
“Vertical” what happens in a box “How does it attach to the network?”
“Horizontal” the communications paths running through the system
Hint: paths are build on top of (“layered over”) other paths

## Slide 8: Layering
A restricted form of abstraction: system functions are divided into layers, one built upon another
Often called a stack; but not a data structure!

## Slide 9: Layers and Communications
Interaction only between adjacent layers
layer n uses services provided by layer n-1
layer n provides service to layer n+1
Bottom layer is physical media
Top layer is application

## Slide 10: Entities and Peers
Entity – a thing (an independent existence)
Entities interact with the layers above and below
Entities communicate with peer entities
  same level but different place (eg different person, different box, different host)
Communications between peers is supported by entities at the lower layers

## Slide 11: Entities and Peers
Entities usually do something useful
  Encryption – Error correction – Reliable Delivery
  Nothing at all is also reasonable
Not all communications is end-to-end
Examples for things in the middle
  IP Router – Mobile Phone Cell Tower
  Person translating French to English

## Slide 12: Channels (This channel definition is very abstract)
Peer entities communicate over channels
Peer entities provide higher-layer peers with higher-layer channels
A channel is that into which an entity puts symbols and which causes those symbols (or a reasonable approximation) to appear somewhere else at a later point in time.

## Slide 13: Channel Characteristics
Symbol type: bits, packets, waveform
Capacity: bandwidth, data-rate, packet-rate
Delay: fixed or variable
Fidelity: signal-to-noise, bit error rate, packet error rate
Cost: per attachment, for use
Reliability
Security: privacy, unforgability
Order preserving: always, almost, usually
Connectivity: point-to-point, to-many, many-to-many
Examples:
Fibre Cable
1 Gb/s channel in a network
Sequence of packets transmitted between hosts
A telephone call (handset to handset)
The audio channel in a room
Conversation between two people

## Slide 14: Layering and Embedding
In Computer Networks we often see higher-layer information embedded within lower-layer information
Such embedding can be considered a form of layering
Higher layer information is generated by stripping off headers and trailers of the current layer
eg an IP entity only looks at the IP headers
BUT embedding is not the only form of layering
Layering is to help understand a communications system
NOT
determine implementation strategy

## Slide 15: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 16: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 17: Internet protocol stack versus OSI Reference Model

## Slide 18: Example Embedding (also called Encapsulation)
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 19: What is the Internet: general public
Web-enabled toaster +
weather forecaster
An Early Internet device….
The Computer Lab Coffee Pot
http://www.cl.cam.ac.uk/coffee/coffee.html

## Slide 20: What is the Internet: “nuts and bolts” view
millions of connected computing devices: hosts = end systems
  running network apps
Home network
Institutional network
Mobile network
Global ISP
National ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers: forward packets (chunks of data)

## Slide 21: What is the Internet: “nuts and bolts” view
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, Ethernet
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
Home network
Institutional network
Mobile network
Global ISP
National ISP

## Slide 22: What is the Internet: a service view
communication infrastructure enables distributed applications:
  Web, VoIP, email, games, e-commerce, file sharing
communication services provided to apps:
  reliable data delivery from source to destination
  “best effort” (unreliable) data delivery

## Slide 23: What is a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 24: What is a protocol?
a human protocol and a computer network protocol:
Q: Other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
request
TCP connection
response
GET http://www.cl.cam.ac.uk/index.html
<file>
time
Notes: Lecture (Question by hands)
Traffic lights/driving

## Slide 25: A closer look at network structure:
network edge: applications and hosts
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks

## Slide 26: The network edge:
end systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server
peer-peer
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
  e.g. Skype, BitTorrent

## Slide 27: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep the channel in mind:
Access bandwidth?
shared or dedicated?

## Slide 28: Dial-up Modem (archeology – unless you travel a lot)
telephone
network
Internet
home dial-up
modem
ISP modem
(e.g., AOL)
home
PC
central office
Uses existing telephony infrastructure
  Home is connected to central office
up to 64Kbps direct access to router (often less)
Can’t surf and phone at same time: not “always on”
Notes: Multiplex phone service by time in increments of 10s of minutes

## Slide 29: Digital Subscriber Line (DSL)
telephone
network
DSL
modem
home
PC
home
phone
Internet
DSLAM
Existing phone line: 0-4KHz phone; 4-50KHz upstream data; 50KHz-1MHz downstream data
splitter
central
office
  Also uses existing telephone infrastruture
  up to 1 Mbps upstream (today typically < 256 kbps)
  up to 8 Mbps downstream (today typically < 1 Mbps)
  dedicated physical line to telephone central office

## Slide 30: Cable Network Architecture: Overview
home
cable headend
cable distribution network (simplified)
HFC: fiber to street and
then cable to home (premises)
server(s)

## Slide 31: Cable Network Architecture: Overview
home
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
Frequency Division Multiplexing
(more in a layer Topic):
cable distribution network (simplified)
HFC: fiber to street and
then cable to home (premises)

## Slide 32: Fiber to the Home
ONT
OLT
central office
optical
splitter
ONT
ONT
optical fiber
optical fibers
Internet
Optical links from central office to the home
Two competing optical technologies:
  Passive Optical network (PON)
  Active Optical Network (PAN)
Much higher Internet rates; fiber also carries television and phone services

## Slide 33: Physical Channels also known as Physical Media
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 6: 1Gbps Ethernet
Shielded (STP)
Unshielded (UTP)
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channels on cable
  HFC (Hybrid Fiber Coax)
Fiber optic cable:
high-speed operation
point-to-point transmission
(10’s-100’s Gps)
low error rate
immune to electromagnetic noise

## Slide 34: Physical media: radio
Bidirectional and multiple access
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  e.g. 45 Mbps channels
LAN (e.g., Wifi)
  11Mbps, 54 Mbps, 200 Mbps
wide-area (e.g., cellular)
  3G cellular: ~ 1 Mbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude
Notes: Think of the CHANNEL between entities.
----- Meeting Notes (20/01/2012 10:56) -----
20/Jan end

## Slide 35: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through each channel?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”: postal service
    Packet-switching = Asynchronous Time Division Multiplexing
Notes: CORE = everything that is not EDGE
INTERNET CORE = every router!
Network CORE = everything that interconnects every edge host/server/device

## Slide 36: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required
network resources (e.g., bandwidth)
are divided into “pieces”
pieces allocated to calls
resource piece idle if not used
by owning call (no sharing)
How?
  frequency division multiplexing
  time division multiplexing
Notes: End-to-End assumes a channel END-TO-END

## Slide 37: Circuit Switching: FDM and TDM
Frequency Division Multiplexing
frequency
time
Time Division Multiplexing
frequency
time
4 users
Example:
Radio2 88.9 MHz
Radio3 91.1 MHz
Radio4 93.3 MHz
RadioX 95.5 MHz
Radio Schedule
…,News, Sports, Weather, Local, News, Sports,…
Notes: Can use more than one!

## Slide 38: Numerical example
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!
1 / 24 * 1.536Mb/s = 64kb/s
640,000 / 64kb/s = 10s
10s + 500ms = 10.5s
Notes: 640,000b * (1/24) * 1/536Mbps + 500ms
640,000b @ 64kbps = 10s
PLUS 500ms setup

## Slide 39: Network Core: Packet Switching
each end-end data stream divided into packets (datagrams)
user A&B packets share network resources
each packet uses full link bandwidth
resources used as needed
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Fun new problems/properties
How does a program(mer) compute available resources e.g., bandwidth, delay, variation in delay (jitter)?
Sharing resources (contention-resolution) is now done by protocol (and precedent) – and all that this implies...
Notes: Pcket Switching – Asynchronous Time Division Multiplexing

## Slide 40: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Packet switching may (does!) allow more users to use network
N users
1 Mbps link
Q: how did we get value 0.0004?

## Slide 41: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004
Q: how did we get value 0.0004?
HINT: Binomial Distribution

## Slide 42: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern, bandwidth shared on demand  statistical multiplexing.
(Recall in TDM: each host gets same slot in revolving TDM frame)
A
B
C
100 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
waiting for output
link
Notes: Cheap UNRELIABLE data
Guarantees are statistical – based on longer-term assumptions mean traffic, etc.
Service guarantees do not exist.

## Slide 43: Packet Switching: store-and-forward
takes L/R seconds to transmit (push out) packet of L bits on to link at R bps
store and forward: entire packet must arrive at each hope before it can be transmitted on next link
delay = 3L/R (assuming zero propagation delay)
Example:
L = 7.5 Mbits
R = 1.5 Mbps
transmission delay = 15 sec
R
R
R
more on delay shortly …
L
L
L
L
L
L
L

## Slide 44: Packet switching versus circuit switching
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still a problem (KR: Ch7 PD: Sec 6.5)
Is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Notes: COST COST COST

## Slide 45: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., Verizon, Sprint, AT&T, Cable and Wireless), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately

## Slide 46: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
….
…
…
…
POP: point-of-presence
Notes: Switched Private Network Telecommunications
South Pacific Railway
-=-=-
End of lecture 23rd Jan 2012

## Slide 47: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other.

## Slide 48: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 49: Internet structure: network of networks
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP

## Slide 50: “Real” Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
Notes: Where did the delay come from??

## Slide 51: Four sources of packet delay
Per-packet processing:
  errors check & lookup output link
depends on per-packet overhead
Queuing delay:
  time waiting for output link
  (depends on link-congestion)
Transmission delay:
  packet length / link bandwidth
Propagation:
  length of physical link /
  propagation speed in medium
  (e.g. 2x108 m/sec)
A
B
Propagation
Transmission delay
Per-packet
processing
Queuing

## Slide 52: 2. Queuing delay
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queuing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 53: Queuing Delay
Does not happen if
  packets are evenly spaced
  And arrival rate is less than service rate
Smooth Arrivals = No Queuing Delays
La/R ~ 0: average queuing delay small

## Slide 54: Queuing Delay
Queuing delay caused by “packet interference”
  Burstiness of arrival schedule
  Variations in packet lengths
There is significant queuing delay even though link is underutilized

## Slide 55: Queuing Delay
Does not happen if packets are evenly spaced
  And arrival rate is less than service rate
Queuing delay caused by “packet interference”
  Burstiness of arrival schedule
  Variations in packet lengths
Made worse at high load
  Less “idle time” to absorb bursts
  Think about traffic jams in rush hour….

## Slide 56: Jitter
Difference between minimum and maximal delay
Latency plays no role in jitter
  Nor does transmission delay for same sized packets
Jitter typically just differences in queuing delay
Why might an application care about jitter?

## Slide 57: Packet Loss
Packet Loss due to a full queue
Statistical Multiplexing at High Load may lead to packet loss
Packet Loss due to corruption
Recall the delay due to per-packet processing;
This processing detect/discards corruption

## Slide 58: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe

## Slide 59: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
link on end-end path that constrains end-end throughput
bottleneck link

## Slide 60: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 61: (Propagation) Delay × Bandwidth also called Bandwidth Delay Product
Consider the channel between entities as a pipe
Properties:
  Propagation delay due to length of the pipe, and
  Bandwidth aka the width of the pipe
Delay of 50 ms and bandwidth of 45 Mbps
50 x 10-3 seconds x 45 x 106 bits/second
2.25 x 106 bits = 280 KB data
Notes: You may wish to consider what PRESSSURE is – if you’re an engineering geek.
Links ARE storage
Bits have length….

## Slide 62: Relationship between bandwidth and link-latency
A MB file would fill the Mbps link 80 times,
but only fill the Gbps link 1/12 of one time
62

## Slide 63: Performance
Second order effects
Image/Audio quality
Other metrics…
Network efficiency (good-put versus throughput)
User Experience? (World Wide Wait)
Network connectivity expectations
Others?

## Slide 64: Lessons to take away
Multiplexing is the key
Lots of ‘definitions’
Consider the Task not the Technology
Internet is an example of a packet network
Why are we waiting? – Delay
Where did my data go? – Loss
Bandwidth vs Throughput
Bandwidth delay product