## Slide 1
Computer Networking
Lent Term M/W/F 11-midday
LT1 in Gates Building
Slide Set 3
Andrew W. Moore
andrew.moore@cl.cam.ac.uk
January 2013

## Slide 2: Topic 3: The Data Link Layer
Our goals:
understand principles behind data link layer services:
  (these are methods & mechanisms in your networking toolbox)
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  reliable data transfer, flow control: \
  instantiation and implementation of various link layer technologies
  Wired Ethernet (aka 802.3)
  Wireless Ethernet (aka 802.11 WiFi)

## Slide 3: Link Layer: Introduction
Some terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
layer-2 packet is a frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link
Notes: ended 12th

## Slide 4: Link Layer (Channel) Services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 5: Link Layer (Channel) Services - 2
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 6: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC)
  Ethernet card, PCMCI card, 802.11 card
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
host schematic
application
transport
network
link
link
physical

## Slide 7: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  encodes data for the physical layer
  adds error checking bits, provide reliability, flow control, etc.
receiving side
  decodes data from the physical layer
  looks for errors, provide reliability, flow control, etc
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 8: Coding – a channel function
Change the representation of data.
Given Data
Changed Data
Encoding
Decoding

## Slide 9
MyPasswd
AA$$$$ff
MyPasswd
AA$$$$ff
AA$$$$ffff
AA$$$$ffff

## Slide 10: Coding
Change the representation of data.
Given Data
Changed Data
Encoding
Decoding
Encryption: MyPasswd <-> AA$$$$ff
Error Detection: AA$$$$ff <-> AA$$$$ffff
Compression: AA$$$$ffff <-> A2$4f4
Analog: A2$4f4 <->

## Slide 11
0
1
1
1
1
1
0
0
0
0
0
1
1
1
1
1
0
0
0
0
0
1
1
1
1
1
0
0
0
0
Non-Return-to-Zero (NRZ)
Non-Return-to-Zero-Mark (NRZM) 1 = transition 0 = no transition
Non-Return-to-Zero Inverted (NRZI) (note transitions on the 1)
Line Coding Examples
where Baud=bit-rate

## Slide 12
0
1
0
1
1
1
1
0
0
0
Non-Return-to-Zero (NRZ) (Baud = bit-rate)
Manchester example (Baud = 2 x bit-rate)
Clock
Line Coding Examples - II
0
1
0
1
1
1
1
0
0
0
0
1
0
1
1
1
1
0
0
0
Quad-level code (2 x Baud = bit-rate)
Clock

## Slide 13
0
1
0
1
1
1
1
0
0
0
Line Coding Examples - III
Name 4b 5b Description
0 0000 11110 hex data 0
1 0001 01001 hex data 1
2 0010 10100 hex data 2
3 0011 10101 hex data 3
4 0100 01010 hex data 4
5 0101 01011 hex data 5
6 0110 01110 hex data 6
7 0111 01111 hex data 7
8 1000 10010 hex data 8
9 1001 10011 hex data 9
A 1010 10110 hex data A
B 1011 10111 hex data B
C 1100 11010 hex data C
D 1101 11011 hex data D
E 1110 11100 hex data E
F 1111 11101 hex data F
Name 4b 5b Description
Q -NONE- 00000 Quiet
I -NONE- 11111 Idle
J -NONE- 11000 SSD #1
K -NONE- 10001 SSD #2
T -NONE- 01101 ESD #1
R -NONE- 00111 ESD #2
H -NONE- 00100 Halt
0
1
1
0
0
1
1
0
1
0
Block coding transfers data with a fixed
overhead: 20% less information per Baud in the case of 4B/5B
So to send data at 100Mbps; the line rate
(the Baud rate) must be 125Mbps.
1Gbps uses an 8b/10b codec; encoding
entire bytes at a time but with 25% overhead
Data to send
Line-(Wire) representation

## Slide 14
Line Coding Examples - IV
Scrambling
Sequence
Scrambling
Sequence
Communications
Channel
Message
Message
Message
XOR
Sequence
Message
XOR
Sequence

## Slide 15
Line Coding Examples - V
Scrambling
Sequence
Scrambling
Sequence
Communications
Channel
Message
Message
Message
XOR
Sequence
Message
XOR
Sequence
δ
δ
δ
δ
δ
e.g. (Self-synchronizing) scrambler

## Slide 16
Line Coding Examples – VI
(Hybrid)
δ
δ
δ
δ
δ
δ
δ
δ
δ
δ
…100111101101010001000101100111010001010010110101001001110101110100…
Inserted bits marking “start of frame/block/sequence”
…10011110110101000101000101100111010001010010110101001001110101110100…
Scramble / Transmit / Unscramble
…0100010110011101000101001011010100100111010111010010010111011101111000…
Identify (and remove) “start of frame/block/sequence”
This gives you the Byte-delineations for free
64b/66b combines a scrambler and a framer. The start of frame is a pair of bits 01 or 10: 01 means “this frame is data” 10 means “this frame contains data and control” – control could be configuration information, length of encoded data or simply “this line is idle” (no data at all)

## Slide 17
?
CLASSIFIED:
TOP SECRET
NO FORNAT

## Slide 18
Multiple Access Mechanisms
Each dimension is orthogonal (so may be trivially combined)
There are other dimensions too; can you think of them?
Notes: polarization (Phase)
weird (electron spin)

## Slide 22: Code Division Multiple Access (CDMA)
used in several wireless broadcast channels (cellular, satellite, etc) standards
unique “code” assigned to each user; i.e., code set partitioning
all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence
allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)

## Slide 23: CDMA Encode/Decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
adds code
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
removes code
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 24: CDMA: two-sender interference
Each sender adds a unique
code
sender
removes
its unique
code

## Slide 25: Coding Examples summary
Common Wired coding
  Block codecs: table-lookups
    fixed overhead, inline control signals
  Scramblers: shift registers
    overhead free
Like earlier coding schemes and error correction/detection; you can combine these
  e.g, 10Gb/s Ethernet may use a hybrid
CDMA (Code Division Multiple Access)
  coping intelligently with competing sources
  Mobile phones

## Slide 26: Error Detection and Correction
How to use coding to deal with errors in data communication?
Noise
0000
0001
Basic Idea :
Add additional information to a message.
Detect an error and re-send a message.
Or, fix an error in the received message.
0000
0000

## Slide 27: Error Detection and Correction
How to use coding to deal with errors in data communication?
Noise
0000
0000
Basic Idea :
Add additional information to a message.
Detect an error and re-send a message.
Or, fix an error in the received message.
0000
0000

## Slide 28: Error Detection
EDC= Error Detection and Correction bits (redundancy = overhead)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
otherwise

## Slide 29: Error Detection Code
Sender:
Y = generateCheckBit(X);
send(XY);
Receiver:
receive(X1Y1);
Y2=generateCheckBit(X1);
if (Y1 != Y2) ERROR;
else NOERROR
Noise
==

## Slide 30: Error Detection Code: Parity
Add one bit, such that the number of 1’s is even.
Noise
0000
0
0001
1
1001
0
0001
0
0001
1
1111
0



Problem: This simple parity cannot detect two-bit errors.

## Slide 31: Parity Checking
Single Bit Parity:
Detect single bit errors
Two Dimensional Bit Parity:
Detect and correct single bit errors
0
0

## Slide 32: Internet checksum
Sender:
treat segment contents as sequence of 1bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?
Goal: detect “errors” (e.g., flipped bits) in transmitted packet (note: used at transport layer only)
Notes: Start here March 2nd 2012

## Slide 33: Error Detection Code: CRC
CRC means “Cyclic Redundancy Check”.
More powerful than parity.
  It can detect various kinds of errors, including 2-bit errors.
More complex: multiplication, binary division.
Parameterized by n-bit divisor P.
  Example: 3-bit divisor 101.
  Choosing good P is crucial.

## Slide 34: CRC with 3-bit Divisor 101
Multiplication by 23
D2 = D * 23
Binary Division by 101
CheckBit = (D2) rem (101)
1001
1001000
11
Add three 0’s at the end
Kurose p478 §5.2.3
Peterson p97 §2.4.3
00
1111000
1111
0
0
CRC
Parity
same check bits from Parity,
but different ones from CRC

## Slide 35: The divisor (G) – Secret sauce of CRC
If the divisor were 100, instead of 101, data 1111 and 1001 would give the same check bit 00.
Mathematical analysis about the divisor:
  Last bit should be 1.
  Should contain at least two 1’s.
  Should be divisible by 11.
ATM, HDLC, Ethernet each use a CRC with well-chosen fixed divisors
Divisor analysis keeps mathematicians in jobs
(a branch of pure math: combinatorial mathematics)

## Slide 36: Checksumming: Cyclic Redundancy Check recap
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (Ethernet, 802.11 WiFi, ATM)

## Slide 37: CRC Another Example – this time with long division
Want:
  D.2r XOR R = nP
equivalently:
  D.2r = nP XOR R
equivalently:
if we divide D.2r by P, want remainder R
R = remainder[ ]
D.2r
P
P
FYI: in K&R P is called the Generator: G

## Slide 38: Error Detection Code becomes….
Sender:
Y = generateCheckBit(X);
send(XY);
Receiver:
receive(X1Y1);
Y2=generateCheckBit(X1);
if (Y1 != Y2) ERROR;
else NOERROR
Noise
==

## Slide 39: Forward Error Correction (FEC)
Sender:
Y = generateCheckBit(X);
send(XY);
Noise
Receiver:
receive(X1Y1);
Y2=generateCheckBit(X1);
if (Y1 != Y2) FIXERROR(X1Y1);
else NOERROR
!=

## Slide 40: Forward Error Correction (FEC)
Sender:
Y = generateCheckBit(X);
send(XY);
Noise
==
Receiver:
receive(X1Y1);
Y2=generateCheckBit(X1);
if (Y1 != Y2) FIXERROR(X1Y1);
else NOERROR

## Slide 41: Basic Idea of Forward Error Correction
Replace erroneous data
by its “closest” error-free data.
00
000
01
011
10
101
11
110
01
000
11
101
10
110
Good
Good
Good
Good
Bad
Bad
Bad
3
4
2
1

## Slide 42: Error Detection vs Correction
Error Correction:
Cons: More check bits. False recovery.
Pros: No need to re-send.
Error Detection:
Cons: Need to re-send.
Pros: Less check bits.
Usage:
Correction: A lot of noise. Expensive to re-send.
Detection: Less noise. Easy to re-send.
Can be used together.

## Slide 43: Multiple Access Links and Protocols
Two types of “links”:
point-to-point
  point-to-point link between Ethernet switch and host
broadcast (shared wire or medium)
  old-fashioned wired Ethernet (here be dinosaurs – extinct)
  upstream HFC (Hybrid Fiber-Coax – the Coax may be broadcast)
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 44: Multiple Access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination

## Slide 45: Ideal Multiple Access Protocol
Broadcast channel of rate R bps
1. when one node wants to transmit, it can send at rate R
2. when M nodes want to transmit, each can send at average rate R/M
3. fully decentralized:
  no special node to coordinate transmissions
  no synchronization of clocks, slots
4. simple

## Slide 46: MAC Protocols: a taxonomy
Three broad classes:
Channel Partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
Random Access
  channel not divided, allow collisions
  “recover” from collisions
“Taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 47: Channel Partitioning MAC protocols: TDMA (time travel warning – we mentioned this earlier)
TDMA: time division multiple access
access to channel in "rounds"
each station gets fixed length slot (length = pkt trans time) in each round
unused slots go idle
example: station LAN, 1,3,4 have pkt, slots 2,5,6 idle
1
3
4
1
3
4
slot
frame

## Slide 48: Channel Partitioning MAC protocols: FDMA (time travel warning – we mentioned this earlier)
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 49: “Taking Turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
Random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 50: “Taking Turns” MAC protocols
Polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 51: “Taking Turns” MAC protocols
Token passing:
control token passed from one node to next sequentially.
token message
concerns:
  token overhead
  latency
  single point of failure (token)
concerns fixed in part by a slotted ring (many simultaneous tokens)
T
data
(nothing
to send)
T
Cambridge students – this is YOUR heritage
Cambridge RING, Cambridge Fast RING,
Cambridge Backbone RING, these things gave us ATDM (and ATM)

## Slide 52: ATM
1
3
4
1
3
4
slot
frame
1
3
4
1
1
4
ATM = Asynchronous Transfer Mode – an ugly expression
think of it as ATDM – Asynchronous Time Division Multiplexing
That’s PACKET SWITCHING to the rest of us – just like Ethernet
but using fixed length slots/packets/cells
Use the media when you need it, but
ATM had virtual circuits and these needed setup….
Worse ATM had an utterly irrational size
In TDM a sender may only use a pre-allocated slot
In ATM a sender transmits labeled cells whenever necessary
3

## Slide 53: ATM Layer: ATM cell (size = best known stupid feature)
48-byte payload
  Why?: small payload -> short cell-creation delay for digitized voice
  halfway between 32 and 64 (compromise!)
5-byte ATM cell header (10% of payload)
Cell header
Cell format

## Slide 54: ATM – redux, the irony (a 60 second sidetrack)
Size issues once plagued ATM
- too little time to do useful work
now plague the common Internet MTU
Even jumbo grams (9kB) are argued as not big enough
Consider issues
default Ethernet CRC not robust for 9k packets
  IPv6 checksum implications
MTU discovery ugliness
  (discovering MTU is hard anyway)
Is time-per-packet a sensible justification?

## Slide 55: None of these are the “Internet way”… (Bezerkely, 60’s, free stuff, no G-man)
Seriously; why not?
What’s wrong with
  TDMA
  FDMA
  Polling
  Token passing
  ATM
Turn to random access
  Optimize for the common case (no collision)
  Don’t avoid collisions, just recover from them….
    Sound familiar?
    What could possibly go wrong….
Management. Suites. Rules. Schedules.
Signs, signs, everywhere a sign….

## Slide 56: Random Access Protocols
When node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
Examples of random access MAC protocols:
  ALOHA and slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 57: Random Access MAC Protocols
When node has packet to send
  Transmit at full channel data rate
  No a priori coordination among nodes
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies:
  How to detect collisions
  How to recover from collisions
Examples
  ALOHA and Slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA (wireless)

## Slide 58: Key Ideas of Random Access
Carrier sense
  Listen before speaking, and don’t interrupt
  Checking if someone else is already sending data
  … and waiting till the other node is done
Collision detection
  If someone else starts talking at the same time, stop
  Realizing when two nodes are transmitting at once
  …by detecting that the data on the wire is garbled
Randomness
  Don’t start talking again right away
  Waiting for a random time before trying again

## Slide 59: Where it all Started: AlohaNet
Norm Abramson left Stanford to surf
Set up first data communication system for Hawaiian islands
Hub at U. Hawaii, Oahu
Had two radio channels:
  Random access:
    Sites sending data
  Broadcast:
    Hub rebroadcasting data
Notes: Brilliant person + practical problem = interesting development

## Slide 60: Aloha Signaling
Two channels: random access, broadcast
Sites send packets to hub (random)
  If received, hub sends ACK (random)
  If not received (collision), site resends
Hub sends packets to all sites (broadcast)
  Sites can receive even if they are also sending
Questions:
  When do you resend? Resend with probability p
  How does this perform? Need a clean model….

## Slide 61: Pure (unslotted) ALOHA
unslotted Aloha: simple, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 62: Pure Aloha efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [p0-1,p0] .
P(no other node transmits in [p0-1,p0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n -> ∞ ...
= 1/(2e) = .18
Best described as unspectacular; but better than what went before.

## Slide 63: Slotted ALOHA
Assumptions
All frames same size
Time divided into equal slots (time to transmit a frame)
Nodes are synchronized
Nodes begin to transmit frames only at start of slots
If multiple nodes transmit, nodes detect collision
Operation
When node gets fresh data, transmits in next slot
No collision: success!
Collision: node retransmits with probability p until success

## Slide 64: Slot-by-Slot Example

## Slide 65: Efficiency of Slotted Aloha
Suppose N stations have packets to send
  Each transmits in slot with probability p
Probability of successful transmission: by a particular node i: Si = p (1-p)(N-1) by any of N nodes: S= N p (1-p)(N-1)
What value of p maximizes prob. of success:
  For fixed p, S  0 as N increases
  But if p = 1/N, then S  1/e = 0.37 as N increases
Max efficiency is only slightly greater than 1/3!

## Slide 66: Pros and Cons of Slotted Aloha
Pros
Single active node can continuously transmit at full rate of channel
Highly decentralized: only need slot synchronization
Simple
Cons
Wasted slots:
  Idle
  Collisions
Collisions consume entire slot
Clock synchronization
Notes: Why is clock synchonization necessary?
It isn’t, but if we get rid of it, efficiency goes down…

## Slide 67: Improving on Slotted Aloha
Fewer wasted slots
  Need to decrease collisions and empty slots
Don’t waste full slots on collisions
  Need to decrease time to detect collisions
Avoid need for synchronization
  Synchronization is hard to achieve
Notes: Which of these are the most important!

## Slide 68: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!
Does this eliminate all collisions?
  No, because of nonzero propagation delay
Notes: end here 2nd Mar Fri

## Slide 69: CSMA Collisions
Propagation delay: two nodes may not hear each other’s before sending.
Would slots hurt or help?
CSMA reduces but does not eliminate collisions
Biggest remaining problem?
Collisions still take full slot!
How do you fix that?
Notes: Ask: who knows? (from knowing ethernet)?
Someone who doesn’t, how to do this?
Listen before sending to detect possible collision
Why not listen to detect current collision!

## Slide 70: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection easy in wired LANs:
  Compare transmitted, received signals
Collision detection difficult in wireless LANs:
  Reception shut off while transmitting (well, perhaps not)
  Not perfect broadcast (limited range) so collisions local
  Leads to use of collision avoidance instead (later)

## Slide 71: CSMA/CD Collision Detection
B and D can tell that collision occurred.
Note: for this to work, need restrictions on minimum frame size and maximum distance. Why?
Notes: Draw failed collision detection….

## Slide 72: Limits on CSMA/CD Network Length
Latency depends on physical length of link
  Time to propagate a packet from one end to the other
Suppose A sends a packet at time t
  And B sees an idle line at a time just before t+d
  … so B happily starts transmitting a packet
B detects a collision, and sends jamming signal
  But A can’t see collision until t+2d
latency d
A
B

## Slide 73: Limits on CSMA/CD Network Length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  … and keep an eye out for a possible collision
Imposes restrictions. E.g., for 10 Mbps Ethernet:
  Maximum length of the wire: 2,500 meters
  Minimum length of a frame: 512 bits (64 bytes)
    512 bits = 51.2 sec (at 10 Mbit/sec)
    For light in vacuum, 51.2 sec ≈ 15,000 meters vs. 5,000 meters “round trip” to wait for collision
  What about 10Gbps Ethernet?
latency d
A
B
Notes: 10Gbps is switched, doesn’t have this problem!!!

## Slide 74: Performance of CSMA/CD
Time wasted in collisions
  Proportional to distance d
Time spend transmitting a packet
  Packet length p divided by bandwidth b
Rough estimate for efficiency (K some constant)
Note:
  For large packets, small distances, E ~ 1
  As bandwidth increases, E decreases
  That is why high-speed LANs are all switched
Notes: K represents number of collisions per transmission….

## Slide 75: Benefits of Ethernet
Easy to administer and maintain
Inexpensive
Increasingly higher speed
Evolvable!

## Slide 76: Evolution of Ethernet
Changed everything except the frame format
  From single coaxial cable to hub-based star
  From shared media to switches
  From electrical signaling to optical
Lesson #1
  The right interface can accommodate many changes
  Implementation is hidden behind interface
Lesson #2
  Really hard to displace the dominant technology
  Slight performance improvements are not enough

## Slide 77: Ethernet: CSMA/CD Protocol
Carrier sense: wait for link to be idle
Collision detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission & send jam signal
Random access: binary exponential back-off
  After collision, wait a random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again
    Using min packet size as “slot”
    If transmission occurring when ready to send, wait until end of transmission (CSMA)

## Slide 78: Binary Exponential Backoff (BEB)
Think of time as divided in slots
After each collision, pick a slot randomly within next 2m slots
  Where m is the number of collisions since last successful transmission
Questions:
  Why backoff?
  Why random?
  Why 2m?
  Why not listen while waiting?
Notes: How would listening help?

## Slide 79: Behavior of BEB Under Light Load
Look at collisions between two nodes
First collision: pick one of the next two slots
  Chance of success after first collision: 50%
  Average delay 1.5 slots
Second collision: pick one of the next four slots
  Chance of success after second collision: 75%
  Average delay 2.5 slots
In general: after mth collision
  Chance of success: 1-2-m
  Average delay (in slots): ½ + 2(m-1)

## Slide 80: BEB: Theory vs Reality
In theory, there is no difference between theory and practice. But, in practice, there is.

## Slide 81: BEB Reality
Performs well (far from optimal, but no one cares)
  Large packets are ~23 times as large as minimal slot
Is now mostly irrelevant
  Almost all current ethernets are switched

## Slide 82: BEB Theory
A very interesting algorithm
Stability for finite N only proved in 1985
  Ethernet can handle nonzero traffic load without collapse
All backoff algorithms unstable for infinite N (1985)
  Poisson model: infinite user pool, total demand is finite
Not of practical interest, but gives important insight
  Multiple access should be in your “bag of tricks”
Notes: e.g., know most important way to spread a rumor…

## Slide 83: Question
Two hosts, each with infinite packets to send
What happens under BEB?
Throughput high or low?
Bandwidth shared equally or not?

## Slide 84: MAC “Channel Capture” in BEB
Finite chance that first one to have a successful transmission will never relinquish the channel
  The other host will never send a packet
Therefore, asymptotically channel is fully utilized and completely allocated to one host

## Slide 85: Example
Two hosts, each with infinite packets to send
  Slot 1: collision
  Slot 2: each resends with prob ½
    Assume host A sends, host B does not
  Slot 3: A and B both send (collision)
  Slot 4: A sends with probability ½, B with prob. ¼
    Assume A sends, B does not
  Slot 5: A definitely sends, B sends with prob. ¼
    Assume collision
  Slot 6: A sends with probability ½, B with prob. 1/8
Conclusion: if A gets through first, the prob. of B sending successfully halves with each collision

## Slide 86: Another Question
Hosts now have large but finite # packets to send
What happens under BEB?
Throughput high or low?

## Slide 87: Answer
Efficiency less than one, no matter how many packets
Time you wait for loser to start is proportion to time winner was sending….

## Slide 88: Different Backoff Functions
Exponential: backoff ~ ai
  Channel capture?
  Efficiency?
Superlinear polynomial: backoff ~ ip p>1
  Channel capture?
  Efficiency?
Sublinear polynomial: backoff ~ ip p≤1
  Channel capture?
  Efficiency?

## Slide 89: Different Backoff Functions
Exponential: backoff ~ ai
  Channel capture (loser might not send until winner idle)
  Efficiency less than 1 (time wasted waiting for loser to start)
Superlinear polynomial: backoff ~ ip p>1
  Channel capture
  Efficiency is 1 (for any finite # of hosts N)
Sublinear polynomial: backoff ~ ip p≤1
  No channel capture (loser not shut out)
  Efficiency is less than 1 (and goes to zero for large N)
    Time wasted resolving collisions

## Slide 90: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, IBM Token Ring

## Slide 91: MAC Addresses (and ARP) or How do I glue my network to my data-link?
32-bit IP address:
  network-layer address
  used to get datagram to destination IP subnet
MAC (or LAN or physical or Ethernet) address:
  function: get frame from one interface to another physically-connected interface (same network)
  48 bit MAC address (for most LANs)
    burned in NIC ROM, also sometimes software settable

## Slide 92: LAN Address (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
(a) MAC address: like Social Security Number
(b) IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  address depends on IP subnet to which node is attached

## Slide 93: LAN Addresses and ARP
Each adapter on LAN has unique LAN address
Ethernet
Broadcast address =
FF-FF-FF-FF-FF-FF
= adapter
1A-2F-BB-709-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-6F7-2B-08-53
LAN
(wired or
wireless)

## Slide 94: Address Resolution Protocol
Every node maintains an ARP table
  <IP address, MAC address> pair
Consult the table when sending a packet
  Map destination IP address to destination MAC address
  Encapsulate and transmit the data packet
But: what if IP address not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches result in its ARP table
Notes: Wed 7th start here.

## Slide 95: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B

## Slide 96: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B
1. A sends packet to R. 2. R sends packet to B.

## Slide 97: Host A Decides to Send Through R
A
R
B
Host A constructs an IP packet to send to B
  Source 111.111.111.111, destination 222.222.222.222
Host A has a gateway router R
  Used to reach destinations outside of 111.111.111.0/24
  Address 111.111.111.110 for R learned via DHCP/config

## Slide 98: Host A Sends Packet Through R
Host A learns the MAC address of R’s interface
  ARP request: broadcast request for 111.111.111.110
  ARP response: R responds with EE9-00-17-BB-4B
Host A encapsulates the packet and sends to R
A
R
B

## Slide 99: R Decides how to Forward Packet
Router R’s adaptor receives the packet
  R extracts the IP packet from the Ethernet frame
  R sees the IP packet is destined to 222.222.222.222
Router R consults its forwarding table
  Packet matches 222.222.222.0/24 via other adaptor
A
R
B

## Slide 100: R Sends Packet to B
Router R’s learns the MAC address of host B
  ARP request: broadcast request for 222.222.222.222
  ARP response: B responds with 49-BD-D2-C7-52A
Router R encapsulates the packet and sends to B
A
R
B

## Slide 101: Security Analysis of ARP
Impersonation
  Any node that hears request can answer …
  … and can say whatever they want
Actual legit receiver never sees a problem
  Because even though later packets carry its IP address, its NIC doesn’t capture them since not its MAC address

## Slide 102: Key Ideas in Both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
  Remember your own address & other host’s addresses
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 103: Why Not Use DNS-Like Tables?
When host arrives:
  Assign it an IP address that will last as long it is present
  Add an entry into a table in DNS-server that maps MAC to IP addresses
Answer:
  Names: explicit creation, and are plentiful
  Hosts: come and go without informing network
    Must do mapping on demand
  Addresses: not plentiful, need to reuse and remap
    Soft-state enables dynamic reuse
Notes: Two key points

## Slide 104: Hubs
… physical-layer (“dumb”) repeaters:
  bits coming in one link go out all other links at same rate
  all nodes connected to hub can collide with one another
  no frame buffering
  no CSMA/CD at hub: host NICs detect collisions
Co-ax or twisted pair
hub

## Slide 105: CSMA/CD Lives….
Home Plug and similar Powerline Networking….

## Slide 106: Switch (like a Hub but smarter)
link-layer device: smarter than hubs, take active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 107: Switch: allows multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ simultaneously, without collisions
  not possible with dumb hub
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 108: Switch Table
Q: how does switch know that A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 109: Switch: self-learning (recap)
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 110: Switch: frame filtering/forwarding
When frame received:
1. record link associated with sending host
2. index switch table using MAC dest address
3. if entry found for destination then {
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 111: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination unknown:
flood
A’ A
destination A location known:
A’
4
60
selective send

## Slide 112: Interconnecting switches
switches can be connected together
A
B
Q: sending from A to G - how does S1 know to forward frame destined to F via S4 and S3?
A: self learning! (works exactly the same as in single-switch case – flood/forward/drop)
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 113: Flooding Can Lead to Loops
Flooding can lead to forwarding loops
  E.g., if the network contains a cycle of switches
  “Broadcast storm”

## Slide 114: Solution: Spanning Trees
Ensure the forwarding topology has no loops
  Avoid using some of the links when flooding
  … to prevent loop from forming
Spanning tree
  Sub-graph that covers all vertices but contains no cycles
  Links not in the spanning tree do not forward frames
Graph Has Cycles!
Graph Has No Cycles!

## Slide 115: What Do We Know?
Shortest paths to (or from) a node form a tree
So, algorithm has two aspects :
  Pick a root
  Compute shortest paths to it
Only keep the links on shortest-path

## Slide 116: Constructing a Spanning Tree
Switches need to elect a root
  The switch w/ smallest identifier (MAC addr)
Each switch determines if each interface is on the shortest path from the root
  Excludes it from the tree if not
Messages (Y, d, X)
  From node X
  Proposing Y as the root
  And the distance is d
root
One hop
Three hops

## Slide 117: Steps in Spanning Tree Algorithm
Initially, each switch proposes itself as the root
  Switch sends a message out every interface
  … proposing itself as the root with distance 0
  Example: switch X announces (X, 0, X)
Switches update their view of the root
  Upon receiving message (Y, d, Z) from Z, check Y’s id
  If new id smaller, start viewing that switch as root
Switches compute their distance from the root
  Add 1 to the distance received from a neighbor
  Identify interfaces not on shortest path to the root
  … and exclude them from the spanning tree
If root or shortest distance to it changed, “flood” updated message (Y, d+1, X)

## Slide 118: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 119: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 Iink from the tree
1
2
3
4
5
6
7

## Slide 120: Robust Spanning Tree Algorithm
Algorithm must react to failures
  Failure of the root node
    Need to elect a new root, with the next lowest identifier
  Failure of other switches and links
    Need to recompute the spanning tree
Root switch continues sending messages
  Periodically reannouncing itself as the root (1, 0, 1)
  Other switches continue forwarding messages
Detecting failures through timeout (soft state)
  If no word from root, times out and claims to be the root
  Delay in reestablishing spanning tree is major problem
  Work on rapid spanning tree algorithms…

## Slide 121: Switches vs. Routers Summary
both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  switches are link layer devices
routers maintain routing tables, implement routing algorithms
switches maintain switch tables, implement filtering, learning algorithms
Notes: FINAL SLIDE IN PART 5

## Slide 122: Wireless

## Slide 123
Notes: Rapid evolution in the wireless eco-system – hard to keep up.
Both technologies and business-models

## Slide 124
Metrics for evaluation / comparison of wireless technologies
Bitrate or Bandwidth
Range - PAN, LAN, MAN, WAN
Two-way / One-way
Multi-Access / Point-to-Point
Digital / Analog
Applications and industries
Frequency – Affects most physical properties: Distance (free-space loss) Penetration, Reflection, Absorption Energy proportionality Policy: Licensed / Deregulated
Line of Sight (Fresnel zone)
Size of antenna
Determined by wavelength – )
Notes: Bitrate or Bandwidth
Range - PAN, LAN, MAN, WAN
Two-way / One-way
Multi-Access / Point-to-Point
Digital / Analog
Applications and industries
Frequency – Affects most physical properties: Distance (free-space loss) Penetration, Reflection, Absorption Energy proportionality Policy: Licensed / Deregulated
Line of Sight (Fresnel zone)
Size of antenna
(determined by wavelength – )

## Slide 125
Modern art?
Notes: Allocated to license holders.
Occasionally (rarely) a chunk gets offered for bidding – for billions of dollars.

## Slide 126
The Wireless Spectrum
Notes: FCC allocates spectrum to users – who are these?
Govt. itself (various agencies), military.
Public-safety.
Broadcasters
Telecommunications providers (aka operators) – license holders.
Different bands behave differently …
Most wave propagation properties are frequency/wave-length dependent:

## Slide 127: Wireless Communication Standards
Cellular (800/900/1700/1800/1900Mhz):
  2G: GSM / CDMA / GPRS /EDGE
  3G: CDMA2000/UMTS/HSDPA/EVDO
  4G: LTE, WiMax
IEEE 802.11 (aka WiFi):
  b: 2.4Ghz band, 11Mbps (~4.5 Mbps operating rate)
  g: 2.4Ghz, 54-108Mbps (~19 Mbps operating rate)
  a: 5.0Ghz band, 54-108Mbps (~25 Mbps operating rate)
  n: 2.4/5Ghz, 150-600Mbps (4x4 mimo).
IEEE 802.15 – lower power wireless:
  802.15.1: 2.4Ghz, 2.1 Mbps (Bluetooth)
  802.15.4: 2.4Ghz, 250 Kbps (Sensor Networks)
127
Notes: start from here 9 March

## Slide 128: Wireless Link Characteristics
128
(Figure Courtesy of Kurose and Ross)
Notes: Naturally – there exist technologies for longer distances…
Also – we already have affordable off-the-shelf gear for gigabit+ speeds…
Why not use any of the outdoors technologies also indoors – surely it would work…?
802.11n can do much faster today – 600Mbps (4x4 MIMO)…
This demonstrates the openness and flexibility of the standard, which mostly deals with link-layer elements while allowing diversity of underlying physical layer technologies.

## Slide 129: Antennas / Aerials
An electrical device which converts electric currents into radio waves, and vice versa.
Q: What does “higher-gain antenna” mean?
A: Antennas are passive devices – more gain means focused and more directional.
Directionality means more energy gets to where it needs to go and less interference everywhere.
What are omni-directional antennas?
2-3dB 8-12dB 15-18dB 28-34dB
Notes: What antennas are inside a cell-phone?

## Slide 130: What has changed?
Notes: I used to make calls from 40 miles away – not anymore…
Cellular towers climbed down from the mountain-tops and attempt to reduce/contain their footprint.

## Slide 131: How many radios/antennas ?
WiFi 802.11n (maybe MiMo?)
2G - GSM
3G – HSDPA+
4G – LTE
Bluetooth (4.0)
NFC
GPS Receiver
FM-Radio receiver (antenna is the headphones cable)

## Slide 132: What Makes Wireless Different?
Broadcast and multi-access medium…
  Just like AlohaNet – isn’t this where we came in?
Signals sent by sender don’t always end up at receiver intact
  Complicated physics involved, which we won’t discuss
  But what can go wrong?

## Slide 133: Path Loss / Path Attenuation
Free Space Path Loss:
d = distance
λ = wave length
f = frequency
c = speed of light
Reflection, Diffraction, Absorption
Terrain contours (Urban, Rural, Vegetation).
Humidity
Notes: reduction in power density (attenuation) of an electromagnetic wave as it propagates through space.
Path loss may be due to many effects, such as free-space loss,refraction, diffraction, reflection, aperture-medium coupling loss, and absorption. Path loss is also influenced by terrain contours, environment (urban or rural, vegetation and foliage), propagation medium (dry or moist air), the distance between the transmitter and the receiver, and the height and location of antennas.

## Slide 134: Multipath Effects
Signals bounce off surface and interfere with one another
Self-interference
134
S
R
Ceiling
Floor

## Slide 135: Ideal Radios (courtesy of Gilman Tolle and Jonathan Hui, ArchRock)

## Slide 136: Real Radios (courtesy of Gilman Tolle and Jonathan Hui, ArchRock)

## Slide 137: The Amoeboed “cell” (courtesy of David Culler, UCB)
137
Signal
Noise
Distance
Notes: 137

## Slide 138: Interference from Other Sources
External Interference
  Microwave is turned on and blocks your signal
  Would that affect the sender or the receiver?
Internal Interference
  Hosts within range of each other collide with one another’s transmission
We have to tolerate path loss, multipath, etc., but we can try to avoid internal interference

## Slide 139: SNR – the key to communication:
Bitrate (aka data-rate)
The higher the SNR –
the higher the (theoretical) bitrate.
Modern radios use adaptive /dynamic bitrates.
Q: In face of loss, should we decrease or increase the bitrate?
A: If caused by free-space loss or multi-path fading -lower the bitrate.
If external interference - often higher bitrates (shorter bursts) are probabilistically better.
Signal to Noise Ratio

## Slide 140: Wireless Bit Errors
The lower the SNR (Signal/Noise) the higher the Bit Error Rate (BER)
We could make the signal stronger…
Why is this not always a good idea?
  Increased signal strength requires more power
  Increases the interference range of the sender, so you interfere with more nodes around you
    And then they increase their power…….
How would TCP behave in face of losses?
  TCP conflates loss (congestion) with loss local errors
Local link-layer Error Correction schemes can correct some problems (should be TCP aware).
140

## Slide 141: 802.11
141
aka - WiFi …
What makes it special?
Deregulation > Innovation > Adoption > Lower cost = Ubiquitous technology
Notes: 141
JUST LIKE ETHERNET – not lovely but sufficient

## Slide 142: 802.11 Architecture
Designed for limited area
AP’s (Access Points) set to specific channel
Broadcast beacon messages with SSID (Service Set Identifier) and MAC Address periodically
Hosts scan all the channels to discover the AP’s
  Host associates with AP
142
802.11 frames exchanges
802.3 (Ethernet) frames exchanged

## Slide 143: Wireless Multiple Access Technique?
Carrier Sense?
  Sender can listen before sending
  What does that tell the sender?
Collision Detection?
  Where do collisions occur?
  How can you detect them?
Notes: stopped here 9 mar

## Slide 144: Hidden Terminals
144
A and C can both send to B but can’t hear each other
  A is a hidden terminal for C and vice versa
Carrier Sense will be ineffective
A
B
C
transmit range
Notes: 144

## Slide 145: Exposed Terminals
145
Exposed node: B sends a packet to A; C hears this and decides not to send a packet to D (despite the fact that this will not cause interference)!
Carrier sense would prevent a successful transmission.
A
B
C
D
Notes: 145

## Slide 146: Key Points
No concept of a global collision
  Different receivers hear different signals
  Different senders reach different receivers
Collisions are at receiver, not sender
  Only care if receiver can hear the sender clearly
  It does not matter if sender can hear someone else
  As long as that signal does not interfere with receiver
Goal of protocol:
  Detect if receiver can hear sender
  Tell senders who might interfere with receiver to shut up

## Slide 147: Basic Collision Avoidance
Since can’t detect collisions, we try to avoid them
Carrier sense:
  When medium busy, choose random interval
  Wait that many idle timeslots to pass before sending
When a collision is inferred, retransmit with binary exponential backoff (like Ethernet)
  Use ACK from receiver to infer “no collision”
  Use exponential backoff to adapt contention window
Notes: Why do we wait?
Why not just send right away as medium becomes clear?

## Slide 148: CSMA/CA -MA with Collision Avoidance
148
Before every data transmission
  Sender sends a Request to Send (RTS) frame containing the length of the transmission
  Receiver respond with a Clear to Send (CTS) frame
  Sender sends data
  Receiver sends an ACK; now another sender can send data
When sender doesn’t get a CTS back, it assumes collision
sender
receiver
other node in
sender’s range
RTS
ACK
data
CTS
Notes: 148

## Slide 149: CSMA/CA, con’t
149
If other nodes hear RTS, but not CTS: send
  Presumably, destination for first sender is out of node’s range …
sender
receiver
other node in
sender’s range
RTS
data
CTS
data
Notes: 149

## Slide 150: CSMA/CA, con’t
150
If other nodes hear RTS, but not CTS: send
  Presumably, destination for first sender is out of node’s range …
  … Can cause problems when a CTS is lost
When you hear a CTS, you keep quiet until scheduled transmission is over (hear ACK)
sender
receiver
other node in
sender’s range
RTS
ACK
data
CTS
Notes: 150

## Slide 151: RTS / CTS Protocols (CSMA/CA)
151
Overcome hidden terminal problems with contention-free protocol
  B sends to C Request To Send (RTS)
  A hears RTS and defers (to allow C to answer)
  C replies to B with Clear To Send (CTS)
  D hears CTS and defers to allow the data
  B sends to C
B
C
D
RTS
CTS
A
B sends to C
Notes: 151
Does not solve the exposed terminal problem.
High overhead and especially increase latency.
assumes symmetric signal qualities - if node A hears node B - than also node B hears node A. - not always the case. (Especially local interference at receiver).

## Slide 152: Preventing Collisions Altogether
Frequency Spectrum partitioned into several channels
  Nodes within interference range can use separate channels
  Now A and C can send without any interference!
Most cards have only 1 transceiver
  Not Full Duplex: Cannot send and receive at the same time
  Aggregate Network throughput doubles
152
A
B
C
D

## Slide 153
802.11: advanced capabilities
Rate Adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER

## Slide 154
802.11: advanced capabilities
Power Management
node-to-AP: “I am going to sleep until next beacon frame”
  AP knows not to transmit frames to this node
  node wakes up before next beacon frame
beacon frame: contains list of mobiles with AP-to-mobile frames waiting to be sent
  node will stay awake if AP-to-mobile frames to be sent; otherwise sleep again until next beacon frame