## Slide 1
Computer Networking
Lent Term M/W/F 11-midday
LT1 in Gates Building
Slide Set 5
Andrew W. Moore
andrew.moore@cl.cam.ac.uk
January 2013

## Slide 2: Topic 5 – Transport
Our goals:
understand principles behind transport layer services:
  multiplexing/demultiplexing
  reliable data transfer
  flow control
  congestion control
learn about transport layer protocols in the Internet:
  UDP: connectionless transport
  TCP: connection-oriented transport
  TCP congestion control

## Slide 3: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
Notes: Difference between Engineers and CS (reliability versus layering)

## Slide 4: Transport vs. network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
Household analogy:
12 kids sending letters to 12 kids
processes = kids
app messages = letters in envelopes
hosts = houses
transport protocol = Ann and Bill
network-layer protocol = postal service

## Slide 5: Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 6: Multiplexing/demultiplexing (Transport-layer style)
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
gathering data from multiple
sockets, enveloping data with
header (later used for
demultiplexing)
Multiplexing at send host:

## Slide 7: How transport-layer demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 8: Connectionless demultiplexing
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(12534);
DatagramSocket mySocket2 = new DatagramSocket(12535);
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 9: Connectionless demux (cont)
DatagramSocket serverSocket = new DatagramSocket(6428);
Client
IP:B
P2
client
IP: A
P1
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428
SP provides “return address”

## Slide 10: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
recv host uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 11: Connection-oriented demux (cont)
Client
IP:B
P1
client
IP: A
P1
P2
P4
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P5
P6
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B

## Slide 12: Connection-oriented demux: Threaded Web Server
Client
IP:B
P1
client
IP: A
P1
P2
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P4
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B

## Slide 13: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

## Slide 14: UDP: more
often used for streaming multimedia apps
  loss tolerant
  rate sensitive
other UDP uses
  DNS
  SNMP
reliable transfer over UDP: add reliability at application layer
  application-specific error recovery!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 15: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 16: Internet Checksum (time travel warning – we covered this earlier)
Note
  When adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 17: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
Notes: MAKE CLEAR THE OBJECTIVE (function)
- RELIABLE data transfer

## Slide 18: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 19: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
rdt_rcv()
udt_rcv()

## Slide 20: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called by rdt to deliver data to upper
rdt_rcv()
udt_rcv()
udt_rcv(): called when packet arrives on rcv-side of channel

## Slide 21: Reliable data transfer: getting started
We’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 22: KR state machines – a note.
Beware
Kurose and Ross has a confusing/confused attitude to state-machines.
I’ve attempted to normalise the representation.
UPSHOT: these slides have differing information to the KR book (from which the RDT example is taken.)
in KR “actions taken” appear wide-ranging, my interpretation is more specific/relevant.
State
name
State
name
Relevant event causing state transition
Relevant action taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 23: Rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver read data from underlying channel
IDLE
udt_send(packet)
rdt_send(data)
rdt_rcv(data)
IDLE
udt_rcv(packet)
sender
receiver
Event
Action

## Slide 24: Rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that packet received is OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that packet had errors
  sender retransmits packet on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) receiver->sender

## Slide 25: rdt2.0: FSM specification
IDLE
udt_send(packet)
rdt_rcv(data)
udt_send(ACK)
udt_rcv(packet) && notcorrupt(packet)
udt_rcv(reply) && isACK(reply)
udt_send(packet)
udt_rcv(reply) &&
isNAK(reply)
udt_send(NAK)
udt_rcv(packet) && corrupt(packet)
Waiting
for reply
IDLE
sender
receiver
rdt_send(data)
L
Note: the sender holds a copy of the packet being sent until the delivery is acknowledged.

## Slide 26: rdt2.0: operation with no errors
L
IDLE
Waiting
for reply
IDLE
udt_send(packet)
rdt_rcv(data)
udt_send(ACK)
udt_rcv(packet) && notcorrupt(packet)
udt_rcv(reply) && isACK(reply)
udt_send(packet)
udt_rcv(reply) &&
isNAK(reply)
udt_send(NAK)
udt_rcv(packet) && corrupt(packet)
rdt_send(data)

## Slide 27: rdt2.0: error scenario
L
IDLE
Waiting
for reply
IDLE
udt_send(packet)
rdt_rcv(data)
udt_send(ACK)
udt_rcv(packet) && notcorrupt(packet)
udt_rcv(reply) && isACK(reply)
udt_send(packet)
udt_rcv(reply) &&
isNAK(reply)
udt_send(NAK)
udt_rcv(packet) && corrupt(packet)
rdt_send(data)

## Slide 28: rdt2.0 has a fatal flaw!
What happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
Handling duplicates:
sender retransmits current packet if ACK/NAK garbled
sender adds sequence number to each packet
receiver discards (doesn’t deliver) duplicate packet
Sender sends one packet,
then waits for receiver
response
stop and wait

## Slide 29: rdt2.1: sender, handles garbled ACK/NAKs
IDLE
sequence=0
udt_send(packet)
rdt_send(data)
Waiting
For reply
udt_send(packet)
udt_rcv(reply) &&
( corrupt(reply) ||
isNAK(reply) )
sequence=1
udt_send(packet)
rdt_send(data)
udt_rcv(reply)
&& notcorrupt(reply)
&& isACK(reply)
udt_send(packet)
udt_rcv(reply) &&
( corrupt(reply) ||
isNAK(reply) )
udt_rcv(reply)
&& notcorrupt(reply)
&& isACK(reply)
IDLE
Waiting
for reply
L
L

## Slide 30: rdt2.1: receiver, handles garbled ACK/NAKs
udt_rcv(packet) && corrupt(packet)
Wait for
0 from below
udt_send(NAK)
receive(packet) &&
not corrupt(packet) &&
has_seq0(packet)
udt_rcv(packet) && not corrupt(packet)
&& has_seq1(packet)
udt_send(ACK)
rdt_rcv(data)
Wait for
1 from below
udt_rcv(packet) && not corrupt(packet)
&& has_seq0(packet)
udt_send(ACK)
rdt_rcv(data)
udt_send(ACK)
receive(packet) &&
not corrupt(packet) &&
has_seq1(packet)
receive(packet) && corrupt(packet)
udt_send(ACK)
udt_send(NAK)

## Slide 31: rdt2.1: discussion
Sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “current” pkt has a
  0 or 1 sequence number
Receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 32: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 33: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sequence=0
udt_send(packet)
rdt_send(data)
udt_send(packet)
rdt_rcv(reply) &&
( corrupt(reply) ||
isACK1(reply) )
udt_rcv(reply)
&& not corrupt(reply)
&& isACK0(reply)
Wait for ACK
0
sender FSM
fragment
Wait for
0 from below
receive(packet) && not corrupt(packet)
&& has_seq1(packet)
send(ACK1)
rdt_rcv(data)
udt_rcv(packet) &&
(corrupt(packet) ||
has_seq1(packet))
udt_send(ACK1)
receiver FSM
fragment
L

## Slide 34: rdt3.0: channels with errors and loss
New assumption: underlying channel can also lose packets (data or ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but use of seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 35: rdt3.0 sender
udt_rcv(reply) &&
( corrupt(reply) ||
isACK(reply,1) )
sequence=0
udt_send(packet)
rdt_send(data)
Wait for ACK0
IDLE
state 1
sequence=1
udt_send(packet)
rdt_send(data)
udt_rcv(reply)
&& notcorrupt(reply)
&& isACK(reply,0)
udt_rcv(packet) &&
( corrupt(packet) ||
isACK(reply,0) )
udt_rcv(reply)
&& notcorrupt(reply)
&& isACK(reply,1)
L
L
udt_send(packet)
timeout
udt_send(packet)
timeout
udt_rcv(reply)
IDLE
state 0
Wait for ACK1
L
udt_rcv(reply)
L
L
L

## Slide 36: rdt3.0 in action

## Slide 37: rdt3.0 in action

## Slide 38: Performance of rdt3.0
rdt3.0 works, but performance stinks
ex: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  U sender: utilization – fraction of time sender busy sending
  1KB pkt every 30 msec -> 33kB/sec thruput over 1 Gbps link
  network protocol limits use of physical resources!

## Slide 39: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
Notes: 29th end

## Slide 40: Pipelined (Packet-Window) protocols
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
Two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 41: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!

## Slide 42: Pipelining Protocols
Go-back-N: big picture:
Sender can have up to N unacked packets in pipeline
Rcvr only sends cumulative acks
  Doesn’t ack packet if there’s a gap
Sender has timer for oldest unacked packet
  If timer expires, retransmit all unacked packets
Selective Repeat: big pic
Sender can have up to N unacked packets in pipeline
Rcvr acks individual packets
Sender maintains timer for each unacked packet
  When timer expires, retransmit only unack packet

## Slide 43: Selective repeat: big picture
Sender can have up to N unacked packets in pipeline
Rcvr acks individual packets
Sender maintains timer for each unacked packet
  When timer expires, retransmit only unack packet

## Slide 44: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
timer for each in-flight pkt
timeout(n): retransmit pkt n and all higher seq # pkts in window

## Slide 45: GBN: sender extended FSM
Wait
udt_send(packet[base])
udt_send(packet[base+1])
…
udt_send(packet[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
udt_send(packet[nextseqnum])
nextseqnum++
}
else
refuse_data(data) Block?
base = getacknum(reply)+1
udt_rcv(reply) &&
notcorrupt(reply)
base=1
nextseqnum=1
udt_rcv(reply)
&& corrupt(reply)
L
L

## Slide 46: GBN: receiver extended FSM
ACK-only: always send an ACK for correctly-received packet with the highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order packet:
  discard (don’t buffer) -> no receiver buffering!
  Re-ACK packet with highest in-order seq #
Wait
udt_send(reply)
L
udt_rcv(packet)
&& notcurrupt(packet)
&& hasseqnum(rcvpkt,expectedseqnum)
rdt_rcv(data)
udt_send(ACK)
expectedseqnum++
expectedseqnum=1
L

## Slide 47: GBN in action

## Slide 48: Selective Repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #’s
  again limits seq #s of sent, unACKed pkts

## Slide 49: Selective repeat: sender, receiver windows

## Slide 50: Selective repeat
data from above :
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 51: Selective repeat in action

## Slide 52: Selective repeat: dilemma
Example:
seq #’s: 0, 1, 2, 3
window size=3
receiver sees no difference in two scenarios!
incorrectly passes duplicate data as new in (a)
Q: what relationship between seq # size and window size?
window size ≤ (½ of seq # size)

## Slide 53: Automatic Repeat Request (ARQ)
+ Self-clocking (Automatic)
+ Adaptive
+ Flexible
- Slow to start / adapt
consider high Bandwidth/Delay product
Now lets move from
the generic to the
specific….
TCP arguably the most successful protocol in the Internet…..
its an ARQ protocol

## Slide 54: TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581, …
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 55: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 56: TCP seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario
This has led to a world of hurt….

## Slide 57: TCP out of order attack
ARQ with SACK means
  recipient needs copies of
  all packets
Evil attack one:
  send a long stream of TCP data to a server but don’t send the first byte
Recipient keeps all the subsequent data and waits…..
  Filling buffers.
    Critical buffers…
Send a legitimate request
GET index.html
this gets through an intrusion-detection system
then send a new segment replacing bytes 4-13 with
“password-file”
A dumb example.
Neither of these attacks would work on a modern system.

## Slide 58: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout
  unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT
Notes: got here 10 feb

## Slide 59: TCP Round Trip Time and Timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
Exponential weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 0.125

## Slide 60: Some RTT estimates are never good
Associating the ACK with (a) original transmission versus (b) retransmission
Karn/Partridge Algorithm – Ignore retransmission in measurements
(and increase timeout; this makes retransmissions decreasingly aggressive)

## Slide 61: Example RTT estimation:

## Slide 62: TCP Round Trip Time and Timeout
Setting the timeout
EstimtedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
first estimate of how much SampleRTT deviates from EstimatedRTT:
TimeoutInterval = EstimatedRTT + 4*DevRTT
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
Then set timeout interval:

## Slide 63: TCP reliable data transfer
TCP creates rdt service on top of IP’s unreliable service
Pipelined segments
Cumulative acks
TCP uses single retransmission timer
Retransmissions are triggered by:
  timeout events
  duplicate acks
Initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control

## Slide 64: TCP sender events:
data rcvd from app:
Create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running (think of timer as for oldest unacked segment)
expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
Ack rcvd:
If acknowledges previously unacked segments
  update what is known to be acked
  start timer if there are outstanding segments

## Slide 65: TCP sender (simplified)
NextSeqNum = InitialSeqNum
SendBase = InitialSeqNum
loop (forever) {
switch(event)
event: data received from application above
create TCP segment with sequence number NextSeqNum
if (timer currently not running)
start timer
pass segment to IP
NextSeqNum = NextSeqNum + length(data)
event: timer timeout
retransmit not-yet-acknowledged segment with
smallest sequence number
start timer
event: ACK received, with ACK field value of y
if (y > SendBase) {
SendBase = y
if (there are currently not-yet-acknowledged segments)
start timer
}
} /* end of loop forever */
Comment:
SendBase-1: last
cumulatively ack’ed byte
Example:
SendBase-1 = 71; y= 73, so the rcvr wants 73+ ; y > SendBase, so that new data is acked

## Slide 66: TCP: retransmission scenarios
Host A
Seq=100, 20 bytes data
ACK=100
time
premature timeout
Host B
Seq=92, 8 bytes data
ACK=120
Seq=92, 8 bytes data
Seq=92 timeout
ACK=120
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
time
Seq=92 timeout
SendBase
= 100
SendBase
= 120
SendBase
= 120
Sendbase
= 100

## Slide 67: TCP retransmission scenarios (more)
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
Host B
X
Seq=100, 20 bytes data
ACK=120
time
SendBase
= 120
Implicit ACK
(e.g. not Go-Back-N)
ACK=120 implicitly ACK’s 100 too

## Slide 68: TCP ACK generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediate send ACK, provided that
segment starts at lower end of gap

## Slide 69: Fast Retransmit
Time-out period often relatively long:
  long delay before resending lost packet
Detect lost segments via duplicate ACKs.
  Sender often sends many segments back-to-back
  If segment is lost, there will likely be many duplicate ACKs.
If sender receives 3 duplicate ACKs, it supposes that segment after ACKed data was lost:
  fast retransmit: resend segment before timer expires

## Slide 70
Host A
timeout
Host B
time
X
resend 2nd segment
Figure 3.37 Resending a segment after triple duplicate ACK

## Slide 71: Fast retransmit algorithm:
event: ACK received, with ACK field value of y
if (y > SendBase) {
SendBase = y
if (there are currently not-yet-acknowledged segments)
start timer
}
else {
increment count of dup ACKs received for y
if (count of dup ACKs received for y = 3) {
resend segment with sequence number y
}
a duplicate ACK for
already ACKed segment
fast retransmit

## Slide 72: Silly Window Syndrome
MSS advertises the amount a receiver can accept
If a transmitter has something to send – it will.
This means small MSS values may persist
indefinitely.
Solution
Wait to fill each segment, but don’t wait indefinitely.
NAGLE’s Algorithm
If we wait too long interactive traffic is difficult
If we don’t want we get silly window syndrome
Solution: Use a timer, when the timer expires – send the (unfilled) segment.

## Slide 73: Flow Control ≠ Congestion Control
Flow control involves preventing senders from overrunning the capacity of the receivers
Congestion control involves preventing too much data from being injected into the network, thereby causing switches or links to become overloaded

## Slide 74: Flow Control – (bad old days?)
In-Line flow control
XON/XOFF (^s/^q)
data-link dedicated symbols aka Ethernet
  (more in the Advanced Topic on Datacenters)
Dedicated wires
RTS/CTS handshaking
Read (or Write) Ready
  signals from memory interface saying slow-down/stop…

## Slide 75: TCP Flow Control
receive side of TCP connection has a receive buffer:
speed-matching service: matching the send rate to the receiving app’s drain rate
app process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control
Notes: 1st of Feb

## Slide 76: TCP Flow control: how it works
(Suppose TCP receiver discards out-of-order segments)
spare room in buffer
= RcvWindow
= RcvBuffer-[LastByteRcvd - LastByteRead]
Rcvr advertises spare room by including value of RcvWindow in segments
Sender limits unACKed data to RcvWindow
  guarantees receive buffer doesn’t overflow

## Slide 77: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
  seq. #s
  buffers, flow control info (e.g. RcvWindow)
client: connection initiator
Socket clientSocket = new Socket("hostname","port number");
server: contacted by client
Socket connectionSocket = welcomeSocket.accept();
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  specifies initial seq #
  no data
Step 2: server host receives SYN, replies with SYNACK segment
  server allocates buffers
  specifies server initial seq. #
Step 3: client receives SYNACK, replies with ACK segment, which may contain data

## Slide 78: TCP Connection Management (cont.)
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 79: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Note: with small modification, can handle simultaneous FINs.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 80: TCP Connection Management (cont)
TCP client
lifecycle
TCP server
lifecycle

## Slide 81: Principles of Congestion Control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
a top-10 problem!

## Slide 82: Causes/costs of congestion: scenario 1
two senders, two receivers
one router, infinite buffers
no retransmission
large delays when congested
maximum achievable throughput
unlimited shared output link buffers
Host A
lin : original data
Host B
lout

## Slide 83: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of lost packet
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in : original data, plus retransmitted data

## Slide 84: Causes/costs of congestion: scenario 2
always: (goodput)
“perfect” retransmission only when loss:
retransmission of delayed (not lost) packet makes larger (than perfect case) for same
l
in
l
out
=
l
in
l
out
>
l
in
l
out
“costs” of congestion:
more work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt
R/2
R/2
lin
lout
b.
R/2
R/2
lin
lout
a.
R/2
R/2
lin
lout
c.
R/4
R/3
Notes: ----- Meeting Notes (13/02/2012 10:56) -----
Monday 13/2/2012

## Slide 85: Causes/costs of congestion: scenario 3
four senders
multihop paths
timeout/retransmit
l
in
Q: what happens as and increase ?
l
in
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in : original data, plus retransmitted data

## Slide 86: Causes/costs of congestion: scenario 3
Another “cost” of congestion:
when packet dropped, any “upstream transmission capacity used for that packet was wasted!
Host A
Host B
lout
Congestion Collapse example: Cocktail party effect

## Slide 87: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
Network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate sender should send at
Two broad approaches towards congestion control:

## Slide 88: TCP congestion control: additive increase, multiplicative decrease
Approach: increase transmission rate (window size), probing for usable bandwidth, until loss occurs
  additive increase: increase CongWin by 1 MSS every RTT for each received ACK until loss detected (W W + 1/W)
  multiplicative decrease: cut CongWin in half after loss
  (W W/2)
time
congestion window size
Saw tooth
behavior: probing
for bandwidth

## Slide 89
SLOW START IS NOT SHOWN!

## Slide 90: TCP Congestion Control: details
sender limits transmission:
LastByteSent-LastByteAcked
 CongWin
Roughly,
CongWin is dynamic, function of perceived network congestion
How does sender perceive congestion?
loss event = timeout or 3 duplicate acks
TCP sender reduces rate (CongWin) after loss event
three mechanisms:
  AIMD
  slow start
  conservative after timeout events
rate =
CongWin
RTT
Bytes/sec
Notes: 3rd Feb

## Slide 91: AIMD Starts Too Slowly!
t
Window
It could take a long time to get started!
Need to start with a small CWND to avoid overloading the network.

## Slide 92: TCP Slow Start
When connection begins, CongWin = 1 MSS
  Example: MSS = 500 bytes & RTT = 200 msec
  initial rate = 20 kbps
available bandwidth may be >> MSS/RTT
  desirable to quickly ramp up to respectable rate
When connection begins, increase rate exponentially fast until first loss event

## Slide 93: TCP Slow Start (more)
When connection begins, increase rate exponentially until first loss event:
  double CongWin every RTT
  done by incrementing CongWin for every ACK received
Summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 94: Slow Start and the TCP Sawtooth
Loss
Exponential “slow start”
t
Window
Why is it called slow-start? Because TCP originally had
no congestion control mechanism. The source would just start by sending a whole window’s worth of data.

## Slide 95: Refinement: inferring loss
After 3 dup ACKs:
  CongWin is cut in half
  window then grows linearly
But after timeout event:
  CongWin instead set to 1 MSS;
  window then grows exponentially
  to a threshold, then grows linearly
3 dup ACKs indicates network capable of delivering some segments
timeout indicates a “more alarming” congestion scenario
Philosophy:

## Slide 96: Refinement
Q: When should the exponential increase switch to linear?
A: When CongWin gets to 1/2 of its value before timeout.
Implementation:
Variable Threshold
At loss event, Threshold is set to 1/2 of CongWin just before loss event

## Slide 97: Summary: TCP Congestion Control
When CongWin is below Threshold, sender in slow-start phase, window grows exponentially.
When CongWin is above Threshold, sender is in congestion-avoidance phase, window grows linearly.
When a triple duplicate ACK occurs, Threshold set to CongWin/2 and CongWin set to Threshold.
When timeout occurs, Threshold set to CongWin/2 and CongWin is set to 1 MSS.

## Slide 98: TCP sender congestion control
State | Event | TCP Sender Action | Commentary
Slow Start (SS) | ACK receipt for previously unacked data | CongWin = CongWin + MSS, If (CongWin > Threshold) set state to “Congestion Avoidance” | Resulting in a doubling of CongWin every RTT
Congestion Avoidance (CA) | ACK receipt for previously unacked data | CongWin = CongWin+MSS * (MSS/CongWin) | Additive increase, resulting in increase of CongWin by 1 MSS every RTT
SS or CA | Loss event detected by triple duplicate ACK | Threshold = CongWin/2, CongWin = Threshold, Set state to “Congestion Avoidance” | Fast recovery, implementing multiplicative decrease. CongWin will not drop below 1 MSS.
SS or CA | Timeout | Threshold = CongWin/2, CongWin = 1 MSS, Set state to “Slow Start” | Enter slow start
SS or CA | Duplicate ACK | Increment duplicate ACK count for segment being acked | CongWin and Threshold not changed

## Slide 99: Repeating Slow Start After Timeout
t
Window
Slow-start restart: Go back to CWND of 1 MSS, but take advantage of knowing the previous value of CWND.
Slow start in operation until it reaches half of previous CWND, I.e., SSTHRESH
Timeout
Fast Retransmission
SSThresh
Set to Here

## Slide 100: TCP throughput
What’s the average throughout of TCP as a function of window size and RTT?
  Ignore slow start
Let W be the window size when loss occurs.
When window is W, throughput is W/RTT
Just after loss, window drops to W/2, throughput to W/2RTT.
Average throughout: .75 W/RTT
Notes: -=-= started here Fri 17th

## Slide 101: TCP Futures: TCP over “long, fat pipes”
Example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
Requires window size W = 83,333 in-flight segments
Throughput in terms of loss rate p:
➜ L = 2·10-10 Ouch!
New versions of TCP for high-speed

## Slide 102: Calculation on Simple Model (cwnd in units of MSS)
Assume loss occurs whenever cwnd reaches W
  Recovery by fast retransmit
Window: W/2, W/2+1, W/2+2, …W, W/2, …
  W/2 RTTs, then drop, then repeat
Average throughput: .75W(MSS/RTT)
  One packet dropped out of (W/2)*(3W/4)
  Packet drop rate p = (8/3) W-2
Throughput = (MSS/RTT) sqrt(3/2p)
HINT: KNOW THIS SLIDE
Notes: KNOW THIS!

## Slide 103: Three Congestion Control Challenges – or Why AIMD?
Single flow adjusting to bottleneck bandwidth
  Without any a priori knowledge
  Could be a Gbps link; could be a modem
Single flow adjusting to variations in bandwidth
  When bandwidth decreases, must lower sending rate
  When bandwidth increases, must increase sending rate
Multiple flows sharing the bandwidth
  Must avoid overloading network
  And share bandwidth “fairly” among the flows

## Slide 104: Problem #1: Single Flow, Fixed BW
Want to get a first-order estimate of the available bandwidth
  Assume bandwidth is fixed
  Ignore presence of other flows
Want to start slow, but rapidly increase rate until packet drop occurs (“slow-start”)
Adjustment:
  cwnd initially set to 1 (MSS)
  cwnd++ upon receipt of ACK

## Slide 105: Problems with Slow-Start
Slow-start can result in many losses
  Roughly the size of cwnd ~ BW*RTT
Example:
  At some point, cwnd is enough to fill “pipe”
  After another RTT, cwnd is double its previous value
  All the excess packets are dropped!
Need a more gentle adjustment algorithm once have rough estimate of bandwidth
  Rest of design discussion focuses on this

## Slide 106: Problem #2: Single Flow, Varying BW
Want to track available bandwidth
Oscillate around its current value
If you never send more than your current rate, you won’t know if more bandwidth is available
Possible variations: (in terms of change per RTT)
Multiplicative increase or decrease:
  cwnd cwnd * / a
Additive increase or decrease:
  cwnd cwnd +- b

## Slide 107: Four alternatives
AIAD: gentle increase, gentle decrease
AIMD: gentle increase, drastic decrease
MIAD: drastic increase, gentle decrease
  too many losses: eliminate
MIMD: drastic increase and decrease
Notes: What do you think about these options?
Which one is obviously bad?
What do you think about the other ones?

## Slide 108: Problem #3: Multiple Flows
Want steady state to be “fair”
Many notions of fairness, but here just require two identical flows to end up with the same bandwidth
This eliminates MIMD and AIAD
  As we shall see…
AIMD is the only remaining solution!
  Not really, but close enough….

## Slide 109: Recall Buffer and Window Dynamics
No congestion  x increases by one packet/RTT every RTT
Congestion  decrease x by factor 2
A
B
C = 50 pkts/RTT
x

## Slide 110: AIMD Sharing Dynamics
A
B
x1
D
E
No congestion  rate increases by one packet/RTT every RTT
Congestion  decrease rate by factor 2
Rates equalize  fair share
x2

## Slide 111: AIAD Sharing Dynamics
A
B
x1
D
E
No congestion  x increases by one packet/RTT every RTT
Congestion  decrease x by 1
x2

## Slide 112: Simple Model of Congestion Control
Two TCP connections
  Rates x1 and x2
Congestion when sum>1
Efficiency: sum near 1
Fairness: x’s converge
Bandwidth for User 1: x1
Bandwidth for User 2: x2
Efficiency
line
2 user example
overload
underload

## Slide 113: Example
User 1: x1
User 2: x2
fairness
line
efficiency
line
1
1
Total bandwidth 1
Inefficient: x1+x2=0.7
(0.2, 0.5)
Congested: x1+x2=1.2
(0.7, 0.5)
Efficient: x1+x2=1
Not fair
(0.7, 0.3)
Efficient: x1+x2=1
Fair
(0.5, 0.5)

## Slide 114: AIAD
Bandwidth for User 1: x1
Bandwidth for User 2: x2
fairness
line
efficiency
line
(x1h,x2h)
(x1h-aD,x2h-aD)
(x1h-aD+aI), x2h-aD+aI))
Increase: x + aI
Decrease: x - aD
Does not converge to fairness

## Slide 115: MIMD
Bandwidth for User 1: x1
Bandwidth for User 2: x2
fairness
line
efficiency
line
(x1h,x2h)
(bdx1h,bdx2h)
(bIbDx1h, bIbDx2h)
Increase: x*bI
Decrease: x*bD
Does not converge to fairness

## Slide 116: AIMD
(bDx1h+aI, bDx2h+aI)
Bandwidth for User 1: x1
Bandwidth for User 2: x2
fairness
line
efficiency
line
(x1h,x2h)
(bDx1h,bDx2h)
Increase: x+aD
Decrease: x*bD
Converges to fairness

## Slide 117: Why is AIMD fair? (a pretty animation…)
Two competing sessions:
Additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Bandwidth for Connection 1
Bandwidth for Connection 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2

## Slide 118: Fairness (more)
Fairness and UDP
Multimedia apps may not use TCP
  do not want rate throttled by congestion control
Instead use UDP:
  pump audio/video at constant rate, tolerate packet loss
(Ancient yet ongoing) Research area: TCP friendly
Fairness and parallel TCP connections
nothing prevents app from opening parallel connections between 2 hosts.
Web browsers do this
Example: link of rate R supporting 9 connections;
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2 !
Recall Multiple browser sessions (and the potential for syncronized loss)
Notes: Note about NetBOOST – Fast Speed and other “stack modifiers”
vs
Riverbed “TCP sanitisers” and so on.

## Slide 119: Some TCP issues outstanding…
Synchronized Flows
Many TCP Flows
Aggregate window has same dynamics
Therefore buffer occupancy has same dynamics
Rule-of-thumb still holds.
Independent, desynchronized
Central limit theorem says the aggregate becomes Gaussian
Variance (buffer size) decreases as N increases
Probability
Distribution
t
Buffer Size
t