## Slide 1
Computer Networking
Michaelmas/Lent Term
M/W/F 11:00-12:00
LT1 in Gates Building
Slide Set 2
Andrew W. Moore
andrew.moore@cl.cam.ac.uk
2015-2016

## Slide 2: Topic 2 – Architecture and Philosophy
Abstraction
Layering
Layers and Communications
Entities and Peers
What is a protocol?
Protocol Standardization
The architects process
  How to break system into modules
  Where modules are implemented
  Where is state stored
Internet Philosophy and Tensions

## Slide 3: Abstraction Concept
A mechanism for breaking down a problem
what not how
eg Specification versus implementation
eg Modules in programs
Allows replacement of implementations without affecting system behavior
Vertical versus Horizontal
“Vertical” what happens in a box “How does it attach to the network?”
“Horizontal” the communications paths running through the system
Hint: paths are build on top of (“layered over”) other paths

## Slide 4: Computer System Modularity
Partition system into modules & abstractions:
Well-defined interfaces give flexibility
  Hides implementation - can be freely changed
  Extend functionality of system by adding new modules
E.g., libraries encapsulating set of functionality
E.g., programming language + compiler abstracts away how the particular CPU works …

## Slide 5: Computer System Modularity (cnt’d)
Well-defined interfaces hide information
  Isolate assumptions
  Present high-level abstractions
But can impair performance!
Ease of implementation vs worse performance

## Slide 6: Network System Modularity
Like software modularity, but:
Implementation is distributed across many machines (routers and hosts)
Must decide:
  How to break system into modules
    Layering
  Where modules are implemented
    End-to-End Principle
  Where state is stored
    Fate-sharing

## Slide 7: Layering Concept
A restricted form of abstraction: system functions are divided into layers, one built upon another
Often called a stack; but not a data structure!
Notes: Wed 22 Jan 2014

## Slide 8: Layers and Communications
Interaction only between adjacent layers
layer n uses services provided by layer n-1
layer n provides service to layer n+1
Bottom layer is physical media
Top layer is application

## Slide 9: Entities and Peers
Entity – a thing (an independent existence)
Entities interact with the layers above and below
Entities communicate with peer entities
  same level but different place (eg different person, different box, different host)
Communications between peers is supported by entities at the lower layers

## Slide 10: Entities and Peers
Entities usually do something useful
  Encryption – Error correction – Reliable Delivery
  Nothing at all is also reasonable
Not all communications is end-to-end
Examples for things in the middle
  IP Router – Mobile Phone Cell Tower
  Person translating French to English

## Slide 11: Layering and Embedding
In Computer Networks we often see higher-layer information embedded within lower-layer information
Such embedding can be considered a form of layering
Higher layer information is generated by stripping off headers and trailers of the current layer
eg an IP entity only looks at the IP headers
BUT embedding is not the only form of layering
Layering is to help understand a communications system
NOT
determine implementation strategy

## Slide 12: Example Embedding (also called Encapsulation)
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 13: Distributing Layers Across Network
Layers are simple if only on a single machine
  Just stack of modules interacting with those above/below
But we need to implement layers across machines
  Hosts
  Routers (switches)
What gets implemented where?
13

## Slide 14: What Gets Implemented on Host?
Bits arrive on wire, must make it up to application
Therefore, all layers must exist at the host
source / destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
14

## Slide 15: What Gets Implemented on a Router?
Bits arrive on wire
  Physical layer necessary
Packets must be delivered to next-hop
  Datalink layer necessary
Routers participate in global delivery
  Network layer necessary
Routers don’t support reliable delivery
  Transport layer (and above) not supported
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
router
15

## Slide 16: What Gets Implemented on Switches?
Switches do what routers do, except they don’t participate in global delivery, just local delivery
They only need to support Physical and Datalink
  Don’t need to support Network layer
Won’t focus on the router/switch distinction
  When I say switch, I almost always mean router
  Almost all boxes support network layer these days
  Routers have switches but switches do not have routers
link
physical
switch
Ht
Hn
Hl
M
16
Notes: 24-nov-2014

## Slide 17: The Internet Hourglass
Data Link
Physical
Applications
The Hourglass Model
Waist
There is just one network-layer protocol, IP.
The “narrow waist” facilitates interoperability.
SMTP
HTTP
NTP
DNS
TCP
UDP
IP
Ethernet
SONET
802.11
Transport
Fiber
Copper
Radio
IP
17

## Slide 18: Internet protocol stack versus OSI Reference Model

## Slide 19: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 20: What is a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 21: What is a protocol?
a human protocol and a computer network protocol:
Q: Other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
request
TCP connection
response
GET http://www.cl.cam.ac.uk/index.html
<file>
time
Notes: Lecture (Question by hands)
Traffic lights/driving

## Slide 22: Protocol Standardization
All hosts must follow same protocol
  Very small modifications can make a big difference
  Or prevent it from working altogether
  Cisco bug compatible!
This is why we have standards
  Can have multiple implementations of protocol
Internet Engineering Task Force
  Based on working groups that focus on specific issues
  Produces “Request For Comments” (RFCs)
  IETF Web site is http://www.ietf.org
  RFCs archived at http://www.rfc-editor.org

## Slide 23: So many Standards Problem
Many different packet-switching networks
Each with its own Protocol
Only nodes on the same network could communicate
Notes: Novell
DECnet
Banyan Vines

## Slide 24: INTERnet Solution
Gateways

## Slide 25: Alternative to Standardization?
Have one implementation used by everyone
Open-source projects
  Which has had more impact, Linux or POSIX?
Or just sole-sourced implementation
  Skype, many P2P implementations, etc.
25

## Slide 26: A Multitude of Apps Problem
Re-implement every application for every technology?
No! But how does the Internet design avoid this?
Skype
SSH
NFS
Radio
Coaxial
cable
Fiber
optic
Application
Transmission
Media
HTTP
26

## Slide 27: Solution: Intermediate Layers
Introduce intermediate layers that provide set of abstractions for various network functionality and technologies
  A new app/media implemented only once
  Variation on “add another level of indirection”
Skype
SSH
NFS
Packet
radio
Coaxial
cable
Fiber
optic
Application
Transmission
Media
HTTP
Intermediate
layers
27

## Slide 28: Remember that slide!
The relationship between architectural principles and architectural decisions is crucial to understand
28

## Slide 29: Internet Design Goals (Clark ‘88)
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability
29

## Slide 30: Real Goals
Build something that works!
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability
Internet Motto
We reject kings , presidents, and voting. We believe in rough consensus and running code.“ – David Clark
30

## Slide 31: In the context of the Internet
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits
31

## Slide 32: Three Observations
Each layer:
  Depends on layer below
  Supports layer above
  Independent of others
Multiple versions in layer
  Interfaces differ somewhat
  Components pick which lower-level protocol to use
But only one IP layer
  Unifying protocol
32
32

## Slide 33: Layering Crucial to Internet’s Success
Reuse
Hides underlying detail
Innovation at each level can proceed in parallel
Pursued by very different communities
33
33

## Slide 34: What are some of the drawbacks of protocols and layering?
34
Notes: 26-nov-2014

## Slide 35: Drawbacks of Layering
Layer N may duplicate lower layer functionality
  e.g., error recovery to retransmit lost data
Information hiding may hurt performance
  e.g., packet loss due to corruption vs. congestion
Headers start to get really big
  e.g., typical TCP+IP+Ethernet is 54 bytes
Layer violations when the gains too great to resist
  e.g., TCP-over-wireless
Layer violations when network doesn’t trust ends
  e.g., firewalls
35

## Slide 36: Placing Network Functionality
Hugely influential paper: “End-to-End Arguments in System Design” by Saltzer, Reed, and Clark (‘84)
  articulated as the “End-to-End Principle” (E2E)
Endless debate over what it means
Everyone cites it as supporting their position
  (regardless of the position!)
36
Notes: Contrary to wisdom of the day!
Talmud

## Slide 37: Basic Observation
Some application requirements can only be correctly implemented end-to-end
  reliability, security, etc.
Implementing these in the network is hard
  every step along the way must be fail proof
Hosts
  Can satisfy the requirement without network’s help
  Will/must do so, since they can’t rely on the network
37
Notes: Contrary to wisdom of the day!
Talmud

## Slide 38: Example: Reliable File Transfer
Solution 1: make each step reliable, and string them together to make reliable end-to-end process
Solution 2: end-to-end check and retry
OS
Appl.
OS
Appl.
Host A
Host B
OK
38

## Slide 39: Discussion
Solution 1 is incomplete
  What happens if any network element misbehaves?
  Receiver has to do the check anyway!
Solution 2 is complete
  Full functionality can be entirely implemented at application layer with no need for reliability from lower layers
Is there any need to implement reliability at lower layers?
39
Notes: Contrary to wisdom of the day!
Talmud

## Slide 40: Summary of End-to-End Principle
Implementing functionality (e.g., reliability) in the network
  Doesn’t reduce host implementation complexity
  Does increase network complexity
  Probably increases delay and overhead on all applications even if they don’t need the functionality (e.g. VoIP)
However, implementing in the network can improve performance in some cases
  e.g., consider a very lossy link
40
Notes: Contrary to wisdom of the day!
Talmud

## Slide 41: “Only-if-Sufficient” Interpretation
Don’t implement a function at the lower levels of the system unless it can be completely implemented at this level
Unless you can relieve the burden from hosts, don’t bother
41

## Slide 42: “Only-if-Necessary” Interpretation
Don’t implement anything in the network that can be implemented correctly by the hosts
Make network layer absolutely minimal
  This E2E interpretation trumps performance issues
  Increases flexibility, since lower layers stay simple
42
Notes: One make hosts as simple as possible. The other makes the network as simple as possible. Which do you prefer?

## Slide 43: “Only-if-Useful” Interpretation
If hosts can implement functionality correctly, implement it in a lower layer only as a performance enhancement
But do so only if it does not impose burden on applications that do not require that functionality
43

## Slide 44: We have some tools:
Abstraction
Layering
Layers and Communications
Entities and Peers
Protocol as motivation
Examples of the architects process
Internet Philosophy and Tensions