## Slide 1: Topic 4: Network Layer
Our goals:
understand principles behind network layer services:
  network layer service models
  forwarding versus routing (versus switching)
  how a router works
  routing (path selection)
  IPv6
  For the most part, the Internet is our example – again.

## Slide 2
Name: a something
Address: Where is a something
Routing: How do I get to the something
Forwarding: What path do I take next
to get to the something

## Slide 3: Addressing (at a conceptual level)
Assume all hosts have unique IDs
No particular structure to those IDs
Later in topic I will talk about real IP addressing
Do I route on location or identifier?
If a host moves, should its address change?
  If not, how can you build scalable Internet?
  If so, then what good is an address for identification?
Notes: 20-jan-17

## Slide 4: Packets (at a conceptual level)
Assume packet headers contain:
  Source ID, Destination ID, and perhaps other information
Destination
Identifier
Source
Identifier
Payload
Why include
this?

## Slide 5: Switches/Routers
Multiple ports (attached to other switches or hosts)
Ports are typically duplex (incoming and outgoing)
incoming links
outgoing links
Switch

## Slide 6: A Variety of Networks
ISPs: carriers
  Backbone
  Edge
  Border (to other ISPs)
Enterprises: companies, universities
  Core
  Edge
  Border (to outside)
Datacenters: massive collections of machines
  Top-of-Rack
  Aggregation and Core
  Border (to outside)
Notes: 19-jan-2015

## Slide 7: Switches forward packets
EDINBURGH
OXFORD
GLASGOW
UCL
Destination | Next Hop
GLASGOW | 4
OXFORD | 5
EDIN | 2
UCL | 3
Forwarding Table
111010010
EDIN
switch#2
switch#5
switch#3
switch#4

## Slide 8: Forwarding Decisions
When packet arrives..
  Must decide which outgoing port to use
  In single transmission time
  Forwarding decisions must be simple
Routing state dictates where to forward packets
  Assume decisions are deterministic
Global routing state is the collection of routing state in each of the routers
  Will focus on where this routing state comes from
  But first, a few preliminaries….

## Slide 9: Forwarding vs Routing
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
Routing: “control plane”
  Computing paths the packets will follow
  Routers talking amongst themselves
  Jointly creating the routing state
Two very different timescales….
Notes: 8/Feb/2012

## Slide 10: Router definitions
1
2
3
4
5
…
N-1
N
N = number of external router “ports”
R = speed (“line rate”) of a port
Router capacity = N x R
R bits/sec

## Slide 11: Networks and routers
AT&T
INTEL
MIT
JANET
core
core
edge (ISP)
edge (enterprise)
home, small business
BT
Notes: Bunch of different kinds of routers: small for homes, routers that connect different ISPs or ISPs to enterprises (edge)
2020-02-10

## Slide 12: Basic Operation of Router
R3
A
B
C
R1
R2
R4
D
E
F
R5
R5
F
R3
E
R3
D
Next Hop
Destination
D

## Slide 13: Basic Operation of Router
R3
A
B
C
R1
R2
R4
D
E
F
R5
R5
F
R4
E
R4
D
Next Hop
Destination
D

## Slide 14: Basic Operation of Router
R3
A
B
C
R1
R2
R4
D
E
F
R5
R5
F
Port E
E
Port D
D
Next Hop
Destination
D

## Slide 15: What does a router do?
R3
A
B
C
R1
R2
R4
D
E
F
R5
R5
F
R3
E
R3
D
Next Hop
Destination
D
16
32
4
1
Data
Options (if any)
Destination Address
Source Address
Header Checksum
Protocol
TTL
Fragment Offset
Flags
Fragment ID
Total Packet Length
T.Service
HLen
Ver
20 bytes

## Slide 16: What does a router do?
A
B
C
R1
R2
R3
R4
D
E
F
R5
Every router performs a per-packet lookup for every packet
Each router performs a lookup in it’s local lookup table
Each router performs lookups (ENTIRELY) independently of every other router

## Slide 17: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Processes packets on their way in
Processes packets before they leave
Transfers packets from input to output ports
Input and Output for the same port are on one physical linecard

## Slide 18: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
(1) Implement IGP and BGP protocols; compute routing tables
(2) Push forwarding tables to the line cards

## Slide 19: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect Fabric
Route/Control Processor
Linecards (output)
Constitutes the data plane
Constitutes the control plane
A decision for each packet.
Makes decisions over long time horizons : network change
Notes: 2019-2-4
Control plane: software. Makes decisions over long time horizons.
Data plane: mostly hardware. A decision for each packet.

## Slide 20: Context and Terminology
“End hosts”
“Clients”, “Users”
“End points”
“Interior Routers”
“Border Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Route” or “Path”
Notes: 2015-12-2

## Slide 21: Context and Terminology
111010010
MIT
Destination
Destination
Destination
Destination
Destination
Destination
Destination
Destination
MIT
Internet routing protocols are responsible for constructing and updating the forwarding tables at routers
Notes: Go through this one fast or remove all together

## Slide 22: Routing Protocols
Routing protocols implement the core function of a network
  Establish paths between nodes
  Part of the network’s “control plane”
Network modeled as a graph
  Routers are graph vertices
  Links are edges
  Edges have an associated “cost”
    e.g., distance, loss
Goal: compute a “good” path from source to destination
  “good” usually means the shortest (least cost) path
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 23: Internet Routing
Internet Routing works at two levels
Each AS runs an intra-domain routing protocol that establishes routes within its domain
  (AS -- region of network under a single administrative entity)
  Link State, e.g., Open Shortest Path First (OSPF)
  Distance Vector, e.g., Routing Information Protocol (RIP)
ASes participate in an inter-domain routing protocol that establishes routes between domains
  Path Vector, e.g., Border Gateway Protocol (BGP)

## Slide 24: Addressing (to date) - a reminder -
Recall each host has a unique ID (address)
No particular structure to those IDs
(e.g. Ethernet)
IP addressing – in contrast – has implicit structure

## Slide 25: Outline
Popular Routing Algorithms:
  Link State Routing
  Distance Vector Algorithm
Routing: goals and metrics

## Slide 26: Link-State Routing
Examples:
Open Shortest Path First (OSPF) or
Intermediate System to Intermediate System
(written as IS-IS/ISIS and pronounced eye-esss-eye-esss)
The two common Intradomain routing or
interior gateway protocols (IGP)

## Slide 27: Link State Routing
Each node maintains its local “link state” (LS)
  i.e., a list of its directly attached links and their costs
(N1,N2)
(N1,N4)
(N1,N5)
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6

## Slide 28: Link State Routing
Each node maintains its local “link state” (LS)
Each node floods its local link state
  on receiving a new LS message, a router forwards the message to all its neighbors other than the one it received the message from
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)
(N1,N2)
(N1, N4)
(N1, N5)

## Slide 29: Link State Routing
Each node maintains its local “link state” (LS)
Each node floods its local link state
Hence, each node learns the entire network topology
  Can use Dijkstra’s to compute the shortest paths between nodes
Host A
Host B
Host E
Host D
Host C
N1
N2
N3
N4
N5
N7
N6
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
A
B
E
D
C
Notes: 21.8 in Forouzan

## Slide 30: Dijkstra’s Shortest Path Algorithm
INPUT:
  Network topology (graph), with link costs
OUTPUT:
  Least cost paths from one node to all other nodes
Iterative: after k iterations, a node knows the least cost path to its k closest neighbors
This is covered in Algorithms
Notes: How many people know this algorithm?
Well, last year….

## Slide 31: The Forwarding Table
Running Dijkstra at node A gives the shortest path from A to all destinations
We then construct the forwarding table
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
Destination | Link
B | (A,B)
C | (A,D)
D | (A,D)
E | (A,D)
F | (A,D)
Notes: Separate routing and forwarding tables - not always the case. For efficiency, hardware implementation

## Slide 32: Issue #1: Scalability
How many messages needed to flood link state messages?
  O(N x E), where N is #nodes; E is #edges in graph
Processing complexity for Dijkstra’s algorithm?
  O(N2), because we check all nodes w not in S at each iteration and we have O(N) iterations
  more efficient implementations: O(N log(N))
How many entries in the LS topology database? O(E)
How many entries in the forwarding table? O(N)

## Slide 33: Issue#2: Transient Disruptions
Inconsistent link-state database
  Some routers know about failure before others
  The shortest paths are no longer consistent
  Can cause transient forwarding loops
A
E
D
C
B
F
A and D think that this is the path to C
E thinks that this is the path to C
A
E
D
C
B
F
Loop!
Notes: here. 12/jan/2014

## Slide 34: Distance Vector Routing
Notes: intra-routing is for LSR and inter is for Distance Vector

## Slide 35: Learn-By-Doing
Let’s try to collectively develop distance-vector routing from first principles

## Slide 36: Experiment
Your job: find the (route to) the youngest person in the room
Ground Rules
  You may not leave your seat, nor shout loudly across the class
  You may talk with your immediate neighbors
  (N-S-E-W only) (hint: “exchange updates” with them)
At the end of 5 minutes, I will pick a victim and ask:
  who is the youngest person in the room? (date&name)
  which one of your neighbors first told you this info.?
EQUIPMENT REQUIRED: PIECE OF PAPER and a PEN (or your emotional equivalent)

## Slide 37: Go!

## Slide 38: Distance-Vector Routing
Example:
Routing Information Protocol (RIP)

## Slide 39: Example of Distributed Computation
I am one hop away
I am one hop away
I am one hop away
I am two hops away
I am two hops away
I am two hops away
I am two hops away
I am three hops away
I am three hops away
Destination
I am three hops away
Notes: 2020-02-12

## Slide 40: Distance Vector Routing
Each router sends its knowledge about the “whole” network to its neighbors. Information sharing at regular intervals.
Each router knows the links to its neighbors
  Does not flood this information to the whole network
Each router has provisional “shortest path” to every other router
  E.g.: Router A: “I can get to router B with cost 11”
Routers exchange this distance vector information with their neighboring routers
  Vector because one entry per destination
Routers look over the set of options offered by their neighbors and select the best one
Iterative process converges to set of shortest paths
Notes: Whole means as much as they know 21.7 in Forouzan
A link has a single cost, the cost is based on hop count

## Slide 41: A few other inconvenient truths
What if we use a non-additive metric?
  E.g., maximal capacity
What if routers don’t use the same metric?
  I want low delay, you want low loss rate?
What happens if nodes lie?
Notes: 23-Jan-17

## Slide 42: Can You Use Any Metric?
I said that we can pick any metric. Really?
What about maximizing capacity?

## Slide 43: What Happens Here?
All nodes want to maximize capacity
A high capacity link gets reduced to low capacity
Problem:“cost” does not change around loop
Additive measures avoid this problem!

## Slide 44: No agreement on metrics?
If the nodes choose their paths according to different criteria, then bad things might happen
Example
  Node A is minimizing latency
  Node B is minimizing loss rate
  Node C is minimizing price
Any of those goals are fine, if globally adopted
  Only a problem when nodes use different criteria
Consider a routing algorithm where paths are described by delay, cost, loss

## Slide 45: What Happens Here?
Low price link
Low loss link
Low delay link
Low loss link
Low delay link
Low price link
Cares about price,
then loss
Cares about delay,
then price
Cares about loss,
then delay
Notes: Figure this out. Break into groups….

## Slide 46: Must agree on loop-avoiding metric
When all nodes minimize same metric
And that metric increases around loops
Then process is guaranteed to converge

## Slide 47: What happens when routers lie?
What if a router claims a 1-hop path to everywhere?
All traffic from nearby routers gets sent there
How can you tell if they are lying?
Can this happen in real life?
  It has, several times….

## Slide 48: Link State vs. Distance Vector
Core idea
  LS: tell all nodes about your immediate neighbors
  DV: tell your immediate neighbors about (your least cost distance to) all nodes

## Slide 49: Link State vs. Distance Vector
LS: each node learns the complete network map; each node computes shortest paths independently and in parallel
DV: no node has the complete picture; nodes cooperate to compute shortest paths in a distributed manner
  LS has higher messaging overhead
  LS has higher processing complexity
  LS is less vulnerable to looping

## Slide 50: Link State vs. Distance Vector
Message complexity
LS: O(NxE) messages;
  N is #nodes; E is #edges
DV: O(#Iterations x E)
  where #Iterations is ideally O(network diameter) but varies due to routing loops or the count-to-infinity problem
Processing complexity
LS: O(N2)
DV: O(#Iterations x N)
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  node can advertise incorrect path cost
  each node’s table used by others; error propagates through network

## Slide 51: Routing: Just the Beginning
Link state and distance-vector are the deployed routing paradigms for intra-domain routing
Inter-domain routing (BGP)
  more Part II (Principles of Communications)
  A version of DV

## Slide 52: What are desirable goals for a routing solution?
“Good” paths (least cost)
Fast convergence after change/failures
  no/rare loops
Scalable
  #messages
  table size
  processing complexity
Secure
Policy
Rich metrics (more later)

## Slide 53: Delivery models
What if a node wants to send to more than one destination?
  broadcast: send to all
  multicast: send to all members of a group
  anycast: send to any member of a group
What if a node wants to send along more than one path?

## Slide 54: Metrics
Propagation delay
Congestion
Load balance
Bandwidth (available, capacity, maximal, bbw)
Price
Reliability
Loss rate
Combinations of the above
In practice, operators set abstract “weights” (much like our costs); how exactly is a bit of a black art

## Slide 55: From Routing back to Forwarding
Routing: “control plane”
  Computing paths the packets will follow
  Routers talking amongst themselves
  Jointly creating the routing state
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
Two very different timescales….

## Slide 56: Basic Architectural Components of an IP Router
Control Plane
network-change
processing
Datapath
per-packet
processing
Switching
Forwarding
Table
Routing
Table
Routing
Protocols
Management
& CLI
Software
Hardware

## Slide 57: Independent operation!
Control Plane
network-change
processing
Datapath
per-packet
processing
Switching
Forwarding
Table
Routing
Table
Routing
Protocols
Management
& CLI
Software
Hardware
If the control-plane fails…..
The data-path is not affected…
like a loyal pet it will keep going using the current (last) table update
This is a feature not a bug

## Slide 58: Per-packet processing in an IP Router
1. Accept packet arriving on an incoming link.
2. Lookup packet destination address in the forwarding table, to identify outgoing port(s).
3. Manipulate packet header: e.g., decrement TTL, update header checksum.
4. Send packet to the outgoing port(s).
5. Buffer packet in the queue.
6. Transmit packet onto outgoing link.

## Slide 59: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Data
Hdr
Data
Hdr
~1M prefixes
Off-chip DRAM
Address
Table
IP Address
Next Hop
Queue
Packet
Buffer
Memory
~1M packets
Off-chip DRAM

## Slide 60: Forwarding tables
Entry | Destination | Port
1 2 ⋮ 232 | 0.0.0.0 0.0.0.1 ⋮ 255.255.255.255 | 1 2 ⋮ 12
~ 4 billion entries
Naïve approach:
One entry per address
Improved approach:
Group entries to reduce table size
Entry | Destination | Port
1 2 ⋮ 50 | 0.0.0.0 – 127.255.255.255 128.0.0.1 – 128.255.255.255 ⋮ 248.0.0.0 – 255.255.255.255 | 1 2 ⋮ 12
IP address
32 bits wide → ~ 4 billion unique address

## Slide 61: Generic Router Architecture
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Lookup
IP Address
Update
Header
Header Processing
Address
Table
Data
Hdr
Data
Hdr
Data
Hdr
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Buffer
Manager
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr

## Slide 62: IP addresses as a line
0
232-1
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
All IP addresses
Europe
USA
Oxford
Cambridge
Your computer
My computer

## Slide 63: Longest Prefix Match (LPM)
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
Universities
Continents
Planet
Data
To: Cambridge
Matching entries:
Cambridge
Europe
Everywhere
Most specific

## Slide 64: Longest Prefix Match (LPM)
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
Universities
Continents
Planet
Data
To: France
Matching entries:
Europe
Everywhere
Most specific

## Slide 65: Implementing Longest Prefix Match
Entry | Destination | Port
1 2 3 4 5 | Cambridge Oxford Europe USA Everywhere (default) | 1 2 3 4 5
Most specific
Least specific
Searching
FOUND
Notes: 2014-1-23
2019-2-6

## Slide 66: Forwarding table realities
High Speed: Must be “packet-rate” lookup
  about 200M lookups / second for 100Gbps
Large (messy) tables – (BGP Jan 2021 stats)
  866,000+ routing prefix entries for IPv4
  104,000+ routing prefix entries for IPv6
Changing and Growing
the harsh side of “up and to the right”
Hudson 2020 report https://blog.apnic.net/2021/01/05/bgp-in-2020-the-bgp-table/
Open problems : continual growth is continual demand for innovation opportunities in control, algorithms, & network hardware

## Slide 67: The Internet version of a Network layer
forwarding
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer
Notes: 2018-2-8

## Slide 68: IPv4 Packet Structure 20 Bytes of Standard Header, then Options
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Notes: 24.2 in Forouzan

## Slide 69: (Packet) Network Tasks One-by-One
Read packet correctly
Get packet to the destination
Get responses to the packet back to source
Carry data
Tell host what to do with packet once arrived
Specify any special network handling of the packet
Deal with problems that arise along the path

## Slide 70: Reading Packet Correctly
Version number (4 bits)
  Indicates the version of the IP protocol
  Necessary to know what other fields to expect
  Typically “4” (for IPv4), and sometimes “6” (for IPv6)
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when IP options are used
Total length (16 bits)
  Number of bytes in the packet
  Maximum size is 65,535 bytes (216 -1)
  … though underlying links may impose smaller limits
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 71: Getting Packet to Destination and Back
Two IP addresses
  Source IP address (32 bits)
  Destination IP address (32 bits)
Destination address
  Unique identifier/locator for the receiving host
  Allows each node to make forwarding decisions
Source address
  Unique identifier/locator for the sending host
  Recipient can decide whether to accept packet
  Enables recipient to send a reply back to source
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 72: Telling Host How to Handle Packet
Protocol (8 bits)
  Identifies the higher-level protocol
  Important for demultiplexing at receiving host
Most common examples
  E.g., “6” for the Transmission Control Protocol (TCP)
  E.g., “17” for the User Datagram Protocol (UDP)
IP header
IP header
TCP header
UDP header
protocol=6
protocol=17
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 73: Special Handling
Type-of-Service (8 bits)
  Allow packets to be treated differently based on needs
  E.g., low delay for audio, high bandwidth for bulk transfer
  Has been redefined several times
Options
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Notes: 26-jan-2015

## Slide 74: Potential Problems
Header Corrupted: Checksum
Loop: TTL
Packet too large: Fragmentation

## Slide 75: Header Corruption
Checksum (16 bits)
  Particular form of checksum over packet header
If not correct, router discards packets
  So it doesn’t act on bogus information
Checksum recalculated at every router
  Why?
  Why include TTL?
  Why only header?
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 76: Preventing Loops (aka Internet Zombie plan)
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Forwarding loops cause packets to cycle forever
  As these accumulate, eventually consume all capacity
Time-to-Live (TTL) Field (8 bits)
  Decremented at each hop, packet discarded if reaches 0
  …and “time exceeded” message is sent to the source
    Using “ICMP” control message; basis for traceroute

## Slide 77: Fragmentation (some assembly required)
Fragmentation: when forwarding a packet, an Internet router can split it into multiple pieces (“fragments”) if too big for next hop link
Must reassemble to recover original packet
  Need fragmentation information (32 bits)
  Packet identifier, flags, and fragment offset
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Notes: Is not frequently used, send big packets, subdivides, never repacks

## Slide 78: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
IPv6 does things differently…
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly

## Slide 79: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
Question: What happens when a fragment is lost?

## Slide 80: Fragmentation Details
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Identifier (16 bits): used to tell which fragments belong together
Flags (3 bits):
  Reserved (RF): unused bit
  Don’t Fragment (DF): instruct routers to not fragment the packet even if it won’t fit
    Instead, they drop the packet and send back a “Too Large” ICMP control message
    Forms the basis for “Path MTU Discovery”
  More (MF): this fragment is not the last one
Offset (13 bits): what part of datagram this fragment covers in 8-byte units
Pop quiz question: Why do frags use offset and not a frag number?
Notes: map into memory
further downstream locations doing fragmentation would be v. hard with frag number (you would need reissue or reassemble or some craziness

## Slide 81: Options
End of Options List
No Operation (padding between options)
Record Route
Strict Source Route
Loose Source Route
Timestamp
Traceroute
Router Alert
…..
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
Notes: Very briefly
2020-2-14

## Slide 82: IP Addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  routers typically have multiple interfaces
  host typically has one interface
  IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 83: Subnets
IP address:
  subnet part (high order bits)
  host part (low order bits)
What’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of 3 subnets
subnet
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Subnet mask: /24
11011111 00000001 00000011 00000000
subnet
part
host
part
223.1.3.0/24
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
Notes: We further divide a network into smaller networks called subnet

## Slide 84: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config (circa 1980’s your mileage will vary)
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 85: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
DHCP
server
DHCP server: 223.1.2.5
arriving
client
time
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
Lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
Lifetime: 3600 secs
arriving DHCP
client needs
address in this
network
Goal: allow host to dynamically obtain its IP address from network server when it joins network
  Can renew its lease on address in use
  Allows reuse of addresses (only hold address while connected an “on”)
  Support for mobile users who want to join network (more shortly)
Notes: 2019—2-11

## Slide 86: IP addresses: how to get one?
Q: How does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 87: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing
information:

## Slide 88: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Notes: 18 feb 2013

## Slide 89: IP addressing: the last word...
Q: How does an ISP get a block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 90: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
Datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
All datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,
different source port numbers
Cant get more IP addresses? well there is always…..
Notes: 28 Jan 2015

## Slide 91: NAT: Network Address Translation
Motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus).

## Slide 92: NAT: Network Address Translation
Implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr.
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 93: NAT: Network Address Translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
Notes: 2016-1-20

## Slide 94: NAT: Network Address Translation
16-bit port-number field:
  60,000+ simultaneous connections with a single WAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument (?)
    NAT possibility must be taken into account by app designers, eg, P2P applications
  address shortage should instead be solved by IPv6

## Slide 95: NAT traversal problem
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible NATted address: 138.76.29.7
solution 1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (138.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
Client
?

## Slide 96: NAT traversal problem
solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATted host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
  i.e., automate static NAT port map configuration
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
IGD
Notes: 2017-2-1

## Slide 97: NAT traversal problem
solution 3: relaying (was used in (really old) Skype)
  NATed client establishes connection to relay
  External client connects to relay
  relay bridges packets between to connections
138.76.29.7
Client
10.0.0.1
NAT
router
1. connection to
relay initiated
by NATted host
2. connection to
relay initiated
by client
3. relaying
established

## Slide 98: Remember this? Traceroute at work…
traceroute munnari.oz.au
traceroute to munnari.oz.au (202.29.151.3), 30 hops max, 60 byte packets
1 gatwick.net.cl.cam.ac.uk (128.232.32.2) 0.416 ms 0.384 ms 0.427 ms
2 cl-sby.route-nwest.net.cam.ac.uk (193.60.89.9) 0.393 ms 0.440 ms 0.494 ms
3 route-nwest.route-mill.net.cam.ac.uk (192.84.5.137) 0.407 ms 0.448 ms 0.501 ms
4 route-mill.route-enet.net.cam.ac.uk (192.84.5.94) 1.006 ms 1.091 ms 1.163 ms
5 xe-11-3-0.camb-rbr1.eastern.ja.net (146.97.130.1) 0.300 ms 0.313 ms 0.350 ms
6 ae24.lowdss-sbr1.ja.net (146.97.37.185) 2.679 ms 2.664 ms 2.712 ms
7 ae28.londhx-sbr1.ja.net (146.97.33.17) 5.955 ms 5.953 ms 5.901 ms
8 janet.mx1.lon.uk.geant.net (62.40.124.197) 6.059 ms 6.066 ms 6.052 ms
9 ae0.mx1.par.fr.geant.net (62.40.98.77) 11.742 ms 11.779 ms 11.724 ms
10 ae1.mx1.mad.es.geant.net (62.40.98.64) 27.751 ms 27.734 ms 27.704 ms
11 mb-so-02-v4.bb.tein3.net (202.179.249.117) 138.296 ms 138.314 ms 138.282 ms
12 sg-so-04-v4.bb.tein3.net (202.179.249.53) 196.303 ms 196.293 ms 196.264 ms
13 th-pr-v4.bb.tein3.net (202.179.249.66) 225.153 ms 225.178 ms 225.196 ms
14 pyt-thairen-to-02-bdr-pyt.uni.net.th (202.29.12.10) 225.163 ms 223.343 ms 223.363 ms
15 202.28.227.126 (202.28.227.126) 241.038 ms 240.941 ms 240.834 ms
16 202.28.221.46 (202.28.221.46) 287.252 ms 287.306 ms 287.282 ms
17 * * *
18 * * *
19 * * *
20 coe-gw.psu.ac.th (202.29.149.70) 241.681 ms 241.715 ms 241.680 ms
21 munnari.OZ.AU (202.29.151.3) 241.610 ms 241.636 ms 241.537 ms
traceroute: rio.cl.cam.ac.uk to munnari.oz.au
(tracepath on windows is similar)
Three delay measurements from
rio.cl.cam.ac.uk to gatwick.net.cl.cam.ac.uk
* means no response (probe lost, router not replying)
trans-continent
link
Notes: Where did the delay come from??

## Slide 99: Traceroute and ICMP
Source sends series of UDP segments to dest
  First has TTL =1
  Second has TTL=2, etc.
  Unlikely port number
When nth datagram arrives to nth router:
  Router discards datagram
  And sends to source an ICMP message (type 11, code 0)
  Message includes name of router& IP address
When ICMP message arrives, source calculates RTT
Traceroute does this 3 times
Stopping criterion
UDP segment eventually arrives at destination host
Destination returns ICMP “host unreachable” packet (type 3, code 3)
When source gets this ICMP, stops.

## Slide 100: ICMP: Internet Control Message Protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 101
Gluing it together:
How does my Network (address) interact
with my Data-Link (address) ?

## Slide 102: Switches vs. Routers Summary
both store-and-forward devices
  routers: network layer devices (examine network layer headers eg IP)
  switches are link layer devices (examine Data-Link-Layer headers eg Ethernet)
Routers: implement routing algorithms, maintain routing tables of the network – create network forwarding tables from routing tables
Switches: implement learning algorithms, learn switch/DLL forwarding tables
Switch

## Slide 103: MAC Addresses (and IPv4 ARP) or How do I glue my network to my data-link?
32-bit IP address:
  network-layer address
  used to get datagram to destination IP subnet
MAC (or LAN or physical or Ethernet) address:
  function: get frame from one interface to another physically-connected interface (same network)
  48 bit MAC address (for most LANs)
    burned in NIC ROM, firmware, etc.

## Slide 104: LAN Addresses and ARP
Each adapter on LAN has unique LAN address
Ethernet
Broadcast address =
FF-FF-FF-FF-FF-FF
= adapter
1A-2F-BB-709-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-6F7-2B-08-53
LAN
(wired or
wireless)

## Slide 105: Address Resolution Protocol
Every node maintains an ARP table
  <IP address, MAC address> pair
Consult the table when sending a packet
  Map destination IP address to destination MAC address
  Encapsulate and transmit the data packet
But: what if IP address not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches result in its ARP table
Notes: Wed 7th start here.

## Slide 106: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B

## Slide 107: Example: A Sending a Packet to B
How does host A send an IP packet to host B?
A
R
B
1. A sends packet to R. 2. R sends packet to B.
B
A
A
R
B
A
R
B

## Slide 108: Host A Decides to Send Through R
A
R
B
Host A constructs an IP packet to send to B
  Source 111.111.111.111, destination 222.222.222.222
Host A has a gateway router R
  Used to reach destinations outside of 111.111.111.0/24
  Address 111.111.111.110 for R learned via DHCP/config
B
A

## Slide 109: Host A Sends Packet Through R
B
A
Host A learns the MAC address of R’s interface
  ARP request: broadcast request for 111.111.111.110
  ARP response: R responds with E6-E9-00-17-BB-4B
Host A encapsulates the packet and sends to R
A
R
B
B
A
A
R
I’m 111.111.111.110 on e6-e9-00-17-bb-4b
MAC address for 111.111.111.110 please
MAC address for 111.111.111.110 please

## Slide 110: R Decides how to Forward Packet
Router R’s adaptor receives the packet
  R extracts the IP packet from the Ethernet frame
  R sees the IP packet is destined to 222.222.222.222
Router R consults its forwarding table
  Packet matches 222.222.222.0/24 via other adaptor
A
R
B
B
A
A
R

## Slide 111: R Sends Packet to B
Router R’s learns the MAC address of host B
  ARP request: broadcast request for 222.222.222.222
  ARP response: B responds with 49-BD-D2-C7-52A
Router R encapsulates the packet and sends to B
A
R
B
B
A
R
B
R broadcasts: Who is 222.222.22.222.222?
B replies to R
Me! I’m 222.22.222.222 on 49-BD-D2-C7-56-2A

## Slide 112: Security Analysis of ARP
Impersonation
  Any node that hears request can answer …
  … and can say whatever they want
Actual legit receiver never sees a problem
  Because even though later packets carry its IP address, its NIC doesn't capture them since the (naughty) packets are not its MAC address
Notes: 1/Fab/2013

## Slide 113: Key Ideas in Both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
  Remember your own address & other host’s addresses
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 114: Why Not Use DNS-Like Tables?
When host arrives:
  Assign it an IP address that will last as long it is present
  Add an entry into a table in DNS-server that maps MAC to IP addresses
Answer:
  Names: explicit creation, and are plentiful
  Hosts: come and go without informing network
    Must do mapping on demand
  Addresses: not plentiful, need to reuse and remap
    Soft-state enables dynamic reuse
Notes: Two key points

## Slide 115: IPv6
Motivated by address exhaustion
  addresses are larger
  packet headers are laid out differently
  address management and configuration are completely different
  some DNS behavior changes
  some sockets code changes
  everybody now has a hard time parsing IP addresses
Steve Deering focused on simplifying IP
  Got rid of all fields that were not absolutely necessary
  “Spring Cleaning” for IP
Result is an elegant, if unambitious, protocol
prematurely

## Slide 116: IPv6
Larger address space
Auto-configuration (not new but better than IPv4)
Cleanup
  Eliminate fragmentation
  Eliminate checksum
    Pseudo-header (w/o Hop Limit) covered by transport layer
  Flow label
  Increase minimum MTU from 576 to 1280
  Replace broadcasts with multicast
IPv6 slides are hugely improved thanks to Stephen Strowes

## Slide 117
IPv4 | IPv6
Addresses are 32 bits (4 bytes) in length. | Addresses are 128 bits (16 bytes) in length
Address (A) resource records in DNS to map host names to IPv4 addresses. | Address (AAAA) resource records in DNS to map host names to IPv6 addresses.
Pointer (PTR) resource records in the IN-ADDR.ARPA DNS domain to map IPv4 addresses to host names. | Pointer (PTR) resource records in the IP6.ARPA DNS domain to map IPv6 addresses to host names.
IPSec is optional and should be supported externally | IPSec support is not optional
Header does not identify packet flow for QoS handling by routers | Header contains Flow Label field, which Identifies packet flow for QoS handling by router.
Both routers and the sending host fragment packets. | Routers do not support packet fragmentation. Sending host fragments packets
Header includes a checksum. | Header does not include a checksum.
Header includes options. | Optional data is supported as extension headers.
ARP uses broadcast ARP request to resolve IP to MAC/Hardware address. | Multicast Neighbor Solicitation messages resolve IP addresses to MAC addresses.
Internet Group Management Protocol (IGMP) manages membership in local subnet groups. | Multicast Listener Discovery (MLD) messages manage membership in local subnet groups.
Broadcast addresses are used to send traffic to all nodes on a subnet. | IPv6 uses a link-local scope all-nodes multicast address.
Configured either manually or through DHCP. | Does not require manual configuration or DHCP.
Must support a 576-byte packet size (possibly fragmented). | Must support a 1280-byte packet size (without fragmentation).

## Slide 118: Larger Address Space
IPv4 = 4,294,967,295 addresses
IPv6 = 340,282,366,920,938,463,374,607,432,768,211,456 addresses
4x in number of bits translates to huge increase in address space!

## Slide 119: Other Significant Protocol Changes - 1
Increased minimum MTU from 576 to 1280
No enroute fragmentation… fragmentation only at source
Header changes (20bytes to 40bytes)
Replace broadcast with multicast
Fragment Offset
Flags
Total Length
Type of Service
IHL
Padding
Options
Destination Address
Source Address
Header Checksum
Protocol
Time to Live
Identification
Version
Next Header
Hop Limit
Flow Label
Traffic Class
Destination Address
Source Address
Payload Length
Version
Field’s Name Kept from IPv4 to IPv6
Fields Not Kept in IPv6
Name and Position Changed in IPv6
New Field in IPv6
Legend
IPv4
IPv6

## Slide 120: Other Significant Protocol Changes - 2
operation is intended to be simpler within the network:
no in-network fragmentation
no checksums in IPv6 header
UDP checksum required (wasn’t in IPv4) rfc6936: No more zero
optional state carried in extension headers
  Extension headers notionally replace IP options
  Each extension header indicates the type of the following header, so they can be chained
  The final ‘next header’ either indicates there is no ‘next’, or escapes into an transport-layer header (e.g., TCP)

## Slide 121: IPv6 Basic Address Structure
IPv6 addresses are split into two primary parts:
► 64 bits is dedicated to an addressable interface (equivalent to the host, if it only has one interface)
► The network prefix allocated to a network by a registry can be up to 64-bits long
► An allocation of a /64 (i.e. a 64-bit network prefix) allows one
subnet (it cannot be subdivided)
► A /63 allows two subnets; a /62 offers four, etc. /48s are common for older allocations (RFC 3177, obsoleted by RFC 6177).
► Longest-prefix matching operates as in IPv4.
Notes: Here 2019-02-15
2020-2-17

## Slide 122: IPv6 Address Representation (quick)
IPv6 addresses represented as eight 16-bit blocks (4 hex chars) separated by colons:
2001:4998:000c:0a06:0000:0000:0002:4011
But we can condense the representation by removing leading zeros in each block:
2001:4998:c:a06:0:0:2:4011
And by reducing the consecutive block of zeros to a “::”
(this double colon rule can only be applied once)
2001:4998:c:a06::2:4011

## Slide 123: IPv6 Address Families
The address space is carved, like v4, into certain categories 1:
host-local : localhost; ::1 is equivalent to 127.0.0.1
link-local : not routed: fe80::/10 is equivalent to
169.254.0.0/16
site-local : not routed globally: fc00::/7 is equivalent to
192.168.0.0/16 or 10.0.0.0/8
global unicast : 2000::/3 is basically any v4 address not reserved in some other way
multicast : ff00::/8 is equivalent to 224.0.0.0/4
1http://www.ripe.net/lir-services/new-lir/ipv6_reference_card.pdf

## Slide 124: Problem with /64 Subnets
Scanning a subnet becomes a DoS attack!
  Creates IPv6 version of 264 ARP entries in routers
  Exhaust address-translation table space
So now we have:
ping6 ff02::1 All nodes in broadcast domain
ping6 ff02::2 All routers in broadcast domain
Solutions
  RFC 6164 recommends use of /127 to protect router-router links
  RFC 3756 suggest “clever cache management” to address more generally

## Slide 125: Neighbour Discovery
The Neighbour Discovery Protocol2 specifies a set of ICMPv6 message types that allow hosts to discover other hosts or routing hardware on the network
  neighbour solicitation
  neighbour advertisement
  router solicitation
  router advertisement
  redirect
In short, a host can solicit neighbour (host) state to determine the layer-2 address of a host or to check whether an address is in use
or it can solicit router state to learn more about the network configuration
In both cases, the solicit message is sent to a well-known multicast address
2http://tools.ietf.org/html/rfc4861

## Slide 126: IPv6 Dynamic Address Assignment
We have the two halves of the IPv6 address: the network component and the host component. Those are derived in different ways.
Network (top 64 bits):
  Router Advertisements (RAs) Interface
Identifier (bottom 64 bits):
  Stateless, automatic: SLAAC
  Stateful, automatic: DHCPv6

## Slide 127: SLAAC: overview
SLAAC is:
... intended to make network configuration easy without manual configuration or even a DHCP server
... an algorithm for hosts to automatically configure their network interfaces (set up addresses, learn routes) without intervention

## Slide 128: SLAAC: overview
When a host goes live or an interface comes up, the system wants to know more about its environment
It can configure link-local addresses for its interfaces: it uses the interface identifier, the EUI-64
It uses this to ask (solicit) router advertisements sooner than the next periodic announcements; ask the network for information

## Slide 129: SLAAC: overview
The algorithm (assuming one interface):
Generate potential link-local address
Ask the network (multicast4) if that address is in use: neighbour solicitation
Assuming no responses, assign to interface
4https://tools.ietf.org/html/rfc2373

## Slide 130: The EUI-64 Interface Identifier
IEEE 64-bit Extended Unique Identifier (EUI-64)3
There are various techniques to derive a 64-bit value, but often times we derive from the 48-bit MAC address
3http://tools.ietf.org/html/rfc2373
the seventh bit from the left, or the universal/local (U/L) bit, needs to be inverted, 0 = local admin 1 = universal admin

## Slide 131: SLAAC: overview; Router Solicitation
Then,
Once the host has a unique link-local address, it can send packets to anything else sharing that link substrate
... but the host doesn’t yet know any routers, or public routes
... bootstrap: routers listen to a well-known multicast address
host asks the network (multicast) for router information: router solicitation
responses from the routers are sent directly (unicast) to the host that sent the router solicitation
the responses may indicate that the host should do more (e.g., use DHCP to get DNS information)

## Slide 132: Router Advertisement
Without solicitation, router advertisements are generated intermittently by routing hardware.
Router Advertisements:
nodes that forward traffic periodically advertise themselves to the network
periodicity and expiry of the advertisement are configurable
Router Advertisement (RA), among other things, tells a host where to derive its network state with two flags: M(anaged) and O(ther info):
M: “Managed Address Configuration”, which means: use DHCPv6 to find your host address (and ignore option O)
O: Other information is available via DHCPv6, such as DNS configuration

## Slide 133: Uh-oh
What problem(s) arises from totally decentralised address configuration?
Concerns that arise from using an EUI-64:
Privacy: SLAAC interface identifiers don’t change over time, so a host can be identified across networks
Security: embedding a MAC address into an IPv6 address will carry that vendor’s ID(s)5, a possible threat vector
5http://standards.ieee.org/develop/regauth/oui/public.html

## Slide 134: Address Configuration: SLAAC Privacy Addresses
Privacy extensions for SLAAC6
  temporary addresses for initiating outgoing sessions
  generate one temporary address per prefix
  when they expire, they are not used for new sessions, but can continue to be used for existing sessions
  the addresses should appear random, such that they are difficult to predict
  lifetime is configurable; this OSX machine sets an 86,400s timer (1 day)
6https://tools.ietf.org/html/rfc4941

## Slide 135: Address Configuration: SLAAC Privacy Addresses
The algorithm:
Assume: a stored 64-bit input value from previous iterations, or a pseudo-randomly generated value
take that input value and append it to the EUI-64
compute the MD5 message digest of that value
set bit 6 to zero
compare the leftmost 64-bits against a list of reserved interface identifiers and those already assigned to an address on the local device. If the value is unacceptable, re-run using the rightmost 64 bits of the result instead of the historic input value in step 1
use the leftmost 64-bits as the randomised interface identifier
store the rightmost 64-bits as the history value to be used in the next iteration of the algorithm

## Slide 136: IPv6: why has the transition taken so long?
IPv4 and IPv6 are not compatible:
  different packet formats
  different addressing schemes
as the Internet has grown bigger and accumulated many IPv4-only services, transition has proven ... Tricky
Incentive issues
Virgin Media policy in 2010
….When IPV6 is rolled out across the whole of the Internet then a lot of the ISP's will roll out IPV6, ….

## Slide 137: IPv6: why has the transition taken so long?
IPv4 has/had the momentum
... which led to CIDR
... and encouraged RFC1918 space and NAT
IPv4 NAT was covered earlier in this topic (reminder)
  your ISP hands you only one IPv4 address
  you share that across multiple devices in your household
  The NAT handles all the translation between internal (“private”) and external (“public”) space

## Slide 138: Transition tech: outline
Tunnelling
dual-stacked services, and happy eyeballs
DNS64 and NAT648
464XLAT
DNS behaviour
8https://tools.ietf.org/html/rfc6146

## Slide 139: Transition tech: outline
Tunnelling
dual-stacked services, and happy eyeballs
DNS64 and NAT648
464XLAT
DNS behaviour
8https://tools.ietf.org/html/rfc6146
Think of it as an IPv6 VPN service; which is essentially what it is

## Slide 140: Dual-Stack Services: Common Deployment
It’s common for web services to play conservatively: dual-stack your edge services (e.g., load balancers), leaving some legacy infrastructure for later:

## Slide 141: Dual-Stack Services: Common Deployment
Aim is to reduce the pain:
  You can dual-stack the edge hosts, and carry state in, say, HTTP headers indicating the user’s IP address (common over v4 anyway)
  You can dual-stack the backend opportunistically, over a longer period of time
  You use DNS to enable/disable the v6 side last (if there is no AAAA record in DNS, no real users will connect to the IPv6 infrastructure

## Slide 142: Happy Eyeballs and DNS
The introduction of IPv6 carried with it an obligation that applications attempt to use IPv6 before falling back to IPv4.
What happens though if you try to connect to a host which doesn’t exist?9
But the presence of IPv6 modifies the behaviour of DNS responses and response preference10
9https://tools.ietf.org/html/rfc5461
10https://tools.ietf.org/html/rfc3484

## Slide 143: Happy Eyeballs
Happy Eyeballs11 was the proposed solution
  the eyeballs in question are yours, or mine, or whoever is sitting in front of their browser getting mad that things are unresponsive
Modifies application behaviour
11https://tools.ietf.org/html/rfc8305

## Slide 144: DNS64 & NAT64

## Slide 145: 464XLAT
Problem: IPv6-only to the host, but an IPv4-only app trying to access an IPv4-only service
  Some applications do not understand IPv6, so having an IPv6 address doesn’t help
  464XLAT12 solves this problem
  In essence, DNS64 + NAT64 + a shim layer on the host itself to offer IPv4 addresses to apps
12https://tools.ietf.org/html/rfc6877

## Slide 146: Where are we now? BGP Connectivity 2005

## Slide 147: Where are we now? BGP Connectivity 2015

## Slide 148: Improving on IPv4 and IPv6?
Why include unverifiable source address?
  Would like accountability and anonymity (now neither)
  Return address can be communicated at higher layer
Why packet header used at edge same as core?
  Edge: host tells network what service it wants
  Core: packet tells switch how to handle it
    One is local to host, one is global to network
Some kind of payment/responsibility field?
  Who is responsible for paying for packet delivery?
  Source, destination, other?
Other ideas?

## Slide 149: Summary Network Layer
understand principles behind network layer services:
  network layer service models
  forwarding versus routing (versus switching)
  how a switch & router works
  routing (path selection)
  IPv6
Algorithms
  Two routing approaches (LS vs DV)
  One of these in detail (LS)
  ARP
Other Core ideas
  Caching, soft-state, broadcast
  Fate-sharing in practice….
Notes: 30-jan-2015 / 25-jan-2016