## Slide 1: P51(bis): High Performance Networked-Systems
Prof. Andrew W. Moore
Lecture 4
With great appreciation to Dick Sites for sharing wisdom, patience, and teaching materials.
A huge thank you to Eben Upton, Raspberry Pi Foundation, and PiHut people for enabling this incarnation of the module at incredibly short notice.

## Slide 2: What we will cover
Characteristics of a datacenter environment
  goals, constraints, workloads, etc.
How and why DC networks are different (vs. WAN)
  e.g., latency, geo, autonomy, …
How traditional solutions fare in this environment
  e.g., IP, Ethernet, TCP, ARP, DHCP
Not details of how datacenter networks operate

## Slide 3: Disclaimer
Material is a snapshot of evolving (not established) wisdom
Material is incomplete
  many details on how and why datacenter networks operate aren’t public

## Slide 4: Datacenter networks
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  reliability
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container, Chicago data center

## Slide 5: Datacenter networks: network elements
Server racks
20- 40 server blades: hosts
Top of Rack (TOR) switch
one per rack
40-100Gbps Ethernet to blades
Tier-2 switches
connecting to ~16 TORs below
Tier-1 switches
connecting to ~16 T-2s below
Border routers
connections outside datacenter
…
…
…
…
…
…
…
…

## Slide 7: Datacenter networks: network elements
Facebook F16 data center network topology:
https://engineering.fb.com/data-center-engineering/f16-minipack/ (posted 3/2019)

## Slide 8: Datacenter networks: multipath
9
10
11
12
13
14
15
16
two disjoint paths highlighted between racks 1 and 11
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 9: Datacenter networks: application-layer routing
…
…
…
…
…
…
…
…
Load
balancer
Internet
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)

## Slide 10: Why Datacenters?
Your <public-life, private-life, banks, government> live in my datacenter.
Security, Privacy, Control, Cost, Energy, (breaking) received wisdom; all this and more come together into sharp focus in datacenters.
Do I need to labor the point?

## Slide 11: What goes into a datacenter (network)?
Servers organized in racks

## Slide 12: What goes into a datacenter (network)?
Servers organized in racks
Each rack has a `Top of Rack’ (ToR) switch

## Slide 13: What goes into a datacenter (network)?
Servers organized in racks
Each rack has a `Top of Rack’ (ToR) switch
An `aggregation fabric’ interconnects ToR switches

## Slide 14: What goes into a datacenter (network)?
Servers organized in racks
Each rack has a `Top of Rack’ (ToR) switch
An `aggregation fabric’ interconnects ToR switches
Connected to the outside via `core’ switches
  note: blurry line between aggregation and core
With network redundancy of ~2x for robustness

## Slide 15: Example 1
Brocade reference design (circa 2007)

## Slide 16: Example 2
CR
CR
AR
AR
AR
AR
. . .
S
S
Internet
S
S
A
A
A
…
S
S
A
A
A
…
. . .
~ 40-80 servers/rack
Cisco reference design

## Slide 17: Observations on DC architecture
Regular, well-defined arrangement
Hierarchical structure with rack/aggr/core layers
Mostly homogenous within a layer
Supports communication between servers and between servers and the external world
Contrast: ad-hoc structure, heterogeneity of WANs

## Slide 18: What’s different?

## Slide 19: SCALE!

## Slide 20: How big exactly?
1Million servers [Microsoft]
  less than google, more than amazon
> $1B to build one site [Facebook]
>$20M/month/site operational costs [Microsoft ’09]
But only O(10-100) sites

## Slide 21: What’s new?
Scale
Service model
  user-facing, revenue generating services
  multi-tenancy
  jargon: SaaS, PaaS, DaaS, IaaS, …

## Slide 22: Implications
Scale
  need scalable solutions
  improving efficiency, lowering cost is critical
  `scale out’ solutions w/ commodity technologies
Service model
  performance means $$
  virtualization for isolation and portability

## Slide 23: Multi-Tier Applications
Applications decomposed into tasks
  Many separate components
  Running in parallel on different machines

## Slide 24: Componentization leads to different types of network traffic
“North-South traffic”
  Traffic between external clients and the datacenter
  Handled by front-end (web) servers, mid-tier application servers, and back-end databases
  Traffic patterns fairly stable, though diurnal variations

## Slide 25: North-South Traffic
Router
Web Server
Web Server
Web Server
Data
Cache
Data
Cache
Database
Database
Front-End
Proxy
Front-End
Proxy
user requests from the Internet
You Live Here

## Slide 26: Componentization leads to different types of network traffic
“North-South traffic”
  Traffic between external clients and the datacenter
  Handled by front-end (web) servers, mid-tier application servers, and back-end databases
  Traffic patterns fairly stable, though diurnal variations
“East-West traffic”
  Traffic between machines in the datacenter
  Comm within “big data” computations (e.g. Map Reduce)
  Traffic may shift on small timescales (e.g., minutes)

## Slide 27: East-West Traffic
Distributed
Storage
Distributed
Storage
Map
Tasks
Reduce
Tasks

## Slide 28: East-West Traffic
CR
CR
AR
AR
AR
AR
S
S
S
S
A
A
A
…
S
S
A
A
A
…
. . .
S
S
S
S
A
A
A
…
S
S
A
A
A
…

## Slide 29: East-West Traffic
Distributed
Storage
Distributed
Storage
Map
Tasks
Reduce
Tasks
Often doesn’t cross the network
Always goes over the network
Some fraction (typically 2/3) crosses the network

## Slide 30: East-West vs North-South
Notes: Taken from https://code.facebook.com/posts/360346274145943/introducing-data-center-fabric-the-next-generation-facebook-data-center-network/

## Slide 31: What’s different about DC networks?
Characteristics
Huge scale:
  ~20,000 switches/routers
  contrast: AT&T ~500 routers

## Slide 32: What’s different about DC networks?
Characteristics
Huge scale:
Limited geographic scope:
  High bandwidth: 10/40/100G
  Contrast: Cable/aDSL/WiFi
  Very low RTT: 10s of microseconds
  Contrast: 100s of milliseconds in the WAN

## Slide 33: What’s different about DC networks?
Characteristics
Huge scale
Limited geographic scope
Single administrative domain
  Can deviate from standards, invent your own, etc.
  “Green field” deployment is still feasible

## Slide 34: What’s different about DC networks?
Characteristics
Huge scale
Limited geographic scope
Single administrative domain
Control over one/both endpoints
  can change (say) addressing, congestion control, etc.
  can add mechanisms for security/policy/etc. at the endpoints (typically in the hypervisor)

## Slide 35: What’s different about DC networks?
Characteristics
Huge scale
Limited geographic scope
Single administrative domain
Control over one/both endpoints
Control over the placement of traffic source/sink
  e.g., map-reduce scheduler chooses where tasks run
  alters traffic pattern (what traffic crosses which links)

## Slide 36: What’s different about DC networks?
Characteristics
Huge scale
Limited geographic scope
Single administrative domain
Control over one/both endpoints
Control over the placement of traffic source/sink
Regular/planned topologies (e.g., trees/fat-trees)
  Contrast: ad-hoc WAN topologies (dictated by real-world geography and facilities)

## Slide 37: What’s different about DC networks?
Characteristics
Huge scale
Limited geographic scope
Single administrative domain
Control over one/both endpoints
Control over the placement of traffic source/sink
Regular/planned topologies (e.g., trees/fat-trees)
Limited heterogeneity
  link speeds, technologies, latencies, …

## Slide 38: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
  recall: all that east-west traffic
  target: any server can communicate at its full link speed
  problem: server’s access link is 10Gbps!

## Slide 39: Full Bisection Bandwidth
CR
CR
AR
AR
AR
AR
. . .
S
S
Internet
S
S
A
A
A
…
S
S
A
A
A
…
. . .
~ 40-80 servers/rack
10Gbps
O(40x10)Gbps
O(40x10x100)Gbps
Traditional tree topologies “scale up”
full bisection bandwidth is expensive
typically, tree topologies “oversubscribed”

## Slide 40: A “Scale Out” Design
Build multi-stage `Fat Trees’ out of k-port switches
  k/2 ports up, k/2 down
  Supports k3/4 hosts:
    48 ports, 27,648 hosts
All links are the same speed (e.g. 10Gps)

## Slide 41: Full Bisection Bandwidth Not Sufficient
To realize full bisectional throughput, routing must spread traffic across paths
Enter load-balanced routing
  How? (1) Let the network split traffic/flows at random (e.g., ECMP protocol -- RFC 2991/2992)
  How? (2) Centralized flow scheduling?
  Many more research proposals

## Slide 42: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
  real money on the line
  current target: 1μs RTTs
  how? cut-through switches making a comeback
    reduces switching time

## Slide 43: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
  real money on the line
  current target: 1μs RTTs
  how? cut-through switches making a comeback
  how? avoid congestion
    reduces queuing delay

## Slide 44: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
  real money on the line
  current target: 1μs RTTs
  how? cut-through switches making a comeback (lec. 2!)
  how? avoid congestion
  how? fix TCP timers (e.g., default timeout is 500ms!)
  how? fix/replace TCP to more rapidly fill the pipe

## Slide 45: An example problem at scale - INCAST
TCP timeout
Worker 1
Worker 2
Worker 3
Worker 4
Aggregator
RTOmin = 300 ms
Synchronized mice collide.
  Caused by Partition/Aggregate.

## Slide 46: The Incast Workload
Client
Switch
Storage Servers
R
R
R
R
1
2
Data Block
Server
Request Unit
(SRU)
3
4
Synchronized Read
Client now sends
next batch of requests
1
2
3
4
46

## Slide 47
Client
Switch
R
R
R
R
1
2
3
4
4
Synchronized Read
1
2
3
4
Server
Request Unit
(SRU)
4
Incast Workload Overfills Buffers
47
Requests Sent
Requests
Received
Responses 1-3 completed
Response 4
dropped
Response 4
Resent
Link Idle!

## Slide 48: Queue Buildup
Sender 1
Sender 2
Receiver
Big flows buildup queues.
  Increased latency for short flows.
Measurements in Bing cluster
  For 90% packets: RTT < 1ms
  For 10% packets: 1ms < RTT < 15ms

## Slide 49: Link-Layer Flow Control Common between switches but this is flow-control to the end host too…
Another idea to reduce incast is to employ Link-Layer Flow Control…..
Recall: the Data-Link can use specially coded symbols in the coding to say “Stop” and “Start”

## Slide 50: Link Layer Flow Control – The Dark side Head of Line Blocking….
Waiting for no good reason….
Such HOL blocking does not even differentiate processes so this can occur between competing processes on a pair of machines – no datacenter required.

## Slide 51: Link Layer Flow Control But its worse that you imagine….
…
Double down on trouble….
Did I mention this is Link-Layer!
That means no (IP) control traffic, no routing messages….
a whole system waiting for one machine
Incast is very unpleasant.
Reducing the impact of Head of Line (blocking) in Link Layer Flow Control can be done through priority queues and overtaking….

## Slide 52: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
Predictable, deterministic performance
  “your packet will reach in Xms, or not at all”
  “your VM will always see at least YGbps throughput”
  Resurrecting `best effort’ vs. `Quality of Service’ debates
  How is still an open question

## Slide 53: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
Predictable, deterministic performance
Differentiating between tenants is key
  e.g., “No traffic between VMs of tenant A and tenant B”
  “Tenant X cannot consume more than XGbps”
  “Tenant Y’s traffic is low priority”

## Slide 54: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
Predictable, deterministic performance
Differentiating between tenants is key
Scalability (of course)
  Q: How’s that Ethernet spanning tree looking?

## Slide 55: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
Predictable, deterministic performance
Differentiating between tenants is key
Scalability (of course)
  Q: How’s that Ethernet spanning tree looking?

## Slide 56: What’s different about DC networks?
Goals
Extreme bisection bandwidth requirements
Extreme latency requirements
Predictable, deterministic performance
Differentiating between tenants is key
Scalability (of course)
Cost/efficiency
  focus on commodity solutions, ease of management
  some debate over the importance in the network case

## Slide 57: Summary
new characteristics and goals
some liberating, some constraining
scalability is the baseline requirement
more emphasis on performance
less emphasis on heterogeneity
less emphasis on interoperability
Notes: -- incast?
-- one big switch abstraction…

## Slide 58: Datacenter overview

## Slide 59: Datacenter Computers modern challenges in CPU design
Dick Sites
Google Inc.

## Slide 60: Enough with Datacenter networks, what about CPU?

## Slide 61: Modern challenges in CPU design
Lots of memory
Multi-issue CPU instructions every cycle that drive full bandwidth
Full bandwidth all the way to RAM, not just to L1 cache
More prefetching in software
Bigger page size(s)
Notes: 20 min

## Slide 62
Thesis: Servers and
desktops require
different design emphasis

## Slide 63: Goals
Draw a vivid picture of a computing environment that may be foreign to your experience so far
Expose some ongoing research problems
Perhaps inspire contributions in this area

## Slide 64: Datacenter Servers are Different
Server programs start and run for months
  Tens of programs per server
Real-time user-facing transactions, not batch
  Minimize latency, not CPU idle time
Big fanout: one transaction to 1000+ servers
  only 1-10ms CPU time per server
10K+ computers, 100K+ disks, 1000k+ network connections

## Slide 65: Datacenter Servers are Different
① Move data: big and small
② Real-time transactions: 1000s per second
③ Isolation between programs
④ Measurement underpinnings
Notes: 5 min

## Slide 66: ① Move data: big and small

## Slide 67: Move data: big and small
Move lots of data
  Disk to/from RAM
  Network to/from RAM
  SSD to/from RAM
  Within RAM
Bulk data
Short data: variable-length items
Compress, encrypt, checksum, hash, sort

## Slide 68: Wakeup Detail
Target CPU was busy; kernel waited
THREADs
50 us
50us
CPUs
CPU 9 busy;
But 3 was idle

## Slide 69: Lots of memory
4004: no memory
i7: 12MB L3 cache

## Slide 70: Little brain, LOTS of memory
Server 64GB-1TB
Drinking straw access

## Slide 71: ② Real-time transactions: 1000s per second

## Slide 72: A Single Transaction Across ~40 Racks of ~60 Servers
Each arc is a related client-server RPC (remote procedure call)

## Slide 73: A Single Transaction RPC Tree: Client & 93 Servers
?
?

## Slide 74: Single Transaction Tail Latency
Canary transaction

## Slide 75: Single Transaction Tail Latency
One slow response out of 93 parallel RPCs slows the entire transaction

## Slide 76: One Server, Four CPUs: User/kernel transitions every CPU every nanosecond (Ktrace)
200 usec
CPU 0
CPU 1
CPU 2
CPU 3

## Slide 77: 16 CPUs, 600us, Many RPCs
CPUs 0..15
RPCs 0..39

## Slide 78: 16 CPUs, 600us, Many RPCs
THREADs 0..46
LOCKs 0..22

## Slide 79: That is A LOT going on at once
Let’s look at just one long-tail RPC in context

## Slide 80: 16 CPUs, 600us, one RPC
CPUs 0..15
RPCs 0..39

## Slide 81: 16 CPUs, 600us, one RPC
THREADs 0..46
LOCKs 0..22

## Slide 82: Wakeup Detail
Thread 25 actually runs
Thread 19 frees lock, sends wakeup to waiting thread 25
50 us
50us wakeup delay ??

## Slide 83: CPU Scheduling, 2 Designs
Re-dispatch on any idle CPU core
  But if idle CPU core is in deep sleep, can take 75-100us to wake up
Wait to re-dispatch on previous CPU core, to get cache hits
  Saves nothing if could use same L1 cache
  Saves ~10us if could use same L2 cache
  Saves ~100us if could use same L3 cache
  Expensive if cross-socket cache refills
  Don’t wait too long…

## Slide 84: Real-time transactions: 1000s per second
Not your father’s SPEC benchmarks
To understand delays, need to track simultaneous transactions across servers, CPU cores, threads, queues, locks

## Slide 85: Modern challenges in CPU design
A single transaction can touch thousands of servers in parallel
The slowest parallel path dominates
Tail latency is the enemy
  Must control lock-holding times
  Must control scheduler delays
  Must control interference via shared resources
Notes: 29 min

## Slide 86: ③ Isolation between programs

## Slide 87: Histogram: Disk Server Latency; Long Tail
Latency 99th %ile = 696 msec

## Slide 88: Non-repeatable Tail Latency Comes from Unknown Interference
Isolation of programs reduces tail latency.
Reduced tail latency = higher utilization.
Higher utilization = $$$.

## Slide 89: Many Sources of Interference
Most interference comes from software
But a bit from the hardware underpinnings
In a shared apartment building, most interference comes from jerky neighbors
But thin walls and bad kitchen venting can be the hardware underpinnings

## Slide 90: Isolation issue: Cache Interference
0000000000000000000000000000000000
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
…
0 1 2 3
Core 0
00000000
4 5 6 7
Core 1
L1 caches
60 61 62 63 PCs
Core 15
L1 caches
0000000000000000000
L2 cache
…
000
000
CPU thread 0 is moving 16B/cycle flat out, filling caches

## Slide 91: Isolation issue: Cache Interference
CPU thread 0 is moving 16B/cycle flat out, filling caches
0000000000000000000000000000000000
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
…
0 1 2 3
Core 0
00000000
4 5 6 7
Core 1
L1 caches
60 61 62 63 PCs
Core 15
L1 caches
0000000000000000000
L2 cache
…
000
000

## Slide 92: Isolation issue: Cache Interference
CPU thread 0 is moving 16B/cycle flat out
000000000000000000000…
0 1 2 3
Core 0
00000000
4 5 6 7
Core 1
77777777
Today
~000111222333444555666777…
0 1 2 3
Core 0
~00112233
4 5 6 7
Core 1
~44556677
Desired

## Slide 93: Isolation between programs
Good fences make good neighbors
We need better hardware support for program isolation in shared memory systems

## Slide 94: Modern challenges in CPU design
Isolating programs from each other on a shared server is hard
As an industry, we do it poorly
  Shared CPU scheduling
  Shared caches
  Shared network links
  Shared disks
More hardware support needed
More innovation needed
Notes: 36 min

## Slide 95: ④ Measurement underpinnings

## Slide 96: Differences from desktop software
Tens of thousands of user-facing transactions per second
Distributed computation across thousands of servers
The important metric is response time, i.e. latency
Excessive tail latency is the most important performance problem
As an industry, we have poor tools for observing and understanding tail latency

## Slide 97: Tail latency
Some transactions, total latency for each one
We seek to understand why the one is slow

## Slide 98: Easy case
A particular transaction is slow every time it is run
It is straightforward to run the transaction repeatedly offline on a few load-test servers
Existing profiling tools, disk byte counts, network byte counts, etc. will reveal where the time goes

## Slide 99: "Interesting" case
A particular transaction is usually fast, but occasionally quite slow
It is only slow under live load during the busiest hour of the day
Running it again it runs fast
Until the reason for slowness is found, we cannot reproduce the problem offline
Existing tools are unable to reveal where the time goes

## Slide 100: "Interesting" case -- why it matters
Until the reason for slowness is found, we cannot reproduce the problem offline
At 10,000 transactions/second and no call tree, the 99th percentile slow cases happen 100 times per second
But, for software with 100:1 fanout transaction call trees, almost everything runs at the 99th percentile slow rate
Existing tools are unable to reveal where the time goes

## Slide 101: Tail latency
Some transactions, total latency
We seek to understand why the one is slow

## Slide 102: Tail latency
Possible tool: average latency
Tells us nothing about the slow one
average

## Slide 103: Tail latency
Possible tool: average latency
Tells us nothing about the slow one
Average is the wrong tool for understanding variance
average

## Slide 104: Tail latency
Possible tool: latency histogram
Tells us what we have but not why
latency
count

## Slide 105: Tail latency
Possible tool: latency histogram
Tells us what we have but not why
Histogram is the wrong tool for understanding variance
latency
count

## Slide 106: Tail latency
Possible tool: Profile of CPU time per source function
But where is the slow transaction?
gather_inputs() | 
process_item() | 
process_more() | 
calculate() | 
produce_output() | 

## Slide 107: Tail latency
Possible tool: Profile of CPU time per source function
But where is the slow transaction?
Profiling is the wrong tool for understanding variance
gather_inputs() | 
process_item() | 
process_more() | 
calculate() | 
produce_output() | 

## Slide 108: Profiling: the wrong tool for understanding variance
Possible tool: Profile of CPU time per source function
It merges together many normal transactions with few slow ones, hiding the 1% signal in 99% noise
gather_inputs() | 
process_item() | 
process_more() | 
calculate() | 
produce_output() | 

## Slide 109: Tail latency
Possible tool: Profile of CPU time per source function
But where is the slow transaction?
CPU Profiling is the wrong tool for a second reason ...
gather_inputs() | 
process_item() | 
process_more() | 
calculate() | 
produce_output() | 

## Slide 110: CPU Profiling: the wrong tool for a second reason
Some transactions, total time
The delay may not be using CPU time at all; it may be waiting for something. CPU profiling is blind to non-CPU wait time

## Slide 111: Tail latency
Possible tool: trace events for each transaction
Now we can see what is different about the slow one.
But we don't know why it is different

## Slide 112: Tail latency
Possible tool: trace events for each transaction, lined up in time
Now we can see what is different about the slow one.
And the time alignment of 6's end-of-green (A) with 8's green blocking until B.
1
2
3
4
5
6
7
8
9
10
B
A

## Slide 113: Tail latency
Possible tool: trace events for each transaction, lined up in time
More detailed events at A or B will reveal the reason for starting or stopping blocking. (Possibly a race condition or a contended software lock.)
1
2
3
4
9
10
A
B
5
6
7
8

## Slide 114: Tail latency, summary
Average is the wrong tool for understanding variance
Histogram is the wrong tool for understanding variance
Profile is the wrong tool for understanding variance
Event tracing is a good tool for understanding variance
Event tracing lined up in time is a great tool for understanding variance --
it can show causes of delay directly
More detailed events at A or B will reveal the reason for starting or stopping blocking. (Possibly a race condition or a contended software lock.)

## Slide 115: Trace: Disk Server, 13 disks, 1.5 sec
Latencies: 250ms, 500ms, … for nine minutes
Read
Write
Read hit
Write hit
4
5
4

## Slide 116: Why?
Probably not on your guessing radar…
Kernel throttling the CPU use of any process that is over purchased quota
Only happened on old, slow servers

## Slide 117: Disk Server, CPU Quota bug
Understanding Why sped up 25% of entire disk fleet worldwide!
  Had been going on for three years
  Savings paid my salary for 10 years
Hanlon's razor: Never attribute to malice that which is adequately explained by stupidity.
Sites’ corollary: Never attribute to stupidity that which is adequately explained by software complexity.
4

## Slide 118: Measurement Underpinnings
All performance mysteries are simple once they are understood
“Mystery” means that the picture in your head is wrong; software engineers are singularly inept at guessing how their view differs from reality

## Slide 119: Modern challenges in CPU design
Need low-overhead tools to observe the dynamics of performance anomalies
  Transaction IDs
  RPC trees
  Timestamped transaction begin/end
Traces
  CPU kernel+user, RPC, lock, thread traces
  Disk, network, power-consumption
Notes: 43 min

## Slide 120: Summary: Datacenter Servers are Different

## Slide 121: Datacenter Servers are Different
① Move data: big and small
② Real-time transactions: 1000s per second
③ Isolation between programs
④ Measurement underpinnings

## Slide 122: References
Claude Shannon, A Mathematical Theory of Communication, The Bell System Technical Journal, Vol. 27, pp. 379–423, 623–656, July, October, 1948.
http://cs.ucf.edu/~dcm/Teaching/COP5611-Spring2013/Shannon48-MathTheoryComm.pdf
Richard Sites, It’s the Memory, Stupid!, Microprocessor Report August 5, 1996.
http://cva.stanford.edu/classes/cs99s/papers/architects_look_to_future.pdf
Ravi Iyer, CQoS: A Framework for Enabling QoS in Shared Caches of CMP Platforms, ACM International Conference on Supercomputing, 2004.
http://cs.binghamton.edu/~apatel/cache_sharing/CQoS_iyer.pdf
M Bligh, M Desnoyers, R Schultz , Linux Kernel Debugging on Google-sized clusters, Linux Symposium, 2007
https://www.kernel.org/doc/mirror/ols2007v1.pdf#page=29

## Slide 123: References
Daniel Sanchez and Christos Kozyrakis , The ZCache: Decoupling Ways and Associativity. IEEE/ACM Symp. on Microarchitecture (MICRO-43), 2010.
http://people.csail.mit.edu/sanchez/papers/2010.zcache.micro.pdf
Benjamin H. Sigelman, Luiz Andre Barroso, Mike Burrows, Pat Stephenson, Manoj Plakal, Donald Beaver, Saul Jaspan, Chandan Shanbhag, Dapper, a Large-Scale Distributed Systems Tracing Infrastructure, Google Technical Report dapper-2010-1, April 2010
http://scholar.google.com/scholar?q=Google+Technical+Report+dapper-2010-1&btnG=&hl=en&as_sdt=0%2C5&as_vis=1

## Slide 124: References
Daniel Sanchez, Christos Kozyrakis, Vantage: Scalable and Efficient Fine-Grained Cache Partitioning, Symp. on Computer Architecture ISCA 2011.
http://ppl.stanford.edu/papers/isca11-sanchez.pdf
Luiz André Barroso and Urs Hölzle , The Datacenter as a Computer An Introduction to the Design of Warehouse-Scale Machines, 2nd Edition 2013.
http://www.morganclaypool.com/doi/pdf/10.2200/S00516ED2V01Y201306CAC024

## Slide 125: Thank You, Questions?