## Slide 1: Protocols for Decentralised Spectrum Co-Allocation
Jon Crowcroft
University of Cambridge
Computer Laboratory
http://www.cl.cam.ac.uk/~jac22

## Slide 2: Assumptions
World can be divided into communities
  Economic, social, political, geographic etc
  Have common interest
  Intra-community trust much higher than inter-
Many communities align social and geo-
  Economics are not just about efficiency
Timescales vary from minutes to years
  Lifetime of use or community

## Slide 3: Variety of Constraints
Dynamics
  Terrain, Vehicles, Power
  Weather, mobility, traffic matrices, etc
Safety
  Power limits
Security
  Payment/tokens need to be unforgeable
  No double spending
  Anonimity versus traceability

## Slide 4: Distributed Reservation v. Decentralised Congestion Control
Resource Reservation Schemes
  In wireline networks (rsvp, q2931) interface to
    admission control, policy management, traffic engineering
    API to routers, act as gatekeepers to resource (which is links)
Congestion Control Schemes
  distributed dual optimisation (TCP/ECN or ABR):
    End systems adapt to signal
    Network signals end systems (through loss or ECN)

## Slide 5: Wireless
MAC protocols traditionally resource share
  Contention, hidden terminal etc etc
  Efficiency considerations (not great)
  CSMA/CA is quite like TCP, but…
  Timescales of feedback quite different
Software radio and software defined radio
  Choose modulation, coding, CRC, MAC
  Downloaded, or selected, based on environment
  Sense environment (congnitive) or ask oracle?
Other constraints
  actual antennae, power budget etc

## Slide 6: Conundrum: where to start?
Anology: give me all the capacity for my download then go to next user, or give me 1/nth of the capacity all the time…
  No single optimum operating point for given community
  Different timescales mean that sensing is not going to detect future (or recent) potential contending community
Strong continuity needs
  => Need to keep state
    => Need infrastructure for repositories
    Has a cost, but given geography…
  Can also use repository for (signed) code
    For token validation (ecash etc)
  A role for incumbents too
    Backhaul (c.f. multihop horizon limitations)

## Slide 7: Conclusions:-- Hybridized world
Decentralised managed thru central neutral agency
  Can then use reservation protocols and auctions and other mechanisms to allocate per community
  Can use center to offer checks and balances (polices spectrum “bill of rights”)
  Can use fully decentralised techniques within power budget and spectrum allocation for re-allocation