## Slide 1: Haggle: a Networking Architecture Designed Around Mobile Users
Jon Crowcroft (University of Cambridge)
James Scott (Intel Research Cambridge)
Pan Hui University of Cambridge)
Christophe Diot (Thomson)

## Slide 2: Coming up in the next few mins…
Motivation for doing mobile networking differently
Problem definition for mobile networking: “Pocket Switched Networking”
A set of guiding principles behind our PSN solution, named Haggle
A 39000 feet overview of Haggle’s initial design
A cool demo

## Slide 3: Motivation: Mobile users currently have a very bad experience of networking
Applications do not work without infrastructure
Local connectivity is plentiful (WiFi, Bluetooth, etc), but very hard to use transparently
E.g. messaging/file transfer to others in this room?
E.g. If I had used a modem to get some cached web content (e.g. news) earlier, and you wanted to access it, how can we share it?
The wireless networking research community has failed to support our end users

## Slide 4: Pocket Switched Networking (PSN): Scenario for Mobile Humans
Study/define problem before attempting solution
Pocket Switched Networking: the scenario that the mobile user of consumer IT apps faces every day
  Humans carry one or more devices with them, each with wireless networking capabilities and storage
  These devices experience neighbourhood (e.g. Bluetooth) and infrastructure (e.g. 802.11 AP) connection opportunities (with differing bandwidths, costs, etc)
  Human mobility generates these opportunities as they move around with their normal mobility patterns.

## Slide 5: Pocket Switched Networking: Application traffic
In PSN, we can identify two classes of application traffic:
known-sender where one node needs to transfer data to a user-level destination (not a network-level address), e.g.:
  Another user (who may own many nodes)
  All users in a certain place/with a certain interest
  Users with a certain role (e.g. “police”), etc.
known-recipient in which a device requires content of some sort, but it is irrelevant where the data comes from, e.g.:
  Publicly distributed content such as “current news webpage”
  Media files, e.g. “songs by the Scissor Sisters”
  Locally generated information, e.g. traffic news
For known-sender, there may be many recipients; for known-recipient, there may be many sources.

## Slide 6: Why status quo (IP) does badly in PSN
IP doesn’t handle many-recipient well, and does not handle many-source at all
IP’s strict layering means infrastructure lookups to find endpoint addresses before data transmission begins
TCP/IP’s stream abstraction means that apps have to implement app-layer protocols; these rely on access to specific infrastructures
  E.g. email user wants “message to James” but email client implements “message to IP address of MX DNS record of James’s email domain”
IP cannot handle non-contemporaneous connectivity, e.g. use of human mobility as data transfer opportunity
Packet switching means that app-layer data is lost to the network; further exchanges of the same data means insertion of the data into the network by an application

## Slide 7: Our approach: Haggle
Clean slate design of networking subsystem for mobile devices
Haggle: a layerless, modular network architecture designed around the needs of mobile users
Aims:
  Allow applications to take advantage of all types of data transfer (neighborhood, infrastructure, mobility)
  Allow networking endpoints to be specified by user-level naming schemes rather than node-specific network addresses,
  Allow limited resources to be used efficiently by mobile devices, taking into account user-level priorities for tasks

## Slide 8: Design principles for Haggle
Forward using application layer information
Asynchronous operation
Empower intermediate nodes
Message switching
All user data kept network-visible
Build request-response into the network
Exploit all data transfer methods
Take advantage of brief connection opportunities
Empowered and informed resource management
Use and integrate with existing application infrastructure where possible

## Slide 9: A. Forward using application layer information
Use names meaningful to apps, e.g. human names, keywords for documents, parameters for content wanted (mime-type, etc)
Delivery of data is accomplished by using the data itself to choose forwarding path, rather than artificial meaningless-to-the-user addresses such as IP.

## Slide 10: B. Asynchronous operation
Apps can indicate network actions when natural to them; actual transfers can happen asynchronously when suitable connectivity occurs
Late binding of user-level names to network-level addresses means that up-to-date context information can be used, e.g. dynamic IP address
Support non-contemporaneous, store-and-forward connections

## Slide 11: C. Empower intermediate nodes
Much content is public/sharable – e.g. webpages
Thus any intermediate node may also be a valid destination, e.g. it’s user might also be interested in the webpage later
Additionally, the intermediate node can be a source for that data too – e.g. it meets another node who is interested in the webpage

## Slide 12: D. Message switching
Message switching is useful for principles A,B,C
Application layer forwarding information applies to whole messages
With variability inherent in non-contemporaneous data paths, packet switching would result in lots of useless half-messages arriving, wasting bandwidth
Intermediate nodes cannot gain benefits unless entire data units are made available to them

## Slide 13: E. All user data kept network visible
Data should not be stored privately by applications, but kept in the Haggle framework where it can be shared with other devices.
Even your most personal data can be shared – with your other devices. Encryption can be used to prevent unauthorised parties snooping.
  Painful data synchronisation systems (e.g. phone/PC) can be made obsolete!
Public data is often popular and duplicated locally, so making this visible allows us to find more sources for it

## Slide 14: F. Build request-response into the network
User-level tasks are sometimes inherently two-way, e.g. a request for content and the response including the content
Supporting this in the network framework itself rather than in apps allows all nodes to be used for the “turnaround point”
I.e. all nodes can cache application data (even if they do not run any app that can understand it), and respond to a request for that data

## Slide 15: G. Exploit all data transfer methods
Different transfer methods have different properties
  Synchronous (Bluetooth), asynchronous (SMS)
  Zero cost (neighbourhood), cost-per-hour (WiFi hotspot), zero cost till monthly limit hit (SMS)
  Physical-layer bandwidths, latencies, loss rates, etc
A given transmission may be sent using multiple diverse paths, e.g. by email and later by Bluetooth directly.

## Slide 16: H. Take advantage of brief connection opportunities
Connection opportunities can be fleeting
  E.g. driving past an AP or another car
Must optimise transmissions to maximum user benefit
N.B. current protocols such as Web, SMTP, are really bad at this (work to be presented in WMCSA 2006)

## Slide 17: I. Empowered and informed resource management
Haggle has the potential to use up all your device’s resources and really piss you off
It also has the potential to do resource management correctly, something today’s devices don’t do
  Storage: your disk is not full, why not?
  Networking: your WiFi interface has one queue, why?
  Battery: why use static levels for “plenty” and “little”?
Resource management must be put centre stage in Haggle

## Slide 18: J. Use and integrate with existing application infrastructure where possible
Incremental deployability if a Haggle node can interact with another node’s legacy apps
Can reuse existing (familiar and complex) apps via pretending to be a legacy protocol rather than having to push out new ones
Leverage vast infrastructures that are already deployed – e.g. email servers, IM servers, the Google index, etc

## Slide 19: Current device software framework
Interfaces
Delivery (IP)
Protocol
App logic + GUI
User Data
Application
Networking
File System
Synchronous, node-centric API
Isolated from network
App has two orthogonal parts
Delivery uses anonymous IP

## Slide 20: Haggle framework design
Interfaces
Haggle
Applications
Resource Mgmt
User Data
Delivery (Names)
Protocols
App Logic + GUI
Less work for new app developers
Asynchronous,
data-centric API
Not tied to one app; exposed metadata
Key component missing before
Multiple protocols usable for each task

## Slide 21: User Data – Application Data Units (ADUs)
ADUs contain many “attributes” each consisting of a “type” “value” 2-tuple. Type is text, value is text or can be a
ADUs contain metadata of all types
  File system (creation, ownership, etc)
  Forwarding (to, from, ttl)
  App metadata (keywords,
  filetype, filename, etc)
Type | Value
Creation date | 9/1/6
Mime-type | Image/Jpeg
Keywords | Paris, sunset
Data | [jpeg file]

## Slide 22: Protocols
Protocols are methods for communicating with other nodes, including Haggle-specific protocols as well as legacy protocols (e.g. email)
Example: protocol to send an ADU over an ad-hoc WiFi connection given a neighbour’s MAC address
Example: protocol using keywords as addresses via Google – e.g. satisfy a query for “world news”
Legacy example: encapsulate an ADU in an email and send it using SMTP to an email address

## Slide 23: Delivery using user-level names
Names come from:
  Network, e.g. using neighbour discovery (12:AB:23:98:BE:FF)
  Applications, e.g. Jon Crowcroft » jon.crowcroft@cl.cam.ac.uk
Some names are also “addresses” i.e. data can be delivered to that name using one of the protocols available
Delivery engine needs to:
  Sense “nearby” addresses (e.g. Bluetooth inquiry gives MAC addresses, Internet connectivity means all email addresses are deliverable)
  Known-sender: Map between ADU’s destination name(s) and addresses of suitable next-hop nodes
  Known-recipient: Determine suitable nearby nodes which may be sources or help find sources for requested data
  Describe these potential transfers and their benefits to the resource manager

## Slide 24: Resource management using tasks
Resource management uses a list of tasks mainly provided by delivery engine
  E.g. perform discovery on interface I
  E.g. send ADU X to neighbour Y on interface Z
Each task has an associated benefit and cost
  Benefit is specified by task provider. May be time-dependent (i.e. using a pointer-to-function)
  To get cost, resource use is estimated, and then the “cost” is a function of the resource use * the resource scarcity
  Resource manager then schedules execution of tasks in order of highest benefit/cost ratio.

## Slide 25: So where are we?
Problem definition and some idea of solution
Other work we’ve done:
  Measurement/analysis of human connectivity patterns
  Measurement of in-motion wireless networking properties
Ongoing work in European project
  More measurement and analysis of possible data paths
  Implementation of modular software framework
  Addressing challenges of naming/addressing, forwarding, security/trust, usability, legacy compatibility