## Slide 1: How to provide reachability in the face of real world mobility…
Wireless Open Systems Interconnection Architecture Grand Challenge
Jon.crowcroft@cl.cam.ac.uk
http://www.cl.cam.ac.uk/~jac22

## Slide 2: Part of UK’s Ubicomp Challenge
UK Grand CS Challenges program last 3 years…
  US Grand Challenge
  Looking over the Fence at Network Research
  Newarch project, etc
  Making the world a different place”, ACM CCR, Jul, 2005
What is the problem?
  Microscopic view - creeping problems
  Macroscopic view - big picture problems

## Slide 3: Micro: Some problems with mobile wireless
Increasingly, more people have noticed more problems
  Manet 3 hop horizon (see REALMAN workshop)
  DTN routing, reliability
  Multiple interfaces
  Power, SIR, etc etc
Let’s just pick just one I’ve been involved in, namely
Real world mobility and reachability

## Slide 4: Why measure human mobility?
Information theoretic capacity of multipoint radio:
  No known “Shannon limit”, but
  Gupta&Kumar say capacity increases with #users.
  Tse&Grossglasuer say: Mobility increases capacity of dense mobile network
Mobility also create dis-connectivity
Human mobility patterns determine communication opportunities
Notes: Mobility provide physical way to carry a large bunch of data from one place to another place, some research actually also shows that mobility increase the capacity of dense network. But moblity at the same time creat the challenge for communication, it creats disconnectivities and make end to end communications less possible. In pocket swich network, mobility has another important role, the mobility patterns determine the next commnication opportunities. Human mobility is so important so worth us to spend sometimes to study it.

## Slide 5: Brief summary of One Experiment
41 intel iMotes distributed at Infocom (50, lost few:)
  182 external devices
  22459 contacts between iMotes
  5791 contacts between iMote/external device
  External devices are non-iMote devices in the environment, e.g. BT mobile phone, Laptop.
Notes: Before the explaining of the data, I want to first explain the term external address. As we know the iMotes will record the devices in the environment includes both iMotes address and other address. So these addresses except iMote are classified as external address, they maybe BT mobile phones and Laptop. And we can see that there are much more contact between iMotes than between iMotes and external addresses.

## Slide 6: Contact and Inter-contact time
Inter-contact is important
  Affect the feasibility of opportunistic network
  Nature of distribution affects choice of forwarding algorithm
  Rarely studied
Notes: Let’s zoom in the picture on page 13, we can see that the contacts between two nodes are sparsely distributed. The solid line in the above plot represent the blue dots in the previous contacts diagram. Between the solid lines are some empty spaces. So we say in the daily life, two persons may meet each other then go away and then meet again some other time. The time they can see each other, or we say within a contact range, is called the contact time. Contact time determine how much data two devices can transfer between each other, but which is also heavily depend on the bandwidth of transmission. Inter contact time is the time between two contact, it detemine how often a communication is possible. Shorter inter contact time means that the two people see each other quite often. If two person with short inter-contact time, then means that we can wait for next contact and send the data directly. If longer inter-contact time is observed, then need to rely on other media to transfer the data instead of waiting forever. In previous reseach, inter-contact is rarely studies. But we think this is a important parameter need to be seriously studied.

## Slide 7: Contact and Inter-contact Distribution
Contacts
Inter-contacts
Notes: These two graphs are the log-log distribution of time and probability. The x-axis shows the time in log scale and the y-axis show the probablity in log sclae. Let look at the point of (10 mins, 0.1), it means that the probability of contact time larger 10 minutes is 0.1 Both graph has a green line and a red line. The green line shows the distribution for an iMote and the red line shows the distribution for a external address. We can see that both the contact time and the inter-contacts time follow a heavy tail log-log distribution, or we can call it a approximate power law distribution. Let’s look at the figure on the right handside, both the imote and exernal address has a power law coefficient of 0.4 as show by the blue line. One day, two day, three day, the cut-off is limited by the duration of experiment.

## Slide 8: What do we see?
Power law curve for contact and Inter-contact time
  Both iMotes and external nodes
  Does not agree with currently used mobility model, e.g. random way point
Power law coefficient < 1
Notes: Our observation here does not agree with the currently used mobility model such as the random way point, which assume an exponential decay for the inter-contact time. This make the human mobility behaviour very different.

## Slide 9: Implication of Power Law Coefficient
Large coefficient => Smaller delay
  Consider 2-hops relaying [tse/grossglauser]
  Analysis [Chaintreau]
Denote power law coefficient as 
For > 2
    Any stateless algorithm with finite expected delay.
For > (m+1)/m and #{nodes} ≥2m :
    forwarding algorithm with m copies and finite expected delay.
For < 1
    No stateless algorithm (even flooding) with bounded delay
Notes: Now we know that human inter-contact time follows an approximate power law. But how the power law coefficient affect the forwarding algorithm? In general, we can say, the larger the coefficient, the smaller the delay. But if we consider a more detail sceneria, we can look at a 2-hops relaying algorithm as analysised in our technical report. The detail of the two relay scheme can be find in [tse/grossglauser] or in our technical report.

## Slide 10: Data from many other sources same
Results above are general
  Dartmouth, UCSD, Toronto
  Large systems (500-5000 nodes)
Only one example of type of problem we encounter:
MANET routing and transport - see work by
  Christian Tschudin at Basel, et al on path density
  Ed Knightly at Rice et al on contention, scheduling in MANET

## Slide 11: Macro-view
Give it to me, I have 1G bytes phone flash.
I have 100M bytes of data, who can carry for me?
I can also carry for you!
Thank you but you are in the opposite direction!
Don’t give to me! I am running out of storage.
Reach an access point.
Internet
Finally, it arrive…
Search La Bonheme.mp3 for me
Search La Bonheme.mp3 for me
Search La Bonheme.mp3 for me
There is one in my pocket…

## Slide 12: Reality could be so much better
Keshav, Hotnets couple of years back, by 2009
  “we’ll be throwing away 1 billion cell phones per year”
  Many new approaches to mitigate:
  Multi-hop, ultra-wideband CDMA, with network coding
  Could provide most world’s capacity and connectivity
  Multiple (overlapping) wireless VPNs
  Context based computing/Exposure to risk/Containers
  Need to have a big picture architecture
Why does this need a new architecture?

## Slide 13: What is the Wireless Systems Interconnection architecture? (software side!)
Encumbered by layered communications models
Inherited from long history of software eng.
  Abstraction & Virtualization - e.g.
    Hardware->Instruction Set->Assembler->C->Ocaml->HOL
  Modularization/Separation of concerns
  “Natural” mapping to a graph
Wire-line networks as a graph
  Added wireless at the edge, so treat as new link type
  Extremists say “make all links look like Ethernet”

## Slide 14: Remember OSI
The seven layers

## Slide 15: Forget OSI
Sad attempts to do “cross-layer optimization”
  PR Kumar cautionary tale:
  We have physical, link, net and transport/application layer routing
  power/capacity management in all “layers”
  Congestion/error aware transport
  coding aware (modem aware codecs) applications
  Steerable antennae, moveable drones, popular users
  Spaghetti and instability
A mess - cannot choose an order to apply

## Slide 16: Challenge - what could a newarch really be?
Are there novel software systems inputs?
Composition/Abstraction tools maybe more mature
  Moved beyond stacks, heaps, layers:-)
  E.g. Reflection, Aspect, HOL etc (c.f mira mezini’s challenge)
How to embed wireless world in a new abstraction?
  Interdisciplinary:
  Need to talk to RF engineers, information theoreticians, graph theory, control theory, etc etc

## Slide 17: Didn’t my micropicture say this is dead end?
Yes, data said won’t work yet in practice
  due to low density of nodes +
  lack of interaction with fixed (classic) infrastructure
But, can work
  If we increase number of nodes (happening), or the range/reachability, and use network coding…
  Or choose nodes to forward carefully, we can get bounded delay forwarding.
Especially if we also interwork via infrastructures
  AP’s to Internet and/or 3G=>
  hyperspace shortcuts between MANET and DTN pockets.

## Slide 18: Subsidiary problems
Architecture requires cooperation far beyond p2p
  Not just use of uplink during my downlink mp3 get
  Use of battery, storage, etc
Also risk from exposure is exponentially worse
  Wire-line Internet attacks due to any-to-any
  are at least constrained to go “down a wire”
    Already getting bad enough:-(
    Traceability feasible
    Multi-hop net code rules this out possibly completely
  Context of any and all devices now global

## Slide 19: Butterfly Effect Plagues
C.f. Alvisi, Syverson challenges here…
  Zero tolerance for some security and reliability problems
  Bug impacts the World from anywhere, anytime (martini bugs? :-)
  Butterfly in Beijing cause Levee to break in New Orleans
  Smartphone in Athens causes Freeway Snarl in Shanghai
A few fun problems to be going on with…

## Slide 20: Any questions?
I have some, if you don’t :-)

## Slide 21: Contacts seen by an iMote
iMoites
External Devices
Notes: We have mentioned that a imote will record the contact information of (Mac address, start time, end time). Let’s go into an iMote and see what is actually inside it. We extract the data from one imote and plot it on a graph. The x-axis of the graph shows the time of the day and the y-axis shows the node ID, since we have promised the participants to keep all information anormous so we will not plot out the Mac addresses of the devices and motes discovered, we give each device a number for indication. On the graph, each blue dot representate a contact. We can see the contacts are quite sparsely distributed, with more contact between the motes than the external devices. One the left figure, we have an interesting observation. The mote see node 28 every night and they stay together the whole night. We can say that these two persons share the same room or live in the next door.