## Slide 1: Network Architecture Research Considerations Or The Internet Conspiracy
Jon Crowcroft (University of Cambridge)
Jon.crowcroft@cl.cam.ac.uk
http://www.cl.cam.ac.uk/~jac22

## Slide 2: Why we shouldn’t do network arch?
Liberally borrowed slides from Mothy Roscoe (ex cambridge, sprint, intel, berkeley, oz, now ETH) and Steven Hand (Cambridge, Ericsson, Sprint)
  Post-modernism (Wenjun Hu, Jon, Mothy)?
  No to FIND/GENI? - n.b. my abstract’s comments(*)
Experience
  Architectures emerge (ANSA/Herbert)
  Papers about them are usually post-hoc rationalisations
First, general Arguments
Then specific (Haggle) example…

## Slide 3: Why have an architecture?
What does an Internet Architecture hope to achieve?
  Interoperability across networks
  Easier for applications to code to
  Framework for providers to compete
Does any Internet architecture really address these issues?

## Slide 4: What is a Network Architecture?
Choose Paradigm
  Given Physical constraint
    Packet/circuit/new(e.g. multihop radio)?
  Fundamentally is net a “graph”?
  Are protocols/services “layered”?
Choose Functional Decomposition
  Trade between packet header and node
    Choose stateless or stateful (e2e v. hbh)
    (e.g. change trade to include transport:
    can do NAT, Header Compression and QoS/Flows)
  Are nodes different (host v. router)?
  Choose Packet Format(s)

## Slide 5: What has the “Internet Architecture” done for us lately?
Interoperability:
  No – not really
Uniform API:
  Bad thing: hides useful features of the underlying network.
  c.f. cross layer optimisations and other oxymorons
Provider framework:
  Has any tier-1 ISP ever made significant profit from offering IP service?
  Net Neutrality Debate etc etc

## Slide 6: What has the “Internet Architecture” done for us lately?
It used to enable rapid innovation
Claim: lack of attention to value flow & economics was a Good Thing!
  High commercial value blunts innovation (c.f. other industries)
  Disruption is bad for business
Idea: goal of networking research should be to enable surprising things

## Slide 7: One (incremental) view: Don’t Panic!
Congestion collapse!
  TCP congestion control
The backbone won’t scale!
  Traffic Engineering, DWDM
We’ll run out of address space!
  CIDR, NAT (and IPNL, 4+4, Triad, …)
Long fat pipes are under-used!
  Scalable TCP, HSTCP
Protocol stacks can’t keep up!
  Zero-copy I/O, TSO, …
TCP doesn’t work on wireless!
  Split-TCP, i-TCP
But what about security!
  Firewalls, Application-level filtering

## Slide 8: So everything’s ok then?
Well, no…
Many solutions are kludges
Many solutions are stop-gaps
  NAT for a billion cellular devices? a trillion sensors?
No management story whatsoever… and security really is a problem
In a nutshell:
  “The Internet: Just-in-time Engineering” (Anon)
  “The Internet has always just been saved from catastrophic failure” (M Handley)
  “The Internet is a triumph of human ingenuity over common sense” (S Hand)
That isn’t architecture, it’s sloppy building repairs!
Notes: Management – as 3rd speaker (TaeSaeng Choi, ETRI) mentioned – is pretty shit today.
Maybe move to autonomic stuff of some kind.

## Slide 9: One (purist?) view of network architecture
“Network Architecture”
Email
IM
Unreal Tournament
Email
IM
Unreal Tournament

## Slide 10: One (pluralist) view of network architecture
“Network Architecture”
Voice over GSM mobile phone
Skype P2P voice over IP

## Slide 11: Different (separatist/corrosive/layered) view of network architecture
“Network Architecture”
“Networking people”
“Systems people”

## Slide 12: A third way…post internet arch (“post” can bind to net or arch:)
Sidestep the whole purist/pluralist debate
Avoid an architecture completely
  It’s unnecessary
  It doesn’t address any problems
  It may be counterproductive
Let me give a detailed worked example from the Haggle Project :- IST-4-027918-IP

## Slide 13: The alternative
There is no architecture
  Just a bunch of computers with links
  Removes “semantic bottleneck” from application writers
Embrace “radically heterogeneous networking”
  Two end-systems should be able to communicate even if they have nothing in common: protocols, address realms, semantics.

## Slide 14: Surely something must be common?
Of course: but it is only the application.
  that what is common is that which is application-specific
Even DTN has single overlay architecture
  (bundle routing)

## Slide 15: By way of example: Haggle (== DTN bis): A framework for Networking Mobile Users
Wireline Networks: Solid
MANET: Liquid
Haggle: Gas
Manage Phase Changes between these – reality of wireless is that we need to move from
  Gas -> Solid
  Gas -> Liquid
More often than we previously realized

## Slide 16: Our approach: Haggle
Clean slate design of networking subsystem for mobile devices
Haggle: a layerless, but modular network architecture
  designed around the needs of mobile users
Aims:
  Allow applications to take advantage of all types of data transfer (neighborhood, infrastructure, mobility)
  Allow networking endpoints to be specified by user-level naming schemes rather than node-specific network addresses,
  Allow limited resources to be used efficiently by mobile devices, taking into account user-level priorities for tasks

## Slide 17: Design principles for Haggle (not an architecture, no no no:-)
Forward using application layer information
  De-layer
Asynchronous operation
  Do not assume path
Empower intermediate nodes
  Do not separate host from router
All user data kept network-visible, and req/resp
  Tx==rx==store - all equal class functions
Exploit all data transfer methods
  Greed is good
Take advantage of brief connection opportunities
  Impatience is good
Empowered and informed resource management
  Know and tell what it costs

## Slide 18: Current device software framework
Interfaces
Delivery (IP)
Protocol
App logic + GUI
User Data
Application
Networking
File System
Synchronous, node-centric API
Isolated from network
App has two orthogonal parts
Delivery uses anonymous IP
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Haggle Overview
Clean-slate redesign of mobile node
Spans MAC to application layers (inclusive), but is itself layerless – uses six “managers”
API is asynchronous and data-centric
Store-and-forward architecture with data persisting inside Haggle not separate file sys
App-layer protocols (SMTP, HTTP, etc) moved into Haggle rather than apps themselves
Naming/addressing done in graphs instead of stacks
Resource management built-in
Haggle Application Interface
Applications (messaging, web, etc)
Protocol
Resource
Data
Name
Connectivity
Forwarding
Connectivities (WiFi, BT, GPRS, etc)

## Slide 20: Data Objects (DOs)
DO = set of attributes = {type, value} pairs
  Exposing metadata facilitates search
Can link to other DOs
  To structure data that should be kept together
  To allow apps to categorise/organise
Apps/Haggle managers can “claim” DOs to assert ownership
DO-Type | Data
Content-Type | message/rfc822
From | James Scott
To | Richard Gass
Subject | Check this photo out!
Body | [text]
DO-Type | Data
Content-Type | image/jpeg
Keywords | Sunset, London
Creation time | 05/06/06 2015 GMT
Data | [binary]
Message
Attachment

## Slide 21: Protocols
Protocols are methods for communicating with other nodes, including Haggle-specific protocols as well as legacy protocols (e.g. email)
Example: protocol to send an ADU over an ad-hoc WiFi connection given a neighbour’s MAC address
Example: protocol using keywords as addresses via Google – e.g. satisfy a query for “world news”
Legacy example: encapsulate an ADU in an email and send it using SMTP to an email address

## Slide 22: Delivery uses user-level names(ANA)
Plutarch, IPNL, RSIP etc etc etc
Names come from:
  Network, e.g. using neighbour discovery (12:AB:23:98:BE:FF)
  Applications, e.g. Jon Crowcroft » jon.crowcroft@cl.cam.ac.uk
Some names are also “addresses” i.e. data can be delivered to that name using one of the protocols available
Delivery engine needs to:
  Sense “nearby” addresses (e.g. Bluetooth inquiry gives MAC addresses, Internet connectivity means all email addresses are deliverable)
  Known-sender: Map between ADU’s destination name(s) and addresses of suitable next-hop nodes
  Known-recipient: Determine suitable nearby nodes which may be sources or help find sources for requested data
  Describe these potential transfers and their benefits to the resource manager

## Slide 23: Resource management using tasks
Task is a network activity
Resource management uses a list of tasks mainly provided by delivery engine
  E.g. perform discovery on interface I
  E.g. send ADU X to neighbour Y on interface Z
Each task has an associated benefit and cost
  Benefit is specified by task provider. May be time-dependent (i.e. using a pointer-to-function)
  To get cost, resource use is estimated, and then the “cost” is a function of the resource use * the resource scarcity
  Resource manager then schedules execution of tasks in order of highest benefit/cost ratio.

## Slide 24: So where are we?
Problem definition and some idea of solution
NOT architecture:- framework for others to use(Sourceforge)
  Others develop use cases
  Architecture will emerge from common uses
Other work we’ve done:
  Measurement/analysis of human connectivity patterns
  Measurement of in-motion wireless networking properties
Ongoing work in European project
  More measurement and analysis of possible data paths
  Implementation of modular software framework
  Addressing challenges of naming/addressing, forwarding, security/trust, usability, legacy compatibility

## Slide 25: Back to FIND/GENI & Architecture/Testbeds & EU v. US
As per my contentious (*) abstract:
  FIND and GENI are to fill a funding gap US has
  EU doesn’t have gap
  Architecture research is philosophy, not science or engineering
The devil is in the details, so:
  Let 1000 architectures bloom
World will pick a winner
  Some ego will declare it the new architecture and become
  The mother-in-law of the Next Generation Internet
FP7 should fund good communications systems research as usual.

## Slide 26: Questions?
Thank you…
Acknowledgements: James Scott, Mothy Roscoe, Mark Handley, Richard Mortier, Steven Hand, Keshav, Nick Feamster, Kevin Fall, for arguments about architecture, post modern or otherwise :-)

## Slide 27: EU Projects/Groupings
Arcadia
Cost action including 2 members per EU
Fire
  Onelab, etc - proposal stage
Eiffel
  FP7 IP just agreed
Alignement with US - weak, but present
National programs: UK JANET + Cambridge/UCL