## Slide 1: Exercise: Stack Data Buffer Overflow Introduction
CHERI offers architectural mechanisms for spatially-safe C.
  What does that mean? How does it work in practice?
📖 Exercise an inter-stack-object buffer overflow

## Slide 2: Exercise: Stack Data Buffer Overflow Introduction: Stack Layout
Straightforward buffer overflow:
Write OOB to lower & damage upper
C rules this undefined behavior
📖👩‍💻!
void write_buf(char *buf, size_t ix)
{
buf[ix] = 'b’;
}
int main(void)
{
char upper[0x10];
char lower[0x10];
printf("upper = %p, lower = %p, diff = %zx\n",
upper, lower, (size_t)(upper - lower));
/* Assert that these get placed how we expect */
assert((ptraddr_t)upper
== (ptraddr_t)&lower[sizeof(lower)]);
upper[0] = 'a';
printf("upper[0] = %c\n", upper[0]);
write_buf(lower, sizeof(lower));
printf("upper[0] = %c\n", upper[0]);
return 0;
}
lower[14]
lower[15]
upper[0]
upper[1]
…
…

## Slide 3: Exercise: Stack Data Buffer Overflow Discussion: So, what happened?
RISC-V Baseline
# ./buffer-overflow-stack-baseline
upper = 0x80d879d0, lower = 0x80d879c0, diff = 10
upper[0] = a
upper[0] = b
CHERI-RISC-V
# ./buffer-overflow-stack-cheri
upper = 0x3fffdfff50, lower = 0x3fffdfff40, diff = 10
upper[0] = a
In-address space security exception
Baseline CPU wrote to “16th” position in lower, aliasing upper
CHERI CPU trapped; kernel delivered fatal SIGPROT
How did the CHERI CPU know to do that?

## Slide 4: Exercise: Stack Data Buffer Overflow Discussion: gdb
Program received signal SIGPROT, CHERI protection violation
Capability bounds fault caused by register ca0.
0x0000000000101ce8 in write_buf (buf=<optimized out>, ix=<optimized out>) at ./buffer-overflow-stack.c:13
13 buf[ix] = 'b';
(gdb) disass
Dump of assembler code for function write_buf:
0x0000000000101ce0 <+0>: cincoffset ca0,ca0,a1
0x0000000000101ce4 <+4>: li a1,98
=> 0x0000000000101ce8 <+8>: sb a1,0(a0)
0x0000000000101cec <+12>: ret
End of assembler dump.

## Slide 5: Exercise: Stack data buffer overflow Discussion: Program .text
void foo(char *buf, size_t ix) {
buf[ix] = 'b';
}
int main(void) { // some lines elided
char lower[0x10];
write_buf(lower, sizeof(lower));
}
RISC-V 64
<write_buf>:
add a0, a0, a1
addi a1, zero, 98
sb a1, 0(a0)
ret
<main>:
addi sp,sp,-48
mv a0,sp
li a1,16
auipc ra,0x0
jalr -86(ra) # <write_buf>
CHERI-RISC-V 64
<write_buf>:
cincoffset ca0, ca0, a1
addi a1, zero, 98
csb a1, 0(ca0)
cret
<main>:
cincoffset csp,csp,-144
cincoffset ca0,csp,48
csetbounds cs0,ca0,16
cmove ca0,cs0
li a1,16
auipc ra,0x0
jalr -138(ra) # <write_buf>
Stores w/o bounds-checking branches
a0 holds address of buf on stack
bounds set at construction;
lower’s size persists in .text
ca0 holds capability to buf
Notes: Capability systems often appeal to “by construction” reasoning.
We can start to get a feel for this from the very basic C program you’ve just compiled and run.
Picking through the assembler listings gives the fragments shown, for baseline RISC-V 64 on the left and CHERI-RISC-V 64 on the right.
The first thing to note is that the stores (of ‘b’, or 98) to memory are identical modulo the use of an integer register vs. a capability register; no bounds-checking instructions are inserted at the use site.
In the baseline version, we see that the compiler simply passes a pointer to the stack by passing the address of a stack location.
By constrast, in the CHERI version, the compiler inserts a “set capability bounds” instruction when the pointer to lower is constructed; later use of the resulting capability will have bounds checked by the processor and, here, will trap, as the access is out of bounds.
In the baseline version, the size of lower was erased during compilation. In the CHERI version, the compiler has generated instructions that preserve its knowledge of C semantics in the program text.