## Slide 1
VoShield: Voice Liveness Detection with
Sound Field Dynamics
1The Hong Kong Polytechnic University, Hong Kong SAR
2Xi’an Jiaotong University, China
Qiang Yang1, Kaiyan Cui1,2, Yuanqing Zheng1
INFOCOM 2023

## Slide 2: Voice assistant as a powerful tool
Voice assistants can perform daily tasks and even critical functions.
  Controlling home appliances
  Online shopping and payment

## Slide 3: Voice commands are not safe!
Voice commands are easily leaked.
Secret recording
Online media
Fake voice command
“Transfer $100 to Bob”

## Slide 4: Replay attack can pass voice verification
Current voice verification systems are vulnerable to replay attacks.
  The voice clip is originally from the same user.
Voice assistant
Attacker
Cloud server
Voice verification
“Transfer $100 to Bob”
Pass!

## Slide 5: VoShield: a liveness detection system
Empowering voice verification with liveness detection
  The voice clip is originally from the same user, but from a loudspeaker.
Voice assistant
Attacker
Cloud server
Voice verification
Liveness detection
“Transfer $100 to Bob”
Pass!
No!
VoShield provides two factor protection for voice assistants.

## Slide 6: VoShield vs. Existing work
Active
Passive
Actively transmitting signals to sense the motion of the human mouth
Wi-Fi
mmWave
Acoustics
REVOLT [Ubicomp’19]
Wivo [MobiHoc’18]
WISE [UbiComp’21]
…
Vocalprint [SenSys’20]
…
VoiceGesture [CCS’17]
Lippass [INFOCOM’18]
Silentkey [UbiComp’18] SONAR [UbiComp’20]
ChestLive[UbiComp’21]
…
 Extra hardware required
 Extra power consumption
 Harmful to babies and pets
Capture physiological features in voice
Voicelive [CCS’2016]
VoicePop [INFOCOM’19]
CaField [CCS’19]
…
 Short distance
 Fixed gesture
VoShield
 Long distance
 Different locations
Suitable for distant smart devices, such as smart speakers

## Slide 7: VoShield: basic idea
The replay attack is always conducted by a loudspeaker.
Key difference
  The size of the loudspeaker is stable and fixed.
  The size of the human mouth is dynamic and varied.
Human mouth
Loudspeaker
Liveness detection: whose aperture size is time-variant?

## Slide 8: Sound directivity and sound field
Sound directivity: sound is not radiated uniformly
Sound field: energy distribution caused by sound directivity
  Three dependent factors: size 𝑠, frequency 𝑓, and volume .
Different sizes 𝑠
Different frequencies 𝑓

## Slide 9: Changing size leads to a more dynamic sound field
Dynamic sound size
How to measure the dynamic level of the sound field?
Dynamic sound directivity
Dynamic sound filed
For a fixed frequency and volume, time-variant mouth leads to a more dynamic sound field.

## Slide 10: Measure sound field dynamics
See the dynamic level of sound energy with a microphone?
  Affected by the sound volume

## Slide 11: Measure sound field dynamics
See the dynamic level of sound energy with a microphone?
  Use to energy ratio of two microphones to remove the volume effect
Time-variant voice contents also cause the dynamics.
  Look at the energy ratio in the frequency domain
2 kHz
2 kHz
Window index
0
0
Sound Field Dynamics: the energy ratio in the frequency domain

## Slide 12: Sound Filed Dynamics (SFD): an example
Voice command: “OK, google”
The SFD spectrograms of loudspeakers exhibit clear “strip” patterns.
Loudspeaker
Human

## Slide 13: Data augmentation
Enhance the representation diversity
  Voice content: ‘Strip’ pattern may appear at different locations
  Voice speed: ‘Strip’ pattern may be stretched or compressed
Horizontal & vertical translation and scaling
Vertical stretching and compression
Speed diversity
Content diversity

## Slide 14: Liveness detection
Learn strip patterns in SFD spectrogram with deep learning models
Fuse multiple microphone pairs: a self-attention mechanism
Samples in the latent space
time
pair
frequency

## Slide 15: Experiment
12 participants
Four loudspeakers
For each user
  Human-spoken voice commands: true
  Record-and-replay voice commands: false
Different locations, distances, orientations: 13,000+ samples

## Slide 16: Overall accuracy
Overall accuracy: 98.2%
Equal Error Rate (EER): 2%
False acceptance rate = False rejection rate = 2%

## Slide 17: Impact of distance and orientation
Accuracy remains 92.9% at 3 m.
Accuracy is 91.5% when users face backward to microphones.
More evaluation results in the paper …

## Slide 18: Conclusion and Takeaway
Voice assistants are vulnerable to replay attacks.
We propose VoShield to protect voice assistants against replay attacks at room-scale without relying on extra hardware.
We explore sound field dynamics to indicate voice liveness and hereby distinguishes between humans and loudspeakers.

## Slide 19
THANKS
Qiang Yang
qiangyang@polyu.edu.hk